Best Practices

Recommendations

Indexing

| Author | Translator | Tools Vendor |
| --- | --- | --- |
| The author should insert index entries immediately after the start tag of the nearest containing block element. If appropriate, the index entry should contain the range of text to be indexed ??? Some entries would have a smaller than block-level range .??? Note: page ranges for incorporation into DITA 1.2 | When index markers/tags are encountered within an element, the translation tools should generate a subflow . Well-configured XLIFF-based tools do this automatically. We'll need guidelines on suggested configurations. | When index elements are encountered, the tool should interpret the location of the container element for the index element as the parent element of the index element. DITA conversion/migration tools - if tool finds an index marker in the middle of an element, instead of at the beginning of an element, best practice is to move it to the beginning of the nearest containing translation segment boundary. |

-        author - *** need examples of these best practices, especially for <item> and <step> *** 
-        output processing -        translation tools - -        . 
-       page ranges for incorporation into DITA 1.2

Footnotes, alt text, draft comments, required cleanup

| Author | Translator | Tools Vendor |
| --- | --- | --- |
| The author should insert -- where ??? | When inline elements, footnote, alt text, draft comments, and required cleanup, are encountered within an element, the translation tools should generate a subflow . Well-configured XLIFF-based tools do this automatically. We'll need guidelines on suggested configurations. | When these elements are encountered, the tool should interpret the location of the container element for the inline element as the parent element of the element. ??? |