Public Review: Comments on Draft ETSI SR 019 020 V0.0.4 (2013-11)

Rationalised Framework of Standards for Advanced Electronic Signatures in Mobile Environment>

| Organization name | Clause/ Subclause | Paragraph Figure/ Table | Type of comment (General/ Technical/Editorial) | COMMENTS | Proposed change | OBSERVATIONS on each comment submitted |
| --- | --- | --- | --- | --- | --- | --- |
| OASIS TC DSS-X |  |  | General | The document is a good description of possible signing scenarios in mobile environments! But we miss the focus on the required building blocks of these scenarios. The blocks are shown in the diagrams explicitly ... why is there no further discussion on this granularity level? These blocks define the required (remote) interfaces and can be matched against existing interface definitions easily. Some of the interfaces are defined by DSS (the signature requesting interface and presumably the digest encryption unit), other may need to be defined. In our opinion all the scenarios can be implemented by an aggregation of local and remote instances of these interfaces. This would ease the aspect discussed in 5.4 (Applicability to General Computing Devices). |  |  |
| OASIS TC DSS-X |  |  | General | The aspects of verification should be discussed a bit more in detail. In analogy the the private key in signing the trust anchor is the crucial part of the verification. The selection of trust roots could vary widely in different scenarios. Sometimes a company / internal root must be used, sometimes a qualified root is required, and sometimes the browser-accepted root set will do. Should this be handled by verification policies? Or does the client match the verification result against his root set? Especially in the mobile environment it should be considered to have a special verification mode for any 'often verified' documents. For e. g. code snippets or apps it shouldn't be necessary to do a full-scale verification each-and-every time when there is a huge advantage of caching, especially on the mobile provider level. |  |  |
| OASIS TC DSS-X |  |  | General | Another topic that should be discussed is the privacy of the document. In analogy to the signing process a pre-hashed variant of the verification should be considered. A more paranoid aspect of privacy is the disclosure of the signer certificate. Maybe it's a valid use case to do basic signature verification locally and leave out the signers' certificate for remote checks. |  |  |
| OASIS TC DSS-X |  |  | General | We missed the aspect of trust setup (how to create trust regarding the different CA’s). |  |  |
| OASIS TC DSS-X | 3.1 Page 9 | Def mobile device | Editorial | The phrase ‘This is typically the tablet’. This might be confused with a signing tablet, only used to record the handwriting. (The icon used for this in the scenario's is a bit confusing.) If a handheld tablet is meant, such as an Apple iPad or MS Surface, a different icon should be used. (Figure 1 on page 13) |  |  |
| OASIS TC DSS-X | 3.1 Page 9 | Def mobile signature service | Technical | It tries to define the service but uses almost the same words. What does the 'mobile signing process' mean? | "Facility that coordinates and manages the process by which an end user can sign a document, or other information, using a mobile device.” |  |
| OASIS TC DSS | 4.1 Page 10 |  | Editorial | Under a) capital letters ‘M’ for Mobile |  |  |
| OASIS TC DSS | 4.2 | Under f) sentence “Note: Use of software for ….” | Editorial | Do you mean: "The use of secure signing software is not required by this standard." (emphasis on 'required' instead of 'supported'). |  |  |
| OASIS TC DSS | 4.3.1 Page 11 | Sentence “Throughout this clause the term “digital signature value” refers to the result of” | Editorial | This sounds like a definition of digital signature value, but it differs from the actual definition. | Extend the definition? |  |
| OASIS TC DSS | 4.3.1 Page 11 | Sentence For generation the set of scenarios range from those where | Editorial | Strange sentence. Reformulate…? | "To generate the set of scenario's, ranging from..." |  |
| OASIS TC DSS | 4.3.2.2 Figure 1 Page 13 | Use of icons | Editorial | The icons that are used, for instance for the MSSP and tablet give the wrong impression. |  |  |
| OASIS TC DSS | 4.2.2.3 | Title | Editorial | Should the title exclude the words "or complete"? Because what does it mean? (Does it actually create scenario R3?) |  |  |
| OASIS TC DSS | 4.2.2.3 | First par. Phrase “the AdES structure is built by the MSSP. ” | Editorial | The title assumes something else as well: ‘the complete generation of AdES in mobile devices…’ |  |  |
| OASIS TC DSS | 4.2.2.3 Page 15 | First par. | Editorial | The term SCD is used but there is no definition given. |  |  |
| OASIS TC DSS | 4.3.2.4 |  | Technical | Does this clause also support a mobile device with an ‘app’ that contains the signing key? Section 5.4 states: "Only scenario L3 is specific to mobile devices, although variations of all the local scenarios (L1, L2, and L3) and potential options within the remote signing scenario R2 can require mobile devices connected to a mobile network". So, the other scenario's do not necessarily need a mobile device?? (I thought they were intended for mobile devices...) Is this scenario only applicable to mobile devices just because of the wireless icon, indicating by 'Mobile service'? By definition the Mobile device needs an antenna, so why is only L3 specific to mobile devices? Or is it assumed that mobile devices can be connected to something by means of a wire (suchg as USB cable)? This is not explicitely mentioned in the definition. |  |  |
| OASIS TC DSS | 4.3.2.4 Page 16 | Paragraph below figure 3 | Editorial/Technical | Is it the SIM that generates the AdES? Could it also be an application on the device? |  |  |
| OASIS TC DSS | 4.3.2.4 Page 16 | 2nd par. Sentence: For example, the mobile device may generate only a digital signature, leaving extension to an AdES to the signing server. | Editorial/Technical | Are you referring to other scenario's than the scenario's of the previous sections? This alternative sounds like scenario R2... |  |  |
| OASIS TC DSS | 4.3.2.4 Page 17 1st par. | Sentence: ‘..meaning that the signing key may have to be stored in another (secure) environment.’ | Technical | What is meant by ‘another (secure) environment’? Do you refer to the 'remote device' (the one that it not held by the user, but contains the private key and is located in another (secure) environment. This is actually another scenario: one where the SCD is NOT part of the mobile device. |  |  |
| OASIS TC DSS | 4.3.3.1 | Sentence The following scenarios are where the AdES is created using a using a signing key… | Editorial | Please rephrase |  |  |
| OASIS TC DSS | 4.3.3.2 Page 18 6th par. | Term SDO | Editorial | What is an “SDO format”? |  |  |
| OASIS TC DSS | 4.3.3.2 Page 18 8th par. | Sentence: The authentication of the user to the signing service provider may involve an external identity provider. | Technical | In some cases the SSP will initiate the authentication (the current scenario assumes that the authentication is done before the request is sent to the SSP). |  |  |
| OASIS TC DSS | 5.3 Page 29 | Sentence EN 319 431 For remote signing s | Editorial | Rephrase ‘are not subject to the open to hostile attack .’ |  |  |
| OASIS TC DSS | 4.2 |  | Editorial | The wording should be improved. For instance “a) Whether document created on to the mobile…” |  |  |
| OASIS TC DSS |  |  | Editorial | Sometime the term ‘digital signature’ is used but usually (?) ‘digital signature value’. |  |  |
| OASIS TC DSS |  |  |  |  |  |  |
| OASIS TC DSS |  |  |  |  |  |  |
| OASIS TC DSS |  |  |  |  |  |  |
| OASIS TC DSS |  |  |  |  |  |  |
| OASIS TC DSS |  |  |  |  |  |  |