From section 8.3,

The CollaborationProtocolProfile element is the root element of the CPP XML document.

The REQUIRED XML [XML] Namespace[XMLNS] declarations for the basic document are as follows:

The CPP/CPA namespace: xmlns:tp="http://www.oasis-open.org/committees/ebxml-cppa/schema/cpp-cpa-2_0.xsd",

The XML Digital Signature namespace: xmlns:ds="http://www.w3.org/2000/09/xmldsig#",

and the XLink namespace: xmlns:xlink="http://www.w3.org/1999/xlink".

The CollaborationProtocolProfile element contains a REQUIRED cppid attribute that supplies a unique identifier for the document. It MUST be a globally unique identifier, and MUST be changed whenever changes are made in the document.

NOTE:  The algorithm used for generating globally unique identifiers is implementation dependent. Several are openly defined, and privacy concerns (deriving from use of network interface MAC) should not be a concern in this context.

# From section  9.2

The CollaborationProtocolAgreement element is the root element of a CPA.   It has a REQUIRED cpaid attribute that supplies a globally unique identifier for the document. The value of the cpaid attribute SHALL be assigned by one Party and used by both.  It is RECOMMENDED that the value of the cpaid attribute be a URI. The value of the cpaid attribute SHALL be used as the value of the CPAId element in the ebXML Message Header[ebMS] or of a similar element in a  Message Header of an alternative messaging service.

NOTE:  Each Party might associate a local configuration record identifier with the cpaid attribute.

NOTE:  The algorithm used for generating globally unique identifiers is implementation dependent.