ebXML Messaging (2.0) Basic Interoperability Test Suite

Version 1.0

OASIS ebXML Implementation, Interoperability and Conformance Technical Committee

February 26, 2003

Status of this Document 4 ebXML Participants 4 Introduction 5 1 Summary of Contents of this Document 5 1.1.1 Document Conventions 5 1.1.2 Audience 5 1.1.3 Caveats and Assumptions 6 1.1.4 Related Documents 6 1.2 Objectives and Methodology 6 1.2.1 Interoperability Profiles 6 1.2.2 A Basic Interoperability Profile 6 1.2.3 Related Initiatives and Contributing Parties 7 1.3 Concept of Operation 8 1.3.1 Driving the Tests 8 1.3.2 Interoperability vs. Conformance 8 1.3.3 Asymmetric Testing 9 1.3.4 Application Contract 9 1.4 Minimal Requirements for Conformance to this Specification 9 2 Harness for MS Interoperability Testing 10 2.1 Architecture 10 2.2 The Test Service and its Actions 11 2.2.1 Test Service Actions 12 3 Test Cases for MS Basic Interoperability Profile 12 3.1 The Basic Interoperability Profile 12 3.2 MS-BIP Test Cases Specification 12 3.2.1 Test Case 1.1: No payload basic exchange 13 3.2.2 Test Case 1.2: Basic exchange with one payload 14 3.2.3 Test Case 1.3: Basic exchange with three payloads 15 3.2.4 Test Case 1.4: Basic exchange with Error message 16 3.2.5 Test Case 1.5: Simple Signed Exchange Using Certificate 17 3.2.6 Test Case 1.6: Synchronous Basic Exchange with one payload 18 3.2.7 Test Case 1.7: Acknowledgment exchange: Unsigned Data, Unsigned Ack 19 3.2.8 Test Case 1.8: Acknowledgment exchange: Signed Data, Signed Ack 21 3.2.9 Test Case 1.9: Synchronous Unsigned Acknowledgment exchange 22 3.3 The two Basic Interoperability Profiles Variants and Test Suites 23 3.3.1 The HTTP Basic Interoperability Profile 23 3.3.2 The SMTP Basic Interoperability Profile 24 4 Details of Test Material 24 4.1 Configuration of the Test Harness and MSH Implementation 24 4.1.1 MSH Config 24 4.1.2 CPA Data 24 4.1.3 Default Message Headers 27 4.1.4 Message Payloads 31 4.2 BIP Test Suite Script 31 5 Appendix A – Implementations of the Test Harness 42 5.1 The “Point-to-point” Test Harness Implementation: 42 5.2 The “Hub Driver” Test Harness Implementation: 42 6 Appendix B – Test Suite XML Script 43 References 44 Non-Normative References 44 Contact Information 45 Acknowledgments 45 The OASIS ebXML-MS Technical Committee would like to thank … 45 Disclaimer 45 Copyright Statement 45 Intellectual Property Rights Statement 45

Status of this Document

This document specifies ebXML interoperability testing specification for the eBusiness community.  Distribution of this document is limited to OASIS ebXML Technical Committee (TC) members only.

The document formatting is based on the Internet Society’s Standard RFC format converted to Microsoft Word 2000 format.

Note:  Implementers of this specification should consult the OASIS ebXML Implementation, Interoperability and Conformance Technical Committee (ebXML IIC TC) web site for current status and revisions to the specification 
(http://www.oasis-open.org/committees/ebxml-iic/ ).

This version

V1.0

This specification addresses conformance of the MS specification in:

V2.0 – http://www.oasis-open.org/committees/ebxml-msg/documents/ebMS_v2_0.pdf

Errata to this version

None

Previous version

None

ebXML Participants

The authors wish to acknowledge the support of the members of the OASIS ebXML IIC TC who contributed ideas, comments and text to this specification by the group’s discussion eMail list, on conference calls and during face-to-face meetings.

Co-authors and editors:

| Steve Yung | Sun Microsystems |
| --- | --- |
| Sinha Prakash | IONA |
| Matt MacKenzie | XML Global |
| Hatem El-Sebaaly | IPNetSolutions |
| Monica Martin | DrakeCertivo |
| Jacques Durand | Fujitsu Software |
| Michael Kass | NIST |

Contributors/reviewers:

| Rik Drummond | DGI |
| --- | --- |
| Eric VanLydegraf | Kinzan |
| Christopher Frank | SEEBURGER |

The OASIS ebXML IIC TC would like to especially thank the Drummond Group for their contribution to the test cases.

Introduction

# Summary of Contents of this Document

This specification defines a test suite for ebXML Messaging basic interoperability.  The testing procedure design and naming conventions follow the format specified in the Standard for Software Test Documentation IEEE Std 829-1998.

This specification is organized around the following topics:

Interoperability testing architecture

Test cases for basic interoperability

Test data materials

### Document Conventions

Terms in Italics are defined in the ebXML Glossary of Terms in the TestFramework specification [ebXMLTestFramework].  Terms listed in Bold Italics represent the element and/or attribute content.  Terms listed in Courier font relate to test data.  Notes are listed in Times New Roman font and are informative (non-normative).  Attribute names begin with lowercase.  Element names begin with Uppercase.

The keywords MUST, MUST NOT, REQUIRED, SHALL, SHALL NOT, SHOULD, SHOULD NOT, RECOMMENDED, MAY and OPTIONAL, when they appear in this document, are to be interpreted as described in [RFC2119] as quoted here:

MUST: This word, or the terms "REQUIRED" or "SHALL", means that the definition is an absolute requirement of the specification.

MUST NOT: This phrase, or the phrase "SHALL NOT", means that the definition is an absolute prohibition of the specification.

SHOULD: This word, or the adjective "RECOMMENDED", means that there may exist valid reasons in particular circumstances to ignore a particular item, but the full implications MUST be understood and carefully weighed before choosing a different course.

SHOULD NOT: This phrase, or the phrase "NOT RECOMMENDED", means that there may exist valid reasons in particular circumstances when the particular behavior is acceptable or even useful, but the full implications should be understood and the case carefully weighed before implementing any behavior described with this label.

MAY: This word, or the adjective "OPTIONAL", mean that an item is truly optional.  One vendor may choose to include the item because a particular marketplace requires it or because the vendor feels that it enhances the product while another vendor may omit the same item.  An implementation which does not include a particular option MUST be prepared to interoperate with another implementation which does include the option, though perhaps with reduced functionality. In the same vein an implementation which does include a particular option MUST be prepared to interoperate with another implementation which does not include the option (except, of course, for the feature the option provides).

### Audience

The target audience for this specification is:

- The community of software developers who implement and/or deploy the ebXML Messaging Service (ebMS),

- The testing or verification authority, which will implement and deploy conformance or interoperability testing for ebXML Messaging implementations.

### Caveats and Assumptions

It is assumed the reader has an understanding of communications protocols, MIME, XML, SOAP, SOAP Messages with Attachments and security technologies.

### Related Documents

The following set of related specifications are developed independent of this specification as part of the ebXML initiative, they can be found on the OASIS web site (http://www.oasis-open.org).

- ebXML Collaboration Protocol Profile and Agreement Specification (CPPA)  – CPP defines one business partner's technical capabilities to engage in electronic business collaborations with other partners by exchanging electronic messages. A CPA documents the technical agreement between two (or more) partners to engage in electronic business collaboration. The MS Test Requirements and Test Cases will refer to CPA documents or data as part of their material, or context of verification.

- ebXML Messaging Service Specification (MS)  – defines the messaging protocol and service for ebXML, which provide a secure and reliable method for exchanging electronic business transactions using the Internet.

- ebXML Test Framework – describes the test architecture, procedures and material that are used to implement the MS Interoperability Test Suite, as well as the test harness for this suite.

- ebXML MS Conformance Test Suite – describes the Conformance test suite and material for Messaging Services.

## Objectives and Methodology

### Interoperability Profiles

It is in general impossible to test all combinations of messaging features and configuration features for interoperability between two message handler implementations: the combinations – and possible failure scenarios - are in much greater number than those occurring in conformance testing, which typically focuses on a single message handler.

When testing interoperability, a small set of significant test cases must be selected. One way to do this selection is to observe what are the interoperability requirements of a user community, and to address them. Because of the “combinatorial” problem of features and scenarios, and also because it involves several business partners, interoperability testing usually must reflect the particular needs of a business community. This is in contrast with conformance testing, which mostly focuses on verifying adherence to the standard.

Interoperability tests should then focus on the kind of usage that is most meaningful for a business community. These forms – or modes - of interoperability are called profiles. An interoperability profile should be verified by an appropriate test suite.

### A Basic Interoperability Profile

This document specifies the Basic Interoperability Profile (BIP) for ebXML messaging. As its primary objectives, this profile defines the baseline of business interoperability (it exercises basic ebXML MS core services, secure and reliable messaging). This profile may not be sufficient to address all the business requirements of a user community: Specific requirements – for example, using very large messages, or security features such as encryption - will be addressed by additional, more specific profiles that expand on basic functions or combinations of functions relevant to user communities.

Users or industry groups will design these additional interoperability profiles, if these are not already specified in the test suites produced by the ebXML IIC Technical Committee. In order to be conforming to the IIC testing guidelines, any new messaging interoperability profile definition MUST:

Include the Basic Interoperability Profile (i.e. extend it)

Be described using the test material (test case scripting, test architecture) specified in the ebXML Test Framework.

The number of test cases for the Messaging BIP is relatively small (as compare to the number of test cases for the conformance test suite.) This is intentional, to enable interoperability and lower the cost of entry of testing. This is because:

Interoperability testing requires more efforts in logistics, as coordination between parties is required.

As interoperability may be affected by several factors such as operating environment, third-party software or utilities, testing should be done under normal operating conditions. This creates constraints and disturbance for business.

### Related Initiatives and Contributing Parties

In accordance with the notion that interoperability testing should be aligned with business requirements – more than conformance testing -, some user communities have been consulted by the IIC TC in order to establish a minimal, yet universal set of messaging interoperability requirements.

In US, UCC (Uniform Code Council) and DGI (Drummond Group, Inc.) have been conducting ebXML interoperability test rounds between several ebXML vendors. The requirements of  UCC-DGI tests have been studied, and after investigation, a subset of test cases defined by UCC-DGI have been used as an input for the Basic Interoperability profile test cases.

In Asia, ECOM (E-Commerce consortium of major Asian IT vendors and government agencies) has also organized ebXML interoperability testing rounds. The requirements of this community of users have also proved valuable and have been taken into account for the Basic Interoperability profile.

In Europe, eBES is a forum for IT vendors and users, focusing on business-to-business and interoperability testing. The group is also organizing ebXML testing, and has provided useful feedback to IIC, in particular about their implementation plan and test harness requirements.

The Basic Interoperability Profile (BIP) is the result of this consulting, and is addressing a common set of interoperability requirements. This common set may not cover every interoperability feature that each community requires, but is quite close and reasonably complete.  We noticed that the test plans in these industry initiatives also included both interoperability tests and (some) conformance tests. The IIC approach is to clearly separate test suites for conformance, and test suites for interoperability. One reason the BIP has a smaller number of test cases is that only the tests relevant to interoperability have been kept. Other tests relevant to conformance have been moved to the MS conformance test suite. By doing so, the cost of operating an interoperability test suite is reduced, as conformance should normally be verified prior to interoperability, by a testing procedure that does not require coordination with other parties.

## Concept of Operation

### Driving the Tests

The MS interoperability test harness described in this document is based on the ebXML  Test Framework [ebXMLTestFramework], described in another document. This test harness is assumed for testing the Basic Interoperability Profile, and has been designed to achieve the following objectives:

- The MS Interoperability Test Suite can be run entirely and validated from one component of the framework, called the Test Driver.  This means that all test outputs will be generated - and test conditions verified - by the Test Driver, even if the test harness involves several – possibly remote – components of the framework. Significant events occurring in such components are supposed to be communicated in some way to the Test Driver.

- The verification of each Test Case can be done at run-time by the Test Driver itself, as soon as the test case is completed.  The outcome of the verification can be obtained immediately as the Test Suite has completed, and a report be generated.

### Interoperability vs. Conformance

It is expected that some level of conformance testing be done prior to interoperability testing.  For example, the interoperability test does not verify or diagnose the following:

Invalid SOAP header and message

Invalid ebXML information in SOAP header and message

CPA Error and Resolution

Unrecognized service

Duplicate messages

Simple error handling

All the tests above are defined in the ebXML Messaging conformance test suite, and are supposed to be passed prior to undergoing interoperability tests.  If only from a logistic perspective, it is preferable to do as many verifications as possible during conformance testing, which typically involves a single message service handler (MSH), and is much easier to set-up than interoperability testing.

In other words, any MSH behavior that can be verified in a test harness that includes a single MSH (plus a test driver simulating another MSH) is relevant to conformance.  Any MSH behavior that requires an exchange between two MSH’s for verification is relevant to interoperability.  Because organizing interoperability tests (administration and logistics) is usually associated with a high cost, only those tests that are really essential to interoperability are considered here.

### Asymmetric Testing

The basic interoperability test suite defined here, is intended to be driven from one party (or node) of the network, called the “driver party” (this is the party that includes the Test Driver).  As it involves two parties, it is called a “binary” test suite.

The test suite is asymmetric.  This means, when run between two parties A and B,  the same test suite may produce different results when driven from A (driver party = A) than when driven from B (driver party = B). For example, a test case that requires a party to sign a message, and the other party to validate the signature, may succeed from A to B, and fail from B to A. This is because the test cases in this suite do not verify exactly the same capability on each side.

In order to achieve a well-rounded interoperability testing, a binary, asymmetric interoperability test suite is supposed to be run twice.  At each run, a different party acts as the driver party.

### Application Contract

The test suites described here – in their current version - are testing interoperability at application level only, not at “wire” level. This means that the combination:

{ MSH1 + communication medium(transport) + MSH2 }

is treated as a black box.  The test cases only verify that the contract Application1 – Application2 is satisfied.  For example, no “sniffing” on the wire is needed in order to process these test cases, as everything related to the internal behavior of an MSH, or message conformance at transport level, is supposed to have been verified by conformance testing.

For example, when verifying that a digital signature is:

- well inserted by the sender, when the CPA requires so, and

- that the recipient is able to validate it, should not require monitoring the wire or the internal behavior of an MSH, during interoperability tests.

Testing for (a) should have occurred during conformance tests, which involve monitoring the “wire” for conformance of message elements such as a well-formed signature.  As for recipient validation (b), only the effect of the “Service” behavior (application contract) will be checked: i.e. the received signed message is passed to the application, and no error is generated.

The other aspect of recipient validation (b), which consists of verifying the ability of the receiver to detect bad signatures and to act appropriately, is supposed to have been verified during conformance testing.

However, because there is an interoperability element to it, it can be reproduced in an interoperability suite.  In that case, the external behavior (i.e. the expected “service”) will be checked: a message will be sent signed with the wrong key.  On the receiver side, the effect should be that the message is not passed to the application, and an error will be generated.

## Minimal Requirements for Conformance to this Specification

An implementation of this specification MUST satisfy ALL of the following conditions to be considered a conforming implementation:

It supports all the mandatory syntax, features and behavior (as identified by the [RFC2119] key words MUST, MUST NOT, REQUIRED, SHALL and SHALL NOT) defined in Part 1.1.1 – Document Conventions.

# Harness for MS Interoperability Testing

## Architecture

This section describes how to configure the Test Framework elements for testing interoperability between two implementations of the ebXML Messaging Service specification (2.0), identified here as party A and party B.

As mentioned above, interoperability testing will be asymmetric: one party – called the driver party – will drive the test cases, the other party – called the responder – will respond to messages initiated by the driver party. Two options for the interoperability test harness are described in Appendix A. This section will focus on the “point-to-point” test harness. With this test harness, the Test Suite will be controlled from the “driver” party, and does not necessarily verifies the same capabilities on both sides i.e. is asymmetric). In order to get a full interoperability test between Party A and Party B, the test suite should be repeated after both parties have swapped the (driver/responder) roles.

The components of the framework that are involved in interoperability testing are:

On the driver party:

An instance of the Test Driver component, coupled with an instance of a Test Service. This coupling consists of: (1) the ability for the Test Driver to trigger an action of the Test Service (typically, the Initiator action), (2) the ability for the Test Driver to be notified of actions triggered in the Test Service by received messages. In this configuration, the Test Driver is said to be used in “service” mode (see TestFramework specification). The driver party will process and initiate all test cases from the Test Driver.

An instance of the Test Service component, which will directly interact with the driver party’s MSH Service Interface. Note that the Test Driver does not need to interact directly with the MSH. In this configuration, the Test Service will operate in “reporting” mode. When installed on the same host, as suggested here, the reporting will be local: notifying the test driver of received messages is done via the “Receive” interface.

On the responder party:

An instance of the Test Service component (same as in the driver party), which will support test actions invoked by messages received by the responder MSH. This Test Service instance will operate in “loop” mode.

Figure 1 illustrates a point-to-pointtest harness for MS interoperability testing.

The typical Interoperability test case procedure will consists of a sequence of test steps.  The Test Driver will control each of these steps.  These steps will:

Sending messages – the content of which is specified in the test case – to some action of the responder’s Test Service.

Receiving messages from the responder’s Test Service.

Analyzing the content of received messages, possibly in correlation with other message data, received or sent during the same test case, in order to validate the requirement of the test case.

Reporting on the test case outcome.

Optionally (and prior to executing a test case), configure the MSH(s) for the message conversation(s) that will be generated by the Test Case(s), with CPA data. Normally, the installation of CPAs to be used for a test suite is supposed to be done prior to executing the test suite. However, the Configurator action of a Test Service may be invoked – either directly by the Test Driver on driver party, or remotely by a message on responder party-, with new CPA data. The expected effect is the dynamic creation and installation of a new CPA, on the MSH associated with this Test Service.

Appendix A illustrates how this test harness can be implemented.

## The Test Service and its Actions

The Test Service name is: urn:ebXML:iic:test

A Test Case is described as a sequence of Test Steps. These Test Steps will consist of atomic operations executed by the components of the test Framework, e.g. sending a message, verifying a condition on a received message, etc. Most operations about messages are supported by the Test Service component, described in the Test Framework specification.

In the following, the “requestor” represents the party that originates the message that triggers the action in the remote (or responder) MSH. The requestor is usually the driver party, where the Test Driver resides.

### Test Service Actions

The standard test actions are more completely described in the ebXML Test Framework specification. They are:

- Mute action

- Dummy action

- Reflector action

- Initiator action

- PayloadVerify action

- ErrorAppNotify action

- ErrorURLNotify action

- Configurator action

# Test Cases for MS Basic Interoperability Profile

## The Basic Interoperability Profile

The ebXML MS basic interoperability profile (ebMS-BIP) is intended to be protocol independent. However, for interoperability, the protocol must be specified. ebMS-BIP is parameterized by the transport protocol. Considering either HTTP or SMTP as protocols, we have two instances of the Basic Interoperability Profile:

MS-BIP(“HTTP/1.1”) for HTTP1.1

MS-BIP(“SMTP”), for SMTP

In a nutshell, the MS-BIP is verifying:

Various types of messages are exchanged: no payloads, multiple payloads, different types of payloads.

Asynchronous responses (as well as Synchronous over HTTP connections).

All signals normally expected from an MSH (Acks and Errors) are tested for interoperability, i.e. making sure the other MSH will “understand” them properly. (the “conformance” semantics of these signals has already been tested during conformance testing, e.g. they manifest as well-formed envelope elements, or they are generated when they should.)

When digital signatures are used, they must be properly understood and validated on each side, especially with various combinations and options that may affect interoperability (about key info, about signature of signals such Ack.)

## MS-BIP Test Cases Specification

The following test cases are specified using test material described in the ebXML TestFramework specification. The test data used (CPAs, default message headers, payloads, configuration) is described in section 4.

### Test Case 1.1:  No payload basic exchange

Rationale:

The test case verifies that an incoming message is well received and triggers the correct action on Responder side. There is no check of the integrity of the received message, except its ability to trigger the Dummy action of the responder Test Service.  A predefined response message (no payload) is generated by the Test Service of responder. There is no check on this message, except its ability to trigger the Mute action of the driver Test Service, which will record the reception.

Test Data Material:

CPAId: urn:config:cpa_basic

MSH-configuration: mshc_1

Message Payloads: none

Message Header default: mhdr_0

Suggested Conversation ID: 10101 (101 = 1.1)

Test Steps:

- Test Driver (driver party) sends a sample message M1 to the Dummy action of the Test Service of the responder party. This is done by invoking the Initiator action of the driver party Test Service.

- Test Driver (driver party) receives within time limit a response message M2 via the Mute action of its local Test Service (sent by Dummy action of Responder). Correlation: (M2.RefToMessageID = M1.MessageId) and (same conversation ID).

- Verification. Test Case succeeds if: (Step 2 successful within time limit)

### Test Case 1.2: Basic exchange with one payload

Rationale:

The test case verifies that an incoming message is well received, triggers the right action on Responder side, and passes its payload to application (Reflector action of Test Service). A response message is generated by the Test Service of responder (Reflector action), sending back the same message - except for expected changes in header - with same payload. The received message triggers the Mute action of the driver Test Service, which will record the reception. The received payload is compared with the payload initially sent.

Test Data Material:

CPAId: urn:config:cpa_basic

MSH-configuration: mshc_1

Message Payloads: payload_1

Message Header default: mhdr_1

Suggested Conversation ID: 10102. (102 = 1.2)

Test Steps:

- Test Driver (driver party) sends a sample message M1 to the Reflector action of the Test Service of the responder party.

- Test Driver (driver party) receives within time limit a response message M2 via the Mute action of its local Test Service (from Reflector action of Responder). Correlation: (M2.RefToMessageID = M1.MessageId) and (same conversation ID).

- Verification. Test Case succeeds if: (Step 2 successful) AND (M2.payload = M1.payload)

### Test Case 1.3: Basic exchange with three payloads

Rationale:

The test case verifies that an incoming message with multiple payloads of different types  (two XML, one binary) is well received, triggers the correct action on Responder side, and passes its payload to application (Reflector action of Test Service). A response message is generated by the Test Service of responder (Reflector action), sending back the same message - except for expected changes in header - with same payloads. The received message triggers the Mute action of the driver Test Service, which will record the reception. The received payloads are compared with the initially sent payloads.

Test Data Material:

CPAId: urn:config:cpa_basic

MSH-configuration: mshc_1

Message Header default: mhdr_3

Message Payloads:  payload_1,  payload_2,  payload_3

Suggested Conversation ID: 10103

Test Steps:

- Test Driver (driver party) sends a sample message M1 to the Reflector action of the Test Service of the responder party.

- Test Driver (driver party) receives within time limit a response message M2 via the Mute action of its local Test Service (from Reflector action of Responder). Correlation: (M2.RefToMessageID = M1.MessageId) and (same conversation ID).

- Verification. Test Case succeeds if: (Step 2 successful) AND (M2.payload1 = M1.payload1) AND (M2.payload2 = M1.payload2) AND (M2.payload3 = M1.payload3)

### Test Case 1.4: Basic exchange with Error message

Rationale:

The test case verifies that error messages are well received by the driver party. The driver party should provide its URL as ErrorURL, as mandated by the CPA “basic_A1”. The test does not cover that errors are generated with the right code: that is done by conformance tests. A “bad” message is sent to the Dummy action of the responder Test Service. The responder MSH should send back an Error, which should be notified to the sender (driver party) via its ErrorURLNotify action, which will record the reception.

Test Data Material:

CPAId: urn:config:cpa_basic

MSH-configuration: mshc_1

Message Header default: mhdr_1

Message Payloads: payload_1

Suggested Conversation ID: 10104

Test Steps:

- Test Driver (driver party) sends a sample message M1 to the wrong action of the Test Service of the responder party. In the message header, the Service/Action fields are set to inexisting Service/Action values.

- Header modified: mhdr_1’ <here, introduce the error by modifying header  Service/Action in default mhdr_1>

- Test Driver (driver party) receives within time limit an error message M2 via the ErrorURLNotify action of its local Test Service. Correlation: (M2.RefToMessageID = M1.MessageId).

- Verification. Test Case succeeds if: (Step 2 successful)

### Test Case 1.5: Simple Signed Exchange Using Certificate

Rationale:

The test case verifies message exchange with digital signature (without key info). The key info is NOT embedded in the message, it is available on recipient side from a certificate. This case exercises the ability to resolve the key info based on the right certificate. It is not essential for the response to be signed, although the CPA setting will require so for the convenience of having similar configurations on each party  (the ability to sign messages from the other party, will be tested when running the same test case from the other party, as the test suite is asymmetric, see Section 1).

Test Data Material:

CPAId: Urn:config:cpa_basic_signed  (with Signature set to Yes)

MSH-configuration: mshc_2

Message Payloads:  payload_1

Message Header default: mhdr_1

Suggested Conversation ID: 10106

Test Steps:

- “Initiator” on driver side sends signed message to Reflector action of recipient. The entire message is signed.

- “Mute” action on driver side receives (unsigned) notification message from Reflector, with same payload.

- Verification: (payloads are same) and (no error message received)

### Test Case 1.6: Synchronous Basic Exchange with one payload

Rationale:

This is the synchronized version of Test Case 1.2 (SyncReply element is present in sent message).  This test case is for synchronous transport only (HTTP).

Test Data Material:

CPAId: Urn:config:cpa_basic_syncresponse (with syncReplyMode set to “signalsAndResponse”)

MSH-configuration: mshc_1

Message Payloads:  payload_1

Message Header default: mhdr_1

Suggested Conversation ID: 10107

Test Steps:

- Test Driver (driver party) sends a sample message M1 to the Reflector action of the Test Service of the responder party.

- Test Driver (driver party) receives within time limit a response message M2 via the Mute action of its local Test Service (from Reflector action of Responder). Correlation: (M2.RefToMessageID = M1.MessageId) and (same conversation ID).

- Verification. Test Case succeeds if: (Step 2 successful) AND (M2.payload = M1.payload)

### Test Case 1.7: Acknowledgment exchange: Unsigned Data, Unsigned Ack

Rationale:

Test the ability of two MSHs to exchange and understand each other’s ack signals.

Test Data Material:

CPAId: Urn:config:cpa_basic_reliable 
(At sending MSH: Retry turned ON, ) 
(At receiver MSH: No duplicate check)

MSH-configuration: mshc_1

Message Payloads: payload_1

Message Header default: mhdr_1 (add Acknowledge element)

Suggested Conversation ID: 10108

Test Steps:

- “Initiator” on driver side sends unsigned message to Dummy action of recipient, with AckRequested element.

- “Mute” action on driver side receives a single (unsigned) response message from Dummy. NOTE: in case Ack is not received or understood, driver MSH will resend message of step 1, and several responses from Dummy will be observed.

- Verification: (exactly  ONE  response message from Dummy is received in Step 2) and (no error message received)

Note: because Acknowledgements are MSH-level signals, it is not possible to observe them from the application side. However, the objective of this test is not to verify the proper generation of well-formed Ack signals: this must have previously been verified using conformance tests.

The objective of this test only consists of verifying that Acks generated by an MSH are well interpreted by the other MSH implementation. In order to do this verification, it is sometimes necessary to check the log of the sender MSH, to verify if an Ack was received. In case the Ack was not well received or understood by the sender, two situations may occur:

- The sender MSH will resend the same original message (M1), causing multiple invocations of the Dummy action on receiver side, which in turn will cause several responses (M2) to be notified to the Test Driver. This would be detected at application level (Test Service of the driver), as in figure below.

- The sender retry mechanism is not working properly, so no multiple invocations of the Dummy action on receiver side will occur – only the initial invocation. In that case, a single response will be observed on sender side, which is also the observed effect in case of successful verification. Therefore, the only way to detect such a failure, is to “manually” access the log of the MSH to ensure the Ack was well received. It must be noted that this case should be considered as exceptional, since the ability to resend is supposed to have been checked by conformance testing.

The failure case (a) above will translate into the following exchange:

### Test Case 1.8: Acknowledgment exchange: Signed Data, Signed Ack

Rationale:

Test the ability of two MSHs to exchange and understand each other’s signed ack signals (for non-repudiation), while the business messages are signed.

Test Data Material:

CPAId: Urn:config:cpa_basic_reliablesig 
(At sending MSH: Retry turned ON, set Signature to Yes)

MSH-configuration: mshc_1

Message Payloads:  payload_1

Message Header default: mhdr_1 (add Acknowledge element)

Suggested Conversation ID: 10109

Test Steps:

- “Initiator” on driver side sends a signed message to Dummy action of recipient, with AckRequested element.

- “Mute” action on driver side receives a single (unsigned) response message from Dummy. NOTE: in case Ack is not received or understood, driver MSH will resend message of step 1, and several responses from Dummy will be observed.

- Verification: (exactly  ONE  response message from Dummy is received in Step 2) and (no error message received)

### Test Case 1.9: Synchronous Unsigned Acknowledgment exchange

Rationale:

Test the ability of two MSHs to exchange and understand each other’s ack signals, in a synchronous set-up. The CPA will have SyncReplyMode set to “signals only”, so there is not overlap with Test Case 1.7.  This is a fairly common case where the HTTP connection is not kept open for business messages (for which response time may be long), but is kept open for MSH signals, for efficiency purpose. So the Ack is immediately sent back on the same connection as the message. . NOTE: The actual ability of the responder to send Acks on a same HTTP connection, based on CPA requirement, is assumed previously tested by conformance tests. Only the interoperability aspect of it is tested here.

Test Data Material:

CPAId: Urn:config:cpa_basic_reliablesync 
(At sending MSH: Retry turned ON) 
(At receiver MSH: No duplicate check)
(At both MSH, set Signature to Yes)

MSH-configuration: mshc_1

Message Payloads: payload_1

Message Header default: mhdr_1 (add Acknowledge element)

Suggested Conversation ID: 10110

Test Steps:

- “Initiator” on driver side sends unsigned message to Dummy action of recipient, with AckRequested element.

- “Mute” action on driver side receives a single (unsigned) response message from Dummy. NOTE: in case Ack is not received or understood, driver MSH will resend message of step 1, and several responses from Dummy will be observed.

- Verification: (exactly  ONE  response message from Dummy is received in Step 2) and (no error message received)

## The two Basic Interoperability Profiles Variants and Test Suites

### The HTTP Basic Interoperability Profile

The test suite is named: MS-BIP-HTTP, and verifies the Basic Interoperability Profile for messaging over HTTP. It includes synchronous and asynchronous test cases (9) which exercise the capabilities of HTTP. The Test Cases are:

- Test Case 1.1: No payload basic exchange over HTTP.

- Test Case 1.2: Basic exchange with one payload over HTTP.

- Test Case 1.3: Basic exchange with three payloads over HTTP.

- Test Case 1.4: Basic exchange with Error message over HTTP.

- Test Case 1.5: Signed Message Without Embedded Key Info over HTTP.

- Test Case 1.6: Synchronous Basic Exchange with one payload over HTTP.

- Test Case 1.7: Acknowledgment exchange: Unsigned Data, Unsigned Ack over HTTP.

- Test Case 1.8: Acknowledgment exchange: Signed Data, Signed Ack over HTTP.

- Test Case 1.9: Synchronous Unsigned Acknowledgment exchange over HTTP.

### The SMTP Basic Interoperability Profile

The test suite is named: MS-BIP-SMTP and verifies the Basic Interoperability Profile for messaging over SMTP. It includes only asynchronous test cases (7) which exercise the capabilities of SMTP. The Test Cases are:

- Test Case 1.1: No payload basic exchange over SMTP.

- Test Case 1.2: Basic exchange with one payload over SMTP.

- Test Case 1.3: Basic exchange with three payloads over SMTP.

- Test Case 1.4: Basic exchange with Error message over SMTP.

- Test Case 1.5: Signed Message Without Embedded Key Info over SMTP.

- Test Case 1.7: Acknowledgment exchange: Unsigned Data, Unsigned Ack over SMTP.

- Test Case 1.8: Acknowledgment exchange: Signed Data, Signed Ack over SMTP.

# Details of Test Material

## Configuration of the Test Harness and MSH Implementation

### MSH Config

#### mshc_1 (default)

Transport:

Protocol				HTTP 1.1

Timeout				300 sec

Security:				No support required

#### mshc_2

Transport:

Protocol				HTTP 1.1

Timeout				300 sec

Security:				Supported

### CPA Data

#### urn:config:cpa_basic (default) (for test cases 1.1, 1.2, 1.3, 1.4)

Transport:

Protocol				HTTP 1.1

SyncReplyMode:				None

Reliability:

Retry/Timeout

Receipt Acknowledgement:	Not required

Response:			Not required

Response Acknowledgement:	Not required (do we need this line? It is more business level, not MSH)

Duplicate Check :			None

Order:					No

Security:

Encryption:				No

Signature:				No

Non-Repudiation

Origin				Not required

Receipt				Not required

Multi Hop:					No

Error:

ErrrorURI:				<URI of driver party>

#### Urn:config:cpa_basic_signed (for test cases 1.5, 1.6)

Transport:

Protocol				HTTP 1.1

SyncReplyMode:				None

Reliability:

Retry/Timeout

Receipt Acknowledgement:	Not required

Response:			Not required

Response Acknowledgement:	Not required

Duplicate Check :			None

Order:					No

Security:

Encryption:				No

Signature:				Yes

Non-Repudiation

Origin				Not required

Receipt				Not required

Multi Hop:					No

Error:

ErrrorURI:				<URI of driver party>

#### Urn:config:cpa_basic_syncresponse (for test cases 1.7)

Transport:

Protocol				HTTP 1.1

SyncReplyMode:				signalsAndResponse

Reliability:

Retry/Timeout

Receipt Acknowledgement:	Not required

Response:			Not required

Response Acknowledgement:	Not required

Duplicate Check :			None

Order:					No

Security:

Encryption:				No

Signature:				No

Non-Repudiation

Origin				Not required

Receipt				Not required

Multi Hop:					No

Error:

ErrrorURI:				<URI of driver party>

#### Urn:config:cpa_basic_reliable (for test cases 1.8)

Transport:

Protocol				HTTP 1.1

SyncReplyMode:				None

Reliability:

Retry/Timeout

Receipt Acknowledgement:	Yes

Response:			Not required

Response Acknowledgement:	Not required

Duplicate Check :			None

Order:					No

Security:

Encryption:				No

Signature:				No

Non-Repudiation

Origin				Not required

Receipt				Not required

Multi Hop:					No

Error:

ErrrorURI:				<URI of driver party>

#### Urn:config:cpa_basic_reliablesig (for test cases 1.9)

Transport:

Protocol				HTTP 1.1

SyncReplyMode:				None

Reliability:

Retry/Timeout

Receipt Acknowledgement:	Yes

Response:			Not required

Response Acknowledgement:	Not required

Duplicate Check :			None

Order:					No

Security:

Encryption:				No

Signature:				Yes

Non-Repudiation

Origin				Not required

Receipt				Yes (is that what will get the Ack signed?)

Multi Hop:					No

Error:

ErrrorURI:				<URI of driver party>

#### Urn:config:cpa_basic_reliablesync (for test cases 1.10)

Transport:

Protocol				HTTP 1.1

SyncReplyMode:				mshSignalsOnly

Reliability:

Retry/Timeout

Receipt Acknowledgement:	Yes

Response:			Not required

Response Acknowledgement:	Not required

Duplicate Check :			None

Order:					No

Security:

Encryption:				No

Signature:				No

Non-Repudiation

Origin				Not required

Receipt				Not required

Multi Hop:					No

Error:

ErrrorURI:				<URI of driver party>

### Default Message Headers

#### Parameters

The default values for these parameters should be set when the test suite is deployed:

- $SenderParty (set to the Test Driver MSH host)

- $ReceiverParty (set to the remote MSH host)

The values of these parameters must be set for each test case:

- $CPA

- $ConversationId

The value of these parameters may vary for each test step:

- $Action

The value of these parameters is not under control of the Test Driver, and will be set by the MSH implementation at run-time:

- $MessageId

- $TimeStamp

#### mhdr_0

This sample header is used as default header for messages with no payload. The parameters will be instantiated by the Test Driver or the MSH implementation.

<SOAP:Envelope	xmlns:xlink="http://www.w3.org/1999/xlink"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xmlns:SOAP="http://schemas.xmlsoap.org/soap/envelope/"

xmlns:eb="http://www.oasis-open.org/committees/ebxml-msg/schema/msg-header-2_0.xsd"		xsi:schemaLocation="http://schemas.xmlsoap.org/soap/envelope/

http://www.oasis-open.org/committees/ebxml-msg/schema/envelope.xsd

http://www.oasis-open.org/committees/ebxml-msg/schema/msg-header-2_0.xsd 												 http://www.oasis-open.org/committees/ebxml-msg/schema/msg-header-2_0.xsd">

<SOAP:Header>

<eb:MessageHeader SOAP:mustUnderstand="1" eb:version="2.0">

<eb:From>

<eb:PartyId> $SenderParty</eb:PartyId>

</eb:From>

<eb:To>

<eb:PartyId>$ReceiverParty </eb:PartyId>

</eb:To>

<eb:CPAId>$CPA </eb:CPAId>

<eb:ConversationId> $ConversationId</eb:ConversationId>

<eb:Service> urn:ebXML:iic:test </eb:Service>

<eb:Action>$Action </eb:Action>

<eb:MessageData>

<eb:MessageId>$MessageId </eb:MessageId>

<eb:Timestamp>$Timestamp </eb:Timestamp>

</eb:MessageData>

</eb:MessageHeader>

</SOAP:Header>

<SOAP:Body>

</SOAP:Body>

</SOAP:Envelope>

#### mhdr_1

This sample header is used as default header for messages with one payload, after instantiation of parameters.

<SOAP:Envelope	xmlns:xlink="http://www.w3.org/1999/xlink"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xmlns:SOAP="http://schemas.xmlsoap.org/soap/envelope/"

xmlns:eb="http://www.oasis-open.org/committees/ebxml-msg/schema/msg-header-2_0.xsd"		xsi:schemaLocation="http://schemas.xmlsoap.org/soap/envelope/

http://www.oasis-open.org/committees/ebxml-msg/schema/envelope.xsd

http://www.oasis-open.org/committees/ebxml-msg/schema/msg-header-2_0.xsd 												 http://www.oasis-open.org/committees/ebxml-msg/schema/msg-header-2_0.xsd">

<SOAP:Header>

<eb:MessageHeader SOAP:mustUnderstand="1" eb:version="2.0">

<eb:From>

<eb:PartyId>$SenderParty </eb:PartyId>

</eb:From>

<eb:To>

<eb:PartyId>$ReceiverParty </eb:PartyId>

</eb:To>

<eb:CPAId>$CPA </eb:CPAId>

<eb:ConversationId>$ConversationId </eb:ConversationId>

<eb:Service>ebXML_IIC_Testing</eb:Service>

<eb:Action>$Action </eb:Action>

<eb:MessageData>

<eb:MessageId>$MessageId </eb:MessageId>

<eb:Timestamp>$Timestamp </eb:Timestamp>

</eb:MessageData>

</eb:MessageHeader>

</SOAP:Header>

<SOAP:Body>

<eb:Manifest eb:version="2.0">

<eb:Reference xlink:href="cid: payload_1"

xlink:role="XLinkRole"   xlink:type="simple">

<eb:Description xml:lang="en-US">Purchase Order 1</eb:Description>

</eb:Reference>

</eb:Manifest>

</SOAP:Body>

</SOAP:Envelope>

#### mhdr_2

This sample header is used as default header for messages with two payloads, after instantiation of parameters.

<SOAP:Envelope	xmlns:xlink="http://www.w3.org/1999/xlink"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xmlns:SOAP="http://schemas.xmlsoap.org/soap/envelope/"

xmlns:eb="http://www.oasis-open.org/committees/ebxml-msg/schema/msg-header-2_0.xsd"		xsi:schemaLocation="http://schemas.xmlsoap.org/soap/envelope/

http://www.oasis-open.org/committees/ebxml-msg/schema/envelope.xsd

http://www.oasis-open.org/committees/ebxml-msg/schema/msg-header-2_0.xsd 												 http://www.oasis-open.org/committees/ebxml-msg/schema/msg-header-2_0.xsd">

<SOAP:Header>

<eb:MessageHeader SOAP:mustUnderstand="1" eb:version="2.0">

<eb:From>

<eb:PartyId>$SenderParty </eb:PartyId>

</eb:From>

<eb:To>

<eb:PartyId>$ReceiverParty </eb:PartyId>

</eb:To>

<eb:CPAId>$CPA </eb:CPAId>

<eb:ConversationId>$ConversationId </eb:ConversationId>

<eb:Service>ebXML_IIC_Testing</eb:Service>

<eb:Action>$Action </eb:Action>

<eb:MessageData>

<eb:MessageId>$MessageId </eb:MessageId>

<eb:Timestamp>$Timestamp </eb:Timestamp>

</eb:MessageData>

</eb:MessageHeader>

</SOAP:Header>

<SOAP:Body>

<eb:Manifest eb:version="2.0">

<eb:Reference xlink:href="cid:payload_1 "

xlink:role="XLinkRole"   xlink:type="simple">

<eb:Description xml:lang="en-US">Purchase Order 1</eb:Description>

</eb:Reference>

<eb:Reference xlink:href="cid:payload_2 "

xlink:role="XLinkRole"   xlink:type="simple">

<eb:Description xml:lang="en-US">Purchase Order 2</eb:Description>

</eb:Reference>

</eb:Manifest>

</SOAP:Body>

</SOAP:Envelope>

.

#### mhdr_3

This sample header is used as default header for messages with three payloads, after instantiation of parameters.

<SOAP:Envelope	xmlns:xlink="http://www.w3.org/1999/xlink"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xmlns:SOAP="http://schemas.xmlsoap.org/soap/envelope/"

xmlns:eb="http://www.oasis-open.org/committees/ebxml-msg/schema/msg-header-2_0.xsd"		xsi:schemaLocation="http://schemas.xmlsoap.org/soap/envelope/

http://www.oasis-open.org/committees/ebxml-msg/schema/envelope.xsd

http://www.oasis-open.org/committees/ebxml-msg/schema/msg-header-2_0.xsd 												 http://www.oasis-open.org/committees/ebxml-msg/schema/msg-header-2_0.xsd">

<SOAP:Header>

<eb:MessageHeader SOAP:mustUnderstand="1" eb:version="2.0">

<eb:From>

<eb:PartyId>$SenderParty </eb:PartyId>

</eb:From>

<eb:To>

<eb:PartyId>$ReceiverParty </eb:PartyId>

</eb:To>

<eb:CPAId>$CPA </eb:CPAId>

<eb:ConversationId>$ConversationId </eb:ConversationId>

<eb:Service>ebXML_IIC_Testing</eb:Service>

<eb:Action>$Action </eb:Action>

<eb:MessageData>

<eb:MessageId>$MessageId </eb:MessageId>

<eb:Timestamp>$Timestamp </eb:Timestamp>

</eb:MessageData>

</eb:MessageHeader>

</SOAP:Header>

<SOAP:Body>

<eb:Manifest eb:version="2.0">

<eb:Reference xlink:href="cid:payload_1 "

xlink:role="XLinkRole"   xlink:type="simple">

<eb:Description xml:lang="en-US">Purchase Order 1</eb:Description>

</eb:Reference>

<eb:Reference xlink:href="cid:payload_2 2"

xlink:role="XLinkRole"   xlink:type="simple">

<eb:Description xml:lang="en-US">Purchase Order 2</eb:Description>

</eb:Reference>

<eb:Reference xlink:href="cid:payload_3 "

xlink:role="XLinkRole"   xlink:type="simple">

<eb:Description xml:lang="en-US">Purchase Order 3</eb:Description>

</eb:Reference>

</eb:Manifest>

</SOAP:Body>

</SOAP:Envelope>

### Message Payloads

#### Payload_1

(a small XML payload)

<purchase_order>

<po_number>1</po_number>

<part_number>123</part_number>

<price currency="USD">500.00</price>

</purchase_order>

#### Payload_2

This payload should be an average size XML business document.

#### Payload_3

This payload should be a binary payload.

## BIP Test Suite Script

The following table shows the detail of each test case and its test steps, described using the notation specified in the TestFramework specification document. The actual XML representation of the test suite is given in Appendix B.

| Test Object | ID | Description | Mode | Operation | Message Expression |
| --- | --- | --- | --- | --- | --- |
| Test Suite |  |  |  |  | Configuration: TestDriver Mode = Service Default CPAId = urn:config:cpa_basic |
| Test Case | urn: TestCase :id:1.1 | Basic exchange, no payload |  |  | CPAId = urn:config:cpa_basic |
| TestStep | 1 |  | service |  |  |
|  |  | Send basic message header |  | PutMessage | <mime:Message> <mime:MessageContainer> <soap:Envelope> <soap:Header> <eb:MessageHeader> <eb:Action>Dummy</eb:Action> </eb:MessageHeader> </soap:Header> </soap:Envelope> </mime:MessageContainer> </mime:Message> |
| TestStep | 2 |  | service |  |  |
|  |  | Correlate returned message |  | GetMessage | /TEST:MessageStore/MIME:Message[ MIME:Container[1]/ SOAP:Envelope/SOAP:Header/eb:MessageHeader[ eb:CPAId=$CPAId and eb:Conversationid=$ConversationId and eb:Action='Mute' ]] |
| Assertion |  |  |  | VerifyContent | /mime:Message[mime:MessageContainer[1]/ soap:Envelope/soap:Header/eb:MessageHeader] |
| Test Case | urn: TestCase :id:1.2 | Basic asyncronous exchange with one payload |  |  | CPAId = urn:config:cpa_basic |
| TestStep | 1 |  | service |  |  |
|  |  | Send basic message header |  | PutMessage | <mime:Message> <mime:MessageContainer> <soap:Envelope> <soap:Header> <eb:MessageHeader> <eb:Action>Reflector</eb:Action> </eb:MessageHeader> </soap:Header> <soap:Body> <eb:Manifest> <eb:Reference xlink:href="cid:payload_1" /> </eb:Manifest> </soap:Body> </soap:Envelope> </mime:MessageContainer> </mime:Message> |
|  |  | Add content-id and payload to mime message |  | SetPayload Content-Id = 'cid:payload_1' messageRef= " payload_1" |  |
| TestStep | 2 |  | service |  |  |
|  |  | Correlate returned messages |  | GetMessage | /TEST:MessageStore/MIME:Message[ MIME:Container[1]/ SOAP:Envelope/SOAP:Header/eb:MessageHeader[ eb:CPAId='cpa_basic' and eb:Conversationid=$ConversationId and eb:Action='Mute' ]] |
| Assertion |  |  |  | VerifyContent | /mime:Message[mime:MessageContainer[1]/ soap:Body/eb:Manifest/eb:Reference[ @xlink:href='cid:payload_1']] |
|  |  | Find payload in message |  | GetPayload | /MIME:Message/MIME:Container[ @Content-Id = 'cid:payload_1'] |
| Assertion |  |  |  | VerifyContent |  |
| Test Case | urn: TestCase :id:1.3 | Basic exchange with three payloads |  |  | CPAId = urn:config:cpa_basic |
| TestStep | 1 |  | service |  |  |
|  |  | Send basic message header |  | PutMessage | <mime:Message> <mime:MessageContainer> <soap:Envelope> <soap:Header> <eb:MessageHeader> <eb:Action>Reflector</eb:Action> </eb:MessageHeader> </soap:Header> <soap:Body> <eb:Manifest> <eb:Reference xlink:href="cid:payload_1" /> <eb:Reference xlink:href="cid:payload_2" /> <eb:Reference xlink:href="cid:payload_3" /> </eb:Manifest> </soap:Body> </soap:Envelope> </mime:MessageContainer> </mime:Message> |
|  |  | Add content-id and payload to mime message |  | SetPayload Content-Id = 'cid:payload_1' messageRef= " payload_1" |  |
|  |  | Add content-id and payload to mime message |  | SetPayload Content-Id = 'cid:payload_2' messageRef= " payload_2" |  |
|  |  | Add content-id and payload to mime message |  | SetPayload Content-Id = 'payload_3' messageRef= " payload_3" |  |
| TestStep | 2 |  | service |  |  |
|  |  | Correlate returned messages |  | GetMessage | /TEST:MessageStore/MIME:Message[ MIME:Container[1]/ SOAP:Envelope/SOAP:Header/eb:MessageHeader[ eb:CPAId='cpa_basic' and eb:Conversationid=$ConversationId and eb:Action='Mute' ]] |
| Assertion |  |  |  | VerifyContent | /mime:Message[mime:MessageContainer[1]/ soap:Body/eb:Manifest/eb:Reference[ @xlink:href='cid:payload_1']] |
|  |  | Find payload in message |  | GetPayload | /MIME:Message/MIME:Container[ @Content-Id = 'cid:payload_1'] |
| Assertion |  |  |  | VerifyContent |  |
|  |  | Find payload in message |  | GetPayload | /MIME:Message/MIME:Container[ @Content-Id = 'cid:payload_2'] |
| Assertion |  |  |  | VerifyContent |  |
|  |  | Find payload in message |  | GetPayload | /MIME:Message/MIME:Container[ @Content-Id = 'cid:payload_3'] |
| Assertion |  |  |  | VerifyContent |  |
| Test Case | urn: TestCas e:id:1.4 | Basic exchange with Error Message |  |  | CPAId = urn:config:cpa_basic |
| TestStep | 1 |  | service |  |  |
|  |  | MessageHeader mustUnderstand set to 'true' |  | PutMessage | <mime:Message> <mime:MessageContainer> <soap:Envelope> <soap:Header> <eb:MessageHeader> <eb:Action>WrongAction</eb:Action> <eb:ExtensionLement soap:mustUnderstand="true" /> </eb:MessageHeader> </soap:Header> </soap:Envelope> </mime:MessageContainer> </mime:Message> [JD]: I have introduced a wrong action name… this should cause an error message with severity “Error”. |
| TestStep | 2 |  | service |  |  |
|  |  | Correlate returned messages |  | GetMessage | /TEST:MessageStore/MIME:Message[ MIME:Container[1]/ SOAP:Envelope/SOAP:Header/eb:MessageHeader[ eb:CPAId='cpa_basic' and eb:Conversationid=$ConversationId and eb:ErrorList]] [JD]: here, we should be ready to catch a stand-alone error message, not a regular message with an ErrorList element, because this is incompatible with “error” severity level. There should be an errorCode elt, its value should be ValueNotRecognized or Inconsistent.. |
| Assertion |  |  |  | VerifyContent | mime:Message[mime:MessageContainer[1]/ soap:Envelope/soap:Body/soap:Fault/soap:Code[ soap:Value='MustUnderstand']] [JD] Not sure this condition is correct or sufficient: error element should have severity = “Error”, and the name of the bad action “WrongAction” should appear in the error description or location attribute of the Error element, to make sure we catch the right error |
| Test Case | urn: TestCase :id:1.5 | Signed message without key info |  |  | CPAId = urn:config:cpa_basic_signed |
| TestStep | 1 |  | service |  |  |
|  |  | Send basic message header |  | PutMessage | <mime:Message> <mime:MessageContainer> <soap:Envelope> <soap:Header> <eb:MessageHeader> <eb:CPAId>cpa_basic_no_key_info</eb:CPAId> <eb:Action>Reflector</eb:Action> </eb:MessageHeader> </soap:Header> <soap:Body> <eb:Manifest> <eb:Reference xlink:href="cid:payload_1" /> </eb:Manifest> </soap:Body> </soap:Envelope> </mime:MessageContainer> </mime:Message> |
|  |  | Add content-id and payload to mime message |  | SetPayload Content-ID= "cid:payload_1 " Content-Id = 'cid:payload_1' messageRef= " payload_1" |  |
|  |  |  |  | DSign | <ds:Signature xmlns= "http://www.w3.org/2000/09/xmldsig#"> <ds:SignedInfo> <ds:CanonicalizationMethod ds:Algorithm= "http://www.w3.org/TR/2001/ REC-xml-c14n-20010315" /> <ds:SignatureMethod ds:Algorithm= "http://www.w3.org/2000/09/xmldsig#dsa-sha1" /> <ds:Reference ds:URI=""> <ds:DigestMethod ds:Algorithm= "http://www.w3.org/2000/09/xmldsig#sha1" /> <ds:DigestValue>abc</ds:DigestValue> </ds:Reference> <ds:Reference ds:URI="cid://blahblahblah/"> <ds:DigestMethod ds:Algorithm= "http://www.w3.org/2000/09/xmldsig#sha1" /> <ds:DigestValue>def</ds:DigestValue> </ds:Reference> </ds:SignedInfo> <ds:SignatureValue>ghi</ds:SignatureValue> </ds:Signature> |
| TestStep | 2 |  | service |  |  |
|  |  | Correlate returned messages |  | GetMessage | /TEST:MessageStore/MIME:Message[ MIME:Container[1]/ SOAP:Envelope/SOAP:Header/eb:MessageHeader[ eb:CPAId='cpa_basic' and eb:Conversationid=$ConversationId and eb:Action='Mute' ]] |
| Assertion |  | Check for returned payload |  | VerifyContent | /mime:Message[mime:MessageContainer[1]/ soap:Body/eb:Manifest/eb:Reference[ @xlink:href='cid:payload_1']] |
|  |  | Find payload in message |  | GetPayload | /MIME:Message/MIME:Container[ @Content-Id = 'cid:payload_1'] |
| Assertion |  | Verify returned payload contents |  | VerifyContent |  |
| Test Case | urn: TestCase :id:1.6 | Basic syncronous exchange with one payload |  |  | CPAId = urn:config:cpa_basic_syncresponse |
| TestStep | 1 |  | service |  |  |
|  |  | Send basic message header with SyncReply |  | PutMessage | <mime:Message> <mime:MessageContainer> <soap:Envelope> <soap:Header> <eb:MessageHeader> <eb:Action>Reflector</eb:Action> </eb:MessageHeader> <eb:SyncReply /> </soap:Header> <soap:Body> <eb:Manifest> <eb:Reference xlink:href="cid:payload_1" /> </eb:Manifest> </soap:Body> </soap:Envelope> </mime:MessageContainer> </mime:Message> |
|  |  | Add content-id and payload to mime message |  | SetPayload Content-ID= "cid:payload_1" Content-Id = 'cid:payload_1' messageRef= " payload_1" |  |
| TestStep | 2 |  | service |  |  |
|  |  | Correlate returned messages |  | GetMessage asycronous= "false" | /TEST:MessageStore/MIME:Message[ MIME:Container[1]/ SOAP:Envelope/SOAP:Header/eb:MessageHeader[ eb:CPAId='cpa_basic' and eb:Conversationid=$ConversationId and eb:Action='Mute' ]] |
| Assertion |  | Check for returned payload |  | VerifyContent | /mime:Message[mime:MessageContainer[1]/ soap:Body/eb:Manifest/eb:Reference[ @xlink:href='cid:payload_1']] |
|  |  | Find payload in message |  | GetPayload | /MIME:Message/MIME:Container[ @Content-Id = 'cid:payload_1'] |
| Assertion |  | Verify returned payload contents |  | VerifyContent |  |
| Test Case | urn: TestCase :id:1.7 | Test unsigned AckRequested message with unsigned Acknowledgment |  |  | CPAId = urn:config:cpa_basic_reliable |
| TestStep | 1 |  | service |  |  |
|  |  | Send basic message with AckRequested element |  | PutMessage | <mime:Message> <mime:MessageContainer> <soap:Envelope> <soap:Header> <eb:MessageHeader> <eb:Action>Dummy</eb:Action> </eb:MessageHeader> <eb:AckRequested /> </soap:Header> <soap:Body> <eb:Manifest> <eb:Reference xlink:href="cid:payload_1" /> </eb:Manifest> </soap:Body> </soap:Envelope> </mime:MessageContainer> </mime:Message> |
| TestStep | 2 |  | service |  |  |
|  |  | Correlate returned messages |  | GetMessage | /TEST:MessageStore/MIME:Message[ MIME:Container[1]/ SOAP:Envelope/SOAP:Header/eb:MessageHeader[ eb:CPAId='cpa_basic' and eb:Conversationid=$ConversationId and ../eb:Acknowledgment]] |
| Assertion |  | Verify that no Error is returned |  | VerifyContent | /mime:Message[not mime:MessageContainer[1]/ soap:Envelope/soap:Header/eb:ErrorList] |
| Assertion |  | Verify that no soap fault is generated for warnings |  | VerifyContent | /mime:Message[not mime:MessageContainer[1]/ soap:Envelope/soap:Body[not soap:Fault]] |
| Assertion |  | Verify that only one Acknowledgment was returned |  | VerifyContent | /mime:Message[[mime:MessageContainer[1]/ soap:Envelope/eb:MessageHeader/eb:Acknowledgment] count()=1] |
| Test Case | Urn: TestCase :id:1.8 | Test signed AckRequested message with signed Acknowledgment |  |  | CPAId = urn:config:cpa_basic_reliablesig |
| TestStep | 1 |  | service |  |  |
|  |  | Send basic message with AckRequested ( signed = 'true' ) element, and signed payload |  | PutMessage | <mime:Message> <mime:MessageContainer> <soap:Envelope> <soap:Header> <eb:MessageHeader> <eb:Action>Dummy</eb:Action> </eb:MessageHeader> <eb:AckRequested eb:signed="true" /> </soap:Header> <soap:Body> <eb:Manifest> <eb:Reference xlink:href="cid:payload_1" /> </eb:Manifest> </soap:Body> </soap:Envelope> </mime:MessageContainer> </mime:Message> |
|  |  | Add content-id and payload to mime message |  | SetPayload Content-ID= "cid:payload_1" Content-Id = 'cid:payload_1' messageRef= " payload_1" |  |
|  |  |  |  | DSign | <ds:Signature xmlns= "http://www.w3.org/2000/09/xmldsig#"> <ds:SignedInfo> <ds:CanonicalizationMethod ds:Algorithm= "http://www.w3.org/ TR/2001/REC-xml-c14n-20010315" /> <ds:SignatureMethod ds:Algorithm= "http://www.w3.org/2000/09/xmldsig#dsa-sha1" /> <ds:Reference ds:URI=""> <ds:DigestMethod ds:Algorithm= "http://www.w3.org/2000/09/xmldsig#sha1" /> <ds:DigestValue>abc</ds:DigestValue> </ds:Reference> <ds:Reference ds:URI="cid://blahblahblah/"> <ds:DigestMethod ds:Algorithm= "http://www.w3.org/2000/09/xmldsig#sha1" /> <ds:DigestValue>def</ds:DigestValue> </ds:Reference> </ds:SignedInfo> <ds:SignatureValue>ghi</ds:SignatureValue> <ds:KeyInfo>jkl</ds:KeyInfo> </ds:Signature> |
| TestStep | 2 |  | service |  |  |
|  |  | Correlate returned messages |  | GetMessage | /TEST:MessageStore/MIME:Message[ MIME:Container[1]/ SOAP:Envelope/SOAP:Header/eb:MessageHeader[ eb:CPAId='cpa_basic' and eb:Conversationid=$ConversationId and eb:Action='Mute' and ../eb:Acknowledgment]] |
| Assertion |  | Verify that no Error is returned |  | VerifyContent | /mime:Message[not mime:MessageContainer[1]/ soap:Envelope/soap:Header/eb:ErrorList] |
| Assertion |  | Verify that no soap fault is generated for warnings |  | VerifyContent | /mime:Message[not mime:MessageContainer[1]/ soap:Envelope/soap:Body[not soap:Fault]] |
| Assertion |  | Verify that only one Acknowledgment was returned |  | VerifyContent | /mime:Message[[mime:MessageContainer[1]/ soap:Envelope/eb:MessageHeader/eb:Acknowledgment] count()=1] |
| Assertion |  | Validate Acknowledgment Signature |  | ValidateContent contentType= signedAck | /mime:Messag/[mime:MessageContainer[1]/ soap:Envelope/eb:MessageHeader/eb:Acknowledgment |
| Test Case | urn: TestCase :id:1.9 | Test unsigned AckRequested message with unsigned Acknowledgment |  |  | CPAId = urn:config:cpa_basic_reliablesync |
| TestStep | 1 |  | service |  |  |
|  |  | Send basic message with AckRequested element |  | PutMessage | <mime:Message> <mime:MessageContainer> <soap:Envelope> <soap:Header> <eb:MessageHeader> <eb:Action>Dummy</eb:Action> </eb:MessageHeader> <eb:AckRequested /> </soap:Header> <soap:Body> <eb:Manifest> <eb:Reference xlink:href="cid:payload_1" /> </eb:Manifest> </soap:Body> </soap:Envelope> </mime:MessageContainer> </mime:Message> |
| TestStep | 2 |  | service |  |  |
|  |  | Correlate returned messages |  | GetMessage asycronous= "false" | /TEST:MessageStore/MIME:Message[ MIME:Container[1]/ SOAP:Envelope/SOAP:Header/eb:MessageHeader[ eb:CPAId='cpa_basic' and eb:Conversationid=$ConversationId and eb:Acknowledgment]] |
| Assertion |  | Verify that no Error is returned |  | VerifyContent | /mime:Message[not mime:MessageContainer[1]/ soap:Envelope/soap:Header/eb:ErrorList] |
| Assertion |  | Verify that no soap fault is generated for warnings |  | VerifyContent | /mime:Message[not mime:MessageContainer[1]/ soap:Envelope/soap:Body[not soap:Fault]] |
| Assertion |  | Verify that only one Acknowledgment was returned |  | VerifyContent | /mime:Message[[mime:MessageContainer[1]/ soap:Envelope/eb:MessageHeader/eb:Acknowledgment] count()=1] |

# Appendix A – Implementations of the Test Harness

Two variants of the test harness described in Section 2 are described below.

## The “Point-to-point” Test Harness Implementation:

This configuration (Figure 12) is appropriate when two parties engage in interoperability testing without any third-party assistance, Each party will in turn play the driver party, and operate the Test Driver (install test cases, drive the executions, generate the reports.)

In this configuration, the Test Driver invokes directly the Initiator action of the associated Test Service in order to trigger an exchange. The Test Driver is in service mode, and the associated Test Service is in local reporting mode, as it directly notifies the Test Driver. There is no need to generate messages on the wire for doing this, as both components reside on the same host.

## The “Hub Driver” Test Harness Implementation:

This configuration (Figure 13) is appropriate when two parties engage in interoperability testing with the help of a third-party, which facilitates the testing. Each party will still in turn play the driver party (due to the asymmetric character of the BIP test suite), but the third party will operate the Test Driver (install test cases, drive the executions, generate the reports.) The two candidate parties would only make sure their MSH and Test Service are up and running, and that the CPAs associated with the test suite are accessible.

In this configuration, the Test Driver invokes remotely the Initiator action of the Test Service of the driver party, in order to trigger an exchange. The Test Driver, in connection mode, interfaces directly at transport level, generating message material as done in conformance testing. The notification from the actions of the Test Service (driver party side), will be done by messages sent to the Test Driver (Hub URL), which is proper to a Test Service in remote reporting mode.Once an exchange is triggered, both end-points can send messages to each other, directly or through the Hub node, used as a simple route.

# Appendix B – Test Suite XML Script

# References

### Non-Normative References

[ebXMLTestFramework

]	ebXML Test Framework specification, Version 1.0, Technical Committee specification, March 4, 2003, (OASIS IIC Web site)

[ebTESTSUITE]	ebXML Business Process Specification Schema, version 1.0, published 27 April 2001, http://www.ebxml.org/specs/ebBPSS.pdf.

[ebRS]	ebXML Registry Services Specification, version 2.0, published 6 December 2001
http://www.oasis-open.org/committees/regrep/documents/2.0/specs/ebrs.pdf,   
published, 5 December 2001.
http://www.oasis-open.org/committees/regrep/documents/2.0/specs/ebrim.pdf

[XMLSchema]	W3C XML Schema Recommendation, 
http://www.w3.org/TR/2001/REC-xmlschema-0-20010502/
http://www.w3.org/TR/2001/REC-xmlschema-1-20010502/
http://www.w3.org/TR/2001/REC-xmlschema-2-20010502/

[ebCPP]	ebXML Collaboration Protocol Profile and Agreement specification, Version 1.0, published 10 May, 2001, http://www.ebxml.org/specs/ebCCP.doc

[ebBPSS]	ebXML Business Process Specification Schema, version 1.0, published 27 April 2001, http://www.ebxml.org/specs/ebBPSS.pdf.

[ebMS] ebXML Messaging Service Specification, Version 2.0 http://ebxml.org/project_teams/transport/private/ebXML_Messaging_Service_Specification_v0-21.pdf

# Contact Information

Team Editor

| Name | Steve Yung (Sun) |
| --- | --- |
|  | Michael Kass (NIST) |

# Acknowledgments

The OASIS ebXML-MS Technical Committee would like to thank …

# Disclaimer

The views and specification expressed in this document are those of the authors and are not necessarily those of their employers.  The authors and their employers specifically disclaim responsibility for any problems arising from correct or incorrect implementation or use of this design.

This document and the information contained herein is provided on an "AS IS" basis and OASIS DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE."

# Copyright Statement

Copyright (C) The Organization for the Advancement of Structured Information Standards [OASIS] 
January 2002. All Rights Reserved.

This document and translations of it may be copied and furnished to others, and derivative works that comment on or otherwise explain it or assist in its implementation may be prepared, copied, published and distributed, in whole or in part, without restriction of any kind, provided that the above copyright notice and this paragraph are included on all such copies and derivative works. However, this document itself may not be modified in any way, such as by removing the copyright notice or references to OASIS, except as needed for the purpose of developing OASIS specifications, in which case the procedures for copyrights defined in the OASIS Intellectual Property Rights document MUST be followed, or as required to translate it into languages other than English.

The limited permissions granted above are perpetual and will not be revoked by OASIS or its successors or assigns.

# Intellectual Property Rights Statement

"OASIS takes no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights. Information on OASIS's procedures with respect to rights in OASIS specifications can be found at the OASIS website. Copies of claims of rights made available for publication and any assurances of licenses to be made available, or the result of an attempt made to obtain a general license or permission for the use of such proprietary rights by implementors or users of this specification, can be obtained from the OASIS Executive Director."

"OASIS invites any interested party to bring to its attention any copyrights, patents or patent applications, or other proprietary rights which may cover technology that may be required to implement this specification. Please address the information to the OASIS Executive Director."

"OASIS has been notified of intellectual property rights claimed in regard to some or all of the contents of this specification. For more information consult the online list of claimed rights."

# Footnotes

By PayloadVerify correct?