## SHA-512/224

|  | Functions |
| --- | --- |
| Mechanism | Encrypt & Decrypt | Sign & Verify | SR & VR1 | Digest | Gen. Key/ Key Pair | Wrap & Unwrap | Derive |
| CKM_SHA512_224 |  |  |  |  |  |  |  |
| CKM_SHA512_224_HMAC_GENERAL |  |  |  |  |  |  |  |
| CKM_SHA512_224_HMAC |  |  |  |  |  |  |  |
| CKM_SHA512_224_KEY_DERIVATION |  |  |  |  |  |  |  |

### Definitions

CKM_SHA512_224

CKM_SHA512_224_HMAC

CKM_SHA512_224_HMAC_GENERAL

CKM_SHA512_224_KEY_DERIVATION

CKK_SHA512_224_HMAC

### SHA-512/224 digest

The SHA-512/224 mechanism, denoted CKM_SHA512_224, is a mechanism for message digesting, following the Secure Hash Algorithm defined in FIPS PUB 180-4, section 5.3.6.  It is based on a 512-bit message digest with a distinct initial hash value and truncated to 224 bits.  CKM_SHA512_224 is the same as CKM_SHA512_T with a parameter value of 224.

It does not have a parameter.

Constraints on the length of input and output data are summarized in the following table.  For single-part digesting, the data and the digest may begin at the same location in memory.

Table 1, SHA-512/224: Data Length

| Function | Input length | Digest length |
| --- | --- | --- |
| C_Digest | any | 28 |

### General-length SHA-512/224-HMAC

The general-length SHA-512/224-HMAC mechanism, denoted CKM_SHA512_224_HMAC_GENERAL, is the same as the general-length SHA-1-HMAC mechanism in Section Error: Reference source not found, except that it uses the HMAC construction based on the SHA-512/224 hash function and length of the output should be in the range 0-28.

### SHA-512/224-HMAC

The SHA-512/224-HMAC mechanism, denoted CKM_SHA512_224_HMAC, is a special case of the general-length SHA-512/224-HMAC mechanism.

It has no parameter, and always produces an output of length 28.

### SHA-512/224 key derivation

SHA-512/224 key derivation, denoted CKM_SHA512_224_KEY_DERIVATION, is the same as the SHA-1 key derivation mechanism in Section Error: Reference source not found, except that it uses the SHA-512/224 hash function and the relevant length is 28 bytes.

## SHA-512/256

|  | Functions |
| --- | --- |
| Mechanism | Encrypt & Decrypt | Sign & Verify | SR & VR1 | Digest | Gen. Key/ Key Pair | Wrap & Unwrap | Derive |
| CKM_SHA512_256 |  |  |  |  |  |  |  |
| CKM_SHA512_256_HMAC_GENERAL |  |  |  |  |  |  |  |
| CKM_SHA512_256_HMAC |  |  |  |  |  |  |  |
| CKM_SHA512_256_KEY_DERIVATION |  |  |  |  |  |  |  |

### Definitions

CKM_SHA512_256

CKM_SHA512_256_HMAC

CKM_SHA512_256_HMAC_GENERAL

CKM_SHA512_256_KEY_DERIVATION

CKK_SHA512_256_HMAC

### SHA-512/256 digest

The SHA-512/224 mechanism, denoted CKM_SHA512_256, is a mechanism for message digesting, following the Secure Hash Algorithm defined in FIPS PUB 180-4, section 5.3.6.  It is based on a 512-bit message digest with a distinct initial hash value and truncated to 256 bits. CKM_SHA512_256 is the same as CKM_SHA512_T with a parameter value of 256.

It does not have a parameter.

Constraints on the length of input and output data are summarized in the following table.  For single-part digesting, the data and the digest may begin at the same location in memory.

Table 2, SHA-512/256: Data Length

| Function | Input length | Digest length |
| --- | --- | --- |
| C_Digest | any | 32 |

### General-length SHA-512/256-HMAC

The general-length SHA-512/256-HMAC mechanism, denoted CKM_SHA512_256_HMAC_GENERAL, is the same as the general-length SHA-1-HMAC mechanism in Section Error: Reference source not found, except that it uses the HMAC construction based on the SHA-512/256 hash function and length of the output should be in the range 0-32.

### SHA-512/256-HMAC

The SHA-512/256-HMAC mechanism, denoted CKM_SHA512_256_HMAC, is a special case of the general-length SHA-512/256-HMAC mechanism.

It has no parameter, and always produces an output of length 32.

### SHA-512/256 key derivation

SHA-512/256 key derivation, denoted CKM_SHA512_256_KEY_DERIVATION, is the same as the SHA-1 key derivation mechanism in Section Error: Reference source not found, except that it uses the SHA-512/256 hash function and the relevant length is 32 bytes.

## General SHA-512/t

|  | Functions |
| --- | --- |
| Mechanism | Encrypt & Decrypt | Sign & Verify | SR & VR1 | Digest | Gen. Key/ Key Pair | Wrap & Unwrap | Derive |
| CKM_SHA512_T |  |  |  |  |  |  |  |
| CKM_SHA512_T_HMAC_GENERAL |  |  |  |  |  |  |  |
| CKM_SHA512_T_HMAC |  |  |  |  |  |  |  |
| CKM_SHA512_T_KEY_DERIVATION |  |  |  |  |  |  |  |

### Definitions

CKM_SHA512_T

CKM_SHA512_T_HMAC

CKM_SHA512_T_HMAC_GENERAL

CKM_SHA512_T_KEY_DERIVATION

CKK_SHA512_T_HMAC

### SHA-512/t digest

The SHA-512/t mechanism, denoted CKM_SHA512_T, is a mechanism for message digesting, following the Secure Hash Algorithm defined in FIPS PUB 180-4, section 5.3.6.  It based on a 512-bit message digest with distinct initial hash values and truncated to t bits.

It has a parameter, a CK_MAC_GENERAL_PARAMS, which holds the value of t in bits.  The length in bytes of the desired output should be in the range 0-ceil(t/8), where 0 < t < 512, and t <> 384.

Constraints on the length of input and output data are summarized in the following table.  For single-part digesting, the data and the digest may begin at the same location in memory.

Table 3, SHA-512/t: Data Length

| Function | Input length | Digest length |
| --- | --- | --- |
| C_Digest | any | ceil(t/8), where 0 < t < 512, and t <> 384 |

### General-length SHA-512/t-HMAC

The general-length SHA-512/t-HMAC mechanism, denoted CKM_SHA512_T_HMAC_GENERAL, is the same as the general-length SHA-1-HMAC mechanism in Section Error: Reference source not found, except that it uses the HMAC construction based on the SHA-512/t hash function and length of the output should be in the range 0-ceil(t/8), where 0 < t < 512, and t <> 384.

### SHA-512/t-HMAC

The SHA-512/t-HMAC mechanism, denoted CKM_SHA512_T_HMAC, is a special case of the general-length SHA-512/t-HMAC mechanism.

It has a parameter, a CK_MAC_GENERAL_PARAMS, which holds the value of t in bits.  The length in bytes of the desired output should be in the range 0-ceil(t/8), where 0 < t < 512, and t <> 384.

### SHA-512/t key derivation

SHA-512/256 key derivation, denoted CKM_SHA512_T_KEY_DERIVATION, is the same as the SHA-1 key derivation mechanism in Section Error: Reference source not found, except that it uses the SHA-512/t hash function and the relevant length is ceil(t/8) bytes, where 0 < t < 512, and t <> 384.

# Manifest Constants

The following definitions can be found in the appropriate header file.

Also, refer [PKCS #11-Base] for additional definitions.

#define CKK_SHA512_224_HMAC			0x00000033

#define CKK_SHA512_256_HMAC			0x00000034

#define CKK_SHA512_T_HMAC				0x00000035

#define CKM_SHA512_224				0x00000280

#define CKM_SHA512_224_HMAC               0x00000281

#define CKM_SHA512_224_HMAC_GENERAL       0x00000282

#define CKM_SHA512_256				0x00000290

#define CKM_SHA512_256_HMAC               0x00000291

#define CKM_SHA512_256_HMAC_GENERAL       0x00000292

#define CKM_SHA512_T					0x000002A0

#define CKM_SHA512_T_HMAC  			0x000002A1

#define CKM_SHA512_T_HMAC_GENERAL		0x000002A2