Conformance Statements for the DASE Standard [reference]

Note: These statements are based on the details contained in the current draft DASE specification [reference] and will need to be modified as the draft matures towards a full standard.  In particular, the manner in which receivers and applications are able to support and use optional features will have an effect on the conformance statement.

DASE Conformance is applicable to:

- implementations of DASE receivers (Receiver Conformance), and

- applications that execute on DASE receivers (Application Conformance).

## Receiver Conformance

### Requirements

A conforming receiver implementation shall meet all the following criteria:

(1)  The receiver implementation shall support all the required interfaces defined within this standard.  These interfaces shall support the functional behavior described in the standard.

The receiver implementation shall provide all the observable functional behavior associated with the Java VM specification, as defined by reference [1].

(2)  The receiver implementation may provide one or more of the following feature sets:

[List of optional feature sets or profiles]

When the implementor of a receiver claims that one or more of the above feature sets are provided, then all the interfaces and the associated functional behavior for those feature sets shall be provided as described in this standard.

(3)  The receiver implementation may provide additional or enhanced facilities not required by this standard.  These non-standard extensions shall not alter the specified behavior of interfaces defined in this standard.  They may add additional behaviors.  In these circumstances, the receiver implementation shall provide a mechanism whereby a DASE conforming application shall be recognized as such, and be executed in an environment that supports the functional behavior defined in this standard.

## Application Conformance

A conforming application shall be able to execute on any conforming receiver implementation.  If an application requires a particular feature set that is not available on a specific receiver implementation, then the application must act within the bounds of the DASE specification even though that means that the application may not perform any useful function.  Specifically, the application shall do no harm, and shall correctly return resources and vacate memory upon discovery that a required element is not present.

### Requirements

A conforming application is an application which requires only the facilities described in, and behaves according to, this standard.  Such an application:

(1)  Shall accept any receiver implementation behavior that results from actions that it takes in areas where this standard allows a conforming receiver implementation to vary.

(2)  Shall tolerate, and is permitted to adapt to, the presence or absence of any feature set defined in this standard.

_____________________________

[1] Lindholm, T. and Yellin, F., "The Java Virtual Machine Specification, 2nd Edition," Addison-Wesley, 1999.

"