## Slide 1: VIRTIO 1.1 FOR HARDWARE Rev2.0
Kully Dhanoa, Intel

## Slide 2: Note
  Proposals made in this presentation are evolving
  This presentation contains proposals as of 8th March 2017

## Slide 3: Objective I
  VirtIO 1.1 Spec to enable efficient implementation for both software AND hardware solutions
  Where software and hardware optimum solutions differ:
    Option 1: Suffer non-optimum performance (assuming not significant) for sake of simpler spec
    Option 2: Allow different implementations via Capability feature to ensure optimum software AND hardware implementations
  Understand software and hardware implementation concerns

## Slide 4: Objective II
  NOTE: Proposals are biased towards:
    FPGA implementation
    VirtIO_net device
    PCIe transport mechanism
  Collectively we must consider implications on:
    Software running on guest
    Pure software implementation
    Other Virtio device types
    Other transport mechanisms?
  THEN decide whether to :
    adopt proposals
    Modify proposals
    Drop proposals

## Slide 5: Agenda
Guest signaling available descriptors
Device signaling used descriptors
Out-of-order processing
Indirect chaining
Rx: Fixed Buffer sizes
Data/Descriptor alignment boundaries

## Slide 6: Guest signaling available descriptors

## Slide 7: Overview
Current Proposal:
  Each descriptor has 1 bit flag DESC_HW
  Guest creates descriptors and then sets DESC_HW flag
  Host/FPGA reads descriptors and can use if DESC_HW is set
    After finishing with descriptor, Host/FPGA clears DESC_HW flag
New Proposal:
  Instead of DESC_HW flag, each VirtIO queue has a single tail pointer
    Ok to have 1 MMIO address for all tail pointers:
      {Queue no, Tail index, <optional values: total pkts, total payload bytes>}

## Slide 8: Cons of current proposal
Desc #0
Create Desc #0
Desc #1
1
1
0
0
0
0
0
0
Cache
Memory
Flush cache line
GUEST
FPGA
Read Desc
Delay ~1us
Read Desc
Rx 2 Desc
Delay ~1us
Read 2 Desc
Rx 2 Desc
Desc are invalid.
Wasted PCIe bandwidth
Wasted PCIe bandwidth
Wasted PCIe bandwidth
Create Desc #1
Desc #0
Desc #1
0
0
1
1
Process valid desc

## Slide 9: New Proposal
No Desc_HW flags
Every VirtIO queue has its own:
  Head pointer (lives in FPGA)
    Not used by guest
    RW for FPGA
  Tail pointer (lives in FPGA)
    W for guest
    RO for FPGA
  No of valid desc for FPGA = tail – head
  Space for guest to add desc = head - tail

## Slide 10: Pros of new proposal
Desc #0
Create Desc #0
Desc #1
1
1
0
0
0
0
0
Cache
Memory
Flush cache line
GUEST
FPGA
Desc avail
Delay ~1us
Read 4 Desc
Update Head pointer
Rx 4 Desc
1 cache line flush per 4 valid descriptors
No wasted PCIe bandwidth
Create Desc #1
Desc #0
Desc #1
0
0
1
1
Process 4 valid descriptors
Desc #3
Desc #2
0
1
1
Create Desc #2
Create Desc #3
Update tail pointer
Tail ptr copy
Tail ptr
Head ptr
0 Desc avail
4 Desc avail
Desc #2
Desc #3
1
1

## Slide 11: Device signaling used Descriptors

## Slide 12: Overview I
Current Proposal:
  FPGA clears each descriptor’s DESC_HW flag (1 bit) after it has finished with the descriptor
New Proposal:
  FPGA does not need to clear DESC_HW flag for every descriptor
  Guest controls which descriptors need to have their DESC_HW cleared:
    Descriptor has an extra 1 bit field, WB (Write-Back):
      WB=1 => FPGA must writeback this descriptor after use
        (at the minimum, clear the DESC_HW flag)
      WB=0 => FPGA need not writeback descriptor
  Saves wasting PCIe bandwidth :
    In many scenarios descriptor data need not be written back i.e. Tx, Rx for network devices, where packet metadata is prepended to packet data.

## Slide 13: Device signaling used descriptors
T3 : Guest detects DESC_HW flag cleared
  This indicates that Desc 3 and ALL previous desc up to last desc with WB=1 are available to guest
Desc #0
Desc #1
Desc #2
Desc #3
Time T0 : Descriptor Table
Guest polling
Tail ptr
GUEST
FPGA
Desc #0
Desc #1
Desc #2
Desc #3
Time T1 : FPGA finished with 4 descriptors
Time T3 : Descriptor Table
Desc #7
1
1 0
1
1 0
1
1 0
1
1 1
1
1 0
1
1 0
1
1 0
Desc #0
Desc #1
Desc #2
Desc #3
Guest polling
Tail ptr
Desc #7
1
1 0
1
1 0
1
1 0
1
0 1
1
1 0
1
1 0
1
1 0
Writeback Desc 3 ONLY
Desc avail to Guest
HW : WB
HW : WB

## Slide 14: VirtIO devices that must write back descriptors
Still supported:
  Device must write back Descriptors whose WB flag is set
  Device may optionally write back Descriptors whose WB flag is clear
Scenarios where Device may have to write back every Descriptor:
  Rx where metadata is contained within descriptor and not in packet buffer
  Out-of-order processing
    Guest should set WB flag for all descriptors

## Slide 15: Out-of-order processing

## Slide 16: Overview
Current Proposal:
  FPGA reads descriptors from queue but can process them in any order.
  Once finished with a descriptor it is written back to the ring with DESC_HW flag cleared
  It need not be written back to same location it was read from. Descriptor can only be written back to a location owned by FPGA (i.e. DESC_HW flag set) and to a location that the FPGA has already cached the descriptor.
No change:
  Hardware implementations will unlikely process descriptors out-of-order from a particular queue.
    Feature will be negotiatable upon startup
  However nothing preventing hardware implementations from processing out of order :

## Slide 17: Out-of-order processing
Out-of-order processing allows descriptors to be written back to Desc Table in any order.
  DESC_HW flag cleared for used Descriptors
Desc #0
Desc #1
Desc #2
Desc #3
Time T0 : Descriptor Table
Tail ptr
GUEST
FPGA
Desc #0
Desc #1
Desc #2
Desc #3
Time T1 : Descriptors copied into FPGA
Desc #3
Desc #2
Desc #2
Desc #3
Time T3 : Descriptor Table
Tail ptr
Desc #0
Desc #1
Desc #2
Desc #3
Time T2 : 2 Descriptors processed
HW : WB
1 1
1 1
1 1
1 1
HW : WB
0 1
0 1
1 1
1 1

## Slide 18: Indirect Chaining

## Slide 19: Overview
Current Proposal:
  Indirect chaining is a negotiable feature?
Hardware:
  Very unlikely that hardware implementations would support this due to extra latency of fetching actual descriptors.
  Is this acceptable?
    i.e. what is the reason for indirect chaining? Would some guests not work unless it is supported?

## Slide 20: Rx Fixed Buffer Sizes

## Slide 21: Overview
Current Proposal:
  Guest is free to chose whatever buffer sizes it wishes for Tx and Rx Buffers
  Theoretically within a ring, a guest could have different buffer sizes
    Is this really done for Rx Buffers? If so, what is the advantage?
    Tx Buffers : I realise some OS create separate small buffers to hold network pkt headers with larger buffers for pkt data
New Proposal:
  Guest negotiates with device the size of a Rx Buffer for a ring
    Each descriptor in that ring will have same size buffer
    Different rings can have different sized buffers
  Device can stipulate minimum (and max?) Rx Buffer sizes
  Device can stipulate Rx Buffer size multiple e.g. Rx Buffer size must be a multiple of 32B
  Is this acceptable?

## Slide 22: Rx Fixed Buffer Size
Rx Desc #0
Rx Desc #1
Rx Desc #2
Rx Desc #3
FPGA Descriptor Buffer
FPGA
Buffer #0
Buffer #1
Buffer #2
Buffer #3
Finite Descriptor Buffer
Total Data Buffer size supported by Descriptor Buffer is UNKNOWN
Therefore difficult to predict data throughput possible to maintain
Assuming smallest buffer size of 12B would lead to oversized Descriptor Buffer in most scenarios
Rx Desc #M
Variable Buffer Sizes
Rx Desc #0
Rx Desc #1
Rx Desc #2
Rx Desc #3
FPGA Descriptor Buffer
FPGA
Buffer #0
Buffer #1
Buffer #2
Buffer #3
Finite Descriptor Buffer
Total Data Buffer size supported by Descriptor Buffer is KNOWN = No desc * Rx Buffer size
Data throughput = func( min{min pkt size, Rx Buffer size})
Rx Desc #M
Fixed Buffer Sizes

## Slide 23: Fixed Rx Buffer size v Minimum Rx Buffer size
From previous slide:
  Appears that just increasing minimum Rx Buffer size from 12B to some sensible value (e.g. 256B) would be sufficient?
  YES, this would help immensely
  BUT more optimum/easier hardware design if Rx Buffer size is fixed
Assuming hardware implementation: Fetch Rx descriptors on demand
  As data enters device, descriptors are fetched as needed
  If device knows the Rx buffer size, it can precalculate how many descriptors would be required for the packet and so fetch them efficiently as a batch.
    No wasting local Descriptor buffer space for descriptors that will not be needed
Note: For hardware implementations: Prefetching Rx descriptors
  Specifying just a sensible minimum Rx Buffer size may be acceptable.
  However having fixed Rx Buffer size would allow it to prefetch the right amount of descriptors to maintain throughput.

## Slide 24: Data/Descriptor Alignment Boundaries

## Slide 25: Overview
Current Proposal:
  Guest is free to chose descriptor alignment to minimum of xByte boundary?
  Guest is free to chose data buffer alignment to any byte boundary?
New Proposal:
  Descriptors are aligned on a 16B boundary
  Guest negotiates with device on required data buffer alignment
    Could be from 4B – 128B boundary ?
  Wouldn’t s/w benefit from :
    cacheline aligned buffer start addresses?
    Integer number of descriptors per cacheline?

## Slide 26: PCIe packets
FPGA
Data Word
PCIe Header
Single 4B aligned access
4B UNaligned accesses add inefficiency to PCIe packets (TLPs)
Guest
FPGA
Data Word
PCIe Header
Single 4B unaligned access
Guest
Data Word
32bits
32bits
PCIe TLP
PCIe TLP

## Slide 27: Internal FPGA data alignment: Implementation dependant
FPGA
Data Word
PCIe Core
Single 32B aligned access
To achieve high throughput, FPGA data widths can be 256bits (or 512bits or even higher in future)
  Note also dependant upon clk frequency
Chained descriptors with buffers starting on unaligned boundaries exacerbates problem
Accesses may have to be aligned to FPGA word boundaries for ease of design.
Guest
256bits (32B)
0
B0
B1
B2
B31
FPGA
Data Word
PCIe Core
Single 32B UNaligned access
Guest
256bits (32B)
0
B0
B1
B2
B31
Data Word
0
B0
B1
B2
B31