Web Services Atomic Transaction Secure Interop Scenarios (WS-AT Secure Interop Scenarios) 1.1

Working Draft 01, May 23, 2006

Document Identifier:

wstx-wsat-1.1-interop_secure-scenarios-wd-01

Location:

http://docs.oasis-open.org/ws-tx/wstx-wsat-1.1-interop_secure-scenarios-wd-01.pdf

Technical Committee:

OASIS WS-TX TC

Chair(s):

Eric Newcomer, Iona

Ian Robinson, IBM

Editor(s):

Abstract:

This document is an addendum to the WS-Atomic Transaction Interop Scenarios document. Using interop scenario 2.1 from WS-AT interop scenarios, this document illustrates how to secure message exchanges.

Status:

This document is a working draft.

This document was last revised or approved by the WS-TX TC on the above date. The level of approval is also listed above. Check the current location noted above for possible later revisions of this document. This document is updated periodically on no particular schedule.

Technical Committee members should send comments on this specification to the Technical Committee’s email list. Others should send comments to the Technical Committee by using the “Send A Comment” button on the Technical Committee’s web page at www.oasis-open.org/committees/ws-tx.

For information on whether any patents have been disclosed that may be essential to implementing this specification, and any offers of patent licensing terms, please refer to the Intellectual Property Rights section of the Technical Committee web page (www.oasis-open.org/committees/ws-tx/ipr.php).

The non-normative errata page for this specification is located at www.oasis-open.org/committees/ws-tx.

Notices

OASIS takes no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights. Information on OASIS's procedures with respect to rights in OASIS specifications can be found at the OASIS website. Copies of claims of rights made available for publication and any assurances of licenses to be made available, or the result of an attempt made to obtain a general license or permission for the use of such proprietary rights by implementors or users of this specification, can be obtained from the OASIS President.

OASIS invites any interested party to bring to its attention any copyrights, patents or patent applications, or other proprietary rights which may cover technology that may be required to implement this specification. Please address the information to the OASIS President.

Copyright  © OASIS Open 2006. All Rights Reserved.

This document and translations of it may be copied and furnished to others, and derivative works that comment on or otherwise explain it or assist in its implementation may be prepared, copied, published and distributed, in whole or in part, without restriction of any kind, provided that the above copyright notice and this paragraph are included on all such copies and derivative works. However, this document itself does not be modified in any way, such as by removing the copyright notice or references to OASIS, except as needed for the purpose of developing OASIS specifications, in which case the procedures for copyrights defined in the OASIS Intellectual Property Rights document must be followed, or as required to translate it into languages other than English.

The limited permissions granted above are perpetual and will not be revoked by OASIS or its successors or assigns.

This document and the information contained herein is provided on an “AS IS” basis and OASIS DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

Table of Contents

1	Introduction	4

1.1 Scope	4

1.2 Namespaces	4

1.2.1 Asynchronous Messaging	4

1.3 Test Application	4

1.3.1 General Flow	5

1.3.2 Roles used in Test Scenarios	6

2	Composition with Security	7

Scenario #1.1.	Using HTTPS Security	7

Scenario #1.2.	Using WS-Coordination Security Model	7

3	Scenario #1.2 details	9

3.1 Application Messages	9

3.2 Registration Messages	13

3.3 2PC Protocol Messages	15

Appendix A. Activation Messages for Scenario 1.2	16

Appendix B. Acknowledgements	21

Appendix C. Revision History	22

Appendix D. Non-normative Text	23

# Introduction

## Scope

This document is an addendum to the WS-Atomic Transaction Interop Scenarios document. This illustrates how to secure message exchanges from one of the scenarios 2.1 using HTTPS and security model described in WS-Coordination specification section 5 “Security Model”.

## Namespaces

The following namespaces are used in this document.

| Prefix | Namespace | Description |
| --- | --- | --- |
| wsa | http://www.w3.org/2005/08/addressing | WS-Addressing |
| wscoor | http://docs.oasis-open.org/ws-tx/wscoor/2006/03 | WS-Coordination |
| wsat | http://docs.oasis-open.org/ws-tx/wsat/2006/03 | WS-AT |
| wsba | http://docs.oasis-open.org/ws-tx/wsba/2006/03 | WS-BA |
| wsse | http://docs.oasis-open.org/wss/2004/01/oasis-200401-wsswssecurity- secext-1.0.xsd | OASIS WSS |
| wssu | http://docs.oasis-open.org/wss/2004/01/oasis-200401-wsswssecurity- utility-1.0.xsd | OASIS WSS |
| wst | http://schemas.xmlsoap.org/ws/2005/02/trust | WS-Trust |
| wsc | http://schemas.xmlsoap.org/ws/2005/02/sc | WS-SecureConversation |
| ds | http://www.w3.org/2000/09/xmldsig# | W3C XML Digital Signature |
| xenc | http://www.w3.org/2001/04/xmlenc# | W3C XML Encryption |
| tns | urn:test | Test Application |
| footx | urn:foo-at-extension | sample WS-AT extensions URI |

### Asynchronous Messaging

All messages used in the interop workshop scenarios below correspond to the asynchronous port types described in the WSDL provided in the specifications.

## Test Application

To facilitate interoperability testing, and drive the scenarios, a Test Application is defined. The application comprises an Initiator Application (IA) role and a Participant Application (PA) role, each implemented using different implementations. WSDL for application-level interactions between an IA and PA is defined below.

An interoperability test of two (or more) implementations can be defined by assigning the role of IA to one implementation and the role of PA to all other implementations. Each implementation should support both roles.

### General Flow

This section describes the detailed message flow common for all scenarios in this document. In the test scenarios descriptions such common details will be omitted for brevity.

Implementation A should accept as input the URL of implementation B. Implementation A then initiates a coordinated activity using an internal/private Activation service to create a CoordinationContext (external Activation services are not required and are not tested.) The CoordinationContext includes the EPR of implementation A’s Registration Service and a unique coordination identifier (the optional expiration time of the activity should not be specified.) From this point forward, the implementations should interact as follows:

In the first phase, the two implementations agree on the scenario being tested and exchange EPRs for the coordination services being tested.

The IA sends an ApplicationRequest message to the PA. This message includes a WS-Addressing “Action” header, which specifies the URI of the scenario being tested, and a WS-Coordination “CoordinationContext” header, which identifies the coordinated activity.  The action URI for each scenario is derived from the Test Application WSDL (see appendix), using the Default Action Pattern defined in WS-Addressing.

The PA joins the coordinated activity by sending a Register message to the Requester’s Registration Service. The Register message targets the Registration Service Endpoint Reference specified in the CoordinationContext, and specifies the EPR of PA’s Protocol service. The coordination protocol(s) that the PA registers for is scenario specific.

The IA’s Registration service enlists the PA in the coordination activity, and responds with a RegisterResponse message correlated with the Register message using RelatesTo. The response message includes the EPR of the IA’s Coordinator service.

The PA sends an Application Response message tns:Response to the IA indicating that the first phase has completed.

All Completion and 2PC protocol messages are delivered according to an asynchronous, one-way message exchange pattern. Detail message descriptions are provided below in Section 7.

In the second phase, the IA and PA execute according to the selected scenario. Messages flows for each scenario are defined below in Sections 2, 3 & 4. In these flows, coordination protocol messages utilize the endpoint references (as defined in WS-Addressing) exchanged during the registration (Register & RegisterResponse) to direct processing to the coordinator or participant instance. All Completion and 2PC protocol messages are delivered according to an asynchronous, one-way message exchange pattern.

### Roles used in Test Scenarios

The test scenarios will use the following roles

- Initiator Application (IA)

- Participant Application (PA)

- Coordinator Service (CS)

- Participant Protocol Service (PS, PS1, PS2)

Each implementation participating in the test should be exercised in each role.

# Composition with Security

Interop scenarios in this section illustrate two approaches for providing security guarantees to the WS-AtomicTransaction message exchange. Within the scope of interoperability testing, we consider only the security of the Registration protocol and the agreement protocol relevant to the coordination type (for example the 2PC protocol in the case of WS-AT).

Using HTTPS Security

All messages use SOAP 1.1 and WS-Addressing (http://www.w3.org/2005/08/addressing).

Initiator and Participant applications (and their respective protocol services) each possess a certificate with associated private key representing their respective identities. Initiator and Participant applications also possess the other party’s public key in the form of a certificate.

For every TX protocol and Application Message the following is true

- Messages Protection is provided by HTTPS.

- Client and Server authentication is provided by HTTPS Client and Server Certificates.

It is worth noting that it is not important which specific mechanism is used to secure application messages, as long as the mechanism provides confidentiality and integrity guarantees for wscoor:CoordinationContext headers, WS-Coordination messages and WS-AT messages.

Message Exchange. Message Exchange in this scenario is the same as in WS-AT Interop Scenario #2.1 2PC Commit: PA registers for Durable2PC, IA initiates Commit, and transaction is committed successfully per 2PC protocol.

Initialization

- IA sends application message tns:Commit to PA

- PA registers PS with CS for the Durable2PC protocol

- PA sends one way message tns:Response to IA.

Message Exchange

(IA initiates Commit)

- CS sends Durable2PC::Prepare to PS

- PS sends Durable2PC::Prepared to CS

- CS sends Durable2PC::Commit to PS

(CS Committed)

- PS sends Durable2PC::Committed to CS

Using WS-Coordination Security Model

When per-transaction authorization is required, a simple Security Model described in WS-Coordination Section 5 can be used.

The following section illustrates the mechanisms employed to secure Application, Registration, and Protocol messages in this scenario. Activation messages are out of scope of interoperability testing in this scenario, appendix I illustrates how they can be used for this scenario.

# Scenario #1.2 details

## Application Messages

It is worth noting that it is not important which specific mechanism is used to secure application messages, as long as the mechanism provides integrity and confidentiality for wscoor:CoordinationContext headers, wst:IssuedTokens headers, WS-Coordination messages and WS-AT messages.

For this scenario we chose X509v3 token -based SOAP Message Security.

Message examples

Application message

<s:Envelope

xmlns:s="http://schemas.xmlsoap.org/soap/envelope/"

xmlns:wssu="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-utility-1.0.xsd"

xmlns:a="http://www.w3.org/2005/08/addressing/"

xmlns:wsse="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-secext-1.0.xsd">

<s:Header>

<a:Action wssu:Id="action">

http://docs.oasis-open.org/ws-tx/wscoor/2006/03/Register</a:Action>

<a:MessageID wssu:Id="messageid">urn:uuid:ed418b86-a75e-4aea-9d4e-a5d0cb5c088e</a:MessageID>

<a:ReplyTo wssu:Id="replyto">

<a:Address>https://...</a:Address>

<a:ReferenceParameters>

...

</a:ReferenceParameters>

</a:ReplyTo>

<a:To wssu:Id="to">https://...</a:To>

<wsse:Security s:mustUnderstand="1">

<wssu:Timestamp wssu:Id="timestamp">

<wssu:Created>2005-10-25T06:29:18.703Z</wssu:Created>

<wssu:Expires>2005-10-25T06:34:18.703Z</wssu:Expires>

</wssu:Timestamp>

<wsse:BinarySecurityToken

wssu:Id="IA_Certificate"

ValueType="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-x509-token-profile-1.0#X509v3"

EncodingType="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-soap-message-security-1.0#Base64Binary">

<!-- IA certificate -->

</wsse:BinarySecurityToken>

<e:EncryptedKey Id="encrypted_key" xmlns:e="http://www.w3.org/2001/04/xmlenc#">

<e:EncryptionMethod Algorithm="http://www.w3.org/2001/04/xmlenc#rsa-oaep-mgf1p"/>

<KeyInfo xmlns="http://www.w3.org/2000/09/xmldsig#">

<wsse:SecurityTokenReference>

<wsse:KeyIdentifier

ValueType="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-x509-token-profile-1.0#X509SubjectKeyIdentifier">

...

</wsse:KeyIdentifier>

</wsse:SecurityTokenReference>

</KeyInfo>

<e:CipherData>

<e:CipherValue>

<!-- ephemeral key encrypted for PA certificate-->

</e:CipherValue>

</e:CipherData>

<e:ReferenceList xmlns:e="http://www.w3.org/2001/04/xmlenc#">

<e:DataReference URI="#encrypted_body"/>

<e:DataReference URI="#encrypted_CCi"/>

<e:DataReference URI="#encrypted_issuedtokens"/>

</e:ReferenceList>

</e:EncryptedKey>

<Signature xmlns="http://www.w3.org/2000/09/xmldsig#">

<SignedInfo>

<CanonicalizationMethod

Algorithm="http://www.w3.org/2001/10/xml-exc-c14n#"/>

<SignatureMethod

Algorithm="http://www.w3.org/2000/09/xmldsig#rsa-sha1"/>

<Reference URI="#action">

<Transforms>

<Transform Algorithm="http://www.w3.org/2001/10/xml-exc-c14n#"/>

</Transforms>

<DigestMethod Algorithm="http://www.w3.org/2000/09/xmldsig#sha1"/>

<DigestValue>dTi3g3L9keG20RK45/u2YZAnweg=</DigestValue>

</Reference>

<Reference URI="#messageid">

<Transforms>

<Transform Algorithm="http://www.w3.org/2001/10/xml-exc-c14n#"/>

</Transforms>

<DigestMethod Algorithm="http://www.w3.org/2000/09/xmldsig#sha1"/>

<DigestValue>dTi3g3L9keG20RK45/u2YZAnweg=</DigestValue>

</Reference>

<Reference URI="#replyto">

<Transforms>

<Transform Algorithm="http://www.w3.org/2001/10/xml-exc-c14n#"/>

</Transforms>

<DigestMethod Algorithm="http://www.w3.org/2000/09/xmldsig#sha1"/>

<DigestValue>dTi3g3L9keG20RK45/u2YZAnweg=</DigestValue>

</Reference>

<Reference URI="#to">

<Transforms>

<Transform Algorithm="http://www.w3.org/2001/10/xml-exc-c14n#"/>

</Transforms>

<DigestMethod Algorithm="http://www.w3.org/2000/09/xmldsig#sha1"/>

<DigestValue>dTi3g3L9keG20RK45/u2YZAnweg=</DigestValue>

</Reference>

<Reference URI="#body">

<Transforms>

<Transform Algorithm="http://www.w3.org/2001/10/xml-exc-c14n#"/>

</Transforms>

<DigestMethod Algorithm="http://www.w3.org/2000/09/xmldsig#sha1"/>

<DigestValue>dTi3g3L9keG20RK45/u2YZAnweg=</DigestValue>

</Reference>

<Reference URI="#timestamp">

<Transforms>

<Transform Algorithm="http://www.w3.org/2001/10/xml-exc-c14n#"/>

</Transforms>

<DigestMethod Algorithm="http://www.w3.org/2000/09/xmldsig#sha1"/>

<DigestValue>m+MfakZa9mN8sH0bTqnT7fnPj4I=</DigestValue>

</Reference>

</SignedInfo>

<SignatureValue>...</SignatureValue>

<KeyInfo>

<wsse:SecurityTokenReference>

<wsse:Reference

ValueType="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-x509-token-profile-1.0#X509v3"

URI="#IA_Certificate"/>

</wsse:SecurityTokenReference>

</KeyInfo>

</Signature>

</wsse:Security>

<wsse11:EncryptedHeader

xmlns:wsse11="http://docs.oasis-open.org/wss/oasis-wss-wssecurity-secext-1.1.xsd">

<!-- encrypted wscoor:CoordinationContext header containing CCi-->

<!--

<wscoor:CoordinationContext>

<wscoor:Identifier>http://fabricam123.com/CCi</wscoor:Identifier>

<wscoor:Expires>...</wscoor:Expires>

<wscoor:CoordinationType>...</wscoor:CoordinationType>

<wscoor:RegistrationService>

<a:Address>https://...</a:Address>

<a:ReferenceParameters>

...

</a:ReferenceParameters>

</wscoor:RegistrationService>

</wscoor:CoordinationContext>

-->

<e:EncryptedData Id="encrypted_CCi"

Type="http://www.w3.org/2001/04/xmlenc#Content"

xmlns:e="http://www.w3.org/2001/04/xmlenc#">

<e:EncryptionMethod

Algorithm="http://www.w3.org/2001/04/xmlenc#aes256-cbc"/>

<KeyInfo xmlns="http://www.w3.org/2000/09/xmldsig#">

<wsse:SecurityTokenReference xmlns:wsse="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-secext-1.0.xsd">

<wsse:Reference URI="#encrypted_key"/>

</wsse:SecurityTokenReference>

</KeyInfo>

<e:CipherData>

<e:CipherValue>...</e:CipherValue>

</e:CipherData>

</e:EncryptedData>

</wsse11:EncryptedHeader>

<wsse11:EncryptedHeader

xmlns:wsse11="http://docs.oasis-open.org/wss/oasis-wss-wssecurity-secext-1.1.xsd">

<!-- encrypted wst:IssuedTokens header containing SCTi-->

<e:EncryptedData Id="encrypted_issuedtokens"

Type="http://www.w3.org/2001/04/xmlenc#Content"

xmlns:e="http://www.w3.org/2001/04/xmlenc#">

<e:EncryptionMethod

Algorithm="http://www.w3.org/2001/04/xmlenc#aes256-cbc"/>

<KeyInfo xmlns="http://www.w3.org/2000/09/xmldsig#">

<wsse:SecurityTokenReference>

<wsse:Reference URI="#encrypted_key"/>

</wsse:SecurityTokenReference>

</KeyInfo>

<e:CipherData>

<e:CipherValue>...</e:CipherValue>

</e:CipherData>

</e:EncryptedData>

<!-- BEGIN: encrypted content

<t:IssuedTokens>

<wst:RequestSecurityTokenResponse

xmlns:wsse="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-secext-1.0.xsd"

xmlns:wssu="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-utility-1.0.xsd"

xmlns:wst="http://schemas.xmlsoap.org/ws/2005/02/trust"

xmlns:wsc="http://schemas.xmlsoap.org/ws/2005/02/sc"

xmlns:wsp="http://schemas.xmlsoap.org/ws/2004/09/policy">

<wst:TokenType>http://schemas.xmlsoap.org/ws/2005/02/sc/sct</wst:TokenType>

<wst:RequestedSecurityToken>

<wsc:SecurityContextToken>

<wssu:Identifier>

http://fabricam123.com/SCTi

</wssu:Identifier>

</wsc:SecurityContextToken>

</wst:RequestedSecurityToken>

<wsp:AppliesTo>

http://fabricam123.com/CCi

</wsp:AppliesTo>

<wst:RequestedAttachedReference>

<wsse:SecurityTokenReference >

<wsse:Reference

ValueType="http://schemas.xmlsoap.org/ws/2005/02/sc/sct"

URI="http://fabricam123.com/SCTi"/>

</wsse:SecurityTokenReference>

</wst:RequestedAttachedReference>

<wst:RequestedUnattachedReference>

<wsse:SecurityTokenReference>

<wsse:Reference

ValueType="http://schemas.xmlsoap.org/ws/2005/02/sc/sct"

URI="http://fabricam123.com/SCTi"/>

</wsse:SecurityTokenReference>

</wst:RequestedUnattachedReference>

<wst:RequestedProofToken>

<wst:BinarySecret

Type="http://schemas.xmlsoap.org/ws/2005/02/trust/SymmetricKey">

<!-- base64 encoded value-->

</wst:BinarySecret>

</wst:RequestedProofToken>

<wst:Lifetime>

<wssu:Created>2005-10-24T20:19:26.526Z</wssu:Created>

<wssu:Expires>2005-10-25T06:24:26.526Z</wssu:Expires>

</wst:Lifetime>

<wst:KeySize>256</wst:KeySize>

</wst:RequestSecurityTokenResponse>

</t:IssuedTokens>

END: encrypted content -->

</wsse11:EncryptedHeader>

</s:Header>

<s:Body wssu:Id="body">

<!-- encrypted content of the Body element of the application message-->

<e:EncryptedData Id="encrypted_body"

Type="http://www.w3.org/2001/04/xmlenc#Content"

xmlns:e="http://www.w3.org/2001/04/xmlenc#">

<e:EncryptionMethod

Algorithm="http://www.w3.org/2001/04/xmlenc#aes256-cbc"/>

<KeyInfo xmlns="http://www.w3.org/2000/09/xmldsig#">

<wsse:SecurityTokenReference>

<wsse:Reference URI="#encrypted_key"/>

</wsse:SecurityTokenReference>

</KeyInfo>

<e:CipherData>

<e:CipherValue>...</e:CipherValue>

</e:CipherData>

</e:EncryptedData>

</s:Body>

</s:Envelope>

## Registration Messages

Message confidentiality and integrity are provided by HTTPS. The wssu:Timestamp is included to ensure message “freshness”.

Client and Server authentication is performed over HTTPS using client and server certificates.

Each participant (PS) that will be authenticated to participate in the 2PC protocol receives an SCTi with associated binary secret as part of the application message that initiates the IA for the scenario. This is shown above in Application Messages. The Register message provides proof-of-possession of the secret associated with the token SCTi, using a supporting signature over the timestamp as shown in the message example below.

Message Examples:

Register from PS to CS

<s:Envelope

xmlns:s="http://schemas.xmlsoap.org/soap/envelope/"

xmlns:a="http://www.w3.org/2005/08/addressing/"

xmlns:wscoor="http://docs.oasis-open.org/ws-tx/wscoor/2006/03"

xmlns:wsc="http://schemas.xmlsoap.org/ws/2005/02/sc">

<s:Header>

<a:Action>http://docs.oasis-open.org/ws-tx/wscoor/2006/03/Register</a:Action>

<a:MessageID>urn:uuid:ed418b86-a75e-4aea-9d4e-a5d0cb5c088e</a:MessageID>

<a:ReplyTo>

<a:Address>https://...</a:Address>

</a:ReplyTo>

<a:To>https://...</a:To>

<wsse:Security

s:mustUnderstand="1"

xmlns:wsse="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-secext-1.0.xsd"

xmlns:wssu="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-utility-1.0.xsd">

<wssu:Timestamp wssu:Id="_0" >

<wssu:Created>2005-12-15T23:36:13.827Z</wssu:Created>

<wssu:Expires>2005-12-15T23:41:13.827Z</wssu:Expires>

</wssu:Timestamp>

<wsc:SecurityContextToken>

<wssu:Identifier>

http://fabricam123.com/SCTi

</wssu:Identifier>

</wsc:SecurityContextToken>

<!-- supporting signature over the timestamp -->

<wsse:Signature xmlns:ds="http://www.w3.org/2000/09/xmldsig#">

<ds:SignedInfo>

<ds:CanonicalizationMethod Algorithm="http://www.w3.org/2001/10/xml-exc-c14n#"/>

<ds:SignatureMethod Algorithm="http://www.w3.org/2000/09/xmldsig#hmac-sha1"/>

<ds:Reference URI="#_0">

<ds:Transforms>

<ds:Transform Algorithm="http://www.w3.org/2001/10/xml-exc-c14n#"/>

</ds:Transforms>

<ds:DigestMethod Algorithm="http://www.w3.org/2000/09/xmldsig#sha1"/>

<ds:DigestValue>

alRzyhjLgoUOYoh8cx4n75eTcUk=

</ds:DigestValue>

</ds:Reference>

</ds:SignedInfo>

<ds:SignatureValue>YZYjnVvSOVasAQqQxaaviTSWtqI=</ds:SignatureValue>

<ds:KeyInfo>

<wsse:SecurityTokenReference

xmlns:wsse="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-secext-1.0.xsd">

<wsse:Reference

URI="http://fabricam123.com/SCTi"/>

</wsse:SecurityTokenReference>

</ds:KeyInfo>

</wsse:Signature>

</wsse:Security>

</s:Header>

<s:Body xmlns:s="http://schemas.xmlsoap.org/soap/envelope/">

<wscoor:Register>

<wscoor:ProtocolIdentifier>...</wscoor:ProtocolIdentifier>

<wscoor:ParticipantProtocolService>

<a:Address>https://... </a:Address>

</wscoor:ParticipantProtocolService>

</wscoor:Register>

</s:Body>

</s:Envelope>

RegisterResponse from PS to CS

<s:Envelope

xmlns:s="http://schemas.xmlsoap.org/soap/envelope/"

xmlns:a="http://www.w3.org/2005/08/addressing/"

xmlns:wscoor="http://docs.oasis-open.org/ws-tx/wscoor/2006/03">

<s:Header>

<a:Action>

http://docs.oasis-open.org/ws-tx/wscoor/2006/03/RegisterResponse

</a:Action>

<a:MessageID>urn:uuid:ed418b86-a75e-4aea-9d4e-a5d0cb5c088d</a:MessageID>

<a:RelatesTo>

urn:uuid:ed418b86-a75e-4aea-9d4e-a5d0cb5c088e

</a:RelatesTo>

<a:To>https://...</a:To>

<wsse:Security

s:mustUnderstand="1"

xmlns:wsse="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-secext-1.0.xsd"

xmlns:wssu="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-utility-1.0.xsd">

<wssu:Timestamp>

<wssu:Created>2005-12-15T23:36:13.827Z</wssu:Created>

<wssu:Expires>2005-12-15T23:41:13.827Z</wssu:Expires>

</wssu:Timestamp>

</wsse:Security>

</s:Header>

<s:Body xmlns:s="http://schemas.xmlsoap.org/soap/envelope/">

<wscoor:RegisterResponse>

<wscoor:CoordinatorProtocolService>

<a:Address>https://...</a:Address>

<a:ReferenceParameters>

...

</a:ReferenceParameters>

</wscoor:CoordinatorProtocolService>

</wscoor:RegisterResponse>

</s:Body>

</s:Envelope>

## 2PC Protocol Messages

Message confidentiality and integrity are provided by HTTPS.

Client and server authentication is performed over HTTPS using client and server certificates.

Message Examples:

Message #14:

<s:Envelope>

<s:Header>

<a:Action>http://.../ws/2004/10/wsat/Commit</a:Action>

<a:To>https://...</a:To>

<wsse:Security

s:mustUnderstand="1"

xmlns:wsse="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-secext-1.0.xsd"

xmlns:wssu="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-utility-1.0.xsd">

</wsse:Security>

</s:Header>

<s:Body xmlns:s="http://schemas.xmlsoap.org/soap/envelope/">

<wsat:Commit />

</s:Body>

</s:Envelope>

Message Exchange

Message Exchange in this scenario is the same as for scenario #1.1 2PC Commit: PA registers for Durable2PC, IA initiates Commit, transaction is committed successfully per 2PC protocol. Details are omitted for brevity.

Activation Messages for Scenario 1.2

This section illustrates optional Activation messages for scenario 1.2

This figure shows details of how an IA and PA may use the optional Activation service in the creation and importing of distributed AT contexts. It uses the previously defined roles: Initiator Application, its Coordinator Service, Participant Application and its Participant Protocol Service.

For convenience we assigned numbers to each protocol and application message:

| 1. CreateCoordinationContext | 12. Application Message Response |
| --- | --- |
| 2. CreateCoordinationContextResponse | 13. Commit (Completion) |
| 3. Register (Completion) | 14. Prepare (2PC) |
| 4. RegisterResponse | 15. Prepare (2PC) |
| 5. Application Message | 16. Prepared (2PC) |
| 6. CreateCoordinationContext w/Context | 17. Prepared (2PC) |
| 7. Register (Durable) | 18. Committed (Completion) |
| 8. RegisterResponse | 19. Commit (2PC) |
| 9. CreateCoordinationContextResponse | 20. Commit (2PC) |
| 10. Register (Durable) | 21. Committed (2PC) |
| 11. RegisterResponse | 22. Committed (2PC) |

Activation Messages

Message confidentiality and integrity are provided by HTTPS. The wssu:Timestamp is included to ensure message “freshness”.

Client and server authentication is performed over HTTPS using client and server certificates.

CreateCoordinationContextResponse messages (#2 and #9) carry the issued coordination context (CCi and CCp respectively) as well as the security context token (SCTi and SCTp respectively) scoped to the corresponding coordination context, with an associated binary secret. The security context token and associated secret are carried inside the wst:IssuedToken header as demonstrated in the message examples below.

The CreateCoordinationContext message sent by PA to PS (message #6) carries the coordination context CCi inside the body as well as the associated security context token SCTi in the wst:IssuedToken header.

Message Examples:

Message #1: CreateCoordinationContext

<s:Envelope>

<s:Header>

<a:Action>http://.../ws/2004/10/wscoor/CreateCoordinationContext</Action>

<a:MessageID>urn:uuid:069f5104-fd88-4264-9f99-60032a82854e</MessageID>

<a:ReplyTo>

<Address>https://...</a:Address>

</a:ReplyTo>

<a:To>https://...</a:To>

<wsse:Security>

<wssu:Timestamp>

<wsu:Created>2005-12-15T23:36:09.921Z</wsu:Created>

<wsu:Expires>2005-12-15T23:41:09.921Z</wsu:Expires>

</wsu:Timestamp>

</wsse:Security>

</s:Header>

<s:Body xmlns:s="http://schemas.xmlsoap.org/soap/envelope/">

<wscoor:CreateCoordinationContext>

<wscoor:CoordinationType>...</wscoor:CoordinationType>

</wscoor:CreateCoordinationContext>

</s:Body>

</s11:Envelope>

Message #2: CreateCoordinationContextResponse

<s:Envelope>

<!-- Data below is shown in the clear for

illustration purposes only -->

<s:Header>

<a:Action>./ws/2004/10/wscoor/CreateCoordinationContextResponse </a:Action>

<a:RelatesTo>urn:uuid:069f5104-fd88-4264-9f99-60032a82854e</a:RelatesTo>

<a:To s:mustUnderstand="1">https://... </a:To>

<t:IssuedTokens>

<wst:RequestSecurityTokenResponse

xmlns:wsse="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-secext-1.0.xsd"

xmlns:wssu="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-utility-1.0.xsd"

xmlns:wst="http://schemas.xmlsoap.org/ws/2005/02/trust"

xmlns:wsc="http://schemas.xmlsoap.org/ws/2005/02/sc"

xmlns:wsp="http://schemas.xmlsoap.org/ws/2004/09/policy">

<wst:TokenType>http://schemas.xmlsoap.org/ws/2005/02/sc/sct</wst:TokenType>

<wst:RequestedSecurityToken>

<wsc:SecurityContextToken>

<wssu:Identifier>

http://fabricam123.com/SCTi

</wssu:Identifier>

</wsc:SecurityContextToken>

</wst:RequestedSecurityToken>

<wsp:AppliesTo>

http://fabricam123.com/CCi

</wsp:AppliesTo>

<wst:RequestedAttachedReference>

<wsse:SecurityTokenReference >

<wsse:Reference

ValueType="http://schemas.xmlsoap.org/ws/2005/02/sc/sct"

URI="http://fabricam123.com/SCTi"/>

</wsse:SecurityTokenReference>

</wst:RequestedAttachedReference>

<wst:RequestedUnattachedReference>

<wsse:SecurityTokenReference>

<wsse:Reference

ValueType="http://schemas.xmlsoap.org/ws/2005/02/sc/sct"

URI="http://fabricam123.com/SCTi"/>

</wsse:SecurityTokenReference>

</wst:RequestedUnattachedReference>

<wst:RequestedProofToken>

<wst:BinarySecret

Type="http://schemas.xmlsoap.org/ws/2005/02/trust/SymmetricKey">

<!-- base64 encoded value-->

</wst:BinarySecret>

</wst:RequestedProofToken>

<wst:Lifetime>

<wssu:Created>2005-10-24T20:19:26.526Z</wssu:Created>

<wssu:Expires>2005-10-25T06:24:26.526Z</wssu:Expires>

</wst:Lifetime>

<wst:KeySize>256</wst:KeySize>

</wst:RequestSecurityTokenResponse>

</t:IssuedTokens>

<wsse:Security xmlns:wsse="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-secext-1.0.xsd">

<wssu:Timestamp u:Id="_0">

<wssu:Created>2005-12-15T23:36:12.015Z</wsu:Created>

<wssu:Expires>2005-12-15T23:41:12.015Z</wsu:Expires>

</wssu:Timestamp>

</wsse:Security>

</s:Header>

<s:Body>

<wscoor:CreateCoordinationContextResponse>

<wscoor:CoordinationContext>

<wscoor:Identifier>

http://fabricam123.com/CCi

</wscoor:Identifier>

<wscoor:Expires>...</wscoor:Expires>

<wscoor:CoordinationType>...</wscoor:CoordinationType>

<wscoor:RegistrationService>

<a:Address>https://...</a:Address>

<a:ReferenceParameters>

...

</a:ReferenceParameters>

</wscoor:RegistrationService>

</wscoor:CoordinationContext>

</wscoor:CreateCoordinationContextResponse>

</s:Body>

</s:Envelope>

Message #6:

<s:Envelope>

<s:Header>

<a:Action>http://.../ws/2004/10/wscoor/CreateCoordinationContext</Action>

<a:MessageID>urn:uuid:069f5104-fd88-4264-9f99-60032a82854e</MessageID>

<a:ReplyTo>

<Address>https://...</a:Address>

</a:ReplyTo>

<a:To>https://...</a:To>

<wsse:Security>

<wssu:Timestamp>

<wssu:Created>2005-12-15T23:36:09.921Z</wssu:Created>

<wssu:Expires>2005-12-15T23:41:09.921Z</wssu:Expires>

</wssu:Timestamp>

</wsse:Security>

</s:Header>

<s:Body xmlns:s="http://schemas.xmlsoap.org/soap/envelope/">

<wscoor:CreateCoordinationContext>

<wscoor:CoordinationType>...</wscoor:CoordinationType>

<wscoor:CoordinationContext>

<wscoor:Identifier>http://fabricam123.com/CCi</wscoor:Identifier>

<wscoor:Expires>...</wscoor:Expires>

<wscoor:CoordinationType>...</wscoor:CoordinationType>

<wscoor:RegistrationService>

<a:Address>https://...</a:Address>

<a:ReferenceParameters>

...

</a:ReferenceParameters>

</wscoor:RegistrationService>

</wscoor:CoordinationContext>

</wscoor:CreateCoordinationContext>

</s:Body>

</s11:Envelope>

Message #9:

<s:Envelope>

<s:Header>

<a:Action>../ws/2004/10/wscoor/CreateCoordinationContextResponse</a:Action>

<a:RelatesTo>urn:uuid:069f5104-fd88-4264-9f99-60032a82854e</a:RelatesTo>

<a:To s:mustUnderstand="1">https://... </a:To>

<t:IssuedTokens>

<wst:RequestSecurityTokenResponse

xmlns:wsse="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-secext-1.0.xsd"

xmlns:wssu="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-utility-1.0.xsd"

xmlns:wst="http://schemas.xmlsoap.org/ws/2005/02/trust"

xmlns:wsc="http://schemas.xmlsoap.org/ws/2005/02/sc"

xmlns:wsp="http://schemas.xmlsoap.org/ws/2004/09/policy">

<wst:TokenType>

http://schemas.xmlsoap.org/ws/2005/02/sc/sct

</wst:TokenType>

<wst:RequestedSecurityToken>

<wsc:SecurityContextToken>

<wssu:Identifier>

http://fabricam123.com/SCTp

</wssu:Identifier>

</wsc:SecurityContextToken>

</wst:RequestedSecurityToken>

<wsp:AppliesTo>

<wscoor:Identifier>http://fabricam123.com/CCp</wscoor:Identifier>

</wsp:AppliesTo>

<wst:RequestedAttachedReference>

<wsse:SecurityTokenReference >

<wsse:Reference

URI="http://fabricam123.com/SCTp"/>

</wsse:SecurityTokenReference>

</wst:RequestedAttachedReference>

<wst:RequestedUnattachedReference>

<wsse:SecurityTokenReference>

<wsse:Reference

ValueType="http://schemas.xmlsoap.org/ws/2005/02/sc/sct"

URI="http://fabricam123.com/SCTp"/>

</wsse:SecurityTokenReference>

</wst:RequestedUnattachedReference>

<wst:RequestedProofToken>

<wst:BinarySecret

Type="http://schemas.xmlsoap.org/ws/2005/02/trust/SymmetricKey">

<!-- base64 encoded value-->

</wst:BinarySecret>

</wst:RequestedProofToken>

<wst:Lifetime>

<wssu:Created>2005-10-24T20:19:26.526Z</wssu:Created>

<wssu:Expires>2005-10-25T06:24:26.526Z</wssu:Expires>

</wst:Lifetime>

</wst:RequestSecurityTokenResponse>

</t:IssuedTokens>

<wsse:Security xmlns:wsse="http://docs.oasis-open.org/wss/2004/01/oasis-200401-wss-wssecurity-secext-1.0.xsd">

<wssu:Timestamp u:Id="_0">

<wssu:Created>2005-12-15T23:36:12.015Z</wssu:Created>

<wssu:Expires>2005-12-15T23:41:12.015Z</wssu:Expires>

</wssu:Timestamp>

</wsse:Security>

</s:Header>

<s:Body>

<wscoor:CreateCoordinationContextResponse>

<wscoor:CoordinationContext>

<wscoor:Identifier>http://fabricam123.com/CCp</wscoor:Identifier>

<wscoor:Expires>...</wscoor:Expires>

<wscoor:CoordinationType>...</wscoor:CoordinationType>

<wscoor:RegistrationService>

<a:Address>https://...</a:Address>

<a:ReferenceParameters>

...

</a:ReferenceParameters>

</wscoor:RegistrationService>

</wscoor:CoordinationContext>

</wscoor:CreateCoordinationContextResponse>

</s:Body>

</s:Envelope>

Acknowledgements

This document is based on initial contribution to OASIS WS-TX Technical Committee by the

following authors:  Kirill Gavrylyuk, Microsoft, Max Feingold, Microsoft, Ian Robinson, IBM.

The following individuals were members of the committee during the development of this

specification:

TBD

Revision History

| Revision | Date | Editor | Changes Made |
| --- | --- | --- | --- |

Non-normative Text

# Text boxes

CS

PS

IA

PA

2

1

3

4

13

18

5

12

9

6

10

11

15

7

8

14

16

20

17

19

22

21