## Slide 1: SCTP Tutorial
Randall Stewart (randall@lakerest.net)
Michael Tüxen (tuexen@fh-muenster.de)

## Slide 2: Outline
Overview
Services provided by SCTP
Deployment considerations
Current developments

## Slide 3: Timeline of Transport Protocols
UDP (RFC 768, August 1980)
TCP (RFC 793, September 1981)
SCTP (RFC 2960, October 2000)
UDP-Lite (RFC 3828, July 2004)
DCCP (RFC 4340, March 2006)
MP-TCP (RFC 6824, January 2013)

## Slide 4: Timeline of SCTP RFCs
Core Protocol
  Initial Base Specification (RFC 2960, October 2000)
  Checksum Change (RFC 3309, September 2002)
  Errata and Issues (RFC 4460, April 2006)
  Updated Base Specification (RFC 4960, September 2007)
Protocol Extensions
  Partial Reliability (RFC 3758, May 2004)
  Chunk Authentication (RFC 4895, August 2007)
  Address Reconfiguration (RFC 5061, September 2007)
  Stream Reconfiguration (RFC 6525, February 2012)
API
  Socket API (RFC 6458, December 2011)

## Slide 5: Protocol Overview
Connection oriented (SCTP association)
Supports unicast
Same port number concept as other transport protocols
Message oriented
  Supports arbitrary large messages (fragmentation and reassembly)
  Supports bundling of multiple small messages in one SCTP packet
  Flexible ordering and reliability
Supports multihoming using IPv4 and IPv6
Packet consists of a common header followed by chunks
Extendable

## Slide 6: Association Setup
Four way handshake
Resistance against “SYN flooding”
Negotiates
  Initial number of streams
  Initial set of IP addresses
  Supported extensions
User messages can already be transmitted on the third leg (after one RTT i.e. same as TCP)
Handles the case of both sides initiating the association.

## Slide 7: Data Transfer
TCP friendly congestion control
User messages are put into DATA chunks (possibly multiple in case of fragmentation)
Each DATA chunk is identified by a Transmission Sequence Number (TSN)
Acknowledgements (SACKs) reporting
  Cumulative TSN
  Gaps (up to approximately 300 in a sack)
  Duplicate TSNs
Retransmissions
  Based on timer
  Based on gaps

## Slide 8: Association Teardown
Graceful shutdown
  Teardown without message loss.
  Based on an exchange of three messages.
  Supervised by timer
  No half close state is allowed
Non-graceful shutdown
  Possibly message loss
  Uses a single message

## Slide 9: Service: Preservation of Message Boundaries
Most application protocols are message based
Simplifies application protocols and its implementation
Awareness of message boundaries makes optimal handling at the transport layer / application layer boundary possible
Special attention needed for supporting arbitrary large messages

## Slide 10: Service: Partial Reliability
Allows to avoid spending resources on user messages not being relevant anymore for the receiver.
The sender can abandon user messages base on criteria called PR-SCTP policy
PR-SCTP policies are implemented on the sender side and does not require negotiation.
Examples of PR-SCTP policies:
  Lifetime
  Number of retransmissions
  Priority with respect to buffering

## Slide 11: Service: Partial Ordering
An SCTP association provides up to 2^16 uni-directional streams in each direction.
Each message is sent on a stream.
Message ordering is only preserved within each stream.
In addition, messages can be marked for unordered delivery.
This minimizes head of line blocking
The stream reconfiguration extension (RFC 6525) allows to
  Add streams during the lifetime of an association
  Reset streams (i.e. start over at stream sequence 0)

## Slide 12: Service: Network Fault Tolerance
Each end-point can have multiple IP-addresses
Each path is continuously supervised
Primary path is used for initial transmission of user data
In case of a failure, another (working) address is used
The Address Reconfiguration extension (RFC 5061) allows
  Add and delete IP-addresses during the lifetime of an association
  Select the local and remote primary path
Currently being specified: loadsharing

## Slide 13: Security
SCTP over IPSec
  Specified in RFC 3554, July 2003
  Multihoming improvements for IPSec
  Not implemented (as far as the authors know)
TLS over SCTP
  Specified in RFC 3436, December 2002
  Doesn’t provide all services (no PR-SCTP, only ordered delivery)
  Doesn’t scale well and can’t be implemented directly in OpenSSL, however can be build as part of the application
DTLS over SCTP
  Specified in RFC 6083, September 2010
  Provides almost all services provided by SCTP and its extensions
  Implemented in OpenSSL 1.0.1

## Slide 14: Usage
SIGTRAN: Telephony signaling networks
RSerPool
Diameter
IPFIX
Forces
RTCWeb

## Slide 15: RTCWeb
Transport layer for data channels
Encapsulated in DTLS running on top of UDP using ICE/STUN/TURN for NAT traversal
Usage of
  multiple streams
  ordered / unordered delivery
  partial reliability
  stream reconfiguration

## Slide 16: Implementations
Provided by OS vendor for
  FreeBSD
  Linux
  Solaris
The FreeBSD has been ported to support
  Mac OS X as a network kernel extension (NKE)
  Windows as a kernel driver
  Windows, Linux, FreeBSD, MacOS X as a userland stack (included in Firefox)
Commercial implementations for various operating systems
Implementations are interoperable as shown in nine interoperability tests.

## Slide 17: Socket API
Two programming models:
  One to one Style API
  One to many Style API
Several socket options allowing fine-tuning of parameters
Notifications (events that happen on the transport connection)
Additional cmsgs for sendmsg()/recvmsg()
Additional functions for
  supporting multiple IP addresses per end-point
  sending and receiving user messages
  Transition of sockets between programming models
Mostly supported by FreeBSD, Linux and Solaris allowing users to write portable programs

## Slide 18: NAT Traversal
Legacy NATs:
  UDP encapsulation, allows UDP port numbers to be modified by middle-boxes
  Requires support in the SCTP end-hosts
  Doesn’t require special support in the middle-boxes
SCTP aware NATs:
  SCTP port numbers are not modified by middle-boxes
  Requires support from the middle-boxes and the end-hosts, however no communication between middle-boxes is required

## Slide 19: Ongoing SCTP-related Work in TSVWG
UDP tunneling (in IESG discussion)
SCTP aware NATs
ECN support
Interleaving of user messages
Loadsharing
Optimizations (sack immediately and others)

## Slide 20: Conclusion
SCTP provides a variety of flexible services
  Network fault tolerance
  Partial reliability
  Partial ordering
Interoperable implementations are available
Middleboxes need to be taken into account