# Programming Interfaces

(…)

## XPath Extension Functions

This section introduces XPath extension functions that are provided to be used within the definition of a human task or notification. A WS-HumanTask Processor MUST support the XPath Functions listed below. When defining properties using these XPath functions, note the initialization order in section 4.7.1.

Definition of these XPath extension functions is provided in the table below. Input parameters that specify task name, message part name or logicalPeopleGroup name MUST be literal strings. This restriction does not apply to other parameters. Because XPath 1.0 functions do not support returning faults, an empty node set is returned in the event of an error.

XPath functions used for notifications in an escalation can access context from the enclosing task by specifying that task’s name.

| Operation Name | Description | Parameters |
| --- | --- | --- |
| getPotentialOwners | Returns the potential owners of the task. It MUST evaluate to an empty htt:organizationalEntity in case of an error. If the task name is not present the current task MUST be considered. | In task name (optional) Out potential owners (htt:organizationalEntity) |
| getActualOwner | Returns the actual owner of the task. It MUST evaluate to an empty htt:user in case there is no actual owner. If the task name is not present the current task MUST be considered. | In task name (optional) Out the actual owner (user id as htt:user) |
| getTaskInitiator | Returns the initiator of the task. It MUST evaluate to an empty htt:user in case there is no initiator. If the task name is not present the current task MUST be considered. | In task name (optional) Out the task initiator (user id as htt:user) |
| getTaskStakeholders | Returns the stakeholders of the task. It MUST evaluate to an empty htt:organizationalEntity in case of an error. If the task name is not present the current task MUST be considered. | In task name (optional) Out task stakeholders (htt:organizationalEntity) |
| getBusinessAdministrators | Returns the business administrators of the task. It MUST evaluate to an empty htt:organizationalEntity in case of an error. If the task name is not present the current task MUST be considered. | In task name (optional) Out business administrators (htt:organizationalEntity) |
| getExcludedOwners | Returns the excluded owners. It MUST evaluate to an empty htt:organizationalEntity in case of an error. If the task name is not present the current task MUST be considered. | In task name (optional) Out excluded owners (htt:organizationalEntity) |
| getTaskPriority | Returns the priority of the task. It MUST evaluate to “5” in case the priority is not explicitly set. If the task name is not present the current task MUST be considered. | In task name (optional) Out priority (htt:tPriority) |
| getInput | Returns the part of the task’s input message. If the task name is not present the current task MUST be considered. | In part name task name (optional) Out input message part |
| getSubtaskOutput | Returns a node-set representing the specified part or contained elements of a sub task’s output message. Only completed sub tasks of the current task MUST be considered | In subtask name part name location path Out node-set of output message element(s) |
| getSubtaskOutputs | Returns a node-set of simple-typed or complex-typed elements, constructed from the subtasks’ output documents in a routing pattern. The string parameter contains a location path evaluated on each subtask’s output document. The individual node-sets are combined into the returned node-set. Only completed sub tasks of the current task MUST be considered | In part name location path Out node-set of output message elements from subtasks |
| getOutput | Returns the part of the task's output message. If the task name is not present the current task MUST be considered | In part name task name (optional) Out output message part |
| getCountOfSubTasks | Returns the number of subtasks of a task If the task name is not present the current task MUST be considered | In task name (optional) Out Number of the task sub-tasks. If the task doesn't have sub tasks then 0 is returned |
| getCountOfFinishedSubTasks | Returns the number of finished subtasks of a task If the task name is not present the current task MUST be considered | In task name (optional) Out Number of the finished task sub-tasks. If the task doesn't have sub tasks then 0 is returned |
| getCountOfSubTasksInState | Returns the number of a task suubtasks that are in the specified state If the task name is not present the current task MUST be considered | In state task name (optional) Out Number of the task sub tasks in the specified state. If the task doesn't have sub tasks then 0 is returned |
| getCountOfSubTasksWithOutcome | Returns the number of a task sub tasks that match the given outcome If the task name is not present the current task MUST be considered | In outcome task name (optional) Out Number of the task sub tasks that match the specified outcome. If the task doesn't have sub tasks then 0 is returned |
| getLogicalPeopleGroup | Returns the value of a logical people group. In case of an error (e.g., when referencing a non existing logical people group) the htt:organizationalEntity MUST contain an empty user list. If the task name is not present the current task MUST be considered. | In name of the logical people group The optional parameters that follow MUST appear in pairs. Each pair is defined as: the qualified name of a logical people group parameter the value for the named logical people group parameter; it can be an XPath expression Out the value of the logical people group (htt:organizationalEntity) |
| getOutcome | Returns the outcome of the task. It MUST evaluate to an empty string in case there is no outcome specified for the task. If the task name is not present the current task MUST be considered. | In task name (optional) Out the task outcome (xsd:string) |
| union | Constructs an organizationalEntity containing every user that occurs in either set1 or set2, eliminating duplicate users. | In set1 (htt:organizationalEntity ¦htt:users ¦htt:user) set2 (htt:organizationalEntity ¦htt:users ¦htt:user) Out result (htt:organizationalEntity) |
| intersect | Constructs an organizationalEntity containing every user that occurs in both set1 and set2, eliminating duplicate users. | In set1 (htt:organizationalEntity ¦htt:users ¦htt:user) set2 (htt:organizationalEntity ¦htt:users ¦htt:user) Out result (htt:organizationalEntity) |
| except | Constructs an organizationalEntity containing every user that occurs in set1 but not in set2. Note: This function is required to allow enforcing the separation of duties (“4-eyes principle”). | In set1 (htt:organizationalEntity ¦htt:users ¦htt:user) set2 (htt:organizationalEntity ¦htt:users ¦htt:user) Out result (htt:organizationalEntity) |

In addition to the general-purpose functions listed above, the following aggregation functions MUST be supported by a WS-HumanTask Processor. All aggregation functions take a node-set of strings, booleans, or numbers as the first input parameter, and produce a result of the same type.

| concat | Returns the concatenation of all string nodes - returns an empty string for an empty node-set | In node-set of string nodes |
| --- | --- | --- |
| concatWithDelimiter | Returns the concatenation of all string nodes, separated by the specified delimiter string - returns an empty string for an empty node-set | In node-set of string nodes delimiter string |
| leastFrequentOccurence | Returns the least frequently occurring string value within all string nodes, or an empty string in case of a tie or for an empty node-set | In node-set of string nodes |
| mostFrequentOccurence | Returns the most frequently occurring string value within all string nodes, or an empty string in case of a tie or for an empty node-set | In node-set of string nodes |
| voteOnString | Returns the most frequently occurring string value if its occurrence is above the specified percentage and there is no tie, or an empty string otherwise (including an empty node-set) | In node-set of string nodes percentage |
| and | Returns the conjunction of all boolean nodes - returns false for an empty node-set | In node-set of boolean nodes |
| or | Returns the disjunction of all boolean nodes - returns false for an empty node-set | In node-set of boolean nodes |
| vote | Returns the most frequently occurring boolean value if its occurrence is above the specified percentage, or false otherwise (including an empty node-set) | In node-set of boolean nodes percentage |
| avg | Returns the average value of all number nodes - returns NaN for an empty node-set | In node-set of number nodes |
| max | Returns the maximum value of all number nodes - returns NaN for an empty node-set | In node-set of number nodes |
| min | Returns the minimum value of all number nodes - returns NaN for an empty node-set | In node-set of number nodes |
| sum | Returns the sum value of all number nodes - returns 0 for for an empty node-set | In node-set of number nodes |