## Meaning of state table events

The tables in this section define the events (rows) in the state tables. Table 1 defines the events corresponding to sending or receiving BTP messages and the disruption events. The other tables specify what conditions and actions are entailed in the “decision” events. The detailed nature of these differs depending on the location of the actor in a BTP transaction tree.

Table 2 covers the simple case of a “pure” Participant – i.e. an Inferior that is not also a Superior. In this case the decisions concern only the effects of the associated application operations and the persistent information of the Participant itself. (Such a Participant may be using similar two-phase commit mechanisms to control resources involved in the application operations, but this is invisible to BTP)

Table 3 covers the corresponding case, for an Atom Coordinator, which has no Superior. The decisions in this case concern the state of any other Inferiors the Coordinator may have, the messages received from the (volatile) Terminator, and the Coordinator’s own persistent state.

Table 4 combines Table 2 and Table 3 in the case of an Atom sub-Coordinator, which is a BTP Inferior in one direction and Superior to  (one or more) Inferiors. The table specifies the interactions between the decision and other events on each branch. The conditions for the Superior decisions apply to all the branches on which the sub-Coordinator is Superior.

Table 5 - <not written yet, but should deal with Coordinator within a Cohesion : or is that identical to table 4>

Table 6 - <not written, intended to be Cohesion Composer>

# Table 1 : send, receive and disruption events

| Event name | Meaning |
| --- | --- |
| send/receive ENROLL/rsp-req | send/receive ENROLL with reply-requested = true |
| send/receive ENROLL/no-rsp-req | send/receive ENROLL with reply-requested = false |
| send/receive RESIGN/rsp-req | send/receive RESIGN with reply-requested = true |
| send/receive RESIGN/no-rsp-req | send/receive RESIGN with reply-requested = false |
| send/receive READY | send/receive READY, with default-cancel = false |
| send/receive READY/cancel | send/receive READY, with default-cancel = true |
| send/receive CONFIRMED/auto | send/receive CONFIRMED, with confirm-received = true |
| send/receive CONFIRMED/response | send/receive CONFIRMED, with confirm-received = false |
| send/receive MIXED | send/receive MIXED |
| send/receive INF_STATE/***/y | send/receive INFERIOR_STATE with status *** and reply-requested = true |
| send/receive INF_STATE/*** | send/receive INFERIOR_STATE with status *** and reply-requested = false |
| send/receive SUP_STATE/***/y | send/receive SUPERIOR_STATE with status *** and reply-requested = true |
| send/receive SUP_STATE/*** | send/receive SUPERIOR_STATE with status *** and reply-requested = false |
| disruption *** | Loss of state event – new state is state applying after any local recovery processes complete |

Table 2: Decision events for Participant (with no visible inferiors)

| Event name | Meaning |
| --- | --- |
| decide to vote ready | Effects of all associated operations can be confirmed or cancelled; information to retain this ability (ready information) has been made persistent |
| decide to vote ready/cancel | Effects of all associated operations can be confirmed or cancelled; information to retain this ability (ready information) has been made persistent; the ready information specifies that the default action will be to cancel |
| decide to confirm autonomously | Decision to confirm autonomously has been made persistent; the effects of associated operations will be confirmed regardless of failures |
| decide to cancel autonomously | Decision to cancel autonomously has been made persistent; the effects of associated operations will be cancelled regardless of failures |
| apply ordered confirmation | Effects of all associated operations have been confirmed; any remaining persistent information can be distinguished from the state after deciding to vote ready |
| remove ready information | Persistent ready information has been effectively removed; any remaining persistent information can be distinguished from the state after deciding to vote ready |
| record mixed result | Some of the associated operations have been confirmed, some cancelled; information recording this has been persisted (to the degree considered appropriate) |

Table 3 : Decision events for a Coordinator (not in a Cohesion)

| Event name | Meaning |
| --- | --- |
| decide to prepare | All associated application messages to be sent to the service have been sent; terminator has requested prepare (by sending REQUEST_CONFIRM or by a non-standard means) |
| decide to confirm | RESIGN, READY or READY/cancel has been received from all other Inferiors of this Coordinator; REQUEST_CONFIRM or information recording the confirm decision (confirm information) identifying this Inferior (and other non-resigning Inferiors) has been made persistent |
| decide to cancel | Any persistent information can be distinguished from confirm information; the atom will not be ordered to confirm, regardless of failures |
| remove confirm information | Persistent confirm information has been effectively removed; any remaining persistent information can be distinguished from the state immediately after deciding to confirm |
| record contradiction | Information recording the contradiction has been persisted (to the degree considered appropriate) |

# Table 4 : Decision events for sub-coordinator in an Atom

| Event name | Meaning |
| --- | --- |
| decide to vote ready | RESIGN, READY or READY/cancel has been received from all Inferiors; ready information includes identity of all Inferiors other than those from which RESIGN was received; otherwise as for Participant |
| decide to vote ready/cancel | RESIGN, READY or READY/cancel has been received from all Inferiors; ready information includes identity of all Inferiors other than those from which RESIGN was received; otherwise as for Participant |
| decide to confirm autonomously | As for Participant; atomic with “decide to confirm” for all Inferiors |
| decide to cancel autonomously | As for Participant; atomic with “decide to cancel” for all Inferiors |
| apply ordered confirmation | “remove confirm information” for each Inferior has either been performed or is atomic with this; otherwise as for Participant |
| remove ready information | As for Participant |
| record mixed result | Some Inferiors and/or some associated operations confirmed, some cancelled; information recording this has been persisted (to the degree considered appropriate) |
| decide to prepare | As for Coordinator, or all associated application messages to be sent to the service have been sent; PREPARE received from Superior. |
| decide to confirm | CONFIRM received from Superior |
| decide to cancel | One of the following must be true: neither “decide to send ready” nor “decide to send ready/cancel” decision will be made as Inferior; CANCEL or SUPERIOR_STATE/unknown received from Superior “decide to cancel autonomously” is made as Inferior |
| remove confirm information | As for Coordinator |
| record contradiction | As for Coordinator; may be atomic with “record mixed result” |

### Persistent information

Persisted information (especially ready information at an Inferior, confirm information at a Superior) may include qualifications of the state carried in Qualifiers of the corresponding message (e.g. participant timeouts in ready information).

In all cases, the degree to which information described as “persistent” will survive failure is a configuration and implementation option. An implementation should describe the level of failure that it is capable of surviving. For applications manipulating information that is itself volatile (e.g. network configurations), an equivalent level of persistence of the BTP state information may be appropriate.

The degree of persistence of the recording of a mixed result at an Inferior and recording of a detected contradiction at a Superior may be different from that applying to the persistent ready and confirm information. Implementations and configuration may choose to pass mix and contradiction information via management mechanisms rather than through the BTP tree. Such passing of information to a management mechanism could be treated as “recording mixed result” or “recording contradiction”.