An OASIS White Paper

DITA 1.2 Feature Overview: Conref Push

Kristen James Eberlein

4 October 2009

OASIS (Organization for the Advancement of Structured Information Standards) is a not-for-profit, international consortium that drives the development, convergence, and adoption of e-business standards. Members themselves set the OASIS technical agenda, using a lightweight, open process expressly designed to promote industry consensus and unite disparate efforts. The consortium produces open standards for Web services, security, e-business, and standardization efforts in the public sector and for application-specific markets. OASIS was founded in 1993. More information can be found on the OASIS website at http://www.oasis-open.org.

The OASIS DITA Adoption Technical Committee members collaborate to provide expertise and resources to educate the marketplace on the value of the DITA OASIS standard. By raising awareness of the benefits offered by DITA, the DITA Adoption Technical Committee expects the demand for, and availability of, DITA conforming products and services to increase, resulting in a greater choice of tools and platforms and an expanded DITA community of users, suppliers, and consultants.

DISCLAIMER: All examples presented in this article were produced using one or more tools chosen at the author's discretion and in no way reflect endorsement of the tools by the OASIS DITA Adoption Technical Committee.

Table of contents

Conref push	2

Overview	2

Example of pushing content after an element in a topic	2

Adding the @id attribute	3

Creating the content to be pushed	4

Modifying the DITA map	5

Example of pushing content before an element in a topic	5

Example of replacing an element in a topic	7

Rules and restrictions	8

What happens with multiple push operations targeting the same element?	8

# Conref push

DITA 1.2 introduces the conref push feature, which enables users to either add content to or replace content in DITA topics. This is accomplished by the introduction of a new @conaction attribute with four values: pushreplace, pushbefore, pushafter, and mark.

## Overview

The conref (content reference) mechanism is a core feature of the Darwin Information Typing Architecture (DITA). An elegant transclusion device, the conref mechanism enables significant reuse of DITA elements, topics, and maps, thus reducing translation costs and increasing consistency.

Until DITA 1.2., the conref mechanism only used a pull feature, that is, you could only pull content into DITA topics. With DITA 1.2, you now have the ability to push content into DITA topics, provided that the topics contain @id attributes that identify the places where the content is to be pushed.

This article contains screen captures of DITA source files (as viewed in Oxygen XML Editor 10.0) and output generated by the DITA Open Toolkit, version 1.5, milestone 17.

## Example of pushing content after an element in a topic

Imagine that you are updating a version of the sample files that ship with the DITA Open Toolkit. This information set contains a helpful topic about changing oil in an automobile.

Figure 1. Original "Changing the oil" topic: HTML Help output

However, the topic fails to address a critical legal issue in your locality: Used motor oil must be properly disposed of. With DITA 1.2, you can push a new <step> element into the "Changing the oil" topic, so that you can generate the following HTML output:

Figure 2. "Changing the oil" topic: HTML Help output after conref push operation

How was this done? What was required?

The person working with the DITA source files only needed to make the following changes to the information set:

- Ensure that the original "Changing the oil" topic had an @id attribute for the <step> element that contained the instruction to "Drain the old oil." If she had access to that file, she could add an @id attribute; otherwise, she'd need to request that the person who owns the file add the necessary attribute.

- Create the <step> element that contains the content to be pushed into the "Changing the oil" topic. This content either could be added to an existing reuse topic or created in a new topic.

- Modify the DITA map to incorporate the DITA topic that contains the material to be pushed, if it does not already include it.

### Adding the @id attribute

The writer arranges for an @id attribute to be added to the applicable <step> element in the "Changing the oil" topic. The modified topic now looks as follows; note that the @id attribute is highlighted in yellow:

Figure 3. "Changing the oil" topic with @id attribute added

### Creating the content to be pushed

The writer now creates a DITA topic to hold the content to be pushed: conref-file.dita. (She also could use an existing reuse file, if one existed.)

Figure 4. Topic that contains the content to be pushed after

Here is an explanation of the content of the topic:

The first <step> element identifies the <step> element after which the content is to be pushed. This happens in two parts:

The @conref attribute uses standard syntax to identify the <step> element.

The  @conaction attribute (new with DITA 1.2) is set to "mark". Setting the @conaction attribute to "mark" indicates that a conref push operation is indicated.

Note that the <cmd> element is empty; the content model for the <step> element requires that a <cmd> element be present.

The second <step> element specifies the content that is to be pushed into the "Changing the oil" topic. The <cmd> element contains the content, and the @conaction attribute indicates that the <step> element is to be pushed after the element with a @conaction attribute set to "mark".

### Modifying the DITA map

The writer then modifies the DITA map for the deliverable so that it includes the topic that contains the content to be pushed:

Figure 5. Modified DITA map that contains the resource file

The conref-file.dita topic  is referenced in the DITA map by a <topicref> element. Note that the @processing-role attribute (new with DITA 1.2) is set to "resource-only". This attribute indicates that the topic referenced should be used only to resolve conref, keyref, or xref operations; it should not appear in the table of contents (TOC), be found in a search operation, or be linked to.

Note also that the <topicref> element appears at the top of the DITA map and is marked with a comment. This is not necessary – the <topicref> element could be placed anywhere in the DITA map – but reflects best practices and helps to make the DITA map easy for humans to read and scan. If a DITA map contains many <topicref> elements that reference conref or keyref resources, consider building a separate DITA map to contain those references.

## Example of pushing content before an element in a topic

The writer also could push the <step> element before the <step> element with the @id attribute. (Let's ignore for the moment that this doesn't make sense, as one would not recycle the used motor oil before draining it from the automobile.) All this would require is a modification to the conref-file.dita topic; the changes that previously were made to the "Changing the oil" and the DITA map would work here, too.

Here is what the conref-file.dita topic would look like, if the writer wanted to push the new <step> element before the <step> element with the @id attribute:

Figure 6. DITA topic that contains the content to be pushed before

Note that the <step> element that contains the content to be pushed is placed before the <step> element with the conaction="mark" attribute; it also has a @conaction attribute that is set to "pushbefore".

When the DITA map that referenced the modified conref-file.dita topic is processed, the following output is generated:

Figure 7. "Changing the oil" topic: HTML Help output after a conref pushbefore operation

## Example of replacing an element in a topic

The writer also could simply choose to replace the <step> element in the "Changing the oil" topic. Here is what the reuse topic would contain:

Figure 8. DITA topic that contains the content to be used as a replacement

Note that for a conref pushreplace operation, only one element is needed. The @conref attribute specifies the element to be replaced, and the @conaction attribute to set to "pushreplace".

Here is a screen shot of the HTML Help generated by the DITA Open Toolkit:

Figure 9. "Changing the oil" topic: After conref pushreplace operation

## Rules and restrictions

All the rules and restriction are designed to ensure that the result of the push operation is valid DITA.

For all push operations, the source element – the element that is pushed – must be of the same type (or more specialized) than the target element. For example, both of the following scenarios are valid scenarios:

- A <step> element is the source element, and a <step> element is the target element. This is what is demonstrated in the examples in this feature article.

- A <step> element is the source element, and a <li> element is the target element. This is possible because the <step> element is specialized from the <li> element. During processing, the <step> element is generalized back to a <li> element. However, the source element cannot be more generalized than the target element. For example, one cannot push a <li> element into a <step> element. The content model for a <li> element permits many children elements (for example, <p> elements) that would not be valid within the <step> element.

For push before or push after operations, some additional restrictions apply:

- The element that specifies the conaction="mark" attribute must be of the same type as the element that specifies the push operation (either conaction="pushbefore" or conaction="pushafter). Both elements will appear in the output.

- The parent of the source element must be of the same type as (or more specialized than) the parent of the target elements. This ensures the validity of the target; for example, comparing the parent elements will prevent a <title> element that is a child of <section> from being pushed before (or after) a <title> element that is a child of <figure>.

## What happens with multiple push operations targeting the same element?

- It is an error for two or more elements to attempt to replace the same target element. According to the DITA 1.2 specification: "Applications may, but need not, warn users if more than element attempts to replace a single target."

- If two or more elements attempt to push content before the same target element, the order in which the pushed content is processed is undefined.

- If two or more elements attempt to push content after the same target element, the order in which the pushed content is processed is undefined.

# Comments

Can one push content into a DITA map? Elliot assumed yes.

Comment from Elliot Kimber: I agree, I think you need a paragraph or two explaining what a “reuse file” is and making it clear that the content to be pushed has to be in its own topic in order to satisfy the syntax rules of the DITA spec.

Comment from Seth Park: this may be distracting if the user asks, “what is a “conref file? Did I miss something?” Maybe you can create a section at the end called “Creating a conref file for managing conref-push elements”],

Comment from Elliot Kimber: “resource file” hasn’t been defined. Not clear if you mean the conref doc or the push target doc.

Comment from Seth Park: why did you change the order of the step elements? We don’t want to suggest that the user has to do this.

Need to rewrite to either 1) remove references to source and target elements, or 2) use more commonly-understood definitions of source and target.