Context management rendering as XML for bpss refinement and business agreement

Version 1.0

DRAFT	DRAFT	DRAFT	DRAFT	DRAFT 	DRAFT

CHANGE HISTORY

| Status | Version | Revision | Date | Editor | Summary of Changes |
| --- | --- | --- | --- | --- | --- |
| Draft | 1.0 | 0.14 | 14 December, 2003 | DRRW | Initial Draft |
|  |  | 0.15 | 26 January, 2004 | DRRW | Initial Draft |
|  |  | 0.151 | 2 February 2004 | DRRW | Revised to include 3 examples |

OASIS COPYRIGHT NOTICE

Copyright (C) The Organization for the Advancement of Structured Information Standards [OASIS] (1 March 2001). All Rights Reserved

This document and translations of it may be copied and furnished to others, and derivative works that comment on or otherwise explain it or assist in its implementation may be prepared, copied, published and distributed, in whole or in part, without restriction of any kind, provided that the above copyright notice and this paragraph are included on all such copies and derivative works. However, this document itself may not be modified in any way, such as by removing the copyright notice or references to OASIS, except as needed for the purpose of developing OASIS specifications, in which case the procedures for copyrights defined in the OASIS Intellectual Property Rights document must be followed, or as required to translate it into languages other than English.

The limited permissions granted above are perpetual and will not be revoked by OASIS or its successors or assigns.

This document and the information contained herein is provided on an "AS IS" basis and OASIS DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE."

OASIS takes no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights. Information on OASIS's procedures with respect to rights in OASIS specifications can be found at the OASIS website. Copies of claims of rights made available for publication and any assurances of licenses to be made available, or the result of an attempt made to obtain a general license or permission for the use of such proprietary rights by implementers or users of this specification, can be obtained from the OASIS Executive Director.

OASIS invites any interested party to bring to its attention any copyrights, patents or patent applications, or other proprietary rights which may cover technology that may be required to implement this specification. Please address the information to the OASIS Executive Director.

OASIS has been notified of intellectual property rights claimed in regard to some or all of the contents of this specification. For more information consult the online list of claimed rights.

TABLE OF CONTENTS

1.0	Acknowledgements	5

2.0	Introduction	6

3.0	Business Process Mechanism (BPM) Context Support	7

3.1 Context Mechanism Syntax	9

3.2 CPP/CPA Usage Technical Note	11

4.0	References	12

# Acknowledgements

OASIS wishes to acknowledge the contributions of the members of the CAM, CPP/CPA and BPSS Technical Committees to this standards work.

# Introduction

Providing a mechanism to manage context in an eBusiness exchange is the focus of this document.  The specification here is intended to supplement the BPSS, CPP/CPA and CAM specifications.  It is also a guide to using the context mechanism described here in, and particularly to help facilitate cooperation between the various other relevant OASIS technical committees – including CPP/CPA, BPSS, ebMS and Registry to provide interoperability of this context feature with those other specifications.

This document provides the main details and aspects of the context mechanism.  For extended technical aspects of the XML functions and behaviour notes, reference should be made to the main CAM specifications for those.  However for a succinct overview this document serves to provide that, and also the key implementation integration details and use with the other OASIS specifications.

Specifically there are five use cases that are supported directly:

#1) provide context to external components that may be directed by BPSS - such as transaction handling software (Java, EDI Mapper, XSLT, CAM,  EAI adaptor, et al), or web service step.

#2) support ability to configure BPSS flows to match locale or other factors globally based on context provided when a CPA is determined between participants based on their own transaction needs (e.g. produceType="mustRefridgerate")

#3) support late binding of specific parameters within the BPSS based on business factors that occur during a BPSS use

#4) support business modellers being able to identify critical factors during creation of a BPSS    that effect linking and switching within a process and be able to specify those and quantify their details - (e.g. deliveryCountry = Mexico, USA, Canada)

#5) a mechanism to determine pre-conditions for BPSS and outcomes – start / wait / or skip - that allows implementers to configure when a BPSS should commence.

The technical details of the handling for each case are addressed directly in the remainder of this document.

# Business Process Mechanism (BPM) Context Support

The focus here is that of supporting the original ebXML vision of eBusiness interactions including the key requirement of “no surprises” at execution time. This in turn means that all behaviour paths should be known and documented at design time.

Therefore the model is one that calls for exposing the context decisions at the level of the CPA process, and then fixing these rules in place as the CPA is decided.   Therefore any context decisions that are used in the BPSS itself and related transaction handling actions from the BPSS that the CPA selects and directs must have the ability to “bubble up” those context decisions that they are using to expose them for design resolution during the CPA setting process.   The mechanism detailed here emphatically supports this “bubbling up” of context decisions.

The need is to support five main different use cases:

#1 – simple generic context passing – where the target is to direct actions of an XML processor such as XSLT, Java, SAX, or CAM associated with a step within the BPSS itself.

#2 – static setting of BPSS parameters from the CPA (making re-usable BPSS models possible) for a given business scenario and configuration needs.

#3 – late binding of BPSS parameters based on transaction payload information or other external sources (such as a web service) so that various behaviours of the BPSS itself can be dynamically adjusted based on the context at that moment.

#4 – model definitions that support business modellers being able to identify critical factors during creation of a BPSS that effect linking and switching within a process and be able to specify those and quantify their details - (e.g. deliveryCountry = Mexico, USA, Canada). This use case actually overlaps with the same technical mechanisms as #2.

#5 – pre-conditions for BPSS and a mechanism to determine pre-conditions for BPSS and outcomes - start, wait, or skip that allows implementers to configure when a BPSS should commence.

There is also of course the combination of one or more of these uses together. This section describes the mechanism for providing these context rules and variables between the BPSS processor and the remainder of the eBusiness architecture stack (see figure 3.1).

The XML instance used to capture context provides the mechanism to carry linkage values between components in the processes of the BPSS.  The need is to provide a consistent mechanism in XML syntax for the propagation and specifying of context variables and their values throughout the components that make up the architecture stack, not just the BPSS.

Particularly this applies to the CPP/CPA Collaboration Profile Agreement, which provides the overarching context drivers for the components in the architecture stack.  Figure 3.5 shows the detail and the accompanying section describes its use.  Within the CPP/CPA XML instance a linking URI reference is provided to associate the XML context instance document that contains the agreed upon values for global context parameters within the business collaboration.  These then provide the ability to affect late binding on a BPSS for a specific business scenario.  Typical examples of such overall context settings include such things as time-to-perform of BPSS steps, messaging options, participant business roles, product features and overall criteria (e.g. refrigerated produce, fragile components, hazardous materials, special handling needs) that drive the terms and conditions across the overall business collaboration.

Also – because BPSS processing may require dynamic behaviour based on the actual document information being passed by a process step (late binding), the context system provides the means to reference a document instance and a value within that to determine what action should occur.

Figure 3.2 shows a basic XML structure for carrying such values.

Also support for the specialized UBL / CCTS context mechanism is inherent in this generalized mechanism, so as to allow correlation between a UMM model and a context parameter instance in a CPA agreement. An example of such context use is also provided here, (see figure 3.4 below for the default set of codes that denote this usage).

Figure 3.1 e-Business Process Component Stack.

This diagram shows how the Supporting Context instance can be referenced by various stages in the overall business collaboration process within the overall ebXML component stack.   The intention is to provide a single consistent context system across all the components so that implementers and users have a uniform and coherent simple lightweight method of establishing context.

Next we look at the actual XML syntax to be used in the Context instance itself for each of the three use cases we have identified.

3.1 Possible Scenarios and Use of Agreed Context

Each scenario is now considered and further defined, and a simple example given (section 3.2 then discusses the full details of the syntax shown here).

#1 – simple generic context passing – where the target is to direct actions of an XML processor such as XSLT, Java, SAX, or CAM associated with a step within the BPSS itself.

In this example the BPSS itself does not require any context directing.  However the associated business process transaction handling does (e.g. setting address format to local delivery country). Therefore the BPSS will simply pass a URI reference (that is specified in the CPA) to the XML processor, which will then retrieve the XML instance, pointed to by that URI and access the context parameter rules and parameters accordingly.   The ebContext example here shows this use.

Figure 3.1a   XML structure for simple context variable passing:

<ebContext UIDref='SDIR03400' interchangeID='123456789' BPMref='ABC123456:01'

CPAref='ABC012345'

xmlns:as="http://www.oasis-open.org/committees/cam"

>

<header>

<description>An example simple context instance</description>

<version>1.0</version>

<language refcode='eng' codelist='ISO639-2' name='English'/>

<usage>XSLT</usage>

<usage>Java</usage>

</header>

<conditions>

<!-- Here is where we specify two example context item variables and settings -->

<!-- at the CPA level participants can see exactly what significant conditions exist

that they must conform to when using the associated BPSS (e.g. “context bubble up”) -->

<condition item="$Country" 	value="USA" label="Ship to Country" as:member="USA,CA,MX"/>

<condition item="$productType" value="nonperishable" label="Produce type:" as:member="nonperishable,perishable,refridgerated,fragile,heavy"/>

</conditions>

</ebContext>

#2 – static setting of BPSS parameters from the CPA (making re-usable BPSS models possible) for a given business scenario and configuration needs.

In this example we now add a second namespace declaration so that the context rules can reference the BPSS associated with the CPA directly.  That namespace is then used with the XPath statement to reference the explicit part of the BPSS (use of XPath wildcards is also permitted).  This then allows us to create generic BPSS models that can be tailored to users own exchange needs and default configurations.   (Note: also, in order to allow generic logical references these could also be urn: based references to components of the BPSS rather than explicit XPath names).

The ebContext example here shows this use.

Figure 3.1b   XML structure for static setting of BPSS behaviour(s):

<ebContext UIDref='SDIR03400' interchangeID='123456789' BPMref='ABC123456:01'

CPAref='ABC012345'

xmlns:as="http://www.oasis-open.org/committees/cam"

xmlns:bpss="http://www.oasis-open.org/committees/bpss"

>

<header>

<description>An example static setting context instance</description>

<version>1.0</version>

<language refcode='eng' codelist='ISO639-2' name='English'/>

<usage>BPSS</usage>

<usage>ebMS</usage>

</header>

<conditions>

<!-- Here is where we specify a static override for a BPSS setting -->

<!-- at the CPA level participants can see exactly what significant conditions exist

that they must conform to when using the associated BPSS (“P1H, P2H, P1D”) -->

<condition item="\\bpss:timeToAcknowledgeAcceptance*" value="P2H"

label=="NORMAL TIMEOUT" as:member="P1H,P2H,P1D" />

</conditions>

</ebContext>

#3 – late binding of BPSS parameters based on transaction payload information or other external sources (such as a web service) so that various behaviours of the BPSS itself can be dynamically adjusted based on the context at that moment.

In this example we now add a third namespace declaration so that the context rules can reference the logical document(s) linked to the BPSS associated with the CPA directly.  That namespace is then used with the XPath statement to reference the explicit part of the document (use of XPath wildcards is not permitted).  This then allows us to create generic BPSS models that can be tailored to users own exchange needs based off values provided at runtime.  However such values are not arbitrary.  They must conform to know values sets dictated by the as:member( ) statement, or number range constraints.  In other words, the CPA dictates for late binding what are the known decision sets that can occur.

The ebContext example here shows this use.

Figure 3.1c   XML structure for late binding behaviour setting:

<ebContext UIDref='SDIR03400' interchangeID='123456789' BPMref='ABC123456:01'

CPAref='ABC012345'

xmlns:as="http://www.oasis-open.org/committees/cam"

xmlns:bpss="http://www.oasis-open.org/committees/bpss"

xmlns:doc="http://www.mycompany.com/bpss/context"

>

<header>

<description>An example late binding BPSS behaviour setting</description>

<version>1.0</version>

<language refcode='eng' codelist='ISO639-2' name='English'/>

<usage>BPSS</usage>

<usage>ebMS</usage>

</header>

<conditions>

<!—- Scenario #3 : Here is a late binding statement, using the XPath to the document

to find out the condition, then adjust the BPSS accordingly from

the allowed list of values of member choices -->

<context condition="doc:\\CustomerPO\Header\orderType='URGENT'"

<condition name=="bpss:timeToAcknowledgeAcceptance*" value="P10M"

label=="URGENT TIMEOUT" as:member="P5M,P10M,P15M" />

</conditions>

</ebContext>

Note: the example here shows static setting, but this could also use an doc:XPath statement in the value=”doc:XPath” to retrieve a value, but that value is not arbitrary, it must be a valid member.

#5 – pre-conditions for BPSS and a mechanism to determine pre-conditions for BPSS and outcomes - start, wait, or skip that allows implementers to configure when a BPSS should commence.

In this example we need to use a simple structure with conditions that reference global parameters to determine if the pre-conditions allow the BPSS to initiate.  The implementation will need to dynamically update this XML instance and or the

The ebContext example here shows this use.

Figure 3.1d   XML structure for static setting of BPSS behaviour(s):

<ebContext UIDref='SDIR03400' interchangeID='123456789' BPMref='ABC123456:01'

CPAref='ABC012345'

xmlns:as="http://www.oasis-open.org/committees/cam"

xmlns:bpss="http://www.oasis-open.org/committees/bpss"

>

<header>

<description>An example static of testing pre-condition for BPSS</description>

<version>1.0</version>

<language refcode='eng' codelist='ISO639-2' name='English'/>

<usage>BPSS</usage>

</header>

<conditions>

<!-- Here is where we specify a pre-condition set for initiating a BPSS -->

<!-- at the CPA level participants can see exactly what significant conditions exist

that must occur when starting the associated BPSS -->

<!-- This mechanism uses the BPSS signal mechanism to retrieve the required trigger conditions -->

<condition bpss:type="SIGNAL" bpss:action="WAIT" bpss:retryPeriod=”P5M”

item="http://bpss.trigger.myprocess.com/?accountapproved=’$account’"

value="Pending"

label=="Account in good standing" as:member="Pending,Approved,Cancelled">

<condition bpss:type="SIGNAL" bpss:action="START"

item="http://bpss.trigger.myprocess.com/?accountapproved=’$account’"

value="Approved"

label=="Account in good standing" as:member="Pending,Approved,Cancelled"/>

</condition>

</conditions>

</ebContext>

3.2 Context Mechanism Syntax Detailed Notes.

An <ebContext> structure is associated directly with a BPSS instance via the CPP/CPA template and it can rely on the content referencing and data typing from the ebContext template to direct the parsing of conditions.  To facilitate standalone use of the <ebContext> structures, re-use is made of a subset of the CAM functions (see table 3.3 below) in conjunction with the CAM xmlns:as namespace declaration.  Most conditions are anticipated to be denominated lists, so the as:member() function can be used for that.  Alternatively for string values such as part numbers, as:setLength() and as:setMask() can be used to specify the data constraints, while standard data types can be used for numeric and date values.

Some condition examples are shown in Figure 3.2 and these equate to the conceptual semantic model using parameters for category, classification, industry, type and language labelling.

This approach provides a lightweight implementation, while stopping short of requiring a complete and complex XML parsing mechanism and template to describe the ebContext structure itself.   Instead a subset of the CAM features should be adequate for the anticipated constrained use cases of context documents (see Figure 3.2 below) that can be easily implemented using existing typical programming language XML parsing libraries.

There are three standard namespaces that can be used to denote how the conditions apply.  The default CAM namespace “as:” (for content assembly) refers to content parsing instructions, a BPSS namespace of “bpss:” that overrides that particular item in the BPSS instance (matching the XPath expression), and then a document namespace “doc:” that relates to a document instance associated with that particular step in the BPSS (can be either a received or response document).

Also in order to allow dynamic assignments of context to a standard BPSS instance the declarative element <context condition=”XPath expression”/> can be used to provide additional flexibility.  These <context/> conditions will typically reference a doc: namespace reference to determine if the context applies.  (Note: more than one <context/> condition may be used to accommodate variations in physical instances of a BPSS step logical document.  The rule that matches the XPath expression will be the one selected.)

Any <condition/> without a <context/> outer block is a default condition that will apply unless overridden by a specific <context/> assignment.  This mirrors the CAM template behaviour where there is a default context section followed by context constraint rules section(s).

Figure 3.2   XML structure for eBusiness context variable multiple condition examples.

<ebContext UIDref='SDIR03400' interchangeID='123456789' BPMref='ABC123456:01'

CPAref='ABC012345'

xmlns:as="http://www.oasis-open.org/committees/cam"

xmlns:bpss="http://www.oasis-open.org/committees/bpss" xmlns:doc="http://www.mycompany.com/bpss/context">

<header>

<description>An example context instance</description>

<version>1.0</version>

<language refcode='eng' codelist='ISO639-2' name='English'/>

<usage>CAM</usage>

<usage>XSLT</usage>

<usage>BPM</usage>

</header>

<conditions>

<condition item="Country" 	value="USA" as:member="USA,CA,MX" as:CCTScategory="GP"/>

<condition item="productType" 	value="nonperishable" label="Item type:" as:member="nonperishable,perishable,refridgerated,fragile,heavy" as:CCTScategory="PC"/>

<condition item="partnerType" 	value="wholesale" label="Partner type:" as:member="wholesale,retail,distributor,oem,service"/>

<condition item="Catalogue" value="A2003-Q1"

as:setLength="8"  as:setMask="XNNNN-QN"

as:UIDreference="SGIR:030451"/>

<condition item="bpss:timeToAcknowledgeAcceptance*" value="P2H"

label=="NORMAL TIMEOUT" as:member="P1H,P2H,P1D" />

<!—- Scenario #3 : Here is a late binding statement, using the XPath to the document

to find out the condition, then adjust the BPSS accordingly from

the allowed list of values of member choices -->

<context condition="doc:\\CustomerPO\Header\orderType='URGENT'"  bpss:RefID='BPSS_DOC1'

<condition item=="bpss:timeToAcknowledgeAcceptance*" value="P10M"

label=="URGENT TIMEOUT" as:member="P5M,P10M,P15M" />

</context>

</conditions>

</ebContext>

Figure 3.3 Table of CAM features subset for ebContext usage

| Function name | Required? |
| --- | --- |
| member() | Optional |
| setLength() | Optional |
| setMask() - see CAM specification | Optional |
| UIDreference() | Optional |
| datatype() | Optional – specify XSD datatype |

This table contains a suggested selection of functions that will provide the bulk of typical functionality in configuring context instances.  Notice that implementers may also choose to allow additional functions to be inserted as annotations that are simply ignored by the processor, but will act of notes for reference.

The optional UBL / CCTS mechanism further categorizes context variables using the following classifications.

Figure 3.4 UBL / CCTS context category classifications

| Business process (BP) | Process, collaboration, or transaction. |
| --- | --- |
| Business process role (BPR) | Sender and receiver roles. |
| Supporting role (SR) | Third party supporting role. |
| Industry classification (IC) | Vertical industry sector |
| Product classification (PC) | Type of product or service |
| Geopolitical (GP) | Trading region |
| Official constraints (OC) | Legal or contractual requirements |
| System capabilities (SC) | Restrictions of physical system or compliance constraints. |

The examples previously provided give constraint examples in the area of geopolitical and supporting role contexts.   The use of the optional in-line attribute as:CCTScategory allows provision for use of this classification of context.

3.3 BPSS and CPP/CPA Usage Technical Note

Figure 3.5 below shows a mark-up fragment that details how and where the required URI is inserted into the CPP/CPA document structure.

Figure 3.5 - Use of URI in CPP/CPA to reference an external context instance.

This allows a CPA to constrain or extend the context declaration that the BPSS references.

# References

- XML Path Language (XPath) specifications document, version 1.0, W3C Recommendation 16 November 1999, http://www.w3.org/TR/xpath/

- Extensible Markup Language (XML) specifications document, version 1.1, W3C Candidate Recommendation, 15 October 2002, http://www.w3.org/TR/xml11/

- XNL: Specifications and Description Document, OASIS CIQ TC, http://www.oasis-open.org/committees/ciq

- XAL: Specifications and Description Document, OASIS CIQ TC, http://www.oasis-open.org/committees/ciq

- ISO 16642 – Representing data categories http://www.loria.fr/projets/TMF/

- CEFACT – Core components specifications - http://webster.disa.org/cefact-groups/tmg/

- UN – eDocs resource site - http://www.unece.org/etrades/unedocs/

- UN – Codelists reference site for eDocs - http://www.unece.org/etrades/unedocs/codelist.htm

- Jaxen reference site - http://jaxen.org/

# Footnotes

See the main CAM specification for details on the picture mask feature set.