### xsi:schemaLocation attribute

The SOAP namespace:

http://schemas.xmlsoap.org/soap/envelope/

resolves to a schema that conforms to an early Working Draft version of the W3C XML Schema specification, specifically identified by the following URI:

http://www.w3.org/1999/XMLSchema

The W3C XML Schema specification[XMLSchema] has since gone to Recommendation status, effective May 2, 2001. The ebXML SOAP extension element schema has been defined using the W3C Recommendation version of the XML Schema specification[XMLSchema] (see Appendix A).

In order to enable validating parsers and various schema validating tools to correctly process and parse ebXML SOAP Messages, it has been necessary that the ebXML TR&P team adopt an equivalent, but updated version of the SOAP schema that conforms to the W3C Recommendation version of the XML Schema specification[XMLSchema]. ebXML MSH implementations are strongly RECOMMENDED to include the XMLSchema-instance namespace qualified schemaLocation attribute in the SOAP Envelope element to indicate to validating parsers the location of the schema document that should be used to validate the document. Failure to include the schemaLocation attribute will possibly preclude Receiving MSH implementations from being able to validate messages received.

For example:

<SOAP-ENV:Envelope xmlns:SOAP-ENV="http://schemas.xmlsoap.org/soap/envelope/"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://schemas.xmlsoap.org/soap/envelope/

http://www.oasis-open.org/committees/ebxml-msg/schemas/envelope.xsd" ...>

In addition, ebXML SOAP Header and Body extension element content must be similarly qualified so as to identify the location that validating parsers can find the schema document that contains the ebXML namespace qualified SOAP extension element definitions. Thus, the XMLSchema-instance namespace qualified schemaLocation attribute should include a mapping of the ebXML SOAP Envelope extensions namespace to its schema document in the same element that declares the ebXML SOAP Envelope extensions namespace.

It is RECOMMENDED that use of a separate schemaLocation attribute be used so that tools that may not correctly use the schemaLocation attribute to resolve schema for more than one namespace will still be capable of validating an ebXML SOAP message. For example:

<SOAP-ENV:Envelope xmlns:SOAP-ENV="http://schemas.xmlsoap.org/soap/envelope/"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://schemas.xmlsoap.org/soap/envelope/

http://www.oasis-open.org/committees/ebxml-msg/schemas/envelope.xsd" ...>

<SOAP-ENV:Header xmlns:eb="http://www.ebxml.org/namespaces/messageHeader"

xsi:schemaLocation="http://www.ebxml.org/namespaces/messageHeader

http://www.oasis-open.org/committees/ebxml-msg/schemas/messageHeaderv1_1.xsd" ...>

<eb:MessageHeader ...> ...

</eb:MessageHeader>

</SOAP-ENV:Header>

<SOAP-ENV:Body xmlns:eb="http://www.ebxml.org/namespaces/messageHeader"

xsi:schemaLocation="http://www.ebxml.org/namespaces/messageHeader

http://www.oasis-open.org/committees/ebxml-msg/schemas/messageHeaderv1_1.xsd" ...>

<eb:Manifest ...> ...

</eb:Manifest>

</SOAP-ENV:Body>

</SOAP-ENV:Envelope>