| Network Working Group | S. Turner |
| --- | --- |
| Internet Draft | IECA, Inc. |
| Intended Status: Standards Track | S. Sudol |
| Expires Month Day, 2007 | National Security Agency |
|  | Month Day, 2007 |

Symmetric Key Package Content Type

Status of this Memo

By submitting this Internet-Draft, each author represents that any applicable patent or other IPR claims of which he or she is aware have been or will be disclosed, and any of which he or she becomes aware will be disclosed, in accordance with Section 6 of BCP 79.

Internet-Drafts are working documents of the Internet Engineering Task Force (IETF), its areas, and its working groups. Note that other groups may also distribute working documents as Internet-Drafts.

Internet-Drafts are draft documents valid for a maximum of six months and may be updated, replaced, or obsoleted by other documents at any time. It is inappropriate to use Internet-Drafts as reference material or to cite them other than as "work in progress."

The list of current Internet-Drafts can be accessed at

http://www.ietf.org/ietf/1id-abstracts.html

The list of Internet-Draft Shadow Directories can be accessed at

http://www.ietf.org/shadow.html.

This Internet-Draft will expire on Month Day, 2007.

Copyright Notice

Copyright (C) The IETF Trust (2007).

Abstract

This document proposes a transport independent format for symmetric keys.

1 Introduction

This document defines the symmetric key format content type.  It is transport independent. The Cryptographic Message Syntax [RFC3852] can be used to digitally sign, digest, authenticate, or encrypt this content type.

1.1 Requirements Terminology

The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT", "SHOULD", "SHOULD NOT", "RECOMMENDED", "MAY", and "OPTIONAL" in this document are to be interpreted as described in [WORDS].

1.2 ASN.1 Syntax Notation

A module for the '88 and the '93 ASN.1 [X.680, X.690] syntax are included.  They result in the same encoding on the wire.

2 Symmetric Key Package Content Type

The symmetric key package content type is used to transfer one or more plaintext symmetric keys from the source that generated the keying material to a receiver.  Multiple intermediaries may be involved in the delivery of the symmetric key package.  A symmetric key package MAY be encapsulated in one or more CMS protecting content types.

The symmetric key package content type has the following syntax:

PKCS7-CONTENT-TYPE ::= TYPE-IDENTIFIER

symmetric-key-package PKCS7-CONTENT-TYPE ::=

{ SymmetricKeyPackage IDENTIFIED BY id-ct-KP-sKeyPackage }

id-ct-KP-sKeyPackage OBJECT IDENTIFIER ::=

{ joint-iso-itu-t(2) country(16) us(840) organization(1)

gov(101) dod(2) infosec(1) formats(2)

key-package-content-types(78) TBD }

SymmetricKeyPackage ::= SEQUENCE {

version          KeyPkgVersion DEFAULT v2,

sKeyPkgProps     [0] KMProperties OPTIONAL,

sKeys            SymmetricKeys }

SymmetricKeys ::= SEQUENCE SIZE (1..MAX) OF OneSymmetricKey

OneSymmetricKey ::= SEQUENCE {

sKeyProps        KMProperties OPTIONAL,

sKey             OCTET STRING }

KeyPkgVersion ::= INTEGER  { v1(1), v2(2) }

KMProperties ::= SEQUENCE SIZE (1..MAX) OF KMProperty

KMProperty ::= SEQUENCE {

kmPropType   KM-PROPERTY.&id({KMPropertySet}),

kmPropValue  KM-PROPERTY.&Type({KMPropertySet}{@kmPropType})

OPTIONAL }

-- All key material properties are identified by either

-- an object identifier or a relative object identifier.

-- Relative object identifiers are relative to

-- { TBD }

The SymmetricKeyPackage fields are used as follows:

- version identifies version of the symmetric key package content structure.  For this version of the specification, the default value, v2, must be used.

- sKeyPkgProps optionally provides properties that apply to all of the symmetric keys in the package.  Key properties are provided in Section 3.

- sKeys contains a sequence of OneSymmetricKey values.  This structure is discussed below.

The OneSymmetricKey fields are used as follows:

- sKeyProps optionally provides properties that apply to one symmetric key.   Key properties are provided in Section 3.

- sKey contains the key value encoded as an OCTET STRING.

The KMProperty fields are used as follows:

- kmPropType is an object identifier or a relative object identifier.  It identifies the keying material property; it also indicates the syntax of the associated kmPropValue.

- kmPropValue contains the keying material property value.

3 Key Properties

This section specifies key material properties.  They can appear within the sKeyPkgProps or sKeyProps fields within the symmetric key package content type.

The following ASN.1 class is used to specify the syntax of key material properties:

KM-PROPERTY ::= CLASS {

&Type       OPTIONAL,

&id         FullOrRelativeOID UNIQUE }

WITH SYNTAX {

WITH SYNTAX &Type

ID          &id }

FullOrRelativeOID ::= CHOICE {

fullOID     OBJECT IDENTIFIER,

relOID      RELATIVE-OID }

-- Key properties are relative to { TBD }

KMPropertySet KM-PROPERTY ::= {

... -- Expect additional objects -- }

4 Security Considerations

The symmetric key package contents are not protected.  This content type MUST be combined with a security protocol to protect the contents of the package.

5 IANA Considerations

None.  Please remove this section prior to publication as an RFC.

6 Acknowledgements

This work was based on work generated by Russ Housley.

7 References

7.1 Normative References

[RFC2119] Bradner, S., "Key words for use in RFCs to Indicate Requirement Levels", BCP 14, RFC 2119, March 1997.

[X.208] ITU-T Recommendation X.680: Information Technology - Abstract Syntax Notation One, 1988.

[X.209] ITU-T Recommendation X.690 Information Technology - ASN.1 encoding rules: Specification of Basic Encoding Rules (BER), Canonical Encoding Rules (CER) and Distinguished Encoding Rules (DER), 1988.

[X.680] ITU-T Recommendation X.680: Information Technology - Abstract Syntax Notation One, 1997.

[X.690] ITU-T Recommendation X.690 Information Technology - ASN.1 encoding rules: Specification of Basic Encoding Rules (BER), Canonical Encoding Rules (CER) and Distinguished Encoding Rules (DER), 1997.

7.2 Non-Normative References

[RFC3852] Housley, R., "Cryptographic Message Syntax (CMS)", RFC3852, July 2004.

Appendix A. ASN.1 Modules

This section describes data objects used by conforming PKI components in an "ASN.1-like" syntax.  This syntax is a hybrid of the 1988 and 1993 ASN.1 syntaxes.  The 1988 ASN.1 syntax is augmented with the 1993 UNIVERSAL Type UTF8String.

The ASN.1 syntax does not permit the inclusion of type statements in the ASN.1 module, and the 1993 ASN.1 standard does not permit use of the new UNIVERSAL types in modules using the 1988 syntax.  As a result, this module does not conform to either version of the ASN.1 standard.

Appendix A.1 may be parsed by an 1988 ASN.1-parser by replacing the definitions for the UNIVERSAL Types with the 1988 catch-all "ANY".

Appendix A.2 may be parsed "as is" by an 1997-compliant ASN.1 parser.

In case of discrepancies between these modules, the 1988 module is the normative one.

Appendix A.1. 88 ASN.1 Module

END

Appendix A.2. 93 ASN.1 Module

SymmetricKeyPackageModulev1

{ tbd }

DEFINITIONS IMPLICIT TAGS ::=

BEGIN

-- EXPORTS ALL

-- IMPORTS NOTHING

PKCS7-CONTENT-TYPE ::= TYPE-IDENTIFIER

KeyPackageContentTypes PKCS7-CONTENT-TYPE ::= {

symmetric-key-package |

... -- Expect additional content types --

}

symmetric-key-package PKCS7-CONTENT-TYPE ::=

{ SymmetricKeyPackage IDENTIFIED BY id-ct-KP-sKeyPackage }

id-ct-KP-sKeyPackage OBJECT IDENTIFIER ::=

{ joint-iso-itu-t(2) country(16) us(840) organization(1)

gov(101) dod(2) infosec(1) formats(2)

key-package-content-types(78) TBD }

SymmetricKeyPackage ::= SEQUENCE {

version          KeyPkgVersion DEFAULT v2,

sKeyPkgProps     [0] KMProperties OPTIONAL,

sKeys            SymmetricKeys }

SymmetricKeys ::= SEQUENCE SIZE (1..MAX) OF OneSymmetricKey

OneSymmetricKey ::= SEQUENCE {

sKeyProps        KMProperties OPTIONAL,

sKey             OCTET STRING }

KeyPkgVersion ::= INTEGER  { v1(1), v2(2) }

KMProperties ::= SEQUENCE SIZE (1..MAX) OF KMProperty

KMProperty ::= SEQUENCE {

kmPropType   KM-PROPERTY.&id({KMPropertySet}),

kmPropValue  KM-PROPERTY.&Type({KMPropertySet}{@kmPropType})

OPTIONAL }

-- All key material properties are identified by either

-- an object identifier or a relative object identifier.

-- Relative object identifiers are relative to

-- { TBD }

KM-PROPERTY ::= CLASS {

&Type       OPTIONAL,

&id         FullOrRelativeOID UNIQUE }

WITH SYNTAX {

WITH SYNTAX &Type

ID          &id }

FullOrRelativeOID ::= CHOICE {

fullOID     OBJECT IDENTIFIER,

relOID      RELATIVE-OID }

-- Key properties are relative to { TBD }

KMPropertySet KM-PROPERTY ::= {

... -- Expect additional objects -- }

END

Editor's Address

Sean Turner

IECA, Inc.

Email: turners (at) ieca (dot) com

Stephanie Sudol

National Security Agency

Email: s (dot) sudol (at) radium (dot) ncsc (dot) mil

Full Copyright Statement

Copyright (C) The IETF Trust (2007).

This document is subject to the rights, licenses and restrictions contained in BCP 78, and except as set forth therein, the authors retain all their rights.

This document and the information contained herein are provided on an "AS IS" basis and THE CONTRIBUTOR, THE ORGANIZATION HE/SHE REPRESENTS OR IS SPONSORED BY (IF ANY), THE INTERNET SOCIETY, THE IETF TRUST AND THE INTERNET ENGINEERING TASK FORCE DISCLAIM ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

Intellectual Property

The IETF takes no position regarding the validity or scope of any Intellectual Property Rights or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; nor does it represent that it has made any independent effort to identify any such rights.  Information on the procedures with respect to rights in RFC documents can be found in BCP 78 and BCP 79.

Copies of IPR disclosures made to the IETF Secretariat and any assurances of licenses to be made available, or the result of an attempt made to obtain a general license or permission for the use of such proprietary rights by implementers or users of this specification can be obtained from the IETF on-line IPR repository at http://www.ietf.org/ipr.

The IETF invites any interested party to bring to its attention any copyrights, patents or patent applications, or other proprietary rights that may cover technology that may be required to implement this standard.  Please address the information to the IETF at ietf-ipr@ietf.org.

Acknowledgment

Funding for the RFC Editor function is provided by the IETF Administrative Support Activity (IASA).