EMIX Version 1.0

Working Draft 06

23 May 2010

Specification URIs:

This Version:

http://docs.oasis-open.org/emix/v1.0/v1.0/emix-1.0-spec-wd-06.html

http://docs.oasis-open.org/emix/v1.0/v1.0/emix-1.0-spec-wd-06.doc

http://docs.oasis-open.org/emix/v1.0/v1.0/emix-1.0-spec-wd-06.pdf

Previous Version:

http://docs.oasis-open.org/emix/v1.0/v1.0/emix-1.0-spec-wd-05.html

http://docs.oasis-open.org/emix/v1.0/v1.0/emix-1.0-spec-wd-05.doc

http://docs.oasis-open.org/emix/v1.0/v1.0/emix-1.0-spec-wd-05.pdf

Latest Version:

http://docs.oasis-open.org/emix/v1.0/v1.0/emix-1.0-spec-wd-06.html

http://docs.oasis-open.org/emix/v1.0/v1.0/emix-1.0-spec-wd-06.doc

http://docs.oasis-open.org/emix/v1.0/v1.0/emix-1.0-spec-wd-06.pdf

Technical Committee:

OASIS Energy Market Information Exchange TC

Chair(s):

Ed Cazalet,

William T. Cox

Editor(s):

Toby Considine

Related work:

This specification replaces or supersedes:

- N/A

This specification is related to:

- OASIS Specification WS-Calendar V1.0, in process

- OASIS Specification Energy Interoperation V1.0, in process

Declared XML Namespace(s):

http://docs.oasis-open.org/emix/2009interim

Abstract:

The data models and XML vocabularies defined by this TC will address issues in energy markets and the Smart Grid, but may be defined so as to support requirements for other markets. The TC will develop a data model and XML vocabulary to exchange prices and product definitions for transactive energy markets.

- Price information

- Bid information

- Time for use or availability

- Units and quantity to be traded

- Characteristics of what is traded

The definition of a price and of other market information exchanged depends on the market context in which it exists. It is not in scope for this TC to define specifications for markets, nor how prices are determined, nor the mechanisms for interoperation. The TC will coordinate with others to ensure that commonly used market and communication models are supported.

Status:

This document was last revised or approved by the Energy Market Information Exchange Technical Committee on the above date. The level of approval is also listed above. Check the “Latest Version” or “Latest Approved Version” location noted above for possible later revisions of this document.

Technical Committee members should send comments on this specification to the Technical Committee’s email list. Others should send comments to the Technical Committee by using the “Send A Comment” button on the Technical Committee’s web page at http://www.oasis-open.org/committees/emix/.

For information on whether any patents have been disclosed that may be essential to implementing this specification, and any offers of patent licensing terms, please refer to the Intellectual Property Rights section of the Technical Committee web page (http://www.oasis-open.org/committees/emix/ipr.php.

The non-normative errata page for this specification is located at http://www.oasis-open.org/committees/emix/

Notices

Copyright © OASIS® 2010. All Rights Reserved.

All capitalized terms in the following text have the meanings assigned to them in the OASIS Intellectual Property Rights Policy (the "OASIS IPR Policy"). The full Policy may be found at the OASIS website.

This document and translations of it may be copied and furnished to others, and derivative works that comment on or otherwise explain it or assist in its implementation may be prepared, copied, published, and distributed, in whole or in part, without restriction of any kind, provided that the above copyright notice and this section are included on all such copies and derivative works. However, this document itself may not be modified in any way, including by removing the copyright notice or references to OASIS, except as needed for the purpose of developing any document or deliverable produced by an OASIS Technical Committee (in which case the rules applicable to copyrights, as set forth in the OASIS IPR Policy, must be followed) or as required to translate it into languages other than English.

The limited permissions granted above are perpetual and will not be revoked by OASIS or its successors or assigns.

This document and the information contained herein is provided on an "AS IS" basis and OASIS DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY OWNERSHIP RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

OASIS requests that any OASIS Party or any other party that believes it has patent claims that would necessarily be infringed by implementations of this OASIS Committee Specification or OASIS Standard, to notify OASIS TC Administrator and provide an indication of its willingness to grant patent licenses to such patent claims in a manner consistent with the IPR Mode of the OASIS Technical Committee that produced this specification.

OASIS invites any party to contact the OASIS TC Administrator if it is aware of a claim of ownership of any patent claims that would necessarily be infringed by implementations of this specification by a patent holder that is not willing to provide a license to such patent claims in a manner consistent with the IPR Mode of the OASIS Technical Committee that produced this specification. OASIS may include such claims on its website, but disclaims any obligation to do so.

OASIS takes no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights. Information on OASIS' procedures with respect to rights in any document or deliverable produced by an OASIS Technical Committee can be found on the OASIS website. Copies of claims of rights made available for publication and any assurances of licenses to be made available, or the result of an attempt made to obtain a general license or permission for the use of such proprietary rights by implementers or users of this OASIS Committee Specification or OASIS Standard, can be obtained from the OASIS TC Administrator. OASIS makes no representation that any information or list of intellectual property rights will at any time be complete, or that any claims in such list are, in fact, Essential Claims.

The names "OASIS",  are trademarks of OASIS, the owner and developer of this specification, and should be used only to refer to the organization and its official outputs. OASIS welcomes reference to, and implementation and use of, specifications, while reserving the right to enforce its marks against misleading uses. Please see http://www.oasis-open.org/who/trademark.php for above guidance.

Table of Contents

1	Introduction	6

1.1 Terminology	6

1.2 Process	6

1.3 Normative References	6

1.4 Non-Normative References	7

2	Information Model	8

2.1 Introduction	8

2.2 Information Structure	8

2.2.1 Sources of message components	8

2.2.2 The Intrinsic Elements	9

2.2.3 Extrinsic Elements	11

2.2.4 Extensible Element Definition	11

2.2.5 Warrant Information Examples	11

3	Energy Artifacts	13

3.1 AC Power Artifact	13

3.1.1 Block AC Power	13

3.1.2 Full-Requirements  AC Power	14

3.1.3 AC Power Quality	15

3.2 Energy Distribution Artifact	15

3.3 DC Power Artifact	16

3.4 DC Power Load Artifact	17

3.4.1 Full-Requirements  DC Power	18

3.4.2 DC Power Quality	19

3.5 Reactive Load Artifact	19

4	EMIX Warrants	20

4.1 Warrant List Definition	20

5	XML Schema for the EMIX Information Model	21

6	Conformance	22

Acknowledgements	23

A.	Notes on Ancillary Services (non-normative)	24

A.1 Common Requirements today	24

Revision History	26

# Introduction

This document defines a set of messages to communicate Price and Product definition for power and energy markets. Product definition includes quantity and quality of supply as well as attributes of interest to consumers distinguishing between power and energy sources. Energy Market Information Exchange (EMIX) is not intended as a stand-alone signal; rather, it is anticipated to be used for information exchange in a variety of market-oriented interactions.

The Energy Market Information Exchange Technical Committee (TC) is developing this specification in support of the US Department of Commerce National Institute of Standards and Technology (NIST) NIST Framework and Roadmap for Smart Grid Interoperability Standards  [NIST] and in support of the US Department of Energy (DOE) as described in the Energy Independence and Security Act of 2007 (EISA 2007) [EISA].

This specification defines the following:

- The characteristics of power and energy that along with price define an product

- An information model for Price and Product definition using the Unified Modeling Language  [UML]

- An XML Schema for Price and Product definition

Key to reading the document:

- BOLD terms are…

- Italicized terms are…

- [bracketed] terms refer to…

- All examples and all Appendices are non-normative.

## Terminology

The key words “MUST”, “MUST NOT”, “REQUIRED”, “SHALL”, “SHALL NOT”, “SHOULD”, “SHOULD NOT”, “RECOMMENDED”, “MAY”, and “OPTIONAL” in this document are to be interpreted as described in Error! Reference source not found..

## Process

This information exchange was developed primarily by integrating requirements and use cases for Price and Product definition developed by the North American Energy Standards Board (NAESB) as part of its response to NIST Priority Action Plan 03 (PAP03), “Develop Common Specification for Price and Product Definition” [PAP03], which was driven by NIST, Federal Energy Regulatory Commission (FERC), and DOE priority items.

Where appropriate, semantic elements from the International Electrotechnical Commission (IEC) Technical Committee (TC) 57 Power systems management and associated information exchange Common Information Model (CIM) are used [IEC]. Business and market information was borrowed from the financial instruments Common Information Models as described in International Standards Organization (ISO) ISO20022 standard and in the financial trading protocol, FIX (Financial Information eXchange). [NEED NON-NORMATIVE REFS]

Energy markets are volatile, so precise time of delivery is always a significant component of product definition. EMIX incorporates schedule and interval definitions from Web Services Calendar (WS-Calendar) to communicate schedule-related information.

Additional guidance was drawn from subject matter experts familiar with the design and implementation of enterprise and other systems that may interact with smart grids.

## Normative References

[RFC2119]	S. Bradner, Key words for use in RFCs to Indicate Requirement Levels, http://www.ietf.org/rfc/rfc2119.txt, IETF RFC 2119, March 1997.

[WS-Calendar]	OASIS WS-Calendar Technical Committee, specification in progress

[CalWS]	CalConnect TC-XML , specification in progress

[CEFACT]	Currency codes, e.g. USD or GBP. Add full reference citation to CEFACT or UBL profile of CEFACT

[UML]	Unified Modeling Language (UML), Version 2.2, Object Management Group, February, 2009. http://www.omg.org/technology/documents/formal/uml.htm .

[XLINK]	XML Linking Language (XLink) Version 1.1. S DeRose, E Maler, D Orchard, N Walsh, http://www.w3.org/TR/xlink11/ May 2010.

xCal	C. Daboo, M Douglas, S Lees xCal: The XML format for iCalendar,  http://tools.ietf.org/html/draft-daboo-et-al-icalendar-in-xml-03, Internet-Draft, April 2010.

Calendar Resource Schema	C. Joy, C. Daboo, M Douglas, Schema for representing resources for calendaring and scheduling services, http://tools.ietf.org/html/draft-cal-resource-schema-00,  (Internet-Draft), April 2010.

CalWS	CalConnect draft in Process.

XPATH	A Berglund,  S Boag, D Chamberlin, MF Fernández, M Kay, J Robie, J Siméon XML Path Language (XPath) 2.0, http://www.w3.org/TR/xpath20/ January 2007.

XLINK	S DeRose, E Maler, D Orchard, N Walsh XML Linking Language (XLink) Version 1.1., http://www.w3.org/TR/xlink11/  May 2010.

XPOINTER	S DeRose, E Maler, R Daniel Jr. XPointer xpointer Scheme, http://www.w3.org/TR/xptr-xpointer/  December 2002.

XML Schema	PV Biron, A Malhotra, XML Schema Part 2: Datatypes Second Edition, http://www.w3.org/TR/xmlschema-2/ October 2004.

[Stoft]	S. Stoft, Power System Economics: Designing Markets for Electricity. Piscataway, NJ: IEEE Press, 2002.

## Non-Normative References

[NAESB 03]	Requirements Specification for Common Electricity Product and Pricing Definition, North American Energy Standards Board [NAESB], March, 2010 (Public Review Draft). http://naesb.org/pdf4/weq_2010_ap6a_retail_2010_ap9a_rec.doc

[FIX]	The FIX protocol (need formal reference)

[ISO20022]	International Standards Organization, ISO 20022 (need full reference)

[TeMIX]	Transactional Energy Market Information Exchange [TeMIX] an approved White Paper of the EMIX TC.

[NIST]	NIST Framework and Roadmap for Smart Grid Interoperability Standards, Release 1.0, online. Link retrieved 06/23/1010: http://www.nist.gov/public_affairs/releases/upload/smartgrid_interoperability_final.pdf

[EISA]	Energy Independence and Security Act (EISA), online. Link retrieved 06/23/2010: http://www.nist.gov/smartgrid/upload/EISA-Energy-bill-110-140-TITLE-XIII.pdf

[IEC]	The home of the IEC TC 57 is http://tc57.iec.ch/index-tc57.html (link retrieved 06/23/2010)

[PAP03]	Details of PAP03 may be found at http://collaborate.nist.gov/twiki-sggrid/bin/view/SmartGrid/PAP03PriceProduct (link retrieved 06/23/2010)

# Information Model

## Introduction

Price and Product Definition is actionable information. The information needed to make decisions should be included in the EMIX artifact exchanged. Present day markets, particularly wholesale markets, may have deferred charges (e.g. balancing charges) that cannot be determined at point of sale; other markets may require other purchases to allow the use of the energy purchased (e.g. same-time transmission rights or pipeline fees when accepting delivery on a forward contract).

Retail markets and prices generally are all inclusive, while other markets may have many components. The MarketContext is a key to determine other aspects of a market including market rules.

For a detailed explanation of Energy Market Context and transactional energy, please refer to the Transactional Energy Market Information Exchange (TeMIX) White Paper, an approved document of the EMIX committee (link later).

## Information Structure

In describing the structure of the information and its contents we use the metaphor of an envelope containing warrants.

The intrinsic qualities of the energy are on the outside of the envelope. The intrinsic qualities appear on the outside of the envelope. In the simplest model, the intrinsic qualities are limited to the price and the information a meter can provide. In a market of homogenous energy sources and commodity energy, only the intrinsic qualities are actionable. The simplest devices, including the proverbial smart toaster, may understand only the intrinsic qualities. We anticipate that the information on the outside of the envelope will be used for many if not most energy decisions.

More information exchanges rely on the extrinsic qualities, that is, information derived from markets and market rules rather than from energy flows. Extrinsic qualities such as source and environmental attributes are known about the energy, but they are not the energy. The extrinsic qualities enable traceability and auditing, increasing public trust in energy markets and on energy differentiation. These warrants are inside the envelope; dumb gateways or dumb devices may ignore the warrants, that is forward or process messages without opening the envelope.

Most of the extrinsic information consists of warrants, that is, assertions made by an authority. That authority may be the original supplier, a market maker, or a supply chain. These warrants can include assertions of

- source

- source characteristics

- carbon freed in generation or use

- air quality related content (e.g. information on oxides of nitrogen produced in generation)

- audit information

Many artifacts defined as consecutive sequences of similar information. An example would be energy prices for 10 consecutive 15 minute intervals. In all such cases the degenerate set, i.e., a single price for a single interval is valid.

### Sources of message components

#### Time

All expressions of time and interval are based upon the IETF iCalendar core calendar model (RFC 5545) and its associated objects. We rely on the XML standard for representing this information (IETF xCal). Models for using this information, including defined time series are based upon the profiles of iCalendar and xCal as defined in the OASIS specification WS-Calendar.

#### Energy Artifacts

The energy models are drawn, when available, for developing work elsewhere. If time permits, the Committee plans to use the information model from the PAP10 Power Load.

The energy models are all in their own chapter. As this is written (May 2010), there are three: Power Load, Reactive Load and Distribution. The model anticipates additional energy models (Natural Gas? Thermal Distribution? …) and therefore maintains a distinction between energy model and the information on the envelope.

EnergyArtifacts are defined in Section 3.

#### EMIX Intervals

EMIX Intervals are a time segment of energy delivery. The term Interval used as defined in the WS-Calendar specification. A WS-Calendar interval is a time segment unbounded to a particular date-time. This is in contrast to Emix Periods (see below).

EMIX Intervals can be grouped using any of the Interval Set information models as defined in the WS-Calendar specification.WS-Calendar intervals always have an attachment, which is either an XML artifact or an XPOINTER to an XML artifact. In EMIX Intervals, the XML Artifacts are Energy Artifacts as defined in section 3.

#### EMIX Periods

EMIX Periods are EMIX Intervals bound to a particular date and time. While an EMIX Interval might indicate the delivery of energy for a 10 minute period, an EMIX Period would instead indicate the delivery of energy for a 10 minute period starting at 3:00 PM. The EMIX Period uses the Period as defined in the WS-Calendar specification.

The group of intervals are can use any of the Interval Set information models as defined in the WS-Calendar specification.WS-Calendar intervals always have an attachment, which is either an XML artifact or an XPOINTER to an XML artifact. The XML Artifacts are Energy Artifacts as defined in section 3.

### The Intrinsic Elements

The following table specifies the Intrinsic elements in the EMIX v1.0 information model. This table contains only those elements of EMIX v1.0 for which there is a consensus description. Elements not included here have no specific constraint or condition for use.

Table 2-1: Intrinsic Elements - the "outside of the envelope"

| EMIX Element | Specification (Normative) | Note (Non-Normative) |
| --- | --- | --- |
| UID | Identifier of this message |  |
| PartyId | ebCore Party ID | Producer of this artifact |
| TimeStamp | Time this message was produced |  |
| MarketContext | An identification of the market in which the product is offered, or the counterparty if part of a bilateral non-market transaction. | This may include standard financial exchanges, markets managed by or for aggregators and distributors, and an identification of the microgrid in which the product is priced. The identification of microgrids is TBD at this time; the Location may be a way to represent this, e.g. a representative point, a point inside, or a polygon |
| EmixIntervals | Array of EMIX Energy Intervals. Indicates the time(s) the product was, is, or will be available and the amount of the product. | Includes prices and quantities. Can be a single Interval. Based upon by [WS-Calendar] definition of Interval with energy artifacts applied. |
| Currency | A code that indicates the currency used | [CEFACT] or UBL Examples include USD, CAD, GBP, EUR, CNY. Should be a nominative or shadow price referenced to e.g. microgrids |
| Extended Price | The total cost of the transaction over the Delivery Interval. | The Extended Price is the sum of Price times the Rate of Delivery times the duration of the IntervalSet. |
| Location | The geospatial location for the product (Point of Delivery) | This may be point of use, point of delivery, or a geospatial polygon. We anticipate that we use a constricted set of the OpenGML standards with an eye toward compatibility standards used in Emergency Response. |
| Meter ID | An identifier designating the meter. | A Point of Delivery is most frequently associated with a meter |
| Energy Type | Identifies type of Energy from the list of approved Energy Artifacts | Some language permitting and encouraging the development and registration of new Artifact types |
| Energy Artifact | Matches the Energy Type | Different types of Energy have different artifacts. See Section 3 for a discussion of Artifacts. |
| Envelope | Container only | Container to hold all extrinsic information elements |

### Extrinsic Elements

The following table specifies the Extrinsic elements in the EMIX v1.0 information model. This table contains only those elements of EMIX v1.0 for which there is a consensus description. Elements not included here have no specific constraint or condition for use.

Table 2-2: Extrinsic Elements - "Inside the Envelope"

| EMIX Element | Specification (Normative) | Note (Non-Normative) |
| --- | --- | --- |
| Warrant List | The container for array of warrants. Optional. | An array of the warrants included in the envelope. See section 4 for warrants. |
| Price Support | Container holding information supporting price information | May include Energy Artifacts, if several are combined to produce the intrinsic price. |
| Program | A possibly structured name for a program in which the price and product are offered or purchased. | This may be analogous to a contract identifier. The variety of DR “programs” inspired this proposed element. |
| Contract ID | An identification of the contract under which the energy is supplied or consumed. | ISSUE should this be with MarketID on the envelope? |
| Energy Quality | Quality measures are specified alongside their associated Artifacts in section 3 | Perhaps using IEEE 1159 or other common metrics |

### Extensible Element Definition

This section blank

### Warrant Information Examples

There are a wide variety of warrant types, issuing authorities, and characteristics described by warrants. For bilateral agreements, we described what may be called self-issued warrants.

We provide some examples; see NEED REF OR INFORMATIVE APPENDIX for a description of the complexities of warrants across jurisdiction boundaries.

Table 2-3: Examples of Warrant Information

| Warrant Element | Specification (Normative) | Note (Non-Normative) |
| --- | --- | --- |
| Warrant Type | Specification (Normative) | Note (Non-Normative) |
| Carbon Warrant | The quantity of carbon released by the production of the energy product in the quantity and units indicated | This could be CO2, amount of elemental carbon. Units defined by UnitsML. |
| Content Warrant | The proportion of the product defined that is from non-fossil fuel sources, including but not limited to “hydroelectric”, “solar”, and “wind”. | The nature of the original input to storage is not altered when drawn from storage. |
| Source Warrant | Individual source warrants | In aggregate may be the same as ContentWarrant |

# Power and Energy Artifacts

Each type of Power and Energy product has its own definitions and its own descriptive parameters. These artifacts are the specific descriptions relevant to defining the potential utility of the power and energy product. The Power and Energy Artifacts describe the intrinsic information. There may be cases when an Artifact is used “inside the envelope”, perhaps as supporting information supporting the internal prices.

To put the terms “Power” and “Energy” into the proper context for this specification, the following definitions will be used:

- Apparent Power: mathematical product of root-mean-square voltage and root-mean-square current, vector sum of Real Power and Reactive Power, absolute value of Complex Power, unit: volt-ampere, VA

- Complex Power (S): square root of sum of squares of Real Power and Reactive Power, unit: volt-ampere, VA

- Current: flow of electric charge, or rate of flow of electric charge, unit: ampere, A

- Energy: the production or consumption of Real Power over time, unit: Watt-hour, Wh (note: this is the contextual unit)

- Power Factor (p.f.): ratio of Real Power to Complex Power, cosine of the phase angle between Current and Voltage, expressed as a number between 0 and 1, expressed as a percentage (i.e., 50% = 0.5), unit: dimensionless

- Reactive Power (Q): mathematical product of the root-mean-square voltage and root-mean-square current multiplied by the sine of the angle between the voltage and current, unit: volt-amperes reactive, VAR, VA-r, var

- Real Power (P): rate at which electricity is produced or consumed, mathematical product of Voltage and Current, unit: Watt, W

- Voltage: difference in electric potential between two points, unit: volt, V

Generically, the use of the term “Power” refers to “Real Power” and is expressed in Watts. Otherwise, one talks of Apparent Power or Complex Power in VA, or Reactive Power in VARs.

In the context of this specification, the price of Power and Energy will be expressed in the same unit, $/MWh. The argument for this comes from [Stoft, p. 32]. The use of Power is as a flow, and its total cost is measured in unit currency (i.e., dollars) per hour, not just unit currency. The price per unit cost of Power is measured in unit currency per hour per megawatt (MW) of Power flow, or unit currency/MWh. In the same manner, the total cost of a certain quantity of Energy is measured in unit currency. The price per unit cost of energy is measured in unit currency/MWh, which is the same as for Power.

To clear up confusion on units for pricing, refer to definitions on pp. 30-33 in [Stoft].

## Power Artifact

The most common Product for delivery of electricity is alternating current (AC) Power. Depending upon the market, Power can be bought in blocks, or made available for use up to the maximum amount deliverable (also known as “Full-requirements Power”) by the in-place transmission and distribution infrastructure. Today, one typically speaks of Block Power for wholesale markets and the latter in residential markets.

The same AC power can be offered to provide multiple services at different market prices. Some markets, known as ancillary services, can offer substantially more for the same load than does the traditional market. Suitability of an offering for these diverse markets is determined by aspects of the response such as how fast the resource can offer the power, how long it can offer the power, how frequently the resource can offer the power, etc. Higher prices come with higher risks; the costs of non-performance in ancillary markets can be substantially higher as well.

Reactive Load Artifact

This section is rudimentary only as of this draft

Attributes describing the utility of Reactive Load

Total Harmonic Distortion (reactive load) (Volt-Amps)

Power Factor

VoltAmps-Hours

### Block Power

Block Power is used today in wholesale power markets and in demand response (DR) markets. It is also acceptable for end-user sales in transactional markets. As Block Power is contained inside or referred to by a [WS-Calendar] interval, it has no native duration. This Artifact can be used in forward bidding, committed purchases, and in after-the fact (post parte) reporting.

Table 3-1: AC Block Power Attributes

| Name | Definition (Normative) | Note (Non-Normative) |
| --- | --- | --- |
| BACRateOfDelivery | Quantity of Power over time | Unit is normally kilowatt-hours (kWh) or megawatt-hours (MWh) |
| BACResponseTime | Duration as defined in [WS-Calendar] | How fast can this resource respond if asked. |
| BACRampTime | Duration as defined in [WS-Calendar] | How long to get up to full service after response. |
| BACCycleTime | Duration as defined in [WS-Calendar] | Minimum time between invocation and re-invocation. |
| BACPowerFactor | Float from 0 to 1. Optional. |  |

### DC Power Artifact

There is a growing discussion of the separate sale of DC Power. This anticipates a growing use for DC distribution within microgrids.

Fundamentally, the sale of power does not distinguish its transport mechanism, i.e., AC transmission/distribution or DC transmission/distribution. If separate Artifacts are needed, the following are recommended:

- BDCRateOfDelivery

- BDCResponseTime

- BDCRampTime

- BDCCycleTime.

The power factor for DC Power is 1.0 so no Artifact is needed.

### Full-Requirements Power

Electricity sold under full-requirements tariffs and contracts to retail customers is a common regulated tariff today. A full-requirements retail contract is an offer to a customer by a retail service provider (RSP) to deliver any amount of power (at a rate-of-delivery up to the capacity of the customer's service connection) at an offer price over a specified interval.

Ancillary services brought to market may have similar limits, including a minimum and a maximum offer. A minimum offer is the smallest load the supplier is willing to bring to market. A maximum offer may be the maximum DR that a customer can provide.

Table 3-2: Full Requirements AC Power

| Name | Definition (Normative) | Note (Non-Normative) |
| --- | --- | --- |
| FRACMinRate | In kWh (optional) | Minimum rate of delivery to acquire this product |
| FRACMaxRate | In kWh | Maximum rate of delivery obtainable from this asset |
| FRACResponseTime | Duration as defined in [WS-Calendar] | How fast can this resource respond if asked |
| FRACRampTime | Duration as defined in [WS-Calendar] | How long to get up to full service after response |
| FRACCycle Time | Duration as defined in [WS-Calendar] | Minimum time between being invocation and re-invocation. |
| FRACPowerFactor | Float from 0 to 1 (optional) |  |

### Full-Requirements DC Power

It is possible that DC Power will be sold in the same manner as today’s full-requirements tariffs. A full-requirements retail contract is an offer to a customer by a retail service provider (RSP) to deliver any amount of power (at a rate-of-delivery up to the capacity of the customer's service connection) at an offer price over a specified interval.

Ancillary services brought to market may have similar limits, including a minimum and a maximum offer. A minimum offer is the smallest load the supplier is willing to bring to market. A maximum offer may be the maximum DR that a customer can provide.

Table 3-6: DC Full Requirements Offering

| Name | Definition (Normative) | Note (Non-Normative) |
| --- | --- | --- |
| FRDCVoltage | Number | For microgrids, often 48 or 325 |
| FRDCMinRate | Volt-Amps/Hour | Maximum rate of delivery required to bring this asset to market |
| FRDCMaxRate | Volt-Amps/Hour | Maximum rate of delivery obtainable from this asset |
| FRDCResponseTime | Duration as defined in WS-Calendar | How fast can this resource respond if asked |
| FRDCRampTime | Duration as defined in WS-Calendar | How long to get up to full service after response |
| FRDCCycleTime | Duration as defined in WS-Calendar | Minimum time between being invocation and re-invocation. |

### DC Power Load Artifact

Table 3-5: DC Power Load Artifact

| Name | Definition (Normative) | Note (Non-Normative) |
| --- | --- | --- |
| Voltage | Number | For microgrids, often 48 or 325 |
| ResponseTime | Duration as defined in WS-Calendar | How fast can this resource respond if asked |
| RampTime | Duration as defined in WS-Calendar | How long to get up to full service after response |
| CycleTime | Duration as defined in WS-Calendar | Minimum time between being invocation and re-invocation. |

## Energy

## Mirror block ac/dc

## Mirror full ac/dc

## Power Quality

Higher quality power can obtain a market premium. A buyer willing to accept lower quality power may be able to obtain inexpensive power. Power Qualities should be measurable, so AC Power Quality from usage can be tracked against the AC Power Quality bid.

Table 3-3: AC Power Quality

| Load Element | Specification (Normative) | Note (Non-Normative) |
| --- | --- | --- |
| Awaiting Input |  | Awaiting metrics of AC Power Quality from committee or PAP10 |

### DC Power Quality

Higher quality power can obtain a market premium. A buyer willing to accept lower quality power may be able to obtain inexpensive power. Power Qualities should be measurable, so DC Power Quality from usage can be tracked against the AC Power Quality bid.

Table 3-7: DC Power Quality

| Load Element | Specification (Normative) | Note (Non-Normative) |
| --- | --- | --- |
| Awaiting Input |  | Awaiting metrics of DC Power Quality from committee or PAP10 |

## Transmission and Distribution Artifact

Artifacts are defined for both Transmission and Distribution. Distribution artifacts are appropriate when there is a distinction between the point of purchase of energy and the point of delivery. For example, A consumer could contract to buy power directly form a desirable power source, such as a particular wind farm. The consumer would then pay the delivery costs to get the energy to the consumer’s meter.

Three types of costs typically can affect delivery costs. Normal delivery charges may be either fixed price or based upon distance, such as a cost per mile. Line losses can reduce the amount delivered to an amount below the amount purchased; if the consumer wants an unblended product, this amount cannot be made up from the distribution factor’s account. Finally, certain distribution assets can be constrained. Energy transiting through a constrained distribution asset may incur congestion charges.

Table 3-4: Transmission and Distribution Artifacts

| Name | Definition (Normative) | Note (Non-Normative) |
| --- | --- | --- |
| Distance | Number | Multiplier for the other elements that need to be extended |
| DistributionDistanceUnits | Unit of Measure | Common units are feet (ft), miles (mi), meters (m) and kilometers (km) |
| TransmissionDistanceUnits | Unit of Measure | Common units are feet (ft), miles (mi), meters (m) and kilometers (km) |
| DistributionDeliveryLoss | Loss per DistributionDistanceUnit | The amount of energy purchased is reduced by the extended loss, i.e., the EDPU to the power of the Distance. |
| TransmissionDeliveryLoss | Loss per TransmissionDistanceUnit | The amount of energy purchased is reduced by the extended loss, i.e., the ETPU to the power of the Distance. |
| ExtendedDistributionDelivery Loss | Effective loss for Distribution delivery. | The amount of energy purchased is reduced by the extended loss, i.e., the (1 – distribution delivery loss) to the power of the Distance. |
| ExtendedTransmissionDelivery Loss | Effective loss for Transmission delivery. | The amount of energy purchased is reduced by the extended loss, i.e., the (1 – transmission delivery loss) to the power of the Distance. |
| DistributionRate | The charge per distance unit of Distribution |  |
| ExtendedDistributionCharge | Total Distribution Charge | DistributionRate times DistributionDistance |
| TransmissionRate | The charge per distance unit of Transmission |  |
| ExtendedTransmissionCharge | Total Transmission Charge | TransmissionRate times TransmissionDistance |
| DistributionCongestionCharge | Charge per unit of energy | Time sensitive charges to allocate scarce distribution capacity |
| DistributionExtendedCongestionCharge | Total congestion charge | Distribution CongestionCharge times purchase quantity |
| TransmissionCongestionCharge | Charge per unit of energy | Time sensitive charges to allocate scarce transmission capacity |
| TransmissionExtendedCongestionCharge | Total congestion charge | TransmissionCongestionCharge times purchase quantity |

There could well be multiple instances of the above Artifacts in a single Price instance.

# EMIX Warrants

In this section we define the detailed information model for EMIX artifacts. In Section 4 we define the XML Schema for the EMIX Information Model.

## Warrant List Definition

Still blank

# XML Schema for the EMIX Information Model

In this section we define the XML Schemas for EMIX.

# Conformance

The last numbered section in the specification must be the Conformance section. Conformance Statements/Clauses go here.

- Acknowledgements

The following individuals have participated in the creation of this specification and are gratefully acknowledged:

Participants:

Timothy Bennett, Drummond Group Inc.

Edward Cazalet, Individual

Toby Considine, University of North Carolina at Chapel Hill*

William Cox, Individual

Phil Davis, Schneider Electric

Pim van der Eijk, Sonnenglanz Consulting

Girish Ghatikar, Lawrence Berkeley National Laboratory

Todd Graves, Microsoft Corporation

Anne Hendry, Individual

David Holmberg, NIST*

Gale Horst, Electric Power Research Institute (EPRI)

Ali Ipakchi, Open Access Technology International Inc. (OATi)

Perry Krol, TIBCO Software Inc.

Derek Lasalle, JPMorganChase

Alex Levinson, Lockheed Martin*

Dirk Mahling, CPower

Scott Neumann, Utility Integration Solutions Inc.

Robert Old, Siemens AG

John Petze, Individual

Ruchi Rajasekhar, Midwest Independent Transmission System Operator, Inc.

Carl Reed, Open Geospatial Consortium, Inc. (OGC)*

Jeremy Roberts, LonMark International*

Anno Scholten, Individual

Pornsak Songkakul, Siemens AG

David Sun, Alstom Power Inc.

Jake Thompson, EnerNOC

David Webber, Individual

Leighton Wolffe, Individual

Notes on Ancillary Services (non-normative)

Some markets, known as ancillary services, can offer substantially more for the same load than does the traditional market. Suitability of an offering for these diverse markets is determined by aspects of the response such as how fast the resource can offer the power, how long it can offer the power, how frequently the resource can offer the power, etc. Higher prices come with higher risks; the costs of non-performance in ancillary markets can be substantially higher as well.

Ancillary services require detailed interval metering. For the regulation product, 4 to 6 second interval metering and direct control of the generator is today required by the balancing system operator. However, there are current initiatives by FERC and many ISOs to allow loads and storage to provide ancillary services.  One of the potential applications of the metering and communications infrastructure of the smart grid is to facilitate the participation of loads and distributed energy resources such as storage in providing balancing / ancillary services to the grid.

There is general agreement across North America on the names of ancillary services. There is general agreement on the performance profile for each ancillary service as well. There are minor differences in some of the actual performance profiles from region to region. Periodically, the performance requirements are changed for named services.

Ancillary service performance can be characterized as “meet or exceed” requirements. A given service level may meet the requirements for more than one named service. A power product that can be sold in more than one market has more potential value to the seller. Transparent service and performance requirements associated with market prices are likely to encourage sellers to make minor upgrades when they can thereby reach new markets.

For these reasons, we opted not to name the ancillary services in the standard, but instead to exchange the actual performance requirements either offered or required.

Common Requirements today

For reference, here are some common performance requirements in use today. These are non-normative. They are include here to assist the practitioner in thinking about ancillary services as a deliverable.

Regulation

Spinning Reserve

Non-Spinning Reserve

- Revision History

| Revision | Date | Editor | Changes Made |
| --- | --- | --- | --- |
| 1 | 2009-12-08 | Toby Considine | Initial Draft from templates and outline |
| 2 | 2010-01-12 | William Cox | Inserted information model details from TC discussions |
| 3 | 2010-03-10 | William Cox | Change to envelope and certificate metaphor. Changes in mandatory and optional definitions. |
| 4 | 2010-03-24 | William Cox | Updates based on TC comments and corrections. Additional open issues in TC agenda. |
| 5 | 2010-05-18 | Toby Considine | Aligned elements with current draft if WS-Calendar, cleaned up some language to align with the last two months of conversation. Extended envelop and intrinsic/extrinsic language |
| 6 | 2010-05-21 | Toby Considine | Began incorporating TeMIX language. Changed Certificates to Warrants. Fleshed out Energy Artifacts |

# Comments

are these in order of appearance or alphabetical?

Reminder to go check names from IEC CIM

needs a definition

This is now in conflict with its earlier definition.

commodity?

"invocation" and "re-invocation" beg for definitions in this context.

Without more explanatory text, it is difficult to see the need for this section.

REcommendation is to either mirror the "power" section above or add the energy artifacts in the same tables. This is left to the technical editor pending committee decision.

This term merits a defintion in this context