# Terms for Layout of Text Documents
## General
If the description mentions the shorthand properties fo:margin, fo:border or fo:padding for a specific direction left, right, top or bottom, then the applicable single property, e.g fo:margin-left, is implicitly meant too.
The descriptions assume a left-to-right, top-to-bottom writing mode.
## Table Cell

Area	Relevant Attributes
table column	A table column has a fixed width by style:column-width or width is calculated from the width of the entire table and the attribute style:rel-column-width. Column width depends on column content, if attribute style:use-optimal-column-width is set. All attributes are from <style:table-column-properties>.
row	A row has a fixed height by style:min-row-height and style:row-height. Row height depends on row content, if attribute style:use-optimal-row-height is set. All attributes are from <style:table-row-properties>.
Border widths / L, R, T, B	Borders belong to cells, not to columns or rows. Borders are not between columns or rows but inside the cells. Border width is set by fo:border attributes and for the special case of border style double by style:border-line-width attributes, all in <style:table-cell-properties>. / In case table:border-model="collapsing" is set for the table, each of two adjacent cells gets half of the calculated border width.
Padding / PL, PR, PT, PB	Padding area is given by fo:padding attributes from <style:table-cell-properties>.
cell content	Width of the cell content area / = column width or the sum of the column widths in case of merged cells − calculated left and right border widths − left and right padding widths. / Height of the cell content area / = row height or the sum of the row heights in case of merged cells − calculated top and bottom border widths − top and border padding widths.

## Page Vertical
Area	Relevant Attributes
page	fo:page-height in <style:page-layout-properties>
1	height of area 1 = sum of height from fo:margin, fo:border and fo:padding, all in <style:page-layout-properties> / In case a shadow is defined by a style:shadow attribute, the width of the shadow is added to the width of the border.
2, 4	height of area 2 or area 4 respectively = sum of height values from fo:margin, fo:border and fo:padding attributes in <style:header-footer-properties> in <style:header-style>. / In case a shadow is defined by a style:shadow attribute, the width of the shadow is added to the width of the border. / The fo:margin-bottom value may shrink dynamically when the header content grows, if style:dynamic-spacing="true" is set.
3 header content	Height is calculated.
header	height of header = height of areas 2 and 4 + height of header content / Height of header can be fixed using svg:height.
9, 11	height of area 9 or area 11 respectively = sum of height values from fo:margin, fo:border and fo:padding attributs in <style:header-footer-properties> in <style:footer-style>. / In case a shadow is defined by a style:shadow attribute, the width of the shadow is added to the width of the border. / The fo:margin-top value may shrink dynamically when the footer content grows, if style:dynamic-spacing="true" is set.
10 footer-content	Height is calculated.
footer	height of footer = height of areas 9 and 11 + height of footer-content / Height of footer can be fixed using svg:height.
12	height of area 12 = sum of height from fo:margin, fo:border and fo:padding, all in <style:page-layout-properties>. / In case a shadow is defined by a style:shadow attribute, the width of the shadow is added to the width of the border.
page-content	height of page-content = page height − height of area 1 − height of header − height of footer −height of area 12.
5, 6, 7 / footnote separator line	height is sum of style:width, style:distance-before-sep and style:distance-after-sep from <style:footnote-sep> from <style:page-layout-properties>.
8 footnotes	Height is calculated from content.
footnote area	height of footnote area = height of footnote separator line (5)(6)(7) + height of footnotes. Height can be limited to style:footnote-max-height from <style:page-layout-properties>.
body text area	height of body text area = height of page content − height of footnote area

Endnotes are handled similar to footnotes in regard to vertical division.

## Section vertical
Sections do not have top or bottom margins, borders, shadows or paddings. Sections act similar to a page content area in regard to vertical division. A section has its own section body text area, its own section footnote area, and its own section endnote area. Section height depends on content, there exists no attribute for a fixed height.
Sections are not directly available for anchor positions.
## Frames and Paragraphs Vertical
Area	Relevant Attributes
1, 13	These areas are specified by fo:margin attributes of <style:graphic-properties>. These areas do not count for the frame height, in contrast to the page height, where areas defined by the fo:margin attributes are included.
frame	The frame height is specified by svg:height in <draw:frame> element or calculated as relative height by the style:rel-height attribute.
2, 3 and 11, 12	Areas 2 and 12 are specified by fo:border attributes, area 3 and 11 by fo:padding attributes, all in <style:graphic-properties>. / In case a shadow is defined by a style:shadow attribute, the width of the shadow is added to the width of the border.
frame content	height of frame content = frame height − height of areas 2 and 3 − height of areas 11 and 12.
4, 10	These areas are defined by fo:margin attributes in <style:paragraph-properties>. Collapse margin is applied in vertical direction.
5, 6, 8, 9	Areas 5 and 9 are specified by fo:border attributes, areas 6 and 8 by fo:padding attributes, all in <style:paragraph-properties>. / In case a shadow is defined by a style:shadow attribute, the width of the shadow is added to the width of the border.
7 paragraph content	Height is calculated from content.

The values page, page-content, frame, frame-content and paragraph-content of the attribute style:vertical-rel correspond to the areas described here. The value paragraph of the attribute style:vertical-rel has a special handling because of margin collapsing.

Problems with position top, center and bottom in combination with value paragraph:
Word has not implemented values paragraph or paragraph-content at all, but has only "line" as reference in the UI.
LibreOffice, Calligra and TextMaker first calculate an ersatz for area 4. They calculate its height =
height of area 4 − height of area 10 of the previous paragraph, at least 0. But the positioning is different then. LibreOffice builds an area of areas 5 to 9 including shadows and the ersatz for area 4. Then it positions the object according value top, center or bottom into this area. In result the bottom margin (10) of a paragraph is always ignored as area for vertical positioning of type paragraph by LibreOffice. Calligra takes the ersatz for area 4 and positions the object into this area. In result the objects are always above the top of border (5). TextMaker takes the top edge line of the ersatz for area 4 and then aligns the objects to this line and not to an area.
## Page, Frame and Section Content Horizontal
### Pages
Area	Related Attributes
page	fo:page-width in <style:page-layout-properties> in <style:page-layout>
1, 7	fo:margin in <style:page-layout-properties>
2, 6	fo:border in <style:page-layout-properties> / In case a shadow is defined by a style:shadow attribute, the width of the shadow is added to the width of the border.
3, 5	fo:padding in <style:page-layout-properties>
page-start-margin	Width of page-start-margin area = / sum of left page margin (1), border (2) and padding (3). / Instead of "left" see special rules in section style:horizontal-rel (20.291) for inside/outside positions.
page-end-margin	Width of page-end-margin area = / sum of right page margin (7), border (6) and padding (5). / Instead of "right" see special rules in style:horizontal-rel (20.291) for inside/outside positions.
4 page-content	Width of page-content area = / width of page − width of page-start-margin − width of page-end-margin.

### Frames
Area	Related Attributes
frame	svg:width in <draw:frame> or calculated from style:rel-width
10, 11	These areas are given by the fo:margin attributes in <style:graphic-properties> of the <draw:frame> element. / In contrast to the similar horizontal division for pages, they do not count for the frame width.
frame-start-margin / frame-end-margin	Width of frame margin area = sum of frame border and padding. / Values are in fo:border and fo:padding, all in <style:graphic-properties>. / In case a shadow is defined by a style:shadow attribute, the width of the shadow is added to the width of the border. / In regard to "left" and "right" see special rules in section style:horizontal-rel (20.291) for inside/outside positions.
frame-content	Width of frame-content = width of frame − width of frame-start-margin − width of frame-end-margin.

### Sections
Area	Related Attributes
	The width of a section is given by the content area of the parent element of the <text:section> element.
8, 9	Left (8) and right (9) margin of a section are given by the fo:margin-left and fo:margin-right attributes in the <style:section-properties> element. / Border, shadow and padding are not available for sections. / Sections are not directly available for positions.
section-content-area	Width of section content area = width of parent content area − section left margin − section right margin

## Text Columns
The content area of pages, sections and frames can be divided into columns. Having one columns is allowed.
The relevant attributes and elements are
in <style:page-layout-properties> element, in case of dividing a page content area,
in <style:section-properties> element, in case of dividing a section content area,
in <style:graphic-properties> element, in case of dividing a frame content area.
Columns are not directly available for positioning.

Area	Related Attributes
10	Attribute fo:start-indent in element <style:column> in element <style:columns>.
11	Attribute fo:end-indent in element <style:column> in element <style:columns>
12	Attribute style:width in <style:column-sep>.
column	The width of the parent-content area is divided with respect to attribute style:rel-width in the <style:column> elements. Instead of widths for individual columns the attributes fo:column-gap and fo:column-count of element <style:columns> can be used in case of equally wide columns.
13 column-content area	Width of column content area = / width of column − width of column start-indent (10) − width of column end-indent (11) The separator line (12) is drawn on top of the indent areas and does not impact other widths.

## Paragraphs Horizontal
Parent content area of a paragraph can be a content area of a page, header, footer, section, frame, text column, or table cell. Always the innermost parent is taken.

Area	Related Attributes
13, 19	Attribute fo:margin in <style:paragraph-properties> in <style:style>.
14, 18	Attribute fo:border in <style:paragraph-properties> / In case a shadow is defined by a style:shadow attribute, the width of the shadow is added to the width of the border.
15, 17	Attribute fo:padding in <style:paragraph-properties>
paragraph-start-margin	Width of paragraph start-margin = / sum of paragraph left margin, border and padding. / Instead of "left" see special rules in section style:horizontal-rel (20.291) for inside/outside positions. / If the paragraph is in a list and the fo:margin-left and fo:text-indent attributes of a <style:list-level-label-alignment> element are used, then the sum of the attribute values is used as width of the paragraph-start-margin. / If the paragraph is in a list and the text:space-before attribute of its <style:list-level-properties> element is used, then that value is used for the width of the paragraph start margin.
paragraph-end-margin	Width of paragraph end-margin = / sum of paragraph right margin, border and padding. / Instead of "right" see special rules in section style:horizontal-rel (20.291) for inside/outside positions.
16 / paragraph-content	Width of paragraph content area = / Width of innermost parent content area − width of paragraph-start-margin − width of paragraph-end-margin

The values page, page-content, page-start-margin, page-end-margin, frame, frame-content, frame-start-margin, frame-end-margin, paragraph-content, paragraph-start-margin, and paragraph-end-margin of the style:horizontal-rel attribute correspond to the areas described here.
The value paragraph of the style:horizontal-rel attribute has no individual definition, but refers to the innermost parent content area of the paragraph.

## Characters