ODF 1.3	ODF 1.4
10.6.3 <draw:handle> / The <draw:handle> element represents a single interaction handle for a drawing shape.	10.6.3 <draw:handle> / The <draw:handle> element represents a single interaction handle for a drawing shape. It is either an XY-handle or a polar-handle If a draw:handle-position-x 19.nn1 attribute together with a draw:handle-position-y 19.nn2 attribute is present, it is an XY-handle. If a draw:handle-polar-pole-x 19.nn3 attribute together with a draw:handle-polar-pole-y 19.nn4 attribute is present, it is a polar-handle. Exactly one of these two pairs shall exist. / The position of an XY-handle is specified in Cartesian coordinates. The x-coordinate is specified by the draw:handle-position-x attribute, the y-coordinate is specified by the draw:handle-position-y attribute. / The position of a polar-handle is specified as tuple of radius and polar angle in a polar coordinate system. The draw:handle-polar-pole-x attribute specifies the x-coordinate and the draw:handle-polar-pole-y attribute specifies the y-coordinate of the pole of the polar coordinate system. The draw:handle-polar-radius 19.nn5 attribute specifies the radius and the draw:handle-polar-angle 19.nn6 attribute defines the polar angle of the position of the polar-handle. / The polar axis of the polar coordinate system points horizontally from the pole to the right. The polar angle is measured clockwise from the polar axis. / Note: The y-axis in the enhanced geometry of a custom shape points down. Therefore the measurement is clockwise and not counter-clockwise. / Parameters in the values of the draw:handle-position-x, draw:handle-position-y, draw:handle-polar-pole-x, draw:handle-polar-pole-y, draw:handle-polar-radius and draw:handle-polar-angle attributes use a common syntax. / A handle-parameter can be a number or it can have one of the following enhancements: / A “?” (U+003F, QUESTION MARK) is used to mark the beginning of a formula name. The result of the <draw:equation> 10.2.5 element's draw:formula 19.171 attribute whose draw:name 19.197.8 attribute is the formula name that is used as the parameter value. / If “$” (U+0024, DOLLAR SIGN) precedes an integer value, the value is an index to a draw:modifiers 19.196 attribute. The corresponding modifier value is used as parameter value. / Instead of a number a value can also be one of the following constants: / Table nn - Handle position constants / Constant Description / bottom The bottom coordinate of the view box as specified by the svg:viewBox 19.574 attribute is used. / hasfill If the shape has a fill style, a value of 1 is used. / hasstroke If the shape has a line style, a value of 1 is used. / height The view box height as specified by the svg:viewBox 19.574 attribute is used. / logheight The height in 1/100th mm as specified by the svg:height 19.543 attribute is used. / logwidth The width in 1/100th mm as specified by the svg:width 19.575 attribute is used. / left The left coordinate of the view box as specified by the svg:viewBox 19.574 attribute is used. / right The right coordinate of the view box as specified by the svg:viewBox 19.574 attribute is used. / top The top coordinate of the view box as specified by the svg:viewBox 19.574 attribute is used. / width The view box width as specified by the svg:viewBox 19.574 attribute is used. / xstretch The value of the draw:path-stretchpoint-x 19.204 attribute is used. / ystretch The value of the draw:path-stretchpoint-y 19.205 attribute is used. / A handle-parameter is formally defined as / handle-parameter::= formula | modifier | constant | number formula::= '?' name modifier::= '$' integer constant::= 'left' | 'top' | 'right' | 'bottom' | 'xstretch' | 'ystretch' | 'hasstroke' | 'hasfill ' | 'width' | 'height' | 'logwidth' | 'logheight' number::=sign? float | sign? integer float::= fractional exponent? | integer exponent fractional::= integer? '.' integer | integer '.' exponent::= ( 'e' | 'E' ) sign? integer sign::= '+'| '-' integer::= [0-9]+ name ::= [^ ]+
The <draw:handle> element is usable within the following element: <draw:enhanced-geometry> 10.6.2.	The <draw:handle> element is usable within the following element: <draw:enhanced-geometry> 10.6.2.
The <draw:handle> element has the following attributes: draw:handle-mirror-horizontal 19.176, draw:handle-mirror-vertical 19.177, draw:handle-polar 19.178, draw:handle-position 19.179, draw:handle-radius-range-maximum 19.180, draw:handle-radius-range-minimum 19.181, draw:handle-range-x-maximum 19.182, draw:handle-range-x-minimum 19.183, draw:handle-range-y-maximum 19.184, draw:handle-range-y-minimum 19.185 and draw:handle-switched 19.186.	The <draw:handle> element has the following attributes: draw:handle-mirror-horizontal 19.176, draw:handle-mirror-vertical 19.177, draw:handle-polar 19.178, draw:handle-polar-angle 19.nn6, draw:handle-polar-pole-x 19.nn3, draw:handle-polar-pole-y 19.nn4, draw:handle-polar-radius 19.nn5, draw:handle-position 19.179, draw:handle-position-x 19.nn1, draw:handle-position-y 19.nn2, draw:handle-radius-range-maximum 19.180, draw:handle-radius-range-minimum 19.181, draw:handle-range-x-maximum 19.182, draw:handle-range-x-minimum 19.183, draw:handle-range-y-maximum 19.184, draw:handle-range-y-minimum 19.185 and draw:handle-switched 19.186.
The <draw:handle> element has no child elements.	The <draw:handle> element has no child elements.

19.178 draw:handle-polar / The draw:handle-polar attribute specifies that a handle is a polar handle. The syntax for this attribute is the same as for the draw:handle-position 19.179 attribute. The first parameter specifies the horizontal center position, the vertical center position is specified by the second parameter. If this attribute is set, the draw:handle-range-x-minimum 19.183, draw:handle-range-x-maximum 19.182, draw:handle-range-y-minimum 19.185 and draw:handle-range-y-maximum 19.184 attributes are ignored, and the draw:handle-radius-range-minimum 19.181 and draw:handle-radius-range-maximum 19.180 attributes are used.	19.178 draw:handle-polar (deprecated) / Note: This attribute is deprecated in favor of the new attributes draw:handle-polar-pole-x, draw:handle-polar-pole-y, draw:handle-polar-radius and draw:handle-polar-angle due to the problematic design of the draw:handle-position attribute and mismatch between previous versions of this specification and ODF implementations. / OpenDocument 1.4 consumers shall ignore this attribute. / The draw:handle-polar attribute specifies that a handle is a polar handle. The syntax for / ⁞ / see ODF 1.3

I think a long form like the following is not needed, because either pair draw:handle-position-x | draw:handle-position-y or pair draw:handle-polar-pole-x | draw:handle-polar-pole-y must exist in a <draw:handle> element.
OpenDocument 1.4 consumers shall ignore this attribute if any of the attribute pairs draw:handle-position-x together with draw:handle-position-y or draw:handle-polar-pole-x together with draw:handle-polar-pole-y is present.
19.179 draw:handle-position / The draw:handle-position attribute specifies the position of a handle and consists of two values. / Each value can be a floating-point number or it can have one of the following enhancements: / A “?” (U+003F, QUESTION MARK) is used to mark the beginning of a formula name. The result of the <draw:equation> 10.2.5 element's draw:formula 19.171 attribute whose draw:name 19.197.8 attribute is the formula name that is used as the value. / If “$” (U+0024, DOLLAR SIGN) precedes an integer value, the value is an index to a draw:modifiers 19.196 attribute. The corresponding modifier value is used as parameter value. / Instead of a number a value can also be one of the following constants: / Table 13 - Handle position constants / … / If the draw:handle-polar 19.178 attribute is not set, the first parameter of the draw:handle-position attribute specifies the horizontal handle position, the vertical handle position is described by the second parameter. If the draw:handle-polar attribute is set, then a handle is a polar handle and the first parameter of the draw:handle-position attribute specifies the angle (as defined in 18.3.1), the handle radius is specified by the second parameter. / The value of a draw:handle-position attribute is formally defined as: / …	19.179 draw:handle-position (deprecated) / Note: This attribute is deprecated in favor of the new attributes draw:handle-position-x, draw:handle-position-y, draw:handle-polar-radius and draw:handle-polar-angle due to the problematic design of this attribute and mismatch between previous versions of this specification and ODF implementations. / OpenDocument 1.4 consumers shall ignore this attribute. / The draw:handle-position attribute specifies the position of a handle and consists of two values. / Each value can be a floating-point number or it can have one of the following enhancements: / ⁞ / see ODF 1.3 / I think a long form like the following is not needed, because either pair draw:handle-position-x | draw:handle-position-y or pair draw:handle-polar-pole-x | draw:handle-polar-pole-y must exist in a <draw:handle> element. / OpenDocument 1.4 consumers shall ignore this attribute if any of the attribute pairs draw:handle-position-x together with draw:handle-position-y or draw:handle-polar-pole-x together with draw:handle-polar-pole-y is present.

new attribute	19.nn1 draw:handle-position-x / The draw:handle-position-x attribute specifies the horizontal position of an XY-handle, see <draw:handle> 10.6.3 element. / The value of the draw:handle-position-x attribute is a string with the following syntax: / handle-position-x-value ::= handle-parameter / where handle-parameter is defined in <draw:handle> 10.6.3. / The resulting value is interpreted as x-coordinate of the position of the XY-handle.

new attribute	19.nn2 draw:handle-position-y / The draw:handle-position-y attribute specifies the vertical position of an XY-handle, see <draw:handle> 10.6.3 element. / The value of the draw:handle-position-y attribute is a string with the following syntax: / handle-position-y-value ::= handle-parameter / where handle-parameter is defined in <draw:handle> 10.6.3. / The resulting value is interpreted as y-coordinate of the position of the XY-handle.

new attribute	19.nn3 draw:handle-polar-pole-x / The draw:handle-polar-pole-x attribute specifies the horizontal position of the pole of the polar coordinate system used for a polar handle, see <draw:handle> 10.6.3 element. / The value of the draw:handle-polar-pole-x attribute is a string with the following syntax: / handle-polar-pole-x-value ::= handle-parameter / where handle-parameter is defined in <draw:handle> 10.6.3. / The resulting value is interpreted as x-coordinate of the pole.

new attribute	19.nn4 draw:handle-polar-pole-y / The draw:handle-polar-pole-y attribute specifies the vertical position of the pole of the polar coordinate system used for a polar handle, see <draw:handle> 10.6.3 element. / The value of the draw:handle-polar-pole-y attribute is a string with the following syntax: / handle-polar-pole-y-value ::= handle-parameter / where handle-parameter is defined in <draw:handle> 10.6.3. / The resulting value is interpreted as y-coordinate of the pole.

new attribute	19.nn5 draw:handle-polar-radius / The draw:handle-polar-radius attribute specifies the radius component of the polar coordinates of the handle position of a polar-handle, see <draw:handle> 10.6.3 element. / The value of the draw:handle-polar-radius attribute is a string with the following syntax: / handle-polar-radius-value ::= handle-parameter / where handle-parameter is defined in <draw:handle> 10.6.3. / The resulting value is interpreted as distance from the pole of the polar coordinate system to the position of the handle. / If the resulting value is negative, the handle position is undefined. / If the resulting value is zero, the handle position is on the pole of the polar coordinate system regardless of the value of the draw:handle-polar-angle 19.nn6 attribute. / The default value of the attribute is the string 0.

new attribute	19.nn6 draw:handle-polar-angle / The draw:handle-polar-angle attribute specifies the polar angle component of the polar coordinates of the handle position of a polar handle, see <draw:handle> 10.6.3 element. / The value of the draw:handle-polar-angle attribute is a string with the following syntax: / handle-polar-angle-value ::= handle-parameter / where handle-parameter is defined in <draw:handle> 10.6.3. / The resulting value is interpreted as angle in degrees. / The default value of the attribute is the string 0.