Service Component Architecture Client and Implementation Model Specification for C++ Version 1.1

Committee Draft 01 Revision 03 + Issue 17

1 December 2008

Specification URIs:

This Version:

http://docs.oasis-open.org/opencsa/sca-c-cpp/sca-cppcni-1.1-spec-cd01-rev3.html

http://docs.oasis-open.org/opencsa/sca-c-cpp/sca-cppcni-1.1-spec-cd01-rev3.doc

http://docs.oasis-open.org/opencsa/sca-c-cpp/sca-cppcni-1.1-spec-cd01-rev3.pdf (Authoritative)

Previous Version:

http://docs.oasis-open.org/opencsa/sca-c-cpp/sca-cppcni-1.1-spec-cd01-rev2.html

http://docs.oasis-open.org/opencsa/sca-c-cpp/sca-cppcni-1.1-spec-cd01-rev2.doc

http://docs.oasis-open.org/opencsa/sca-c-cpp/sca-cppcni-1.1-spec-cd01-rev2.pdf (Authoritative)

Latest Version:

http://docs.oasis-open.org/opencsa/sca-c-cpp/sca-cppcni-1.1-spec.html

http://docs.oasis-open.org/opencsa/sca-c-cpp/sca-cppcni-1.1-spec.doc

http://docs.oasis-open.org/opencsa/sca-c-cpp/sca-cppcni-1.1-spec.pdf (Authoritative)

Technical Committee:

OASIS Service Component Architecture / C and C++ (SCA-C-C++) TC

Chair:

Bryan Aupperle, IBM <mailto:aupperle@us.ibm.com>

Editors:

Bryan Aupperle, IBM <mailto:aupperle@us.ibm.com>

David Haney, Rogue Wave Software <mailto:haney@roguewave.com>

Pete Robbins, IBM <mailto:robbins@uk.ibm.com>

Related work:

This specification replaces or supercedes:

OSOA SCA C++ Client and Implementation V1.00

This specification is related to:

OASIS Service Component Architecture Assembly Model Version 1.1

OASIS SCA Policy Framework Version 1.1

OASIS Service Component Architecture Web Service Binding Specification Version 1.1

Declared XML Namespace(s):

http://docs.oasis-open.org/ns/opencsa/sca/200712

http://docs.oasis-open.org/ns/opencsa/sca-c-cpp/cpp/200901

Abstract:

This document describes the SCA Client and Implementation Model for the C++ programming language.

The SCA C++ implementation model describes how to implement SCA components in C++. A component implementation itself can also be a client to other services provided by other components or external services. The document describes how a C++ implemented component gets access to services and calls their operations.

The document also explains how non-SCA C++ components can be clients to services provided by other components or external services. The document shows how those non-SCA C++ component implementations access services and call their operations.

Status:

This document was last revised or approved by the Service Component Architecture / C and C++ TC on the above date. The level of approval is also listed above. Check the “Latest Version” or “Latest Approved Version” location noted above for possible later revisions of this document.

Technical Committee members should send comments on this specification to the Technical Committee’s email list. Others should send comments to the Technical Committee by using the “Send A Comment” button on the Technical Committee’s web page at http://www.oasis-open.org/committees/sca-c-cpp/.

For information on whether any patents have been disclosed that may be essential to implementing this specification, and any offers of patent licensing terms, please refer to the Intellectual Property Rights section of the Technical Committee web page (http://www.oasis-open.org/committees/sca-c-cpp/ipr.php).  The non-normative errata page for this specification is located at http://www.oasis-open.org/committees/sca-c-cpp/.

Notices

Copyright © OASIS® 2006, 2008. All Rights Reserved.

All capitalized terms in the following text have the meanings assigned to them in the OASIS Intellectual Property Rights Policy (the "OASIS IPR Policy"). The full Policy may be found at the OASIS website.

This document and translations of it may be copied and furnished to others, and derivative works that comment on or otherwise explain it or assist in its implementation may be prepared, copied, published, and distributed, in whole or in part, without restriction of any kind, provided that the above copyright notice and this section are included on all such copies and derivative works. However, this document itself may not be modified in any way, including by removing the copyright notice or references to OASIS, except as needed for the purpose of developing any document or deliverable produced by an OASIS Technical Committee (in which case the rules applicable to copyrights, as set forth in the OASIS IPR Policy, must be followed) or as required to translate it into languages other than English.

The limited permissions granted above are perpetual and will not be revoked by OASIS or its successors or assigns.

This document and the information contained herein is provided on an "AS IS" basis and OASIS DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY OWNERSHIP RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

OASIS requests that any OASIS Party or any other party that believes it has patent claims that would necessarily be infringed by implementations of this OASIS Committee Specification or OASIS Standard, to notify OASIS TC Administrator and provide an indication of its willingness to grant patent licenses to such patent claims in a manner consistent with the IPR Mode of the OASIS Technical Committee that produced this specification.

OASIS invites any party to contact the OASIS TC Administrator if it is aware of a claim of ownership of any patent claims that would necessarily be infringed by implementations of this specification by a patent holder that is not willing to provide a license to such patent claims in a manner consistent with the IPR Mode of the OASIS Technical Committee that produced this specification. OASIS may include such claims on its website, but disclaims any obligation to do so.

OASIS takes no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights. Information on OASIS' procedures with respect to rights in any document or deliverable produced by an OASIS Technical Committee can be found on the OASIS website. Copies of claims of rights made available for publication and any assurances of licenses to be made available, or the result of an attempt made to obtain a general license or permission for the use of such proprietary rights by implementers or users of this OASIS Committee Specification or OASIS Standard, can be obtained from the OASIS TC Administrator. OASIS makes no representation that any information or list of intellectual property rights will at any time be complete, or that any claims in such list are, in fact, Essential Claims.

The name "OASIS" is a trademark of OASIS, the owner and developer of this specification, and should be used only to refer to the organization and its official outputs. OASIS welcomes reference to, and implementation and use of, specifications, while reserving the right to enforce its marks against misleading uses. Please see http://www.oasis-open.org/who/trademark.php for above guidance.

Table of Contents

1	Introduction	9

1.1	Terminology	9

1.2	Normative References	9

1.3	Non-Normative References	10

2	Basic Component Implementation Model	11

2.1	Implementing a Service	11

2.1.1	Implementing a Remotable Service	12

2.1.2	Implementing a Local Service	13

2.2	Conversational and Non-Conversational services	13

2.3	Component Implementation Scopes	13

2.3.1	Stateless scope	14

2.3.2	Composite scope	14

2.3.3	Conversation scope	14

2.4	Implementing a Configuration Property	14

2.5	Component Type and Component	15

2.5.1	Interface.cpp	16

2.5.2	Function and CallbackFunction	17

2.5.3	Implementation.cpp	17

2.5.4	Implementation Function	18

2.6	Instantiation	19

3	Basic Client Model	20

3.1	Accessing Services from Component Implementations	20

3.2	Accessing Services from non-SCA component implementations	21

3.3	Calling Service Operations	21

4	Conversational Services	22

4.1	Conversational Client	22

4.2	Conversational Service Provider	22

4.3	Operations that End the Conversation	23

4.4	Passing Conversational Services as Parameters	24

4.5	Conversation Lifetime Summary	24

4.6	Application Specified Conversation IDs	25

4.7	Accessing Conversation IDs from Clients	25

5	Asynchronous Programming	26

5.1	Non-blocking Calls	26

5.2	Callbacks	26

5.2.1	Stateful Callbacks	27

5.2.2	Stateless Callbacks	28

5.2.3	Implementing Multiple Bidirectional Interfaces	28

5.2.4	Customizing the Callback Identity	28

6	Error Handling	30

7	C++ API	31

7.1	Reference Counting Pointers	31

7.1.1	operator*	31

7.1.2	operator->	31

7.1.3	operator void*	32

7.1.4	operator!	32

7.2	Component Context	32

7.2.1	getCurrent	33

7.2.2	getURI	33

7.2.3	getService	33

7.2.4	getServices	33

7.2.5	getServiceReference	34

7.2.6	getServiceReferences	34

7.2.7	getProperties	34

7.2.8	getDataFactory	34

7.2.9	getSelfReference	35

7.3	ServiceReference	35

7.3.1	getService	35

7.3.2	getConversationID	36

7.3.3	setConversationID	36

7.3.4	getCallbackID	36

7.3.5	setCallbackID	36

7.3.6	getCallback	37

7.3.7	endConversation	37

7.4	SCAException	37

7.4.1	getEClassName	37

7.4.2	getMessageText	38

7.4.3	getFileName	38

7.4.4	getLineNumber	38

7.4.5	getFunctionName	38

7.5	SCANullPointerException	39

7.6	ServiceRuntimeException	39

7.7	ServiceUnavailableException	39

7.8	NoRegisteredCallbackException	39

7.9	ConversationEndedException	39

7.10	MultipleServicesException	39

7.11	ConversationStateException	39

7.12	NoConversationException	40

8	C++ Contributions	41

8.1	Executable files	41

8.1.1	Executable in contribution	41

8.1.2	Executable shared with other contribution(s) (Export)	41

8.1.3	Executable outside of contribution (Import)	42

8.2	componentType files	43

8.3	C++ Contribution Extensions	43

8.3.1	Export.cpp	43

8.3.2	Import.cpp	44

9	Types Supported in Service Interfaces	45

9.1	Local service	45

9.2	Remotable service	45

10	Restrictions on C++ header files	46

11	WSDL to C++ and C++ to WSDL Mapping	47

11.1	Augmentations for WSDL to C++ Mapping	47

11.1.1	Mapping WSDL targetNamespace to a C++ namespace	47

11.1.2	Mapping WSDL Faults to C++ Exceptions	48

11.1.3	Mapping of in, out, in/out parts to C++ member function parameters	48

11.2	Augmentations for C++ to WSDL Mapping	49

11.2.1	Mapping C++ namespaces to WSDL namespaces	49

11.2.2	Parameter and return type classification	49

11.2.3	C++ to WSDL Type Conversion	49

11.2.4	Service-specific Exceptions	49

11.3	SDO Data Binding	49

11.3.1	Simple Content Binding	49

11.3.2	Complex Content Binding	51

12	Conformance	52

12.1	Conformance Targets	52

12.2	Conformance Claims	52

12.3	SCA Implementations	52

12.4	SCDL Documents	52

12.5	C++ Component Implementations	52

12.6	C++ Header Files	52

12.7	WSDL Files	53

12.8	Extensions	53

A	C++ SCA Annotations	54

A.1 Application of Annotations to C++ Program Elements	54

A.2 Interface Header Annotations	54

A.2.1 @Interface	55

A.2.2 @Remotable	55

A.2.3 @Callback	56

A.2.4 @OneWay	56

A.2.5 @Conversational	57

A.2.6 @EndsConversation	57

A.3 Implementation Header Annotations	58

A.3.1 @ComponentType	58

A.3.2 @Scope	58

A.3.3 @EagerInit	59

A.3.4 @AllowsPassByReference	60

A.3.5 @ConversationAttributes	60

A.3.6 @Property	61

A.3.7 @Reference	61

A.1 Base Annotation Grammar	62

B	C++ SCA Policy Annotations	64

B.1 General Intent Annotations	64

B.2 Specific Intent Annotations	65

B.2.1 Security Interaction	66

B.2.2 Security Implementation	66

B.2.3 Reliable Messaging	67

B.2.4 Transactions	67

B.2.5 Miscellaneous	67

B.3 Application of Intent Annotations	67

B.4 Inheritance and Intent Annotations	68

B.5 Relationship of Declarative and Annotated Intents	69

B.6 Policy Set Annotations	69

B.7 Policy Annotation Grammar Additions	70

B.8 Annotation Constants	70

C	C++ WSDL Mapping Annotations	71

C.1 Interface Header Annotations	71

C.1.1 @WebService	71

C.1.2 @WebFunction	72

C.1.3 @OneWay	74

C.1.4 @WebParam	75

C.1.5 @WebResult	77

C.1.6 @SOAPBinding	79

C.1.7 @WebFault	80

C.1.8 @WebThrows	82

D	WSDL C++ Mapping Extensions	83

D.1 <cpp:bindings>	83

D.2 <cpp:class>	83

D.3 <cpp:enableWrapperStyle>	84

D.4 <cpp:namespace>	85

D.5 <cpp:memberFunction>	86

D.6 <cpp:parameter>	87

D.7 JAX-WS WSDL Extensions	89

D.8 WSDL Extensions Schema	90

E	XML Schemas	91

E.1 sca-interface-cpp-1.1.xsd	91

E.2 sca-implementation-cpp-1.1.xsd	92

E.3 sca-contribution-cpp-1.1.xsd	92

F	Conformance Items	94

F.1 JAX-WS Conformance	97

F.1.1 Ignored Conformance Statements	99

G	Migration	101

G.1 Annotations related to conversations	101

G.2 Method child elements of interface.cpp and implementation.cpp	101

H	Acknowledgements	102

I	Non-Normative Text	103

J	Revision History	104

# Introduction

This document describes the SCA Client and Implementation Model for the C++ programming language.

The SCA C++ implementation model describes how to implement SCA components in C++. A component implementation itself can also be a client to other services provided by other components or external services. The document describes how a C++ implemented component gets access to services and calls their operations.

The document also explains how non-SCA C++ components can be clients to services provided by other components or external services. The document shows how those non-SCA C++ component implementations access services and call their operations.

## Terminology

The key words “MUST”, “MUST NOT”, “REQUIRED”, “SHALL”, “SHALL NOT”, “SHOULD”, “SHOULD NOT”, “RECOMMENDED”, “MAY”, and “OPTIONAL” in this document are to be interpreted as described in [RFC2119]

This specification uses predefined namespace prefixes throughout; they are given in the following list. Note that the choice of any namespace prefix is arbitrary and not semantically significant.

Table 1-1 Prefixes and Namespaces used in this specification

| Prefix | Namespace | Notes |
| --- | --- | --- |
| xs | "http://www.w3.org/2001/XMLSchema" | Defined by XML Schema 1.0 specification |
| sca | "http://docs.oasis-open.org/ns/opencsa/sca/200712" | Defined by the SCA specifications |
| cpp | "http://docs.oasis-open.org/ns/opencsa/sca-c-cpp/cpp/200901" |  |

## Normative References

[RFC2119]	S. Bradner, Key words for use in RFCs to Indicate Requirement Levels, http://www.ietf.org/rfc/rfc2119.txt, IETF RFC 2119, March 1997.

[ASSEMBLY]	M. Beisiegel, et al., Service Component Architecture Assembly Model Specification Version 1.1, http://docs.oasis-open.org/opencsa/sca-assembly/sca-assembly-1.1-spec.pdf, OASIS Service Component Architecture  Assembly Model Specification Version 1.1, XXX 2009

[POLICY]	J. Anderson, et al., SCA Policy Framework Version 1.1, http://docs.oasis-open.org/opencsa/sca-policy/sca-policy-1.1-spec.pdf, OASIS SCA Policy Framework Version 1.1, XXX 2009

[SDO21]	J. Beatty, et al., Service Data Objects For C++ Specification, http://www.osoa.org/download/attachments/36/CPP-SDO-Spec-v2.1.0-FINAL.pdf, SDO 2.1, December 2006.

[WSDL11]	E. Christensen, et al., Web Service Description Language (WSDL), http://www.w3.org/TR/wsdl, W3C Note Web Service Description Language (WSDL), March 2001

[XSD]	P. Brion, et al., XML Schema Part 2: Datatypes Second Edition, http://www.w3.org/TR/xmlschema-2/, W3C XML Schema Part 2: Datatypes Second Edition, October 2004

[JAXWS21]	D. Kohlert, et al., The Java API for XML-Based Web Services (JAX-WS) 2.1, http://jcp.org/aboutJava/communityprocess/mrel/jsr224/index2.html, JCP Java API for XML-Based Web Services (JAX-WS) 2.1, May 2007

## Non-Normative References

# Basic Component Implementation Model

This section describes how SCA components are implemented using the C++ programming language.  It shows how a C++ implementation based component can implement a local or remotable service, and how the implementation can be made configurable through properties.

A component implementation can itself be a client of services. This aspect of a component implementation is described in the basic client model section.

## Implementing a Service

A component implementation based on a C++ class (a C++ implementation) provides one or more services.

A service provided by a C++ implementation has an interface (a service interface) which is defined using one of:

a C++ abstract base class

a WSDL 1.1 portType [WSDL11]

An abstract base class is a class which has only pure virtual member functions. A C++ implementation MUST implement all of the operation(s) of the service interface(s) of its componentType. [CPP20001]

The following snippets show the C++ service interface and the C++ implementation class of a C++ implementation.

Service interface.

// LoanService interface

class LoanService {

public:

virtual bool approveLoan(unsigned long customerNumber,

unsigned long loanAmount) = 0;

};

Implementation declaration header file.

class LoanServiceImpl : public LoanService {

public:

LoanServiceImpl();

virtual ~LoanServiceImpl();

virtual bool approveLoan(unsigned long customerNumber,

unsigned long loanAmount);

};

Implementation.

#include "LoanServiceImpl.h"

LoanServiceImpl::LoanServiceImpl()

{

…

}

LoanServiceImpl::~LoanServiceImpl()

{

…

}

bool LoanServiceImpl::approveLoan(unsigned long customerNumber,

unsigned long loanAmount)

{

…

}

The following snippet shows the component type for this component implementation.

<?xml version="1.0" encoding="ASCII"?>

<componentType xmlns="http://docs.oasis-open.org/ns/opencsa/sca/200712">

<service name="LoanService">

<interface.cpp header="LoanService.h"/>

</service>

</componentType>

The following picture shows the relationship between the C++ header files and implementation files for a component that has a single service and a single reference.

### Implementing a Remotable Service

A @remotable=”true” attribute on an interface.cpp element indicates that the interface is remotable as described in the Assembly Specification [ASSEMBLY]. The following snippet shows the component type for a remotable service:

<?xml version="1.0" encoding="ASCII"?>

<componentType xmlns="http://docs.oasis-open.org/ns/opencsa/sca/200712">

<service name="LoanService">

<interface.cpp header="LoanService.h" remotable="true"/>

</service>

</componentType>

Complex data types exchanged via remotable service interfaces MUST be compatible with the marshalling technology that is used by the service binding.

An implementation of a remotable service can declare whether it allows pass by reference data exchange semantics on calls to it, meaning that the by-value semantics can be maintained without requiring that the parameters be copied. A C++ implementation of a remotable service that allow pass by reference MUST NOT alter its input data during or after the invocation, and MUST NOT modify return data after invocation.  [CPP20002] The @allowsPassByReference=true attribute on the implementation.cpp element of a remotable service is used to declare that calls to the whole interface allows pass by reference. Alternatively, this attribute can be used on a specific member function.

### Implementing a Local Service

A service interface not marked as remotable is local.

## Conversational and Non-Conversational services

A @requires=”conversational” attribute on an interface.cpp element indicates that the service contract is conversational, as described in the Assembly Specification [ASSEMBLY].

A non-conversational service, the default when no annotation is specified, indicates that the service contract is stateless between requests. A conversational service indicates that requests to the service are correlated.

## Component Implementation Scopes

Component implementations can either manage their own state or allow the SCA runtime to do so. In the latter case, SCA defines the concept of implementation scope, which specifies the visibility and lifecycle contract an implementation has with the runtime. Invocations on a service offered by a component will be dispatched by the SCA runtime to an implementation instance according to the semantics of its scope.

Scopes are specified using the @scope attribute of the implementation.cpp element.

When a scope is not specified on an implementation class, the SCA runtime will interpret the implementation scope as stateless.

An SCA runtime MUST support these four scopes; stateless, conversation, and composite. Additional scopes MAY be provided by SCA runtimes. [CPP20003]

The following snippet shows the component type for a composite scoped component:

<component name="LoanService">

<implementation.cpp library="loan" class="LoanServiceImpl”

scope="composite"/>

</component>

For stateless scoped implementations, the SCA runtime MUST prevent concurrent execution of member functions on an instance of that implementation.  However, composite scoped implementations MUST be able to handle multiple threads running its member functions concurrently.

### Stateless scope

For stateless implementations, a different instance may be used to service each request. Implementation instances may be created or drawn from a pool of instances.

### Composite scope

All service requests are dispatched to the same implementation instance for the lifetime of the containing composite. The lifetime of the containing composite is defined as the time it becomes active in the runtime to the time it is deactivated, either normally or abnormally.

A composite scoped implementation may also specify eager initialization using the @eagerInit=”true” attribute on the implementation.cpp element of a component definition. When marked for eager initialization, the composite scoped instance will be created when its containing component is started.

### Conversation scope

A conversation is defined as a series of correlated interactions between a client and a target service. A conversational scope starts when the first service request is dispatched to an implementation instance offering the target service. A conversational scope completes after an end operation defined by the service contract is called and completes processing or the conversation expires (see Operations that End the Conversation). A conversation is potentially long-running and the SCA runtime MAY choose to passivate implementation instances. If this occurs, the runtime MUST guarantee implementation instance state is preserved.

A conversational-scoped C++ implementation MUST NOT expose a service using a non-conversational interface. [CPP20004]

Note that in the case where a conversational service is implemented by a C++ implementation that is marked as conversation scoped, the SCA runtime will transparently handle implementation state. It is also possible for an implementation to manage its own state. For example, a C++ implementation having a stateless (or other) scope could implement a conversational service.

## Implementing a Configuration Property

Component implementations can be configured through properties. The properties and their types (not their values) are defined in the component type file. The C++ component can retrieve the properties using the getProperties() on the ComponentContext class.

The following code extract shows how to get the property values.

#include "ComponentContext.h"

using namespace oasis::sca;

void clientFunction()

{

…

ComponentContext context = ComponentContext::getCurrent();

DataObjectPtr properties = context.getProperties();

long loanRating = properties->getInteger(“maxLoanValue”);

…

}

## Component Type and Component

For a C++ component implementation, a component type is specified in a side file. By default, the componentType side file is in the root directory of the composite containing the component or some subdirectory of the composite root directory with a name matching the implementation class of the component.  The location can be modified as described below.

This Client and Implementation Model for C++ extends the SCA Assembly model [ASSEMBLY] providing support for the C++ interface type system and support for the C++ implementation type.

The following snippets show the C++ service interface and the C++ implementation class of a C++ service.

// LoanService interface

class LoanService {

public:

virtual bool approveLoan(unsigned long customerNumber,

unsigned long loanAmount) = 0;

};

Implementation declaration header file.

class LoanServiceImpl : public LoanService {

public:

LoanServiceImpl();

virtual ~LoanServiceImpl();

virtual bool approveLoan(unsigned long customerNumber,

unsigned long loanAmount);

};

Implementation.

#include "LoanServiceImpl.h"

//////////////////////////////////////////////////////////////////////

// Construction/Destruction

//////////////////////////////////////////////////////////////////////

LoanServiceImpl::LoanServiceImpl()

{

…

}

LoanServiceImpl::~LoanServiceImpl()

{

…

}

//////////////////////////////////////////////////////////////////////

// Implementation

//////////////////////////////////////////////////////////////////////

bool LoanServiceImpl::approveLoan(unsigned long customerNumber,

unsigned long loanAmount)

{

…

}

The following snippet shows the component type for this component implementation.

<?xml version="1.0" encoding="ASCII"?>

<componentType xmlns="http://docs.oasis-open.org/ns/opencsa/sca/200712">

<service name="LoanService">

<interface.cpp header="LoanService.h"/>

</service>

</componentType>

The following snippet shows the component using the implementation.

<?xml version="1.0" encoding="ASCII"?>

<composite xmlns="http://docs.oasis-open.org/ns/opencsa/sca/200712"

name="LoanComposite" >

…

<component name="LoanService">

<implementation.cpp library="loan" class="LoanServiceImpl”/>

</component>

</composite>

### Interface.cpp

The following snippet shows the schema for the C++ interface element used to type services and references of component types.

<?xml version="1.0" encoding="ASCII"?>

<!—- interface.cpp schema snippet -->

<interface.cpp xmlns="http://docs.oasis-open.org/ns/opencsa/sca/200712"

header="NCName" class="Name"? remotable="boolean"?

callbackHeader="NCName" callbackClass="Name"? >

<function … />*

<callbackFunction … />*

</interface.cpp>

The interface.cpp element has the following attributes:

header : NCName (1..1) – full name of the header file that describes the interface, including relative path from the composite root.

class : Name (0..1)  – name of the class declaration for the interface in the header file, including any namespace definition. If the header file identified by the @header attribute of an <interface.cpp/> element contains more than one class, then the @class attribute MUST be specified for the <interface.cpp/> element. [CPP20005]

callbackHeader : NCName (0..1) – full name of the header file that describes the callback interface, including relative path from the composite root.

callbackClass : Name (0..1) – name of the class declaration for the callback interface in the callback header file, including any namespace definition. If the header file identified by the @callbackHeader attribute of an <interface.cpp/> element contains more than one class, then the @callbackClass attribute MUST be specified for the <interface.cpp/> element. [CPP20006]

remotable : boolean (0..1) – indicates whether the service is remotable or local. The default is local. See Implementing a Remotable Service

The interface.cpp element has the following child elements:

function : CPPFunction (0..n) – see Function and CallbackFunction

callbackFunction : CPPFunction (0..n) – see Function and CallbackFunction

### Function and CallbackFunction

Some member functions of an interface have behavioral characteristics, which will be described later, that need to be identified.  This is done using a function or callbackFunction child element of interface.cpp

The following snippet shows the interface.cpp schema with the schema for the function and callbackFunction child elements:

<?xml version="1.0" encoding="ASCII"?>

<!—- Function schema snippet -->

<interface.cpp xmlns="http://docs.oasis-open.org/ns/opencsa/sca/200712" … >

<function name="NCName" oneWay="Boolean"? endsConversation="Boolean"? />*

<callbackFunction name="NCName" oneWay="Boolean"?

endsConversation="Boolean"? />*

</interface.cpp>

The function and callbackFunction elements have the following attributes:

name : NCName (1..1) – name of the method being decorated. The @name attribute of a <function/> child element of a <interface.cpp/> MUST be unique amongst the <function/> elements of that <interface.cpp/>. [CPP20007]

The @name attribute of a <callbackFunction/> child element of a <interface.cpp/> MUST be unique amongst the <callbackFunction/> elements of that <interface.cpp/>. [CPP20008]

oneWay : boolean (0..1) – see Non-blocking Calls

endsConversation : boolean (0..1) – see Operations that End the Conversation

### Implementation.cpp

The following snippet shows the schema for the C++ implementation element used to define the implementation of a component.

<?xml version="1.0" encoding="ASCII"?>

<!—- implementation.cpp schema snippet -->

<implementation.cpp xmlns="http://docs.oasis-open.org/ns/opencsa/sca/200712"

library="NCName" path="Name"? class="Name"

scope="scope"? componentType="NCName"? allowsPassByReference="Boolean"?

eagerInit="boolean"? conversationMaxAge="string "?

conversationMaxIdle="string"? conversationSinglePrincipal="Boolean "? >

<method … />*

</implementation.cpp>

The implementation.cpp element has the following attributes:

library : NCName (1..1) – name of the dll or shared library that holds the factory for the service component. This is the root name of the library.

path : Name (0..1) - path to the library which is either relative to the root of the contribution containing the composite or is prefixed with a contribution import name and is relative to the root of the import.  See C++ Contributions.

class : Name (1..1) – name of the class declaration of the implementation, including any namespace definition. The name of the componentType file for a C++ implementation MUST match the class name (excluding any namespace definition) of the implementations as defined by the @class attribute of the <implementation.cpp/> element. [CPP20009] The SCA runtime will append .componentType to the class name to find the componentType file.

scope : CPPImplementationScope (0..1) – identifies the scope of the component implementation. The default is stateless. See Component Implementation Scopes

componentType : NCName (0..1) – path to the componentType file which is relative to the root of the contribution containing the composite or is prefixed with a contribution import name and is relative to the root of the import.

allowsPassByReference : boolean (0..1) – indicates the service allows pass by reference data exchange semantics on calls to it. See Implementing a Remotable Service

eagerInit type : boolean (0..1) –  indicates a composite scoped implementation should be initialized when it is loaded. See Composite scope

conversationMaxAge : string (0..1) – see Conversational Service Provider.

conversationMaxIdle : string (0..1) – see Conversational Service Provider.

conversationSinglePrincipal : boolean (0..1) – see Conversational Service Provider.

The implementation.cpp element has the following child element:

function : CPPImplementationMethod (0..n) – see Implementation Function

### Implementation Function

Some member functions of an implementation have operational characteristics that need to be identified.  This is done using a function child element of implementation.cpp

The following snippet shows the implementation.cpp schema with the schema for a method child element:

<?xml version="1.0" encoding="ASCII"?>

<!—- ImplementationFunction schema snippet -->

<implementation.cpp xmlns="http://docs.oasis-open.org/ns/opencsa/sca/200712" … >

<function name="NCName" allowsPassByReference="boolean"? />*

</implementation.cpp>

The function element has the following attributes:

name : NCName (1..1) – name of the method being decorated. The @name attribute of a <function/> child element of a <implementation.cpp/> MUST be unique amongst the <function/> elements of that <implementation.cpp/>. [CPP20010]

allowsPassByReference : boolean (0..1) – indicates the method allows pass by reference data exchange semantics.

## Instantiation

A C++ implementation class MUST be default constructable by the SCA runtime to instantiate the component. [CPP20011]

# Basic Client Model

This section describes how to get access to SCA services from both SCA components and from non-SCA components. It also describes how to call methods of these services.

## Accessing Services from Component Implementations

A component can get access to a service using a component context.

The following snippet shows the ComponentContext C++ class with its getService() member function.

namespace oasis {

namespace sca {

class ComponentContext {

public:

static ComponentContextPtr getCurrent();

virtual void * getService(

const std::string& referenceName) const = 0;

…

}

}

}

The getService() member function takes as its input argument the name of the reference and returns a pointer to an object providing access to the service. The returned object will implement the abstract base class definition that is used to describe the reference.

The following shows a sample of how the ComponentContext is used in a C++ component implementation.  The getService() member function is called on the ComponentContext passing the reference name as input. The return of the getService() member function is cast to the abstract base class defined for the reference.

#include "ComponentContext.h"

#include "CustomerService.h"

using namespace oasis::sca;

void clientFunction()

{

unsigned long customerNumber = 1234;

ComponentContextPtr context = ComponentContext::getCurrent();

CustomerService* service =

(CustomerService* )context->getService("customerService");

short rating = service->getCreditRating(customerNumber);

}

## Accessing Services from non-SCA component implementations

Non-SCA components can access component services by obtaining a ComponentContextPtr from the SCA runtime and then following the same steps as a component implementation as described above.

How an SCA runtime implementation allows access to and returns a ComponentContextPtr is not defined by this specification.

## Calling Service Operations

The previous sections show the various options for getting access to a service. Once you have access to the service, calling an operation of the service is like calling a member function of a C++ class.

If you have access to a service whose interface is marked as remotable, then on calls to operations of that service you will experience remote semantics. Arguments and return are passed by-value and it is possible to get a ServiceUnavailableException, which is a ServiceRuntimeException.

# Conversational Services

A frequent pattern that occurs during the execution of remotable services is that a conversation is started between the client of the service and the provider of the service.  The conversation is a series of operation invocations that all pertain to a single common topic.  For example, a conversation might be the series of service calls that are necessary in order to apply for a bank loan.

## Conversational Client

No special coding is necessary in the client of a conversational service.  The developer of the client knows that the service is conversational from the service interface definition.  The following shows an example client of the conversational service described above:

#include "LoanApplicationClientImpl.h"

#include "ComponentContext.h"

#include "LoanService.h"

#include “LoanApplication.h”

using namespace oasis::sca;

void LoanApplicationClientImpl::clientFunction( LoanApplication loanApp,

unsigned int term )

{

unsigned long customerNumber = 1234;

ComponentContextPtr context = ComponentContext::getCurrent();

// service is defined as member field: LoanService* service;

service = (LoanService* )context->getService("loanService");

service->apply( loanApp );

service->lockCurrentRate( term );

}

bool LoanApplicationClientImpl::isApproved()

{

return (service->getLoanStatus() == 1);

}

## Conversational Service Provider

A class which provides a service with a conversational interface can have any scope. In particular, it is not necessary for the class to have conversation scope. However, the provider of the conversational service does not need to write special code to maintain state if the implementation has conversation scope since the runtime maintains state associated with the conversation, by routing each operation invocation associated with the conversation to the same logical instance of the class, with state data held in instance variables within the class. However, for classes with other scopes, when an operation of a conversational interface is executing, the ServiceReference::getConversationID() returns the conversation ID of the conversation. The conversation ID can be used by the class as an index to store and to look up state data associated with the conversation, using some suitable storage mechanism.

ComponentContextPtr context = ComponentContext::getCurrent();

ServiceReferencePtr serviceRef = context->getSelfReference();

std:string conversationID = serviceRef->getConversationID();

The service implementation might also have conversation attributes that control the lifetime and operation of the conversations it supports.  These attributes are specified on the implementation.cpp element:

@maxIdleTime  - The maximum time that can pass between operations within a single conversation.  An SCA runtime MAY end a conversation if the idle timeout expires.  [CPP40001]

@maxAge  - The maximum time that the entire conversation can remain active.  An SCA runtime MAY end a conversation if the conversation age timeout expires. [CPP40002]

@singlePrincipal – If true, only the principal (the user) that started the conversation has authority to continue the conversation.

The two attributes that take a time express the time as a string that starts with an integer, is followed by a space and then one of the following: "seconds", "minutes", "hours", "days" or "years".

Not specifying timeouts means that timeout values are defined by the implementation of the SCA runtime, however it chooses to do so.

Here is an example definition of a conversational service.

<component name="LoanService">

<implementation.cpp library="loan" class="LoanServiceImpl”

conversationMaxAge="30 days” />

</component>

## Operations that End the Conversation

An operation of a conversational service interface can be marked with an @endsConversation=”true” attribute.  This means that once this operation has been called, no further operations are to be called, allowing both the client and the target to free up resources that were associated with the conversation.  It is also possible to mark an operation on a callback interface (described later) as @endsConversation=”true”, in order for the service provider to be the party that chooses to end the conversation.  If an operation is called after the conversation completes a ConversationEndedException (which extends ServiceRuntimeException) is thrown.  This can also occur if there is a race condition between the client and the service provider calling their respective endsConversation operations.  Calling the endConversation() member function on a service reference also ends a conversation.

The following is an example implementation with a member function that has been marked as ending a conversation:

<?xml version="1.0" encoding="ASCII"?>

<componentType xmlns="http://docs.oasis-open.org/ns/opencsa/sca/200712">

<service name="LoanService">

<interface.cpp header="LoanService.h" remotable="true"

requires="conversational">

<function name="cancelApplication" endsConversation="true" />

</interface.cpp>

</service>

</componentType>

The cancelApplication() operation is annotated to end the conversation.

## Passing Conversational Services as Parameters

The service reference which represents a single conversation can be passed as a parameter to another service, even if that other service is remote.  This may be used in order to allow one component to continue a conversation that had been started by another.

A service provider may also create a service reference for itself that it can pass to other services.  A service implementation does this with a call to

ComponentContext::getSelfReference()

or

ComponentContext::getSelfReference(const std::string& serviceName)

The second variant, which takes a serviceName parameter, is used if the component implements multiple services.

This can be used to support complex callback patterns, such as when a callback is applicable only to a subset of a larger conversation.  Simple callback patterns are handled by the built-in callback support described later.

## Conversation Lifetime Summary

Starting conversations

Conversations start on the client side when one of the following occur:

A service is located using ComponentContext::getService() or ComponentContext::getServices().

A service reference is obtained using ComponentContext::getServiceReference() or ComponentContext::getServiceReferences().

A service operation is called on a reference that has no active conversation.

ServiceReference::setConversationID() is called for a service reference that has no active conversation.

Continuing conversations

The client can continue an existing conversation, by:

Holding the service reference that was created when the conversation started.

Getting the service reference object passed as a parameter from another service, even remotely.

Ending conversations

A conversation ends, and any state associated with the conversation is freed up, when:

A service operation with attribute @endsConveration=”true” is called.

The service calls an operation with attribute @endsConversation=”true” on a callback interface.

The service's conversation lifetime timeout occurs.

The client calls ServiceReference::endConversation().

If an operation is invoked on a service reference after an operation with attribute @endsConversation=”true” has been called then a new conversation will automatically be started.  If ServiceReference::getConversationID() is called after an operation with attribute @endsConversation=”true”  is called, but before the next conversation has been started, it will return null.

If a service reference is used after the service provider's conversation timeout has caused the conversation to be ended, then ConversationEndedException will be thrown.  In order to use that service reference for a new conversation, its endConversation() member function has to be called.

## Application Specified Conversation IDs

It is also possible to take advantage of the state management aspects of conversational services while using a client-provided conversation ID.  To do this, the client would use the ServiceReference::setConversationID() member function. If a client provides the conversationID, the interface object has to be obtained using ServiceReference::setService() and not ComponentContext::setConversationID().

ComponentContextPtr ctx = ComponentContext::getCurrent();

std:string conversationID("myID");

ServiceReferencePtr serviceReference =

ctx->getServiceReference("loanService");

serviceReference->setConversationID(conversationID);

LoanService* service = (LoanService*)serviceReference->getService();

A service provider can also provide the conversation ID.  To do this, the provider would use the ServiceReference::setConversationID() member function while processing the first operation of the conversation.

ComponentContextPtr ctx = ComponentContext::getCurrent();

std:string conversationID("myID");

ServiceReferencePtr serviceRef = ctx->getSelfReference();

serviceRef->setConversationID(conversationID);

The ID MUST be unique to the SCA component over all time. If the client is not an SCA component, then the ID MUST be globally unique.

Not all conversational service bindings support application-specified conversation IDs.

## Accessing Conversation IDs from Clients

Whether the conversation ID is chosen by the client or is generated by the system, the client accesses the conversation ID of a conversation by calling the ServiceReference::getConversationID() member function on the service reference for the conversation.

If the conversation ID is not application specified, then the getConversationID() member function is only guaranteed to return a valid value after the first operation has been invoked, otherwise it returns an empty string.

# Asynchronous Programming

Asynchronous programming of a service is where a client invokes a service and carries on executing without waiting for the service to execute.  Typically, the invoked service executes at some later time.  Output from the invoked service, if any, is fed back to the client through a separate mechanism, since no output is available at the point where the service is invoked. This is in contrast to the call-and-return style of synchronous programming, where the invoked service executes and returns any output to the client before the client continues.  The SCA asynchronous programming model consists of support for non-blocking operation calls, callbacks, and conversational services.  Each of these topics is discussed in the following sections.

## Non-blocking Calls

Non-blocking calls represent the simplest form of asynchronous programming, where the client of the service invokes the service and continues processing immediately, without waiting for the service to execute.

Any member function that returns void, has only by-value parameters and has no declared exceptions can be marked with the @oneWay=”true” attribute in the interface definition of the service. A member function marked as oneWay=”true” is considered non-blocking and the SCA runtime MAY use a binding that buffers the requests to the member function and sends them at some time after they are made. [CPP50001]

The following snippet shows the component type for a service with the reportEvent() member fucntion declared as a one-way operation:

<componentType xmlns="http://docs.oasis-open.org/ns/opencsa/sca/200712">

<service name="LoanService">

<interface.cpp header="LoanService.h">

<function name="reportEvent" oneWay="true" />

</interface.cpp>

</service>

</componentType>

SCA does not currently define a mechanism for making non-blocking calls to methods that return values or are declared to throw exceptions.  It is considered to be a best practice that service designers define one-way member function as often as possible, in order to give the greatest degree of binding flexibility to deployers.

## Callbacks

Callback services are used by bidirectional services as defined in the Assembly Specification [ASSEMBLY].

A callback interface is declared by the @callbackHeader and @callbackClass attributes in the interface definition of the service. The following snippet shows the component type for a service MyService with the interface defined in MyService.h and the interface for callbacks defined in MyServiceCallback.h,

<componentType xmlns="http://docs.oasis-open.org/ns/opencsa/sca/200712" >

<service name="MyService">

<interface.cpp header="MyService.h"

callbackHeader="MyServiceCallback.h"/>

</service>

</componentType>

### Stateful Callbacks

A stateful callback represents a specific implementation instance of the component that is the client of the service.  The interface of a stateful callback normally is conversational.

A component gets access to the callback service by using the getCallback() member function of the ServiceReference (obtained from the ComponentContext).

The following is an example service implementation for the service and callback declared above. When the someFunction() has completed its processing it retrieves the callback service from the ServiceReference and invokes a callback operation.

#include "MyServiceImpl.h"

#include "MyServiceCallback.h"

#include "oasis/sca/ComponentContext.h"

using namespace oasis::sca;

MyServiceImpl::someFunction( unsigned int arg )

{

…

// do some processing…

ComponentContextPtr context = ComponentContext::getCurrent();

ServiceReferencePtr serviceRef = context->getSelfReference();

MyServiceCallback* callback =

(MyServiceCallback* ) serviceRef->getCallback();

callback->receiveResult(result);

}

The following shows how a client component would to invoke the MyService service and receive the callback.

#include "MyServiceImpl.h"

#include "MyServiceCallback.h"

#include "oasis/sca/ComponentContext.h"

using namespace oasis::sca;

void clientMethod( unsigned int arg )

{

// locate the service

ComponentContextPtr context = ComponentContext::getCurrent();

MyService* service = (MyService*)context->getService("myservice");

service->someFunction(arg);

}

MyServiceCallback::receiveResult(unsigned int result)

{

// code to process result

}

Stateful callbacks support some of the same use cases as are supported by the ability to pass service references as parameters.  The primary difference is that stateful callbacks do not require that any additional parameters be passed with service operations.  This can be a great convenience.  If the service has many operations and any of those operations could be the first operation of the conversation, it would be unwieldy to have to take a callback parameter as part of every operation, just in case it is the first operation of the conversation.  It is also more natural than requiring the application developers to invoke an explicit operation whose only purpose is to pass the callback object to be used.

### Stateless Callbacks

A stateless callback interface is a callback whose interface is not conversational. Unlike stateful services, the client that uses stateless callbacks will not have callback operations routed to an instance of the client that contains any state that is relevant to the conversation.  As such, it is the responsibility of such a client to perform any persistent state management itself.  The only information that the client has to work with (other than the parameters of the callback operation) is a callback ID that is passed with requests to the service and is guaranteed to be returned with any callback. The callback ID is retrieved from the ServiceReference.

The following snippets show a client setting a callback id before invoking the asynchronous service and the callback member function retrieving the callback ID:

void clientFunction( unsigned int arg )

{

// locate the service

ComponentContextPtr context = ComponentContext::getCurrent();

ServiceReferencePtr svcRef = context->getServiceReference("myservice");

svcRef->setCallbackID(“1234”);

MyService* service = (MyService*)svcRef->getService();

service->someFunction(arg);

}

MyServiceCallback::receiveResult(unsigned int result)

{

ComponentContextPtr context = ComponentContext::getCurrent();

ServiceReferencePtr serviceRef = context->getSelfReference();

std::string id = serviceRef->getCallbackID();

// code to process result

}

### Implementing Multiple Bidirectional Interfaces

Since it is possible for a single class to implement multiple services, it is also possible for callbacks to be defined for each of the services that it implements. To access the callbacks the ServiceReference::getCallback(serviceName) member function must be used, passing in the name of the service for which the callback is to be obtained.

### Customizing the Callback Identity

The identity that is used to identify a callback request is, by default, generated by the SCA runtime.  However, it is possible to provide an application specified identity to be used to identify the callback by calling the ServiceReference::setCallbackID() member function.  This can be used in either stateful or stateless callbacks.  The identity will be sent to the service provider, and the binding MUST guarantee that the SCA runtime will send the ID back when any callback operation is invoked.

The callback ID has the same restrictions as the conversation ID. It MUST be unique to the client component over all time or it MUST be globally unique if the client is not an SCA component. Bindings determine the particular mechanisms to use for transmission of the identity and these may lead to further restrictions when using a given binding.

# Error Handling

Clients calling service operations will experience business exceptions, and SCA runtime exceptions.

Business exceptions are raised by the implementation of the called service operation. It is expected that these will be caught by client invoking the operation on the service.

SCA runtime exceptions are raised by the SCA runtime and signal problems in the management of the execution of components, and in the interaction with remote services. Currently the following SCA runtime exceptions are defined:

SCAException – defines a root exception type from which all SCA defined exceptions derive.

SCANullPointerException – signals that code attempted to dereference a null pointer from a RefCountingPointer object.

ServiceRuntimeException - signals problems in the management of the execution of SCA components.

ServiceUnavailableException – signals problems in the interaction with remote services.  This extends ServiceRuntimeException.  These are exceptions that may be transient, so retrying is appropriate.  Any exception that is a ServiceRuntimeException that is not a ServiceUnavailableException is unlikely to be resolved by retrying the operation, since it most likely requires human intervention.

MultipleServicesException – signals that a member function expecting identification of a single service is called where there are multiple services defined. Thrown by ComponentContext::getService(), ComponentContext::getSelfReference() and ComponentContext::getServiceReference().

ConversationEndedException – signals that an operation has been called on a conversational service after the conversation was ended.

ConversationStateException – signals an attempt to set the conversationID while a conversation is active. Thrown by ServiceReference::setConversationID().

NoConversationException – signals an attempt to set the conversationID  when the interface associated with the ServiceReference is not conversational. Thrown by ServiceReference::setConversationID().

NoRegisteredCallbackException – signals that a callback was invoked on a service, but a callback member function was not registered.

# C++ API

All the C++ interfaces are found in the namespace oasis::sca, which has been omitted from the following descriptions for clarity.

## Reference Counting Pointers

These are a derived version of the familiar smart-pointer.  The pointer class holds a real (dumb) pointer to the object.  If the reference counting pointer is copied, then a duplicate pointer is returned with the same real pointer.  A reference count within the object is incremented for each copy of the pointer, so only when all pointers go out of scope will the object be freed.

Reference counting pointers in SCA have the same name as the type they are pointing to, with a suffix of Ptr. (E.g. ComponentContextPtr, ServiceReferencePtr).

RefCountingPointer defines member functions with raw pointer like semantics.  This includes defining operators for dereferencing the pointer (*, ->), as well as operators for determining the validity of the pointer.

template <typename T>

class RefCountingPointer {

public:

T& operator* () const;

T* operator-> () const;

operator void* () const;

bool operator! () const;

};

The RefCountingPointer class has the following member functions:

### operator*

A C++ component implementation uses the * operator to dereferences the underlying pointer of a reference counting pointer.  This is equivalent to calling *p where p is the underlying pointer.

| Precondition | C++ component instance is running and has a reference counting pointer |
| --- | --- |
| Return | A reference to the value of the pointer |
| Throws | SCANullPointerException if the pointer is NULL |
| Post Condition | No change |

### operator->

A C++ component implementation uses the -> operator to invoke member functions on the underlying pointer of a reference counting pointer.  This is equivalent to invoking p->func() where func() is a member function defined on the underlying pointer type.

| Precondition | C++ component instance is running and has a reference counting pointer |
| --- | --- |
| Return |  |
| Throws | SCANullPointerException if the pointer is NULL |
| Post Condition | The underlying member functions has been processed. |

### operator void*

A C++ component implementation uses the void* operator to determine if the underlying pointer of a reference counting pointer is set, i.e. if (p) { /* do something */ }.

| Precondition | C++ component instance is running and has a reference counting pointer |
| --- | --- |
| Return | Zero if the underlying pointer is null, otherwise a non-zero value |
| Post Condition | No change |

### operator!

A C++ component implementation uses the ! operator to determine if the underlying pointer of a reference counting pointer is not set, i.e. if (!p) { /* do something */ }.

| Precondition | C++ component instance is running and has a reference counting pointer |
| --- | --- |
| Return | A non-zero value if the underlying pointer is null, otherwise zero |
| Post Condition | No change |

## Component Context

The following shows the ComponentContext interface.

class ComponentContext {

public:

static ComponentContextPtr getCurrent();

virtual std::string getURI() const = 0;

virtual void * getService(const std::string& referenceName) const = 0;

virtual std::list<void*> getServices(

const std::string& referenceName) const = 0;

virtual ServiceReferencePtr getServiceReference(

const std::string& referenceName) const = 0;

virtual std::list<ServiceReferencePtr> getServiceReferences(

const std::string& referenceName) const = 0;

virtual DataObjectPtr getProperties() const = 0;

virtual DataFactoryPtr getDataFactory() const = 0;

virtual ServiceReferencePtr getSelfReference() const = 0;

virtual ServiceReferencePtr getSelfReference(

const std::string& serviceName)const = 0;

};

The ComponentContext C++ interface has the following member functions:

### getCurrent

A C++ component implementation uses ComponentContext::getCurrent() to get a ComponentContext object for itself.

| Precondition | C++ component instance is running |
| --- | --- |
| Input Parameter |  |  |
| Return | ComponentContext for the current component |
| Post Condition | The component instance has a valid context object to use for subsequent runtime calls. |

### getURI

A C++ component implementation uses getURI() to get an absolute URI for itself.

| Precondition | C++ component instance is running and has a ComponentContext |
| --- | --- |
| Input Parameter |  |  |
| Return | Absolute URI for the current component |
| Post Condition | No change |

### getService

A C++ component implementation uses getService() to get an object implementing the interface defined for a Reference.

| Precondition | C++ component instance is running and has a ComponentContext |
| --- | --- |
| Input Parameter | referenceName | Name of the Reference to get an interface object for |
| Return | Pointer to an object implementing the interface of the Reference. This will be NULL if referenceName is not defined for the component. |
| Throws | MultipleServicesException if the reference resolves to more than one service |
| Post Condition | An interface object for the Reference is constructed. This interface object is independent of any ServiceReference that may be obtained for the Reference. |

### getServices

A C++ component implementation uses getServices() to get a list of object implementing the interface defined for a Reference.

| Precondition | C++ component instance is running and has a ComponentContext |
| --- | --- |
| Input Parameter | referenceName | Name of the Reference to get an interface object for |
| Return | List of pointers to objects implementing the interface of the Reference. This list will be empty if referenceName is not defined for the component. Operations must be invoked on each object in the list. |
| Post Condition | Interface objects for the Reference are constructed. These interface objects are independent of any ServiceReferences that may be obtained for the Reference. |

### getServiceReference

A C++ component implementation uses getServiceReference() to get a ServiceReference for a Reference.

| Precondition | C++ component instance is running and has a ComponentContext |
| --- | --- |
| Input Parameter | referenceName | Name of the Reference to get a ServiceReference for |
| Return | ServiceReference for the Reference. This will be NULL if referenceName is not defined for the component. |
| Throws | MultipleServicesException if the reference resolves to more than one service |
| Post Condition | A ServiceReference for the Reference is constructed. |

### getServiceReferences

A C++ component implementation uses getServiceReferences() to get a list of ServiceReference for a Reference.

| Precondition | C++ component instance is running and has a ComponentContext |
| --- | --- |
| Input Parameter | referenceName | Name of the Reference to get a list of ServiceReferences for |
| Return | List of ServiceReferences for the Reference. This will be empty if referenceName is not defined for the component. |
| Post Condition | ServiceReferences for the Reference are constructed. |

### getProperties

A C++ component implementation uses getProperties() to get its configured property values.

| Precondition | C++ component instance is running and has a ComponentContext |
| --- | --- |
| Input Parameter |  |  |
| Return | An SDO [SDO21] from which all the properties defined in the componentType file can be retrieved. |
| Post Condition | An SDO with the property values for the component instance is constructed. |

### getDataFactory

A C++ component implementation uses getDataFactory() to get its an SDO DataFactory which can be used to create DataObjects for complex data types used by this component.

| Precondition | C++ component instance is running and has a ComponentContext |
| --- | --- |
| Input Parameter |  |  |
| Return | An SDO DataFactory which has definitions for all complex data types used by a component. |
| Post Condition | An SDO DataFactory is constructed |

### getSelfReference

A C++ component implementation uses getSelfReference()to get a ServiceReference for use with some conversation and callback APIs.

There are two variations of this API.

| Precondition | C++ component instance is running and has a ComponentContext |
| --- | --- |
| Input Parameter |  |  |
| Return | A ServiceReference for the service provided by this component. |
| Throws | MultipleServicesException if the component implements more than one Service |
| Post Condition | A ServiceReference object is constructed |

and

| Precondition | C++ component instance is running and has a ComponentContext |
| --- | --- |
| Input Parameter | serviceName | Name of the Service to get a ServiceReference for |
| Return | A ServiceReference for the service provided by this component. |
| Post Condition | A ServiceReference object is constructed |

## ServiceReference

The following shows the ServiceReference interface.

class ServiceReference {

public:

virtual void* getService() const = 0;

virtual std::string getConversationID() const = 0;

virtual void  setConversationID(const std::string& id) = 0;

virtual std::string getCallbackID() const = 0;

virtual void  setCallbackID(const std::string& id) = 0;

virtual void* getCallback() const = 0;

virtual void  endConversation() = 0;

};

The ServiceReference interface has the following member functions (the detailed description of the usage of these member functions is described in the sections Conversational Services and Asynchronous Programming):

### getService

A C++ component implementation uses getService() to get an object implementing the interface defined for a ServiceReference.

| Precondition | C++ component instance is running and has a ServiceReference |
| --- | --- |
| Input Parameter |  |  |
| Return | Pointer to an object implementing the interface of the ServiceReference. |
| Post Condition | An interface object for the ServiceReference is constructed. |

### getConversationID

A C++ component implementation uses getConversationID()to retrieve the ID associated with a particular conversation.

| Precondition | C++ component instance is running and has a ServiceReference |
| --- | --- |
| Input Parameter |  |  |
| Return | ID for the conversation. If the ID for the conversation has not been set and no operation has been invoked, the string will be empty. If the interface associated with the ServiceReference is not conversational, the string will also be empty. |
| Post Condition | No change |

### setConversationID

A C++ component implementation uses getSetCallbackID() to define a specific ID for a conversation.

| Precondition | C++ component instance is running and has a ServiceReference |
| --- | --- |
| Input Parameter | id | Conversation ID to be set |
| Return |  |
| Throws | ConversationStateException if there is an active conversation for this ServiceReference. NoConversationException if the interface associated with the ServiceReference is not conversational. |
| Post Condition | A new conversation with the specified id is started. |

### getCallbackID

A C++ component implementation uses getCallbackID() to retrieve the callback ID associated with a particular callback request.

| Precondition | C++ component instance is running and has a ServiceReference |
| --- | --- |
| Input Parameter |  |  |
| Return | ID for the callback request. The string will be empty if called while not processing a callback request. |
| Post Condition | The component can correlate the callback request to a forward invocation. |

### setCallbackID

A C++ component implementation uses getSetCallbackID() to define a specific callback ID for subsequent operation invocation(s).

| Precondition | C++ component instance is running and has a ServiceReference |
| --- | --- |
| Input Parameter | id | Callback ID to be set |
| Return |  |
| Post Condition | The id will be associated with all subsequent operation invocations until replaced. |

### getCallback

A C++ component implementation uses getCallback() to get an object implementing the callback interface defined for a ServiceReference.

| Precondition | C++ component instance is running and has a ServiceReference |
| --- | --- |
| Input Parameter |  |  |
| Return | Pointer to an object implementing the callback interface of the ServiceReference. |
| Throws | NoRegisteredCallbackException if no callback interface is defined. |
| Post Condition | An interface object for the callback interface of the ServiceReference is constructed. |

### endConversation

A C++ component implementation uses endConversation() to explicitly end a conversation.  This can be called by either a service provider or a client.

| Precondition | C++ component instance is running and has a ServiceReference |
| --- | --- |
| Input Parameter |  |  |
| Post Condition | The current conversation is ended |

## SCAException

The following shows the SCAException interface.

class SCAException : public std::exception {

public:

const char* getEClassName() const;

const char* getMessageText() const;

const char* getFileName() const;

unsigned long getLineNumber() const;

const char* getFunctionName() const;

};

The SCAException C++ interface has the following member functions (the details concerning this class and its derived types are described in the section 6):

### getEClassName

A C++ component implementation uses getEClassName() to get the name of the exception type.

| Precondition | C++ component instance is running and has caught an SCA Exception |
| --- | --- |
| Input Parameter |  |  |
| Return | The type of the exception as a string. e.g. “ServiceUnavailableException” |
| Post Condition | No change |

### getMessageText

A C++ component implementation uses getMessageText() to get any message included with the exception.

| Precondition | C++ component instance is running and has caught an SCA Exception |
| --- | --- |
| Input Parameter |  |  |
| Return | The message which the SCA runtime attached to the exception |
| Post Condition | No change |

### getFileName

A C++ component implementation uses getFileName() to get the filename containing the function where the exception occurred.

| Precondition | C++ component instance is running and has caught an SCA Exception |
| --- | --- |
| Input Parameter |  |  |
| Return | The filename within which the exception occurred – Will be an empty string if the filename is not known |
| Post Condition | No change |

### getLineNumber

A C++ component implementation uses getLineNumber() to get the line number in the source file where the exception occurred.

| Precondition | C++ component instance is running and has caught an SCA Exception |
| --- | --- |
| Input Parameter |  |  |
| Return | The line number at which the exception occurred – Will 0 if the line number is not known |
| Post Condition | No change |

### getFunctionName

A C++ component implementation uses getFunctionName() to get the function name where the exception occurred.

| Precondition | C++ component instance is running and has caught an SCA Exception |
| --- | --- |
| Input Parameter |  |  |
| Return | The function name in which the exception occurred – Will be an empty string if the function name is not known |
| Post Condition | No change |

## SCANullPointerException

The following shows the SCANullPointerException interface.

class SCANullPointerException : public SCAException {

};

## ServiceRuntimeException

The following shows the ServiceRuntimeException interface.

class ServiceRuntimeException : public SCAException {

};

## ServiceUnavailableException

The following shows the ServiceUnavailableException interface.

class ServiceUnavailablException : public ServiceRuntimeException {

};

## NoRegisteredCallbackException

The following shows the NoRegisteredCallbackException interface.

class NoRegisteredCallbackException : public ServiceRuntimeException {

};

## ConversationEndedException

The following shows the ConversationEndedException interface.

class ConversationEndedException : public ServiceRuntimeException {

};

## MultipleServicesException

The following shows the MultipleServicesException interface.

class MultipleServicesException : public ServiceRuntimeException {

};

## ConversationStateException

The following shows the ConversationStateException interface.

class ConversationStateException : public ServiceRuntimeException {

};

## NoConversationException

The following shows the NoConversationException interface.

class NoConversationException : public ServiceRuntimeException {

};

# C++ Contributions

Contributions are defined in the Assembly specification [ASSEMBLY]. C++ contributions are typically, but not necessarily contained in .zip files.  In addition to SCDL and potentially WSDL artifacts, C++ contributions include binary executable files, componentType files and potentially C++ interface headers.  No additional discussion is needed for header files, but here are some additional considerations for executable and componentType files discussed in the following sections.

## Executable files

Executable files containing the C++ implementations for a contribution can be contained in the contribution, contained in another contribution or external to any contribution.  In some cases, it could be desirable to have contributions share an executable.  In other cases, an implementation deployment policy might dictate that executables are placed in specific directories in a file system.

### Executable in contribution

When the executable file containing a C++ implementation is in the same contribution, the @path attribute of the implementation.cpp element is used to specify the location of the executable.  The specific location of an executable within a contribution is not defined by this specification.

The following shows a contribution containing a DLL.

META-INF/

sca-contribution.xml

bin/

autoinsurance.dll

AutoInsurance/

AutoInsurance.composite

AutoInsuranceService/

AutoInsurance.h

AutoInsuranceImpl.componentType

include/

Customers.h

Underwriting.h

RateUtils.h

The SCDL for the AutoInsuranceService component is:

<component name="AutoInsuranceService">

<implementation.cpp library="autoinsurance" path="bin/"

class="AutoInsuranceImpl” />

</component>

### Executable shared with other contribution(s) (Export)

If a contribution contains an executable that also implements C++ components found in other contributions, the contribution has to export the executable.  An executable in a contribution is made visible to other contributions by adding an export.cpp element to the contribution definition as shown in the following snippet.

<contribution>

<deployable composite="myNS:RateUtilities"

<export.cpp name="contribNS:rates" >

</contribution>

It is also possible to export only a subtree of a contribution.  If a contribution contains the following:

META-INF/

sca-contribution.xml

bin/

rates.dll

RateUtilities/

RateUtilities.composite

RateUtilitiesService/

RateUtils.h

RateUtilsImpl.componentType

An export of the form:

<contribution>

<deployable composite="myNS:RateUtilities"

<export.cpp name="contribNS:ratesbin" path="bin/" >

</contribution>

only makes the contents of the bin directory visible to other contributions.  By placing all of the executable files of a contribution in a single directory and exporting only that directory, the amount of information contribution that uses the exported executable files is limited.  This is considered a best practice.

### Executable outside of contribution (Import)

When the executable that implements a C++ component is located outside of a contribution, the contribution MUST import the executable.  If the executable is located in another contribution, the import.cpp element of the contribution definition uses a @location attribute that identifies the name of the export as defined in the contribution that defined the export as shown in the following snippet.

<contribution>

<deployable composite="myNS:Underwriting"

<import.cpp name="rates" location="contribNS:rates">

</contribution>

The SCDL for the UnderwritingService component is:

<component name="UnderwritingService">

<implementation.cpp library="rates" path="rates:bin/"

class="UnderwritingImpl” />

</component>

If the executable is located in the file system, the @location attribute identifies the location in the files system used as the root of the import as shown in this snippet.

<contribution>

<deployable composite="myNS:CustomerUtilities"

<import.cpp name="usr-bin" location="/usr/bin/" >

</contribution>

## componentType files

As stated in section 2.5, each component implemented in C++ has a corresponding componentType file.  This componentType file is, by default, located in the root directory of the composite containing the component or a subdirectory of the composite root with the name <implementation class>.componentType, as shown in the following example.

META-INF/

sca-contribution.xml

bin/

autoinsurance.dll

AutoInsurance/

AutoInsurance.composite

AutoInsuranceService/

AutoInsurance.h

AutoInsuranceImpl.componentType

The SCDL for the AutoInsuranceService component is:

<component name="AutoInsuranceService">

<implementation.cpp library="autoinsurance" path="bin/"

class="AutoInsuranceImpl” />

</component>

Since there is a one-to-one correspondence between implementations and componentTypes, when an implementation is shared between contributions, it is desirable to also share the componentType file.  ComponentType files can be exported and imported in the same manner as executable files.  The location of a .componentType file can be specified using the @componentType attribute of the implementation.cpp element.

<component name="UnderwritingService">

<implementation.cpp library="rates" path="rates:bin/"

class="UnderwritingImpl” componentType="rates:types/UnderwritingImpl" />

</component>

## C++ Contribution Extensions

### Export.cpp

The following snippet shows the schema for the C++ export element used to make an executable or componentType file visible outside of a contribution.

<?xml version="1.0" encoding="ASCII"?>

<!—- export.cpp schema snippet -->

<export.cpp xmlns="http://docs.oasis-open.org/ns/opencsa/sca/200712"

name="QName" path="string"? >

The export.cpp element has the following attributes:

name : QName (1..1) – name of the export. The@name attribute of a <export.cpp/> element MUST be unique amongst the <export.cpp/> elements in a domain.  [CPP80001]

path : string (0..1)  – path of the exported executable relative to the root of the contribution.  If not present, the entire contribution is exported.

### Import.cpp

The following snippet shows the schema for the C++ import element used to reference an executable or componentType file that is outside of a contribution.

<?xml version="1.0" encoding="ASCII"?>

<!—- import.cpp schema snippet -->

<import.cpp xmlns="http://docs.oasis-open.org/ns/opencsa/sca/200712"

name="QName" location="string" >

The import.cpp element has the following attributes:

name : QName (1..1) – name of the import. The@name attribute of a <import.cpp/> child element of a <contribution/> MUST be unique amongst the <import.cpp/> elements in of that contribution. [CPP80002]

location : string (1..1)  – either the QName of a export or a file system location.  If the value does not match an export name it is taken as an absolute file system path.

# Types Supported in Service Interfaces

A service interface can support a restricted set of the types available to a C++ programmer. This section summarizes the valid types that can be used.

## Local service

For a local service the types that are supported are:

Any of the C++ primitive types (for example, int, short, char). In this case the types will be passed by value as is normal for C++.

Pointers to any of the C++ primitive types (for example, int *, short *, char *).

The const keyword can be used for any pointer to a C++ primitive type (for example const char *). If this is used on a parameter then the destination may not change the value.

C++ class. The class will be passed by value as is normal for C++.

Pointer to a C++ class. A pointer will be passed to the destination which can then modify the original contents.

DataObjectPtr. An SDO pointer. This will be passed by reference.

References to C++ classes (passed by reference)

## Remotable service

For a remotable service being called by another service the data exchange semantics is by-value. In this case the types that are supported are:

Any of the C++ primitive types (for example, int, short, char). This will be copied.

C++ classes. These will be passed using the copy constructor. The copy constructor must make sure that any embedded references, pointers or objects are copied appropriately.

DataObjectPtr. An SDO pointer. The SDO will be copied and passed to the destination.

Unless the interface is marked as allowing pass by reference semantics, the behavior of the following are not defined:

Pointers.

References.

# Restrictions on C++ header files

A C++ header file that is used to describe an interface has some restrictions.

A C++ header file used to define an interface MUST:

Declare at least one class with:

At least one public member function.

All public member functions must be pure virtual (virtual with no implementation) [CPP100001]

A C++ header file used to define an interface MUST NOT use the following constructs:

Macros

Inline member functions

Friend classes [CPP100002]

# WSDL to C++ and C++ to WSDL Mapping

The SCA Client and Implementation Model for C++ applies the WSDL to Java and Java to WSDL mapping rules (augmented for C++) as defined by the JAX-WS specification [JAXWS21] for generating remotable C++ interfaces from WSDL portTypes and vice versa.  Use of the JAX-WS specification as a guideline for WSDL to C++ and C++ to WSDL mappings should not imply that any support for the Java language is required by this specification.

For the purposes of the Java-to-WSDL mapping algorithm, the interface is treated as if it had a @WebService annotation on the class, even if it doesn't. For the WSDL-to-Java mapping, the generated @WebService annotation implies that the interface is @Remotable.

For the mapping from C++ types to XML schema types SCA supports the SDO 2.1 [SDO21] mapping.  A detailed mapping of C++ to WSDL types and WSDL to C++ types is covered in section 11.3.

The following limitations apply:

- JAX-WS style external binding files are not supported. (See JAX-WS Sec. 2)

- MIME binding is not supported. (See JAX-WS Sec. 2.1.1)

- Holder classes are not supported. (See JAX-WS Sec. 2.3.3)

- Asynchronous mapping is not supported. (See JAX-WS Sec. 2.3.4)

- Generation of Service classes from WSDL is not supported. (See JAX-WS Sec. 2.7)

- Generation of WSDL from Service implementation classes  is not supported (See JAX-WS Sec. 3.3)

- Templates are not supported when converting from C++ to WSDL (See JAX-WS Sec. 3.9)

The following general rules apply to the application of JAX-WS to C++.

- References to Java should be considered references to C++.

- References to Java classes should be considered references to C++ classes.

- References to Java methods should be considered references to C++ member functions.

- References to Java interfaces should be considered references to C++ classes which only define pure virtual member functions.

- For the purposes of the C++-to-WSDL mapping algorithm, a C++ class with only pure-virtual functions and no state is treated as if it had a @WebService annotation on the class.  All default values are assumed for the @WebService annotation.

Major divergences from JAX-WS:

- Algorithms for converting WSDL namespaces to C++ namespaces (and vice-versa).

- Mapping of WSDL faults to C++ exceptions and vice-versa.

- Managing of data bindings.

## Augmentations for WSDL to C++ Mapping

### Mapping WSDL targetNamespace to a C++ namespace

Since C++ does not define a standard convention for the use of namespaces, the SCA specification does not define an implicit mapping of WSDL targetNamespaces to C++ namespaces.  WSDLs MAY define a namespace using the <sca:namespace> WSDL extension (see D.4), otherwise all C++ classes will be placed in a default namespace as determined by the implementation.  Implementations SHOULD provide a mechanism for overriding the default namespace. [CPP110001]

### Mapping WSDL Faults to C++ Exceptions

WSDL operations that specify one or more <wsdl:fault> elements will produce a C++ member function that is annotated with an @WebThrows annotation listing a C++ exception class associated with each <wsdl:fault>.

The C++ exception class associated with a fault will be generated based on the message that is associated with the <wsdl:fault> element, and in particular with the global element that the wsd:fault/wsdl:message/@part indicates.

FaultException(const char* message, const FaultInfo& faultInfo);

FaultInfo getFaultInfo() const;

Where FaultException is the name of the generated exception class, and where FaultInfo is the name of the C++ type representing the fault’s global element type.

#### Multiple Fault References

If multiple operations within the same portType indicate that they throw faults that reference the same global element, a single C++ exception class MUST be created, with each C++ member function referencing this class in its @WebThrows annotation. [CPP110002]

### Mapping of in, out, in/out parts to C++ member function parameters

C++ diverges from the JAX-WS specification in it’s handling of some parameter types, especially around how passing of out and in/out parameters are handled in the context of C++’s various pass-by styles.  The following outlines an updated mapping for use with C++.

- For unwrapped messages:

  - in The message part is mapped to a member function parameter, passed by const-reference.

  - out The message part is mapped to a member function parameter, passed by reference, or to the member function return type, returned by-value.

  - in/out The message part is mapped to a member function parameter, passed by reference. [CPP110003]

- For wrapped messages:

  - in The wrapper child is mapped to a member function parameter, passed by const-reference.

  - out The wrapper child is mapped to a member function parameter, passed by reference, or to the member function return type, returned by-value.

  - in/out The wrapper child is mapped to a member function parameter, passed by reference. [CPP110004]

## Augmentations for C++ to WSDL Mapping

### Mapping C++ namespaces to WSDL namespaces

Since C++ does not define a standard convention for the use of namespaces, the SCA specification does not define an implicit mapping of C++ namespaces to WSDL namespace URIs.  The default targetNamespace is defined by the implementation.  An implementation SHOULD provide a mechanism for overriding the default targetNamespace. [CPP110005]

### Parameter and return type classification

The classification of parameters and return types in C++ are determined based on how the value is passed into the function.

A methods return type is always considered out.  A parameter passed by-reference or by-pointer is considered either in/out or out.  All other parameters, including those passed by-const-reference are considered in. [CPP110006]

### C++ to WSDL Type Conversion

C++ types are mapped to WSDL and schema types based on the mapping described in Section 11.3.1.

### Service-specific Exceptions

C++ classes that define a web service interface MAY indicate which faults they may throw using the @WebThrows annotation. [CPP110007] @WebThrows lists the names of each C++ class that may be thrown as a fault from a particular member function.  Each class that is referenced from an @WebThrows annotation MUST itself have a @WebFault annotation that associates the fault with a particular global element that will be associated with the fault message. [CPP110008]

## SDO Data Binding

### Simple Content Binding

The translation of XSD simple content types to C++ types follows the convention defined in the SDO specification.  The following table summarizes that mapping as it applies to SCA services.

The following mapping is derived from the mappings for SDO types to XSD schema types [SDO 11.1], XSD schema types to SDO types [SDO 10.3.3], and SDO types to C++ types [SDO 9.1].

| XSD Schema Type ( | SDO Type ( | C++ Type | ( XSD Schema Type |
| --- | --- | --- | --- |
| anySimpleType | Object | UNDEFINED |
| anyType | DataObject | commonj::sdo::DataObject | anyType |
| anyURI | URI | std::string | string |
| base64Binary | Bytes | char* | hexBinary |
| Boolean | Boolean | bool | Boolean |
| Byte | Byte | int8_t | Byte |
| Date | YearMonthDay | std::string | string |
| dateTime | DateTime | std::string | string |
| Decimal | Decimal | UNDEFINED |
| Double | Double | long double | double |
| Duration | Duration | std::string | string |
| ENTITIES | Strings | UNDEFINED |
| ENTITY | String | std::string | string |
| Float | Float | float | float |
| gDay | Day | std::string | string |
| gMonth | Month | std::string | stirng |
| gMonthDay | MonthDay | std::string | string |
| gYear | Year | std::string | string |
| gYearMonth | YearMonth | std::string | string |
| hexBinary | Bytes | char* | hexBinary |
| ID | String | std::string | string |
| IDREF | String | std::string | string |
| IDREFS | Strings | UNDEFINED |
| Int | Int | int32_t | int |
| Integer | Integer | UNDEFINED |
| language | String | std::string | string |
| Long | Long | int64_t | long |
| Name | String | std::string | string |
| NCName | String | std::string | string |
| negativeInteger | Integer | UNDEFINED |
| NMTOKEN | String | std::string | string |
| NMTOKENS | Strings | UNDEFINED |
| nonNegativeInteger | Integer | UNDEFINED |
| nonPositiveInteger | Integer | UNDEFINED |
| normalizedString | String | std::string | string |
| NOTATION | String | std::string | string |
| positiveInteger | Integer | UNDEFINED |
| QName | URI | std::string | string |
| short | Short | int16_t | short |
| string | String | std::string | string |
| time | Time | std::string | string |
| Token | String | std::string | string |
| unsignedByte | Short | int16_t | short |
| unsignedInt | Long | int64_t | long |
| unsignedLong | Integer | UNDEFINED |
| unsignedShort | Int | int32_t | int |

### Complex Content Binding

Any XSD complex types are mapped to an instance of an SDO DataObject.

# Conformance

This section specifies the conformance targets of this specification and the requirements that apply to each of them.

## Conformance Targets

The conformance targets of this specification are:

SCA implementations, which provide a runtime for SCA components and potentially tools for authoring SCA artifacts, component descriptions and/or runtime operation .

SCDL documents, which describe SCA artifacts, and specific elements within these documents.

C++ component implementations, which execute under the control of an SCA runtime.

C++ header files, which are used to defind SCA service interfaces.

## Conformance Claims

A claim of conformance with this specification MUST meet the following requirements:

It MUST state which conformance targets it implements.

## SCA Implementations

An implementation conforms to this specification if it meets the following conditions:

It MUST conform to the SCA Assembly Model Specification [ASSEMBLY] and the SCA Policy Framework [POLICY].

It MUST implement the SCA C++ API defined in section C++ API.

It MUST implement the mapping between C++ and WSDL 1.1 [WSDL11] as described in section 11.

It MUST support C++ contributions as defined in C++ Contributions

It MAY support source file annotations as defined in C++ SCA Annotations and C++ SCA Policy Annotations.

## SCDL Documents

A SCDL file conforms to this specification if it meets the following conditions:

- It MUST conform to the SCA Assembly Model Specification [ASSEMBLY] and, if appropriate, the SCA Policy Framework [POLICY].

It conforms to the requirements in section Component Type and Component or section C++ Contributions according to the document type.

## C++ Component Implementations

A C++ component implementation conforms to this specification if it meets the following conditions:

- It conforms to the requirements for a C++ component implementation specified in section Basic Component Implementation Model.

## C++ Header Files

A C++ header files conforms to this specification if it meets the following conditions:

- It confoms to the requirements and restrictions for a C++ header file specified in section Restrictions on C++ header files.

If it contains annotations, the formats and restrictions in section C++ SCA Annotations, C++ SCA Policy Annotations, and C++ WSDL Mapping Annotations are followed.

## WSDL Files

A WSDL conforms to this specification if it meets the following conditions:

- It is a valid WSDL 1.1 [WSDL11] document.

If it contains C++ WSDL extensions, the restrictions in section WSDL C++ Mapping Extensions are followed.

## Extensions

[What extention points do we want to identify?].

C++ SCA Annotations

To allow developers to define SCA related information directly in source files, without having to separately author SCDL files, a set of annotations are defined.  An SCA implementation MAY support source file annotations.  If annotations are supported by an implementation, the annotations defined here MUST be supported and MUST be mapped to SCDL as described.  The SCA runtime MUST only process the SCDL files and not the annotations. [CPPA0001]

The annotations are defined as C++ comments in interface and implementation header files, for example:

// @Scope("stateless")

Application of Annotations to C++ Program Elements

In general an annotation immediately precedes the program element it applies to.  If multiple annotations apply to a program element, all of the annotations SHOULD be in the same comment block. [CPPA0002]

Class

The annotation immediately precedes the class.

Example

// @Scope("composite")

class LoanServiceImpl : public LoanService {

…

};

Member function

The annotation immediately precedes the member function.

Example:

class LoanService

{

public:

// @OneWay

virtual void reportEvent(int eventId) = 0;

…

};

Data Member

The annotation immediately precedes the data member.

Example:

// @Property(name="loanType", type="xsd:int")

long loanType;

Annotations follow normal inheritance rules.  An annotation on a base class or any element of a base class applies to any classes derived from the base class.

Interface Header Annotations

This section lists the annotations that can be used in the header file that defines a service interface.

@Interface

Annotation used to indicate a class defines an interface when multiple classes exist in a header file.  A class with an @WebService annotation specified MUST be treated as if @Interface was defined.

Corresponds to: @class attribute of an interface.cpp element.

Format:

// @Interface

Applies to: Class

Example

Interface header:

// @Interface

class LoanService {

...

};

Service definition:

<service name="LoanService">

<interface.cpp header="LoanService.h" class="LoanService" />

</service>

@Remotable

Annotation on service interface class to indicate that a service is remotable.

Corresponds to: @remotable=”true” attribute of an interface.cpp element.

Format:

// @Remotable

The default is false (not remotable).

Applies to: Class

Example

Interface header:

// @Remotable

class LoanService {

...

};

Service definition:

<service name="LoanService">

<interface.cpp header="LoanService.h" remotable="true" />

</service>

@Callback

Annotation on a service interface class to specify the callback interface.

Corresponds to: @callbackHeader and @callbackClass attributes of an interface.cpp element.

Format:

// @Callback(header="headerName", class="className")

where

headerName : (1..1) –  is the name of the header defining the callback service interface.

className : (0..1) – is the name of the class for the callback interface.

Applies to: Class

Example

Interface header:

// @Callback(header="MyServiceCallback.h", class="MyServiceCallback")

class MyService {

public:

virtual void someFunction( unsigned int arg ) = 0;

};

Service definition:

<service name="MyService">

<interface.cpp header="MyService.h"

callbackHeader="MyServiceCallback.h"

callbackClass="MyServiceCallback"  />

</service>

@OneWay

Annotation on a service interface member function to indicate the member function is one way.  The @OneWay annotation also affects the representation of a service in WSDL, see C.1.3.

Corresponds to: @oneWay=”true” attribute of function element of an interface.cpp element.

Format:

// @OneWay

The default is false (not OneWay).

Applies to: Member function

Example

Interface header:

class LoanService

{

public:

// @OneWay

virtual void reportEvent(int eventId) = 0;

…

};

Service definition:

<service name="LoanService">

<interface.cpp header="LoanService.h">

<function name="reportEvent" oneWay="true" />

</interface.cpp>

</service>

@Conversational

Annotation on a service interface to denote a conversational service contract.

Corresponds to: @requires=”conversational” attribute of a service element.

Format:

// @Conversational

Applies to: Class

Example

Interface header:

//@Conversational

class LoanService

{

…

}

Service definition:

<service name="LoanService" requires="conversational">

<interface.cpp header=”LoanService.h”>

</service>

@EndsConversation

Annotation on a service interface member function to indicate that the conversation will be ended when this member function is called

Corresponds to: @endsConversationy=”true” attribute of function child element of an interface.cpp element.

Format:

// @EndsConversation

The default is false (invoking the function does not end the conversation).

Applies to: Member function

Example

Interface header:

class LoanService

{

public:

// @EndsConversation

virtual void cancelApplication( ) = 0;

…

};

Service definition:

<service name="LoanService">

<interface.cpp header="LoanService.h">

<function name="cancelApplication" endsConversation="true" />

</interface.cpp>

</service>

Implementation Header Annotations

This section lists the annotations that can be used in the header file that defines a service implementation.

@ComponentType

Annotation used to indicate which class implements a componentType when multiple classes exist in an implementation file.

Corresponds to: @class attribute of an implementation.cpp element.

Format:

// @ComponentType

Applies to: Class

Example

Implementation header:

// @ComponentType

class LoanServiceImpl : public LoanService {

...

};

Component definition:

<component name="LoanService">

<implementation.cpp library="loan" class="LoanServiceImpl”

class="LoanServiceImpl" />

</component>

@Scope

Annotation on a service implementation class to indicate the scope of the service.

Corresponds to: @scope attribute of an implementation.cpp element.

Format:

// @Scope("value")

where

value : [ stateless | composite | conversation] (1..1) – specifies the scope of the implementation. The default value is stateless.

Applies to: Class

Example

Implementation header:

// @Scope("composite")

class LoanServiceImpl : public LoanService {

...

};

Component definition:

<component name="LoanService">

<implementation.cpp library="loan" class="LoanServiceImpl"

scope="composite" />

</component>

@EagerInit

Annotation on a service implementation class to indicate the implantation is to be instantiated when its containing component is started.

Corresponds to: @eagerInit=”true” attribute of an implementation.cpp element.

Format:

// @EagerInit

The default is false (the service should be initialized lazily).

Applies to: Class

Example

Implementation header:

// @EagerInit

class LoanServiceImpl : public LoanService {

...

};

Component definition:

<component name="LoanService">

<implementation.cpp library="loan" class="LoanServiceImpl”

eagerInit="true" />

</component>

@AllowsPassByReference

Annotation on service implementation class or member function to indicate that a service or member function allows pass by reference semantics.

Corresponds to: @allowsPassByReference=”true” attribute of an implementation.cpp element or a function child element of an implementation.cpp element.

Format:

// @AllowsPassByReference

The default is false (the service does not allow by reference parameters).

Applies to: Class or Member function

Example

Implementation header:

// @AllowsPassByReference

class LoanService {

...

};

Component definition:

<component name="LoanService">

<implementation.cpp library="loan" class="LoanServiceImpl"

allowsPassByReference="true" />

</component>

@ConversationAttributes

Annotation on a service implementation class to specify attributes of a conversational service.

Corresponds to: @conversationMaxAge, @conversationMaxIdle or @conversationSinglePrincipal attributes of an implementation.cpp element.

Format:

// @ConversationAttributes(maxIdleTime="value", maxAge="value", singlePrincipal="boolValue")

where

maxIdleTime : string (0..1) – specifies the maximum time that can pass between operations within a single conversation. value is a time expressed as an integer followed by a space and then one of the following: "seconds", "minutes", "hours", "days" or "years".

maxAge : string (0..1) – specifies the maximum time that the entire conversation can remain active.  value is a time expressed as an integer followed by a space and then one of the following: "seconds", "minutes", "hours", "days" or "years".

singlePrincipal : boolean (0..1) – specifies if only the principal (the user) that started the conversation has authority to continue the conversation.

Applies to: Class

Example

Implementation header:

// @ConversationAttributes(maxAge="30 days", maxIdleTime="5 minutes",

//               singlePrincipal="false")

class LoanServiceImpl : public LoanService

{

…

};

Component definition:

<component name="LoanService">

<implementation.cpp library="loan" class="LoanServiceImpl"

conversationMaxAge="30 days" conversationMaxIdle="5 minutes"

conversationSinglePrincipal="false" />

</component>

@Property

Annotation on a service implementation class data member to define a property of the service.

Corresponds to: property element of a componentType element.

Format:

// @Property(name="propertyName", type="typeQName"

//                 default="defaultValue", required="true")

where

name : NCName (0..1) - specifies the name of the property. If name is not specified the property name is taken from the name of the following data member.

type : QName (0..1) - specifies the type of the property. If not specified the type of the property is based on the C++ mapping of the type of the following data member to an xsd type as defined in section 11.3.1.  If the data member is an array, then the property is many-valued.

required : boolean (0..1) - specifies whether a value has to be set in the component definition for this property. Default is false

default : <type> (0..1) - specifies a default value and is only needed if required is false,

Applies to: DataMember

Example

Implementation:

// @Property(name="loanType", type="xsd:int")

long loanType;

Component Type definition:

<componentType … >

<service … />

<property name="loanType" type="xsd:int" />

</componentType>

@Reference

Annotation on a service implementation class data member to define a reference of the service.

Corresponds to: reference element of a componentType element.

Format:

// @Reference(name="referenceName", interfaceHeader="LoanService.h",

//                   interfaceClass="LoanService", required="true")

where

name : NCName (0..1) - specifies the name of the reference. If name is not specified the reference name is taken from the name of the following data member.

interfaceHeader : Name (1..1) - specifies the C++ header defining the interface for the reference.

interfaceClass : Name (0..1) - specifies the C++ class defining the interface for the reference. If not specified the class is derived from the type of the annotated data member.

required : boolean (0..1) - specifies whether a value has to be set for this reference. Default is true.

If the annotated data member is a std::list then the implied component type has a reference with a multiplicity of either 0..n or 1..n depending on the value of the @Reference required attribute – 1..n applies if required=true. Otherwise a multiplicity of 0..1 or 1..1 is implied.

Applies to: Data Member

Example

Implementation:

// @Reference(interfaceHeader="LoanService.h" required="true")

LoanService* loanService;

// @Reference(interfaceHeader="LoanService.h" required="false")

std::list<LoanService*> loanServices;

Component Type definition:

<componentType … >

<service … />

<reference name="loanService" multiplicity="1..1">

<interface.cpp header="LoanService.h" class="LoanService" />

</reference>

<reference name="loanServices" multiplicity="0..n">

<interface.cpp header="LoanService.h" class="LoanService" />

</reference>

</componentType>

  - Base Annotation Grammar

<annotation> ::= // @<baseAnnotation>

<baseAnnotation> ::= <name> [(<params>)]

<params> ::= <paramNameValue>[, <paramNameValue>]* |

<paramValue>[, <paramValue>]*

<paramNameValue> ::= <name>=”<value>”

<paramValue> ::= “<value>”

<name> ::= NCName

<value> ::= string

Adjacent string constants are concatenated

NCName is as defined by XML schema [XSD]

Whitespace including newlines between tokens is ignored.

Annotations with parameters may span multiple lines within a comment, and are considered complete when the terminating “)” is reached.

C++ SCA Policy Annotations

SCA provides facilities for the attachment of policy-related metadata to SCA assemblies, which influence how implementations, services and references behave at runtime.  The policy facilities are described in [POLICY].  In particular, the facilities include Intents and Policy Sets, where intents express abstract, high-level policy requirements and policy sets express low-level detailed concrete policies.

Policy metadata can be added to SCA assemblies through the means of declarative statements placed into Composite documents and into Component Type documents.  These annotations are completely independent of implementation code, allowing policy to be applied during the assembly and deployment phases of application development.

However, it can be useful and more natural to attach policy metadata directly to the code of implementations.  This is particularly important where the policies concerned are relied on by the code itself.  An example of this from the Security domain is where the implementation code expects to run under a specific security Role and where any service operations invoked on the implementation must be authorized to ensure that the client has the correct rights to use the operations concerned.  By annotating the code with appropriate policy metadata, the developer can rest assured that this metadata is not lost or forgotten during the assembly and deployment phases.

The SCA C++ policy annotations provide the capability for the developer to attach policy information to C++ implementation code.  The annotations concerned first provide general facilities for attaching SCA Intents and Policy Sets to C++ code.  Secondly, there are further specific annotations that deal with particular policy intents for certain policy domains such as Security.

General Intent Annotations

SCA provides the annotation @Requires for the attachment of any intent to a C++ class, to a C++ interface or to elements within classes and interfaces such as member functions and data members.

The @Requires annotation can attach one or multiple intents in a single statement.

Each intent is expressed as a string.  Intents are XML QNames, which consist of a Namespace URI followed by the name of the Intent. The precise form used is as follows:

"{" + Namespace URI + "}" + intentname

Intents may be qualified, in which case the string consists of the base intent name, followed by a ".", followed by the name of the qualifier.  There may also be multiple levels of qualification.

This representation is quite verbose, so we expect that reusable constants will be defined for the namespace part of this string, as well as for each intent that is used by C++ code.  SCA defines constants for intents such as the following:

// @Define SCA_PREFIX "{http://docs.oasis-open.org/ns/opencsa/sca/200712}"

// @Define CONFIDENTIALITY SCA_PREFIX ## "confidentiality"

// @Define CONFIDENTIALITY_MESSAGE CONFIDENTIALITY ## ".message"

Notice that, by convention, qualified intents include the qualifier as part of the name of the constant, separated by an underscore.  These intent constants are defined in the file that defines an annotation for the intent (annotations for intents, and the formal definition of these constants, are covered in a following section).

Multiple intents (qualified or not) are expressed as separate strings within an array declaration.

Corresponds to: @requires attribute of a service, reference, operation or property element.

Format:

// @Requires("qualifiedIntent" | {"qualifiedIntent" [, "qualifiedIntent"]})

where

qualifiedIntent ::= QName | QName.qualifier | QName.qualifier1.qualifier2

Applies to: Class, Member function, Data Member

Examples

Attaching the intents "confidentiality.message" and "integrity.message".

// @Requires({CONFIDENTIALITY_MESSAGE, INTEGRITY_MESSAGE})

A reference requiring support for confidentiality:

class Foo {

…

// @Requires(CONFIDENTIALITY)

// @Reference(interfaceHeader="SetBar.h")

void setBar(Bar* bar);

…

}

Users may also choose to only use constants for the namespace part of the QName, so that they may add new intents without having to define new constants.  In that case, this definition would instead look like this:

class Foo {

…

// @Requires(SCA_PREFIX "confidentiality ")

// @Reference(interfaceHeader="SetBar.h")

void setBar(Bar* bar);

…

}

Specific Intent Annotations

In addition to the general intent annotation supplied by the @Requires annotation described above, there are C++ annotations that correspond to some specific policy intents.

The general form of these specific intent annotations is an annotation with a name derived from the name of the intent itself.  If the intent is a qualified intent, qualifiers are supplied as an attribute to the annotation in the form of a string or an array of strings.

For example, the SCA confidentiality intent described in General Intent Annotations using the @Requires(CONFIDENTIALITY) intent can also be specified with the specific @Confidentiality intent annotation.  The specific intent annotation for the "integrity" security intent is:

// @Integrity

Corresponds to: @requires=”<Intent>” attribute of a service, reference, operation or property element.

Format:

// @<Intent>[(qualifiers)]

where Intent is an NCName that denotes a particular type of intent.

Intent ::= NCName

qualifiers ::= "qualifier " | {"qualifier" [, "qualifier"] }

qualifier ::= NCName | NCName/qualifier

Applies to: Class, Member function, Data Member – but see specific intents for restrictions

Example

// @Authentication( {“message”, “transport”} )

This annotation attaches the pair of qualified intents: authentication.message and authentication.transport (the sca: namespace is assumed in both of these cases – "http://docs.oasis-open.org/opencsa/ns/sca/200712").

The Assembly Specification [ASSEMBLY] defines the conversational intent. The corresponding annotation is @Conversational, defined in section @Conversational. In addition, the Policy Framework [POLICY] defines a number of intents and qualifiers.  The following sections define the annotations for those intents.

    - Security Interaction

| Intent | Annotation |
| --- | --- |
| authentication | @Authentication |
| confidentiality | @Confidentiality |
| integrity | @Integrity |

These three intents can be qualified with

transport

message

    - Security Implementation

| Intent | Annotation |
| --- | --- |
| runAs | @RunAs(role”role”) |
| Allow | @Allow(roles=”<comma separated list of roles>”) |
| permitAll | @PermitAll |
| denyAll | @DenyAll |

In addition to allow roles to defined, an SCA runtime MAY use the following annotation

@DeclareRoles(<comma separated list of roles>”)

    - Reliable Messaging

| Intent | Annotation |
| --- | --- |
| atLeastOnce | @AtLeastOnce |
| atMostOnce | @AtMostOnce |
| Ordered | @Ordered |
| exactlyOnce | @ExactlyOnce |

    - Transactions

| Intent | Annotation | Qualifiers |
| --- | --- | --- |
| managedTransaction | @ManagedTransaction | Local global |
| transactedOneWay | @TransactedOneWay |  |
| immediateOneWay | @ImmediateOneWay |  |
| propagates Transaction | @PropagatesTransaction |  |
| suspendsTransaction | @SuspendsTransaction |  |

    - Miscellaneous

| Intent | Annotation | Qualifiers |
| --- | --- | --- |
| SOAP | @SOAP | 1_1 1_2 |
| JMS | @JMS |  |

Application of Intent Annotations

Where multiple intent annotations (general or specific) are applied to the same C++ element, they are additive in effect.  An example of multiple policy annotations being used together follows:

// @Authentication
// @Requires({CONFIDENTIALITY_MESSAGE, INTEGRITY_MESSAGE})

In this case, the effective intents are authentication, confidentiality.message and integrity.message.

If an annotation is specified at both the class/interface level and the member function or data member level, then the member function or data member level annotation completely overrides the class level annotation of the same type.

The intent annotation can be applied either to classes or to class member functions when adding annotated policy on SCA services.  Applying an intent to the setter method in a reference injection approach allows intents to be defined at references.

Inheritance and Intent Annotations

The following example shows the inheritance relations of intents on classes, operations, and super classes.

// @Remotable

// @Integrity("transport")

// @Authentication

class HelloService {

public:

// @Integrity

// @Authentication("message")

wchar_t* hello(wchar_t* message) {...}

// @Integrity

// @Authentication("transport")

wchar_t* helloThere() {...}

}

// @Remotable

// @Confidentiality("message")

class HelloChildService : public HelloService {

public:

// @Confidentiality("transport")

wchar_t* hello(wchar_t* message) {...}

// @Authentication

wchar_t* helloWorld(){...}

}

Example 1a.  Usage example of annotated policy and inheritance.

The effective intent annotation on the helloWorld member function is @Integrity(“transport”),  @Authentication, and @Confidentiality(“message”).

The effective intent annotation on the hello member function of the HelloChildService is @Integrity(“transport”), @Authentication, and @Confidentiality(“transport”),

The effective intent annotation on the helloThere member function of the HelloChildService is @Integrity and @Authentication(“transport”), the same as in HelloService class.

The effective intent annotation on the hello member function of the HelloService is @Integrity and @Authentication(“message”)

The listing below contains the equivalent declarative security interaction policy of the HelloService and HelloChildService implementation corresponding to the C++ classes shown in Example 1a.

<?xml version="1.0" encoding="ASCII"?>

<composite xmlns="http://docs.oasis-open.org/ns/opencsa/sca/200712"

name="HelloServiceComposite" >

<service name="HelloService " requires="integrity/transport

authentication">

…

</service>

<service name="HelloChildService" requires="integrity/transport

authentication confidentiality/message">

…

</service>

...

<component name="HelloServiceComponent">*

<implementation.cpp library="HelloService.dll"

class=”HellowServiceImpl”/>

<operation name=”hello” requires=”integrity

authentication/message”/>

<operation name=”helloThere” requires=”integrity

authentication/transport”/>

</component>

<component name="HelloChildServiceComponent">*

<implementation.cpp library="HelloChildService.dll"

class="HelloChilDServiceImpl" />

<operation name="hello" requires="confidentiality/transport"/>

<operation name="helloThere " requires="integrity/transport

authentication"/>

<operation name="helloWorld" requires="authentication"/>

</component>

...

</composite>

Example 1b.  Declaratives intents equivalent to annotated intents in Example 1a.

Relationship of Declarative and Annotated Intents

Annotated intents on a C++ class cannot be overridden by declarative intents either in a composite document which uses the class as an implementation or by statements in a componentType document associated with the class.  This rule follows the general rule for intents that they represent fundamental requirements of an implementation.

An unqualified version of an intent expressed through an annotation in the C function or function declaration may be qualified by a declarative intent in a using composite document.

Policy Set Annotations

The SCA Policy Framework uses Policy Sets to capture detailed low-level concrete policies (for example, a concrete policy is the specific encryption algorithm to use when encrypting messages when using a specific communication protocol to link a reference to a service).

Policy Sets can be applied directly to C++ implementations using the @PolicySets annotation.  The PolicySets annotation either takes the QName of a single policy set as a string or the name of two or more policy sets as an array of strings.

Corresponds to: @policySets attribute of a service, reference, operation or property element.

Format:

// @PolicySets("<policy set QName>" | 
		 { "<policy set QName>" [, "<policy set QName>"] })

As for intents, PolicySet names are QNames – in the form of “{Namespace-URI}localPart”.

Applies to: Class, Member function, Data Member

Example

// @Reference(name="helloService", interfaceHeader="helloService.h",

//            required="true")

// @PolicySets({ MY_NS “WS_Encryption_Policy",

//               MY_NS "WS_Authentication_Policy"})

HelloService* helloService;

…

In this case, the Policy Sets WS_Encryption_Policy and WS_Authentication_Policy are applied, both using the namespace defined for the constant MY_NS.

PolicySets must satisfy intents expressed for the implementation when both are present, according to the rules defined in [POLICY].

Policy Annotation Grammar Additions

<annotation> ::= // @<baseAnnotation> | @<requiresAnnotation> |

@<intentAnnotation> | @<policySetAnnotation>

<requiresAnnotation> ::= Requires(<intents>)

<intents> ::= “<qualifiedIntent>” |

{“<qualifiedIntent>”[, “<qualifiedIntent>”]*})

<qualifiedIntent> ::= <intentName> | <intentName>.<qualifier> |

<intentName>.<qualifier>.qualifier>

<intentName> ::= {aAnyURI}NCName

<intentAnnotation> ::= <intent>[(<qualifiers>)]

<intent> ::= NCName [(param)]

<qualifiers> ::= “<qualifier>” | {“<qualifier>”[, “<qualifier>”]*}

<qualifier> ::= NCName | NCName/<qualifier>

<policySetAnnotation> ::= policySets(<policysets>)

<policySets> ::= “<policySetName>” | {“<policySetName>”[, “<policySetName>”]*}

<policySetName> ::= {aAnyURI}NCName

anyURI is as defined by XML schema [XSD]

Annotation Constants

<annotationConstant> ::= // @Define <identifier> <token string>

<identifier> ::= token

<token string> ::= “string” | “string”[ ## <token string>]

Constants are immediately expanded

C++ WSDL Mapping Annotations

To allow developers to control the mapping of C++ to WSDL, a set of annotations are defined. An SCA implementation MUST treat any instance of a @Interface annotation and without an explicit @WebService annotation as if a @WebService annotation with a name value equal to the name value of the @Interface annotation and no other parameters was specified. [CPPC0001]

Interface Header Annotations

@WebService

Annotation on a C++ class indicating that it represents a web service.  A class annotated with a @Interface annotation and without an explicit @WebService annotation MUST be treated as if an @WebService annotation with no parameters was specified. [CPPC0002]

Corresponds to: javax.jws.WebService annotation in the JAX-WS specification (7.11.1)

Format:

// @WebService(name=<string>, targetNamespace=<string>, serviceName=<string>,

//       portName=<string>)

where:

- name: (0..1) – The name of the web service portType.  The default is the name of the C++ class the annotation is applied to.

- targetNamespace: (0..1) – The target namespace for the web service.  The default namespace is determined by the implementation.

- serviceName: (0..1) – The target name for the associated service.  The default service name is the name of the C++ class suffixed with “Service”.  The name of the associated binding is also determined by the serviceName.  In the case of a SOAP binding, the binding name is the name of the service suffixed with “SoapBinding”.

- portName: (0..1) – The name that should be used for the associated WSDL port for the service.  If not provided, an implementation MUST use the value associated with the name element, suffixed with “Port” (See JAX-WS 3.11). [CPPC0003]

Applies to: Class

Example:

Given an input C++ source file containing:

// @WebService(name=”StockQuote”, targetNamespace=”http://www.example.org/”,

//       serviceName=”StockQuoteService”)

class StockQuoteService {

};

The following WSDL file would be generated:

<definitions xmlns=”http://schemas.xmlsoap.org/wsdl/”

xmlns:soap=”http://schemas.xmlsoap.org/wsdl/soap/”

xmlns:tns=”http://www.example.org/”

xmlns:cpp=”http://docs.oasis-open.org/ns/opencsa/sca-c-cpp/cpp/200901”

targetNamespace=”http://www.example.org/”>

<portType name=”StockQuote”>

<cpp:bindings>

<cpp:class name=”StockQuoteService”/>

</cpp:bindings>

</portType>

<binding name=”StockQuoteServiceSoapBinding”>

<soap:binding style=”document”

transport=”http://schemas.xmlsoap.org/soap/http”/>

</binding>

<service name=”StockQuoteService”>

<port name=”StockQuotePort” binding=”tns:StockQuoteServiceSoapBinding”>

<soap:address location=”REPLACE_WITH_ACTUAL_URL”/>

</port>

</service>

</definitions>

@WebFunction

Annotation on a C++ member function indicating that it represents a web service operation.

Corresponds to: javax.jws.WebMethod annotation in the JAX-WS specification (7.11.2)

Format:

// @WebFunction(operationName=<string>, action=<string>,

//       exclude=<boolean>)

where:

- operationName: (0..1) – The name of the WSDL operation to associate with this function.  The default is the name of the C++ member function the annotation is applied to.

- action: (0..1) – Specifies the value associated with the soap:operation/@soapAction attribute in the resulting code.  The default value is an empty string.

- exclude: (0..1) – A boolean value indicating whether this member function should be included in the web service interface.  The default value is “false”.

Applies to: Member function.

Example:

Given an input C++ source file containing:

// @WebService(name=”StockQuote”, targetNamespace=”http://www.example.org/”

//       serviceName=”StockQuoteService”)

class StockQuoteService {

// @WebFunction(operationName=”GetLastTradePrice”,

//       action=”urn:GetLastTradePrice”)

float getLastTradePrice(const std::string& tickerSymbol);

// @WebFunction(exclude=true)

void setLastTradePrice(const std::string& tickerSymbol, float value);

};

The following WSDL file would be generated:

<definitions xmlns=”http://schemas.xmlsoap.org/wsdl/”

xmlns:soap=”http://schemas.xmlsoap.org/wsdl/soap/”

xmlns:tns=”http://www.example.org/”

xmlns:cpp=”http://docs.oasis-open.org/ns/opencsa/sca-c-cpp/cpp/200901”

targetNamespace=”http://www.example.org/”>

<xs:schema xmlns:xs="http://www.w3.org/2001/XMLSchema"

xmlns:tns="http://www.example.org/"

attributeFormDefault="unqualified"

elementFormDefault="unqualified"

targetNamespace="http://www.example.org/">

<xs:element name="GetLastTradePrice" type="tns:GetLastTradePrice"/>

<xs:element name="GetLastTradePriceResponse"

type="tns:GetLastTradePriceResponse"/>

<xs:complexType name="GetLastTradePrice">

<xs:sequence>

<xs:element name="tickerSymbol" type="xs:string"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="GetLastTradePriceResponse">

<xs:sequence>

<xs:element name="return" type="xs:float"/>

</xs:sequence>

</xs:complexType>

</xs:schema>

< message name="GetLastTradePrice">

<part name="parameters" element="tns:GetLastTradePrice">

</part>

</message>

< message name="GetLastTradePriceResponse">

<part name="parameters" element="tns:GetLastTradePriceResponse">

</part>

</ message>

<portType name=”StockQuote”>

<cpp:bindings>

<cpp:class name=”StockQuoteService”/>

</cpp:bindings>

<operation name="GetLastTradePrice">

<cpp:bindings>

<cpp:memberFunction name=”getLastTradePrice”/>

</cpp:bindings>

<input name="GetLastTradePrice" message="tns:GetLastTradePrice">

</input>

<output name="GetLastTradePriceResponse"

message="tns:GetLastTradePriceResponse">

</output>

</operation>

</portType>

<binding name=”StockQuoteServiceSoapBinding”>

<soap:binding style=”document”

transport=”http://schemas.xmlsoap.org/soap/http”/>

<wsdl:operation name="GetLastTradePrice">

<soap:operation soapAction="urn:GetLastTradePrice" style="document"/>

<wsdl:input name="GetLastTradePrice">

<soap:body use="literal"/>

</wsdl:input>

<wsdl:output name="GetLastTradePriceResponse">

<soap:body use="literal"/>

</wsdl:output>

</wsdl:operation>

</binding>

<service name=”StockQuoteService”>

<port name=”StockQuotePort” binding=”tns:StockQuoteServiceSoapBinding”>

<soap:address location=”REPLACE_WITH_ACTUAL_URL”/>

</port>

</service>

</definitions>

@OneWay

Annotation on a C++ member function indicating that it represents a one-way request.  The @OneWay annotation also affects the service interface, see A.2.4.

Corresponds to: javax.jws.OneWay annotation in the JAX-WS specification (7.11.3)

Format:

// @OneWay

Applies to: Member function.

Example:

Given an input C++ source file containing:

// @WebService(name=”StockQuote”, targetNamespace=”http://www.example.org/”

//       serviceName=”StockQuoteService”)

class StockQuoteService {

// @WebFunction(operationName=”GetLastTradePrice”,

//       action=”urn:GetLastTradePrice”)

// @OneWay

float getLastTradePrice(const std::string& tickerSymbol);

};

The following WSDL file would be generated:

<definitions xmlns=”http://schemas.xmlsoap.org/wsdl/”

xmlns:soap=”http://schemas.xmlsoap.org/wsdl/soap/”

xmlns:tns=”http://www.example.org/”

xmlns:cpp=”http://docs.oasis-open.org/ns/opencsa/sca-c-cpp/cpp/200901”

targetNamespace=”http://www.example.org/”>

<xs:schema xmlns:xs="http://www.w3.org/2001/XMLSchema"

xmlns:tns="http://www.example.org/"

attributeFormDefault="unqualified"

elementFormDefault="unqualified"

targetNamespace="http://www.example.org/">

<xs:element name="GetLastTradePrice" type="tns:GetLastTradePrice"/>

<xs:complexType name="GetLastTradePrice">

<xs:sequence>

<xs:element name="tickerSymbol" type="xs:string"/>

</xs:sequence>

</xs:complexType>

</xs:schema>

< message name="GetLastTradePrice">

<part name="parameters" element="tns:GetLastTradePrice">

</part>

</message>

<portType name=”StockQuote”>

<cpp:bindings>

<cpp:class name=”StockQuoteService”/>

</cpp:bindings>

<operation name="GetLastTradePrice">

<cpp:bindings>

<cpp:memberFunction name=”getLastTradePrice”/>

</cpp:bindings>

<input name="GetLastTradePrice" message="tns:GetLastTradePrice">

</input>

</operation>

</portType>

<binding name=”StockQuoteServiceSoapBinding”>

<soap:binding style=”document”

transport=”http://schemas.xmlsoap.org/soap/http”/>

<wsdl:operation name="GetLastTradePrice">

<soap:operation soapAction="urn:GetLastTradePrice" style="document"/>

<wsdl:input name="GetLastTradePrice">

<soap:body use="literal"/>

</wsdl:input>

</wsdl:operation>

</binding>

<service name=”StockQuoteService”>

<port name=”StockQuotePort” binding=”tns:StockQuoteServiceSoapBinding”>

<soap:address location=”REPLACE_WITH_ACTUAL_URL”/>

</port>

</service>

</definitions>

@WebParam

Annotation on a C++ member function parameter indicatingit’s mapping to the associated input and output WSDL messages.

Corresponds to: javax.jws.WebParam annotation in the JAX-WS specification (7.11.4)

Format:

// @WebParam(paramName=<string>, name=<string>, targetNamespace=<string>,

//       mode=IN|OUT|INOUT, header=<boolean>, partName=<string>,

//       type=<string>)

where:

- paramName: (1..1) – The name of the parameter that this annotation applies to.  Unnamed parameters CANNOT be referenced by an @WebParam annotation. [CPPC0004]

- name: (0..1) – The name of the associated WSDL part or element.  The default value is the name of the parameter.  If an @WebParam annotation is not present, and the parameter is unnamed, then a name of “argN”, where N is an incrementing value from 1 indicating the position of he parameter in the argument list, will be used.

- targetNamespace: (0..1) – The target namespace for the part.  The default namespace is the namespace of the associated @WebService.  The targetNamespace attribute is ignored unless the binding style is document, and the binding parameterStyle is bare.  (See @SOAPBinding).

- mode: (0..1) – Indicates whether the parameter is associated with the input message, output message, or both.  The default value is determined by the passing mechanism for the parameter, see 11.2.2.

- header: (0..1) – A boolean indicating whether this parameter is associated with a SOAP header element.  The default value is false.

- partName: (0..1) – The name of the WSDL part associated with this item.  The default value is the value of name.

- type : (0..1) – specifies the XML Schema type of the WSDL part or element associated with this parameter. The The value of the type property of a @WebParam annotation MUST be one of the simpleTypes defined in namespace http://www.w3.org/2001/XMLSchema. [CPPC0005] The default type is determined by the mapping defined in 11.3.1.

Applies to: Member function parameter.

Example:

Given an input C++ source file containing:

// @WebService(name=”StockQuote”, targetNamespace=”http://www.example.org/”

//       serviceName=”StockQuoteService”)

class StockQuoteService {

// @WebFunction(operationName=”GetLastTradePrice”,

//       action=”urn:GetLastTradePrice”)

// @WebParam(paramName=”tickerSymbol”, name=”symbol”)

float getLastTradePrice(const std::string& tickerSymbol);

};

The following WSDL file would be generated:

<definitions xmlns=”http://schemas.xmlsoap.org/wsdl/”

xmlns:soap=”http://schemas.xmlsoap.org/wsdl/soap/”

xmlns:tns=”http://www.example.org/”

xmlns:cpp=”http://docs.oasis-open.org/ns/opencsa/sca-c-cpp/cpp/200901”

targetNamespace=”http://www.example.org/”>

<xs:schema xmlns:xs="http://www.w3.org/2001/XMLSchema"

xmlns:tns="http://www.example.org/"

attributeFormDefault="unqualified"

elementFormDefault="unqualified"

targetNamespace="http://www.example.org/">

<xs:element name="GetLastTradePrice" type="tns:GetLastTradePrice"/>

<xs:element name="GetLastTradePriceResponse"

type="tns:GetLastTradePriceResponse"/>

<xs:complexType name="GetLastTradePrice">

<xs:sequence>

<xs:element name="symbol" type="xs:string"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="GetLastTradePriceResponse">

<xs:sequence>

<xs:element name="return" type="xs:float"/>

</xs:sequence>

</xs:complexType>

</xs:schema>

< message name="GetLastTradePrice">

<part name="parameters" element="tns:GetLastTradePrice">

</part>

</message>

< message name="GetLastTradePriceResponse">

<part name="parameters" element="tns:GetLastTradePriceResponse">

</part>

</ message>

<portType name=”StockQuote”>

<cpp:bindings>

<cpp:class name=”StockQuoteService”/>

</cpp:bindings>

<operation name="GetLastTradePrice">

<cpp:bindings>

<cpp:memberFunction name=”getLastTradePrice”/>

<cpp:parameter name=”tickerSymbol”

part=”tns:GetLastTradePrice/parameter”

childElementName=”symbol”/>

</cpp:bindings>

<input name="GetLastTradePrice" message="tns:GetLastTradePrice">

</input>

<output name="GetLastTradePriceResponse"

message="tns:GetLastTradePriceResponse">

</output>

</operation>

</portType>

<binding name=”StockQuoteServiceSoapBinding”>

<soap:binding style=”document”

transport=”http://schemas.xmlsoap.org/soap/http”/>

<wsdl:operation name="GetLastTradePrice">

<soap:operation soapAction="urn:GetLastTradePrice" style="document"/>

<wsdl:input name="GetLastTradePrice">

<soap:body use="literal"/>

</wsdl:input>

<wsdl:output name="GetLastTradePriceResponse">

<soap:body use="literal"/>

</wsdl:output>

</wsdl:operation>

</binding>

<service name=”StockQuoteService”>

<port name=”StockQuotePort” binding=”tns:StockQuoteServiceSoapBinding”>

<soap:address location=”REPLACE_WITH_ACTUAL_URL”/>

</port>

</service>

</definitions>

@WebResult

Annotation on a C++ member function parameter indicating it’s mapping to the associated output WSDL messages.

Corresponds to: javax.jws.WebResult annotation in the JAX-WS specification (7.11.5)

Format:

// @WebResult(name=<string>, targetNamespace=<string>, header=<boolean>,

//     partName=<string>, type=<string>)

where:

- name: (0..1) – The name of the associated WSDL part or element.  The default value is “return”.

- targetNamespace: (0..1) – The target namespace for the part.  The default namespace is the namespace of the associated @WebService.  The targetNamespace attribute is ignored unless the binding style is document, and the binding parameterStyle is bare.  (See @SOAPBinding).

- header: (0..1) – A boolean indicating whether the result is associated with a SOAP header element.  The default value is false.

- partName: (0..1) – The name of the WSDL part associated with this item.  The default value is the value of name.

- type : (0..1) – specifies the XML Schema type of the WSDL part or element associated with this parameter.  The value of the type property of a @WebParam annotation MUST be one of the simpleTypes defined in namespace http://www.w3.org/2001/XMLSchema. [CPPC0006] The default type is determined by the mapping defined in 11.3.1.

Applies to: Member function return value.

Example:

Given an input C++ source file containing:

// @WebService(name=”StockQuote”, targetNamespace=”http://www.example.org/”

//       serviceName=”StockQuoteService”)

class StockQuoteService {

// @WebFunction(operationName=”GetLastTradePrice”,

//       action=”urn:GetLastTradePrice”)

// @WebResult(name=”price”)

float getLastTradePrice(const std::string& tickerSymbol);

};

The following WSDL file would be generated:

<definitions xmlns=”http://schemas.xmlsoap.org/wsdl/”

xmlns:soap=”http://schemas.xmlsoap.org/wsdl/soap/”

xmlns:tns=”http://www.example.org/”

xmlns:cpp=”http://docs.oasis-open.org/ns/opencsa/sca-c-cpp/cpp/200901”

targetNamespace=”http://www.example.org/”>

<xs:schema xmlns:xs="http://www.w3.org/2001/XMLSchema"

xmlns:tns="http://www.example.org/"

attributeFormDefault="unqualified"

elementFormDefault="unqualified"

targetNamespace="http://www.example.org/">

<xs:element name="GetLastTradePrice" type="tns:GetLastTradePrice"/>

<xs:element name="GetLastTradePriceResponse"

type="tns:GetLastTradePriceResponse"/>

<xs:complexType name="GetLastTradePrice">

<xs:sequence>

<xs:element name="tickerSymbol" type="xs:string"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="GetLastTradePriceResponse">

<xs:sequence>

<xs:element name="price" type="xs:float"/>

</xs:sequence>

</xs:complexType>

</xs:schema>

< message name="GetLastTradePrice">

<part name="parameters" element="tns:GetLastTradePrice">

</part>

</message>

< message name="GetLastTradePriceResponse">

<part name="parameters" element="tns:GetLastTradePriceResponse">

</part>

</ message>

<portType name=”StockQuote”>

<cpp:bindings>

<cpp:class name=”StockQuoteService”/>

</cpp:bindings>

<operation name="GetLastTradePrice">

<cpp:bindings>

<cpp:memberFunction name=”getLastTradePrice”/>

</cpp:bindings>

<input name="GetLastTradePrice" message="tns:GetLastTradePrice">

</input>

<output name="GetLastTradePriceResponse"

message="tns:GetLastTradePriceResponse">

</output>

</operation>

</portType>

<binding name=”StockQuoteServiceSoapBinding”>

<soap:binding style=”document”

transport=”http://schemas.xmlsoap.org/soap/http”/>

<wsdl:operation name="GetLastTradePrice">

<soap:operation soapAction="urn:GetLastTradePrice" style="document"/>

<wsdl:input name="GetLastTradePrice">

<soap:body use="literal"/>

</wsdl:input>

<wsdl:output name="GetLastTradePriceResponse">

<soap:body use="literal"/>

</wsdl:output>

</wsdl:operation>

</binding>

<service name=”StockQuoteService”>

<port name=”StockQuotePort” binding=”tns:StockQuoteServiceSoapBinding”>

<soap:address location=”REPLACE_WITH_ACTUAL_URL”/>

</port>

</service>

</definitions>

@SOAPBinding

Annotation on a C++ member function indicating that it represents a web service operation.

Corresponds to: javax.jws.SOAPBinding annotation in the JAX-WS specification (7.11.6)

Format:

// @SOAPBinding(style=DOCUMENT|RPC, use=LITERAL|ENCODED, parameterStyle=BARE|WRAPPED)

where:

- style: (0..1) – The WSDL binding style.  The default value is DOCUMENT.

- use: (0..1) – The WSDL binding use.  The default value is LITERAL.

- parameterStyle: (0..1) – The WSDL parameter style.  The default value is WRAPPED..

Applies to: Class, Member function.

Example:

Given an input C++ source file containing:

// @WebService(name=”StockQuote”, targetNamespace=”http://www.example.org/”,

//       serviceName=”StockQuoteService”)

// @SOAPBinding(style=RPC)

class StockQuoteService {

};

The following WSDL file would be generated:

<definitions xmlns=”http://schemas.xmlsoap.org/wsdl/”

xmlns:soap=”http://schemas.xmlsoap.org/wsdl/soap/”

xmlns:tns=”http://www.example.org/”

xmlns:cpp=”http://docs.oasis-open.org/ns/opencsa/sca-c-cpp/cpp/200901”

targetNamespace=”http://www.example.org/”>

<portType name=”StockQuote”>

<cpp:bindings>

<cpp:class name=”StockQuoteService”/>

</cpp:bindings>

</portType>

<binding name=”StockQuoteServiceSoapBinding”>

<soap:binding style=”rpc”

transport=”http://schemas.xmlsoap.org/soap/http”/>

</binding>

<service name=”StockQuoteService”>

<port name=”StockQuotePort” binding=”tns:StockQuoteServiceSoapBinding”>

<soap:address location=”REPLACE_WITH_ACTUAL_URL”/>

</port>

</service>

</definitions>

@WebFault

Annotation on a C++ exception class indicating that it may be thrown as a fault by a web service function.  The C++ class MUST provide a constructor that takes two parameters, a std::string and a type representing the fault information.  Additionally, the class MUST provide a const member function “getFaultInfo” that takes no parameters, and returns the same type as defined in the constructor. [CPPC0007]

Corresponds to: javax.xml.ws.WebFault annotation in the JAX-WS specification (7.2)

Format:

// @WebFault(name=<string>, targetNamespace=<string>)

where:

- name: (1..1) – The local name of the global element mapped to this fault.

- targetNamespace: (0..1) – The namespace of the global element mapped to this fault.  The default namespace is determined by the implementation.

Applies to: Class.

Example:

Given an input C++ source file containing:

// @WebFault(name=”UnknownSymbolFault”,

//     targetNamespace=”http://www.example.org/”)

class UnknownSymbol {

UnknownSymbol(const char* message,

const std::string& faultInfo);

std:string getFaultInfo() const;

};

// @WebService(name=”StockQuote”, targetNamespace=”http://www.example.org/”

//       serviceName=”StockQuoteService”)

class StockQuoteService {

// @WebFunction(operationName=”GetLastTradePrice”,

//       action=”urn:GetLastTradePrice”)

// @WebThrows(faults=”UnknownSymbol”)

float getLastTradePrice(const std::string& tickerSymbol);

};

The following WSDL file would be generated:

<definitions xmlns=”http://schemas.xmlsoap.org/wsdl/”

xmlns:soap=”http://schemas.xmlsoap.org/wsdl/soap/”

xmlns:tns=”http://www.example.org/”

xmlns:cpp=”http://docs.oasis-open.org/ns/opencsa/sca-c-cpp/cpp/200901”

targetNamespace=”http://www.example.org/”>

<xs:schema xmlns:xs="http://www.w3.org/2001/XMLSchema"

xmlns:tns="http://www.example.org/"

attributeFormDefault="unqualified"

elementFormDefault="unqualified"

targetNamespace="http://www.example.org/">

<xs:element name="GetLastTradePrice" type="tns:GetLastTradePrice"/>

<xs:element name="GetLastTradePriceResponse"

type="tns:GetLastTradePriceResponse"/>

<xs:complexType name="GetLastTradePrice">

<xs:sequence>

<xs:element name="tickerSymbol" type="xs:string"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="GetLastTradePriceResponse">

<xs:sequence>

<xs:element name="return" type="xs:float"/>

</xs:sequence>

</xs:complexType>

<xs:element name=”UnknownSymbolFault” type=”xs:string”/>

</xs:schema>

<message name="GetLastTradePrice">

<part name="parameters" element="tns:GetLastTradePrice">

</part>

</message>

<message name="GetLastTradePriceResponse">

<part name="parameters" element="tns:GetLastTradePriceResponse">

</part>

</message>

<message name=”UnknownSymbol”>

<part name=”parameters” element=”tns:UnknownSymbolFault”>

</part>

</message>

<portType name=”StockQuote”>

<cpp:bindings>

<cpp:class name=”StockQuoteService”/>

</cpp:bindings>

<operation name="GetLastTradePrice">

<cpp:bindings>

<cpp:memberFunction name=”getLastTradePrice”/>

</cpp:bindings>

<input name="GetLastTradePrice" message="tns:GetLastTradePrice">

</input>

<output name="GetLastTradePriceResponse"

message="tns:GetLastTradePriceResponse">

</output>

<fault name=”UnknownSymbol” message=”tns:UnknownSymbol”>

</fault>

</operation>

</portType>

<binding name=”StockQuoteServiceSoapBinding”>

<soap:binding style=”document”

transport=”http://schemas.xmlsoap.org/soap/http”/>

<wsdl:operation name="GetLastTradePrice">

<soap:operation soapAction="urn:GetLastTradePrice" style="document"/>

<wsdl:input name="GetLastTradePrice">

<soap:body use="literal"/>

</wsdl:input>

<wsdl:output name="GetLastTradePriceResponse">

<soap:body use="literal"/>

</wsdl:output>

<wsdl:fault>

<soap:fault name=”UnknownSymbol” use=”literal”/>

</wsdl:fault>

</wsdl:operation>

</binding>

<service name=”StockQuoteService”>

<port name=”StockQuotePort” binding=”tns:StockQuoteServiceSoapBinding”>

<soap:address location=”REPLACE_WITH_ACTUAL_URL”/>

</port>

</service>

</definitions>

@WebThrows

Annotation on a C++ class indicating which faults may be thrown by this class.

Corresponds to: No equivalent in JAX-WS.

Format:

// @WebThrows(faults=<string>[, <string>]*)

where:

- faults: (1..n) – The names of all faults that may be thrown by this member function.  The name of the fault is the name of its associated C++ class name.  A C++ class that is listed in a @WebThrows annotation MUST itself have a @WebFault annotation. [CPPC0008]

Applies to: Member function.

Example:

See @WebFault.

WSDL C++ Mapping Extensions

The following WSDL extensions are used to augment the conversion process from WSDL to C++.  All of these extensions are defined in the namespace http://docs.oasis-open.org/ns/opencsa/sca-c-cpp/cpp/200901.  For brevity, all definitions of these extensions will be fully qualified, and all references to the “cpp” prefix are associated with the namespace above. An SCA implementation MAY support these WSDL extensions. If these extensions are supported by an implementation, all the extensions defined here MUST be supported and MUST be mapped to C++ as described. [CPPD0001]

<cpp:bindings>

<cpp:bindings> is a container type which may be used as a WSDL extension.  All other SCA wsdl extensions will be specified as children of a <cpp:bindings> element.  A <cpp:bindings> element may be used as an extension to any WSDL type that accepts extensions.

<cpp:class>

<cpp:class> provides a mechanism for defining an alternate C++ class name for a WSDL construct.

Format:

<cpp:class name=”xsd:string”/>

where:

- class/@name - The name of the C++ class associated with this WSDL element.

Applicable WSDL element(s):

- wsdl:portType

- wsdl:fault

A <cpp:bindings/> element MUST NOT have more than one <cpp:class/> child element. [CPPD0002]

Example:

Given a WSDL file file containing:

<definitions xmlns=”http://schemas.xmlsoap.org/wsdl/”

xmlns:soap=”http://schemas.xmlsoap.org/wsdl/soap/”

xmlns:tns=”http://www.example.org/”

xmlns:cpp=”http://docs.oasis-open.org/ns/opencsa/sca-c-cpp/cpp/200901”

targetNamespace=”http://www.example.org/”>

<portType name=”StockQuote”>

<cpp:bindings>

<cpp:class name=”StockQuoteService”/>

</cpp:bindings>

</portType>

</definitions>

The following C++ file would be generated:

// @WebService(name=”StockQuote”, targetNamespace=”http://www.example.org/”,

//       serviceName=”StockQuoteService”)

class StockQuoteService {

};

<cpp:enableWrapperStyle>

<cpp:enableWrapperStyle> indicates whether or not the wrapper style for messages should be applied, when otherwise applicable.  If false, the wrapper style will never be applied.

Format:

<cpp:enableWrapperStyle>boolean</cpp:enableWrapperStyle>

where:

- enableWrapperStyle/text() – A boolean value indicating whether wrapper style should be enabled or disabled for this element and any of it’s children.  The default value is “true”.

Applicable WSDL element(s):

- wsdl:definitions

- wsdl:portType – overrides a binding applied to wsdl:definitions

- wsdl:portType/wsdl:operation – overrides a binding applied to wsdl:definitions or the enclosing wsdl:portType

<cpp:bindings/> element MUST NOT have more than one <cpp:enableWrapperStyle/> child element. [CPPD0003]

Example:

Given a WSDL file file containing:

<definitions xmlns="http://schemas.xmlsoap.org/wsdl/"

xmlns:soap="http://schemas.xmlsoap.org/wsdl/soap/"

xmlns:tns="http://www.example.org/"

xmlns:cpp="http://docs.oasis-open.org/ns/opencsa/sca-c-cpp/cpp/200901"

targetNamespace="http://www.example.org/">

<xs:schema xmlns:xs="http://www.w3.org/2001/XMLSchema"

xmlns:tns="http://www.example.org/"

attributeFormDefault="unqualified"

elementFormDefault="unqualified"

targetNamespace="http://www.example.org/">

<xs:element name="GetLastTradePrice" type="tns:GetLastTradePrice"/>

<xs:element name="GetLastTradePriceResponse"

type="tns:GetLastTradePriceResponse"/>

<xs:complexType name="GetLastTradePrice">

<xs:sequence>

<xs:element name="tickerSymbol" type="xs:string"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="GetLastTradePriceResponse">

<xs:sequence>

<xs:element name="return" type="xs:float"/>

</xs:sequence>

</xs:complexType>

</xs:schema>

< message name="GetLastTradePrice">

<part name="parameters" element="tns:GetLastTradePrice">

</part>

</message>

< message name="GetLastTradePriceResponse">

<part name="parameters" element="tns:GetLastTradePriceResponse">

</part>

</ message>

<portType name="StockQuote">

<cpp:bindings>

<cpp:class name=”StockQuoteService”/>

<cpp:enableWrapperStyle>false</cpp:enableWrapperStyle>

<cpp:bindings>

<operation name="GetLastTradePrice">

<cpp:bindings>

<cpp:memberFunction name=”getLastTradePrice”/>

</cpp:bindings>

<input name="GetLastTradePrice" message="tns:GetLastTradePrice">

</input>

<output name="GetLastTradePriceResponse"

message="tns:GetLastTradePriceResponse">

</output>

</operation>

</portType>

</definitions>

The following C++ file would be generated:

// @WebService(name="StockQuote", targetNamespace="http://www.example.org/"

//       serviceName="StockQuoteService")

class StockQuoteService {

// @WebFunction(operationName="GetLastTradePrice",

//       action="urn:GetLastTradePrice")

commonj::sdo::DataObjectPtr

getLastTradePrice(commonj::sdo::DataObjectPtr parameters);

};

<cpp:namespace>

<cpp:namespace> specifies the name of the C++ namespace that the associated WSDL element (and any of it’s children) should be created in.

Format:

<cpp:namespace name=”xsd:string”/>

where:

- namespace/@name - The name of the C++ namespace associated with this WSDL element.

Applicable WSDL element(s):

- wsdl:definitions

A <cpp:bindings/> element MUST NOT have more than one <cpp:namespace/> child element. [CPPD0004]

Example:

Given a WSDL file file containing:

<definitions xmlns=”http://schemas.xmlsoap.org/wsdl/”

xmlns:soap=”http://schemas.xmlsoap.org/wsdl/soap/”

xmlns:tns=”http://www.example.org/”

xmlns:cpp=”http://docs.oasis-open.org/ns/opencsa/sca-c-cpp/cpp/200901”

targetNamespace=”http://www.example.org/”>

<cpp:bindings>

<cpp:namespace name=”stock”/>

</cpp:bindings>

<portType name=”StockQuote”>

<cpp:bindings>

<cpp:class name=”StockQuoteService”/>

</cpp:bindings>

</portType>

</definitions>

The following C++ file would be generated:

namespace stock

{

// @WebService(name=”StockQuote”,

//       targetNamespace=”http://www.example.org/”,

//       serviceName=”StockQuoteService”)

class StockQuoteService {

};

}

<cpp:memberFunction>

<cpp:memberFunction> specifies the name of the C++ member function that the associated WSDL operation should be associated with.

Format:

<cpp:memberFunction name=”xsd:string”/>

where:

- memberFunction/@name - The name of the C++ member function associated with this WSDL operation.

Applicable WSDL element(s):

- wsdl:portType/wsdl:operation

A <cpp:bindings/> element MUST NOT have more than one <cpp:memberFunction/> child element. [CPPD0005]

Example:

Given a WSDL file file containing:

<definitions xmlns="http://schemas.xmlsoap.org/wsdl/"

xmlns:soap="http://schemas.xmlsoap.org/wsdl/soap/"

xmlns:tns="http://www.example.org/"

xmlns:cpp="http://docs.oasis-open.org/ns/opencsa/sca-c-cpp/cpp/200901"

targetNamespace="http://www.example.org/">

<xs:schema xmlns:xs="http://www.w3.org/2001/XMLSchema"

xmlns:tns="http://www.example.org/"

attributeFormDefault="unqualified"

elementFormDefault="unqualified"

targetNamespace="http://www.example.org/">

<xs:element name="GetLastTradePrice" type="tns:GetLastTradePrice"/>

<xs:element name="GetLastTradePriceResponse"

type="tns:GetLastTradePriceResponse"/>

<xs:complexType name="GetLastTradePrice">

<xs:sequence>

<xs:element name="tickerSymbol" type="xs:string"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="GetLastTradePriceResponse">

<xs:sequence>

<xs:element name="return" type="xs:float"/>

</xs:sequence>

</xs:complexType>

</xs:schema>

< message name="GetLastTradePrice">

<part name="parameters" element="tns:GetLastTradePrice">

</part>

</message>

< message name="GetLastTradePriceResponse">

<part name="parameters" element="tns:GetLastTradePriceResponse">

</part>

</ message>

<portType name="StockQuote">

<cpp:bindings>

<cpp:class name=”StockQuoteService”/>

</cpp:bindings>

<operation name="GetLastTradePrice">

<cpp:bindings>

<cpp:memberFunction name=”getTradePrice”/>

</cpp:bindings>

<input name="GetLastTradePrice" message="tns:GetLastTradePrice">

</input>

<output name="GetLastTradePriceResponse"

message="tns:GetLastTradePriceResponse">

</output>

</operation>

</portType>

</definitions>

The following C++ file would be generated:

// @WebService(name="StockQuote", targetNamespace="http://www.example.org/"

//       serviceName="StockQuoteService")

class StockQuoteService {

// @WebFunction(operationName=”GetLastTradePrice”,

//       action=”urn:GetLastTradePrice”)

float getTradePrice(const std::string& tickerSymbol);

};

<cpp:parameter>

<cpp:parameter> specifies the name of the C++ member function parameter associated with a specifc WSDL message part or wrapper child element.

Format:

<cpp:parameter name=”xsd:string” part=”xsd:string”

childElementName=”xsd:string” type="xsd:string"/>

where:

- parameter/@name - The name of the C++ member function parameter associated with this WSDL operation.

- parameter/@part - An XPath expression identifying the wsdl:part of a wsdl:message.

- parameter/@childElementName – The qualified name of a child element of the global element identified by parameter/@part.

- parameter/@type – Specifies the type of the parameter or struct member or return type.  The @type attribute of a <parameter/> element MUST be a valid C++ type. [CPPD0006] The default type is determined by the mapping defined in 11.3.1.

Applicable WSDL element(s):

- wsdl:portType/wsdl:operation

Example:

Given a WSDL file file containing:

<definitions xmlns=”http://schemas.xmlsoap.org/wsdl/”

xmlns:soap=”http://schemas.xmlsoap.org/wsdl/soap/”

xmlns:tns=”http://www.example.org/”

xmlns:cpp=”http://docs.oasis-open.org/ns/opencsa/sca-c-cpp/cpp/200901”

targetNamespace=”http://www.example.org/”>

<xs:schema xmlns:xs="http://www.w3.org/2001/XMLSchema"

xmlns:tns="http://www.example.org/"

attributeFormDefault="unqualified"

elementFormDefault="unqualified"

targetNamespace="http://www.example.org/">

<xs:element name="GetLastTradePrice" type="tns:GetLastTradePrice"/>

<xs:element name="GetLastTradePriceResponse"

type="tns:GetLastTradePriceResponse"/>

<xs:complexType name="GetLastTradePrice">

<xs:sequence>

<xs:element name="symbol" type="xs:string"/>

</xs:sequence>

</xs:complexType>

<xs:complexType name="GetLastTradePriceResponse">

<xs:sequence>

<xs:element name="return" type="xs:float"/>

</xs:sequence>

</xs:complexType>

</xs:schema>

< message name="GetLastTradePrice">

<part name="parameters" element="tns:GetLastTradePrice">

</part>

</message>

< message name="GetLastTradePriceResponse">

<part name="parameters" element="tns:GetLastTradePriceResponse">

</part>

</ message>

<portType name=”StockQuote”>

<cpp:bindings>

<cpp:class name=”StockQuoteService”/>

</cpp:bindings>

<operation name="GetLastTradePrice">

<cpp:bindings>

<cpp:memberFunction name=”getLastTradePrice”/>

<cpp:parameter name=”tickerSymbol”

part=”tns:GetLastTradePrice/parameter”

childElementName=”symbol”/>

</cpp:bindings>

<input name="GetLastTradePrice" message="tns:GetLastTradePrice">

</input>

<output name="GetLastTradePriceResponse"

message="tns:GetLastTradePriceResponse">

</output>

</operation>

</portType>

<binding name=”StockQuoteServiceSoapBinding”>

<soap:binding style=”document”

transport=”http://schemas.xmlsoap.org/soap/http”/>

<wsdl:operation name="GetLastTradePrice">

<soap:operation soapAction="urn:GetLastTradePrice" style="document"/>

<wsdl:input name="GetLastTradePrice">

<soap:body use="literal"/>

</wsdl:input>

<wsdl:output name="GetLastTradePriceResponse">

<soap:body use="literal"/>

</wsdl:output>

</wsdl:operation>

</binding>

<service name=”StockQuoteService”>

<port name=”StockQuotePort” binding=”tns:StockQuoteServiceSoapBinding”>

<soap:address location=”REPLACE_WITH_ACTUAL_URL”/>

</port>

</service>

</definitions>

The following C++ file would be generated:

// @WebService(name=”StockQuote”, targetNamespace=”http://www.example.org/”

//       serviceName=”StockQuoteService”)

class StockQuoteService {

// @WebFunction(operationName=”GetLastTradePrice”,

//       action=”urn:GetLastTradePrice”)

// @WebParam(paramName=”tickerSymbol”, name=”symbol”)

float getLastTradePrice(const std::string& tickerSymbol);

};

JAX-WS WSDL Extensions

An SCA implementation MAY support the reading and interpretation of JAX-WS defined WSDL extensions; however it MUST give precedence to the corresponding SCA WSDL extension if present.  The following is a list of JAX-WS WSDL extensions and their corresponding SCA WSDL extension. [CPPD0007]

| JAX-WS Extension | SCA Extension |
| --- | --- |
| jaxws:bindings | cpp:bindings |
| jaxws:class | cpp:class |
| jaxws:method | cpp:memberFunction |
| jaxws:parameter | cpp:parameter |
| jaxws:enableWrapperStyle | cpp:enableWrapperStyle |

WSDL Extensions Schema

<?xml version="1.0" encoding="UTF-8"?>

<schema xmlns="http://www.w3.org/2001/XMLSchema"

targetNamespace="http://docs.oasis-open.org/ns/opencsa/sca-c-cpp/cpp/200901"

xmlns:cpp="http://docs.oasis-open.org/ns/opencsa/sca-c-cpp/cpp/200901"

xmlns:xsd="http://www.w3.org/2001/XMLSchema"

elementFormDefault="qualified">

<element name="bindings" type="cpp:BindingsType" />

<complexType name="BindingsType">

<choice minOccurs="0" maxOccurs="unbounded">

<element ref="cpp:namespace" />

<element ref="cpp:class" />

<element ref="cpp:enableWrapperStyle" />

<element ref="cpp:memberFunction" />

<element ref="cpp:parameter" />

</choice>

</complexType>

<element name="namespace" type="cpp:NamespaceType" />

<complexType name="NamespaceType">

<attribute name="name" type="xsd:string" use="required" />

</complexType>

<element name="class" type="cpp:ClassType" />

<complexType name="ClassType">

<attribute name="name" type="xsd:string" use="required" />

</complexType>

<element name="memberFunction" type="cpp:MemberFunctionType" />

<complexType name="MemberFunctionType">

<attribute name="name" type="xsd:string" use="required" />

</complexType>

<element name="parameter" type="cpp:ParameterType" />

<complexType name="ParameterType">

<attribute name="part" type="xsd:string" use="required" />

<attribute name="childElementName" type="xsd:QName"

use="required" />

<attribute name="name" type="xsd:string" use="required" />

<attribute name="type" type="xsd:string" use="optional" />

</complexType>

<element name="enableWrapperStyle" type="xsd:boolean" />

</schema>

XML Schemas

Three XML schemas are defined to support the use of C++ for implementation and definition of interfaces.

The normative schemas are located at:

http://docs.oasis-open.org/opencsa/sca/2007/12/sca-interface-cpp-1.1-cd01.xsd

http://docs.oasis-open.org/opencsa/sca/2007/12/sca-implementation-cpp-1.1-cd01.xsd

http://docs.oasis-open.org/opencsa/sca/2007/12/sca-contribution-cpp-1.1-cd01.xsd

The following copies are provided for reference.

sca-interface-cpp-1.1.xsd

<?xml version="1.0" encoding="UTF-8"?>

<schema xmlns="http://www.w3.org/2001/XMLSchema"

targetNamespace="http://docs.oasis-open.org/ns/opencsa/sca/200712"

xmlns:sca="http://docs.oasis-open.org/ns/opencsa/sca/200712"

xmlns:sdo="commonj.sdo/XML"

elementFormDefault="qualified">

<include schemaLocation="sca-core.xsd"/>

<element name="interface.cpp" type="sca:CPPInterface"

substitutionGroup="sca:interface"/>

<complexType name="CPPInterface">

<complexContent>

<extension base="sca:Interface">

<sequence>

<element name="function" type="sca:CPPFunction"

minOccurs="0" maxOccurs="unbounded" />

<element name="callbackFunction" type="sca:CPPFunction"

minOccurs="0" maxOccurs="unbounded" />

<any namespace="##other" processContents="lax"

minOccurs="0" maxOccurs="unbounded"/>

</sequence>

<attribute name="header" type="NCName" use="required"/>

<attribute name="class" type="Name" use="required"/>

<attribute name="callbackHeader" type="NCName" use="optional"/>

<attribute name="callbackClass" type="Name" use="optional"/>

<attribute name="remotable" type="boolean" use="optional"/>

<anyAttribute namespace="##other" processContents="lax"/>

</extension>

</complexContent>

</complexType>

<complexType name="CPPFunction">

<attribute name="name" type="NCName" use="required"/>

<attribute name="oneWay" type="boolean" use="optional"/>

<attribute name="endsConversation" type="boolean" use="optional"/>

<anyAttribute namespace="##other" processContents="lax"/>

</complexType>

</schema>

sca-implementation-cpp-1.1.xsd

<?xml version="1.0" encoding="UTF-8"?>

<schema	xmlns="http://www.w3.org/2001/XMLSchema"

targetNamespace="http://docs.oasis-open.org/ns/opencsa/sca/200712"

xmlns:sca="http://docs.oasis-open.org/ns/opencsa/sca/200712"

xmlns:sdo="commonj.sdo/XML"

elementFormDefault="qualified">

<include schemaLocation="sca-core.xsd"/>

<element name="implementation.cpp" type="sca:CPPImplementation"

substitutionGroup="sca:implementation" />

<complexType name="CPPImplementation">

<complexContent>

<extension base="sca:Implementation">

<sequence>

<element name="function" type="sca:CPPImplementationFunction"

minOccurs="0" maxOccurs="unbounded" />

<any namespace="##other" processContents="lax"

minOccurs="0" maxOccurs="unbounded"/>

</sequence>

<attribute name="library" type="NCName" use="required"/>

<attribute name="header" type="NCName" use="required"/>

<attribute name="path" type="Name" use="optional"/>

<attribute name="class" type="Name" use="optional"/>

<attribute name="componentType" type="NCName" use="optional"/>

<attribute name="scope" type="sca:CPPImplementationScope"

use="optional"/>

<attribute name="eagerInit" type="boolean" use="optional"/>

<attribute name="allowsPassByReference" type="boolean"

use="optional"/>

<attribute name="conversationMaxAge" type="string"

use="optional"/>

<attribute name="conversationMaxIdle" type="string"

use="optional"/>

<attribute name="conversationSinglePrincipal" type="boolean"

use="optional"/>

<anyAttribute namespace="##other" processContents="lax"/>

</extension>

</complexContent>

</complexType>

<simpleType name="CPPImplementationScope">

<restriction base="string">

<enumeration value="stateless"/>

<enumeration value="composite"/>

<enumeration value="converstion"/>

</restriction>

</simpleType>

<complexType name="CPPImplementationFunction">

<attribute name="name" type="NCName" use="required"/>

<attribute name="allowsPassByReference" type="boolean"

use="optional"/>

<anyAttribute namespace="##other" processContents="lax"/>

</complexType>

</schema>

sca-contribution-cpp-1.1.xsd

<?xml version="1.0" encoding="UTF-8"?>

<schema xmlns="http://www.w3.org/2001/XMLSchema"

targetNamespace="http://docs.oasis-open.org/ns/opencsa/sca/200712"

xmlns:sca="http://docs.oasis-open.org/ns/opencsa/sca/200712"

elementFormDefault="qualified">

<include schemaLocation="sca-contributions.xsd"/>

<element name="export.cpp" type="sca:CPPExport"

substitutionGroup="sca:export"/>

<complexType name="CPPExport">

<complexContent>

<sequence>

<any namespace="##other" processContents="lax"

minOccurs="0" maxOccurs="unbounded"/>

</sequence>

<attribute name="name" type="QName" use="required"/>

<attribute name="path" type="string" use="optional"/>

<anyAttribute namespace="##other" processContents="lax"/>

</complexContent>

</complexType>

<element name="import.cpp" type="sca:CPPImport"

substitutionGroup="sca:import"/>

<complexType name="CPPImport">

<complexContent>

<sequence>

<any namespace="##other" processContents="lax"

minOccurs="0" maxOccurs="unbounded"/>

</sequence>

<attribute name="name" type="QName" use="required"/>

<attribute name="location" type="string" use="required"/>

<anyAttribute namespace="##other" processContents="lax"/>

</complexContent>

</complexType>

</schema>

Conformance Items

This section contains a list of conformance items for the SCA C++ Client and Implementation Model specification.

| Conformance ID | Description |
| --- | --- |
| [CPP20001] | A C++ implementation MUST implement all of the operation(s) of the service interface(s) of its componentType. |
| [CPP20002] | A C++ implementation of a remotable service that allow pass by reference MUST NOT alter its input data during or after the invocation, and MUST NOT modify return data after invocation. |
| [CPP20003] | An SCA runtime MUST support these four scopes; stateless, conversation, and composite. Additional scopes MAY be provided by SCA runtimes. |
| [CPP20004] | A conversational-scoped C++ implementation MUST NOT expose a service using a non-conversational interface. |
| [CPP20005] | If the header file identified by the @header attribute of an <interface.cpp/> element contains more than one class, then the @class attribute MUST be specified for the <interface.cpp/> element. |
| [CPP20006] | If the header file identified by the @callbackHeader attribute of an <interface.cpp/> element contains more than one class, then the @callbackClass attribute MUST be specified for the <interface.cpp/> element. |
| [CPP20007] | The @name attribute of a <function/> child element of a <interface.cpp/> MUST be unique amongst the <function/> elements of that <interface.cpp/>. |
| [CPP20008] | The @name attribute of a <callbackFunction/> child element of a <interface.cpp/> MUST be unique amongst the <callbackFunction/> elements of that <interface.cpp/>. |
| [CPP20009] | The name of the componentType file for a C++ implementation MUST match the class name (excluding any namespace definition) of the implementations as defined by the @class attribute of the <implementation.cpp/> element. |
| [CPP20010] | The @name attribute of a <function/> child element of a <implementation.cpp/> MUST be unique amongst the <function/> elements of that <implementation.cpp/>. |
| [CPP20011] | A C++ implementation class MUST be default constructable by the SCA runtime to instantiate the component. |
| [CPP40001] | An SCA runtime MAY end a conversation if the idle timeout expires. |
| [CPP40002] | An SCA runtime MAY end a conversation if the conversation age timeout expires. |
| [CPP50001] | A member function marked as oneWay=”true” is considered non-blocking and the SCA runtime MAY use a binding that buffers the requests to the member function and sends them at some time after they are made. |
| [CPP80001] | The@name attribute of a <export.cpp/> element MUST be unique amongst the <export.cpp/> elements in a domain. |
| [CPP80002] | The@name attribute of a <import.cpp/> child element of a <contribution/> MUST be unique amongst the <import.cpp/> elements in of that contribution. |
| [CPP100001] | A C++ header file used to define an interface MUST: Declare at least one class with: At least one public member function. All public member functions must be pure virtual (virtual with no implementation) |
| [CPP100002] | A C++ header file used to define an interface MUST NOT use the following constructs: Macros Inline member functions Friend classes |
| [CPP110001] | WSDLs MAY define a namespace using the <sca:namespace> WSDL extension (see D.4), otherwise all C++ classes will be placed in a default namespace as determined by the implementation. Implementations SHOULD provide a mechanism for overriding the default namespace. |
| [CPP110002] | If multiple operations within the same portType indicate that they throw faults that reference the same global element, a single C++ exception class MUST be created, with each C++ member function referencing this class in its @WebThrows annotation. |
| [CPP110003] | For unwrapped messages: in The message part is mapped to a member function parameter, passed by const-reference. out The message part is mapped to a member function parameter, passed by reference, or to the member function return type, returned by-value. in/out The message part is mapped to a member function parameter, passed by reference. |
| [CPP110004] | For wrapped messages: in The wrapper child is mapped to a member function parameter, passed by const-reference. out The wrapper child is mapped to a member function parameter, passed by reference, or to the member function return type, returned by-value. in/out The wrapper child is mapped to a member function parameter, passed by reference. |
| [CPP110005] | An implementation SHOULD provide a mechanism for overriding the default targetNamespace. |
| [CPP110006] | A methods return type is always considered out. A parameter passed by-reference or by-pointer is considered either in/out or out. All other parameters, including those passed by-const-reference are considered in. |
| [CPP110007] | C++ classes that define a web service interface MAY indicate which faults they may throw using the @WebThrows annotation. |
| [CPP110008] | Each class that is referenced from an @WebThrows annotation MUST itself have a @WebFault annotation that associates the fault with a particular global element that will be associated with the fault message. |
| [CPPA0001] | An SCA implementation MAY support source file annotations. If annotations are supported by an implementation, the annotations defined here MUST be supported and MUST be mapped to SCDL as described. The SCA runtime MUST only process the SCDL files and not the annotations. |
| [CPPA0002] | If multiple annotations apply to a program element, all of the annotations SHOULD be in the same comment block. |
| [CPPC0001] | An SCA implementation MUST treat any instance of a @Interface annotation and without an explicit @WebService annotation as if a @WebService annotation with a name value equal to the name value of the @Interface annotation and no other parameters was specified. |
| [CPPC0002] | A class annotated with a @Interface annotation and without an explicit @WebService annotation MUST be treated as if an @WebService annotation with no parameters was specified. |
| [CPPC0003] | If not provided, an implementation MUST use the value associated with the name element, suffixed with “Port” (See JAX-WS 3.11). |
| [CPPC0004] | Unnamed parameters CANNOT be referenced by an @WebParam annotation. |
| [CPPC0005] | The value of the type property of a @WebParam annotation MUST be one of the simpleTypes defined in namespace http://www.w3.org/2001/XMLSchema. |
| [CPPC0006] | The value of the type property of a @WebParam annotation MUST be one of the simpleTypes defined in namespace http://www.w3.org/2001/XMLSchema. |
| [CPPC0007] | Additionally, the class MUST provide a const member function “getFaultInfo” that takes no parameters, and returns the same type as defined in the constructor. |
| [CPPC0008] | A C++ class that is listed in a @WebThrows annotation MUST itself have a @WebFault annotation. |
| [CPPD0001] | An SCA implementation MAY support these WSDL extensions. If these extensions are supported by an implementation, all the extensions defined here MUST be supported and MUST be mapped to C++ as described. |
| [CPPD0002] | A <cpp:bindings/> element MUST NOT have more than one <cpp:class/> child element. |
| [CPPD0003] | <cpp:bindings/> element MUST NOT have more than one <cpp:enableWrapperStyle/> child element. |
| [CPPD0004] | A <cpp:bindings/> element MUST NOT have more than one <cpp:namespace/> child element. |
| [CPPD0005] | A <cpp:bindings/> element MUST NOT have more than one <cpp:memberFunction/> child element. |
| [CPPD0006] | The @type attribute of a <parameter/> element MUST be a valid C++ type. |
| [CPPD0007] | An SCA implementation MAY support the reading and interpretation of JAX-WS defined WSDL extensions; however it MUST give precedence to the corresponding SCA WSDL extension if present. The following is a list of JAX-WS WSDL extensions and their corresponding SCA WSDL extension. |

JAX-WS Conformance

The JAX-WS 2.1 specification [JAXWS21] defines conformance statements for various requirements defined by that specification.  The following table outlines those conformance statements, and describes whether the conformance statement applies to the WSDL binding described in this specification.

| Section | Conformance Statement | Notes | Conformance ID |
| --- | --- | --- | --- |
| 2 | WSDL 1.1 support | [A] | [CPPF0001] |
| 2 | Customization required | [CPPD0001] The reference to the JAX-WS binding language should be treated as a reference to the C++ WSDL extensions defined in section D. |  |
| 2 | Annotations on generated classes |  | [CPPF0002] |
| 2.1 | WSDL and XML Schema import directives |  | [CPPF0003] |
| 2.1.1 | Optional WSDL extensions |  | [CPPF0004] |
| 2.2 | SEI naming |  | [CPPF0005] |
| 2.2 | javax.jws.WebService required | [B] References to javax.jws.WebService in the conformance statement should be treated as the C++ annotation @WebService. | [CPPF0006] |
| 2.3 | Method naming |  | [CPPF0007] |
| 2.3 | javax.jws.WebMethod required | [A], [B] References to javax.jws.WebMethod in the conformance statement should be treated as the C++ annotation @WebFunction. | [CPPF0008] |
| 2.3 | Transmission primitive support |  | [CPPF0009] |
| 2.3 | Using javax.jws.OneWay | [A], [B] References to javax.jws.OneWay in the conformance statement should be treated as the C++ annotation @OneWay. | [CPPF0010] |
| 2.3.1 | Using javax.jws.SOAPBinding | [A], [B] References to javax.jws.SOAPBinding in the conformance statement should be treated as the C++ annotation @SOAPBinding. | [CPPF0011] |
| 2.3.1 | Using javax.jws.WebParam | [A], [B] References to javax.jws.WebParam in the conformance statement should be treated as the C++ annotation @WebParam. | [CPPF0012] |
| 2.3.1 | Using javax.jws.WebResult | [A], [B] References to javax.jws.WebResult in the conformance statement should be treated as the C++ annotation @WebResult. | [CPPF0013] |
| 2.3.1.1 | Non-wrapped parameter naming |  | [CPPF0014] |
| 2.3.1.2 | Default mapping mode |  | [CPPF0015] |
| 2.3.1.2 | Disabling wrapper style | [B] References to jaxws:enableWrapperStyle in the conformance statement should be treated as the WSDL extension cpp:enableWrapperStyle. | [CPPF0016] |
| 2.3.1.2 | Wrapped parameter naming |  | [CPPF0017] |
| 2.3.1.2 | Parameter name clash | [A] | [CPPF0018] |
| 2.5 | javax.xml.ws.WebFault required | [B] References to javax.jws.WebFault in the conformance statement should be treated as the C++ annotation @WebFault. | [CPPF0019] |
| 2.5 | Exception naming |  | [CPPF0020] |
| 2.5 | Fault equivalence | [A] | [CPPF0021] |
| 2.6 | Required WSDL extensions | MIME Binding not required | [CPPF0022] |
| 2.6.1 | Unbound message parts | [A] | [CPPF0023] |
| 2.6.2.1 | Duplicate headers in binding |  | [CPPF0024] |
| 2.6.2.1 | Duplicate headers in message |  | [CPPF0025] |
| 3 | WSDL 1.1 support | [A] | [CPPF0026] |
| 3 | Standard annotations | [A] [CPPC0001] |  |
| 3.1 | Java identifier mapping | [A] | [CPPF0027] |
| 3.1.1 | Method name disambiguation | [A] References to javax.jws.WebMethod in the conformance statement should be treated as the C++ annotation @WebFunction. | [CPPF0028] |
| 3.2 | WSDL and XML Schema import directives |  | [CPPF0029] |
| 3.4 | portType naming |  | [CPPF0030] |
| 3.5 | Operation naming |  | [CPPF0031] |
| 3.5.1 | One-way mapping | [B] References to javax.jws.OneWay in the conformance statement should be treated as the C++ annotation @OneWay. | [CPPF0032] |
| 3.5.1 | One-way mapping errors |  | [CPPF0033] |
| 3.6.1 | Parameter classification |  | [CPPF0034] |
| 3.6.1 | Parameter naming |  | [CPPF0035] |
| 3.6.1 | Result naming |  | [CPPF0036 |
| 3.6.1 | Header mapping of parameters and results | References to javax.jws.WebParam in the conformance statement should be treated as the C++ annotation @WebParam. References to javax.jws.WebResult in the conformance statement should be treated as the C++ annotation @WebResult. | [CPPF0037] |
| 3.7 | Exception naming | [A] References to javax.jws.WebFault in the conformance statement should be treated as the C++ annotation @WebFault. | [CPPF0038] |
| 3.8 | Binding selection | References to the BindingType annotation should be treated as references to SOAP related intents defined by [POLICY]. | [CPPF0039] |
| 3.10 | SOAP binding support | [A] | [CPPF0040] |
| 3.10.1 | SOAP binding style required |  | [CPPF0041] |
| 3.11 | Port selection |  | [CPPF0042] |
| 3.11 | Port binding | References to the BindingType annotation should be treated as references to SOAP related intents defined by [POLICY]. | [CPPF0043] |

[A] All references to Java in the conformance statement should be treated as C++.

[B] Annotation generation is only required if annotations are supported by an SCA implementatio

Ignored Conformance Statements

| Section | Conformance Statement | Notes |
| --- | --- | --- |
| 2.1 | Definitions mapping |  |
| 2.2 | javax.xml.bind.XmlSeeAlso required |  |
| 2.3.1 | use of JAXB annotations |  |
| 2.3.1.2 | Using javax.xml.ws.RequestWrapper |  |
| 2.3.1.2 | Using javax.xml.ws.ResponseWrapper |  |
| 2.3.3 | Use of Holder |  |
| 2.3.4 | Asynchronous mapping required | Pending Issue 55 |
| 2.3.4 | Asynchronous mapping option | Pending Issue 55 |
| 2.3.4.2 | Asynchronous method naming | Pending Issue 55 |
| 2.3.4.2 | Asynchronous parameter naming | Pending Issue 55 |
| 2.3.4.2 | Failed method invocation | Pending Issue 55 |
| 2.3.4.4 | Response bean naming | Pending Issue 55 |
| 2.3.4.5 | Asynchronous fault reporting | Pending Issue 55 |
| 2.3.4.5 | Asychronous fault cause | Pending Issue 55 |
| 2.4 | JAXB class mapping |  |
| 2.4 | JAXB customization use |  |
| 2.4 | JAXB customization clash |  |
| 2.4.1 | javax.xml.ws.wsaddressing.W3CEndpointReference |  |
| 2.6.3.1 | Use of MIME type information |  |
| 2.6.3.1 | MIME type mismatch |  |
| 2.6.3.1 | MIME part identification |  |
| 2.7 | Service superclass required |  |
| 2.7 | Service class naming |  |
| 2.7 | javax.xml.ws.WebServiceClient required |  |
| 2.7 | Default constructor required |  |
| 2.7 | 2 argument constructor required |  |
| 2.7 | Failed getPort Method |  |
| 2.7 | javax.xml.ws.WebEndpoint required |  |
| 3.2 | Package name mapping |  |
| 3.3 | Class mapping |  |
| 3.4.1 | Inheritance flattening |  |
| 3.4.1 | Inherited interface mapping |  |
| 3.6 | use of JAXB annotations |  |
| 3.6.2.1 | Default wrapper bean names |  |
| 3.6.2.1 | Default wrapper bean package |  |
| 3.6.2.3 | Null Values in rpc/literal |  |
| 3.7 | java.lang.RuntimeExceptions and java.rmi.RemoteExceptions |  |
| 3.7 | Fault bean name clash |  |
| 3.11 | Service creation |  |

Migration

To aid migration of an implementation or clients using an implementation based the version of the Service Component Architecture for C++ defined in OSOA SCA C++ Client and Implementation V1.00, this appendix identifies the relevant changes to APIs, annotations, or behavior defined in V1.00.

Annotations related to conversations

@Conversation has been changed to @ConversationAttributes.  @Conversation is removed.

@EndConversation has been changed to @EndsConversation.  @EndConversation is removed.

Method child elements of interface.cpp and implementation.cpp

The <method/> child element of <interface.cpp/> and the <method/> child element of <implementation.cpp/> have both been renamed to <function/> to be consistent with C++ terminology.

Acknowledgements

The following individuals have participated in the creation of this specification and are gratefully acknowledged:

Participants:

Andrew Borley, IBM

Bryan Aupperle, IBM

David Haney, Rogue Wave Software

Jeff Mischkinsky, Oracle

Mike Edwards, IBM

Pete Robbins, IBM

Non-Normative Text

Revision History

| Revision | Date | Editor | Changes Made |
| --- | --- | --- | --- |
| 3 | 2008-12-01 | Bryan Aupperle | Apply changes for CCPP-30, CCPP-37 and CCPP-46 |
| 2 | 2008-11-06 | Bryan Aupperle | Editorial cleanup Apply changes for CCPP-28, CCPP-44, CCPP-48 and CCPP-51 |
| 1 | 2008-07-31 | Bryan Aupperle | Font consistency for in-line literals and code. Apply changes for CCPP-9, CCPP-23, CCPP-41 |

# Comments

Editorial Notes:

- Review smart quotes from all code and samples (should they be removed in normal text as well?)

- Update revision history

- Update revision number and date

- Update footnotes to reflect current date.

- Update copyright year.

- Update language throughout the document to US English.

- Move to a common convention for referencing other documents, sections within other documents, and sections within this document.

This currently links to the TC page, however it should eventually link to an errata page.

Do we want this restriction? [Java doe not have it]

Move to section 2.3.2? Remove it? [Java does not have it]  Reword as a best practice?

Current Java text: For stateless scope components, there is no implied correlation between implementation instances used to dispatch service requests.

Can this fail if the ID is not a form the binding can accept?

Add conformance statements and rules.

A number of standard C++ types are not included in this mapping since there isn’t a mapping to them from SDO types (for instance, for unsigned types), should we define a mapping for those C++ types even though SDO doesn’t support them, or should we wait until SDO can support them?

SDO doesn’t define types for unsigned values, which makes these mappings a little uninituitive.  Should we ignore the SDO mapping and define our own, or continue to defer to SDO, and expect them to resolve this at some point?

Does this make sense in C++?

This will eventually need to be changed

Should non-voting members also be listed?

Should we have a section listing contributors from the OSOA spec that was used as a basis, even if they aren’t continuing with OASIS, i.e., all of the people originally attributed on the OSOA spec.