Universal Business Language (UBL) 
Configuration File

Instruction Paper 1, 22 October 2002

Document identifier:

i-stuhec-configfile-0p1.doc (Word)

Location:

http://www.oasis-open.org/committees/ubl/ndrsc/drafts/

Editors:

Gunther Stuhec, SAP AG <gunther.stuhec@sap.com>

Contributors:

Abstract:

This paper describes the characteristics of the configuration file.

Status:

This is a draft document and is likely to change on a weekly basis.

If you are on the ubl-ndrsc@lists.oasis-open.org list for NDR subcommittee members, send comments there. If you are not on that list, subscribe to the ubl-comment@lists.oasis-open.org list and send comments there. To subscribe, send an email message to ubl-comment-request@lists.oasis-open.org with the word "subscribe" as the body of the message.

For information on whether any patents have been disclosed that may be essential to implementing this specification, and any offers of patent licensing terms, please refer to the Intellectual Property Rights section of the Security Services TC web page (http://www.oasis-open.org/committees/security/).

Copyright © 2001, 2002 The Organization for the Advancement of Structured Information Standards [OASIS]

Table of Contents

1	Introduction	3

2	Structure and Functions	4

2.1	Reading or creating of a row	5

2.2	Reading or creating a cell-content	5

2.3	Reading/Writing Header-Information	5

2.4	IF-command for selecting information	5

2.5	Concatenation	6

2.6	Regular Expression	6

Appendix A. Notices	7

# Introduction

The new perl scripts generates UBL based XML Schemas from and into an Excel spreadsheet by a XML based configuration file. This configuration file contents all information for the convertion between both media. It describes the UBL schema structure and have all information where each information of the UBL schema structure exactly placed in the Excel spreadsheet.

This instruction paper describes the structure and the characteristics of the configuration file.

# Structure and Functions

The following structure represents a whole configuration file. The normal styled font represents the xml schema output and the bold styled font represents the specific functions for requesting information from the excel spreadsheet or putting specific content into the excel spread sheet.

<?xml version="1.0" encoding="UTF-8"?>

<!-- 10/12/2002 - Version 0.5 - source: draft-UBL_Library-0.5.xls -->

<!-- generated by Gunther Stuhec (UBL-Group) -->

<xsd:schema xmlns:cct="CoreComponentTypes.xsd" 
xmlns:xsd="http://www.w3.org/2001/XMLSchema" elementFormDefault="qualified" attributeFormDefault="unqualified">

<xsd:import namespace="CoreComponentTypes.xsd" 
		schemaLocation="CoreComponentTypes.xsd"/>

<xsd:complexType name="[content(4)]" id="[content(2)]" 
			config:row="if(content(12) == 'Aggregate')">

<xsd:annotation>

<xsd:documentation>

<xhtml:div 
				class="[header(14,5,10,11,13,15,16,17,18,19,20,21,22,23,24,25,26)]" 
				config:loop="if(header:count)">

<xhtml:p>[content(header:count)]</xhtml:p>">

</xhtml:div>

</xsd:documentation>

</xsd:annotation>

<xsd:sequence>

<xsd:element name="[content(4)]" 
				type="[if content(13) == 'Basic' then 'cct:[content(9)]Type' else if 
				content(13) == 'Aggregate' then 9]" id="[content(2)]" 
				minOccurs="[content(12:regexp(s/\.\..*//g))]" 
				maxOccurs="[content(12:regexp(s/\.\..*//g))]" 
				config:row="if(content(13) != 'Aggregate')>

<xsd:annotation>

<xsd:documentation>

<xhtml:div 
						class="[header(14,5,10,11,13,15,16,17,18,19,20,21,22,23,24,25,26)]" 
						config:loop="if(header:count)">

<xhtml:p>[content(header:count)]</xhtml:p>">

</xhtml:div>

</xsd:documentation>

</xsd:annotation>

</xsd:element>

</xsd:sequence>

</xsd:complexType>

</xsd:schema>

The following subsections explains this functions in more detail.

## Reading or creating of a row

A new row (except the header row) of a excel spreadsheet will be selected/created by

config:loop=”if (instruction)”

The optional if-command provides the possibility to select/create a new row in specific circumstances (see chapter 2.4).

Example:

<xsd:complexType name="[content(4)]" id="[content(2)]"  config:row="if(content(9) == 'Aggregate')">

## Reading or creating a cell-content

A cell content (except the header content) of a excel spreadsheet can be selected/created by

[content(n)]

All commands for reading/writing a content placed within square brackets. The (n) in the round brackets represents the cell-number (beginning with 0).

Example:

<xsd:complexType name="[content(4)]" id="[content(2)]" config:loop="if(content(9) = 'Aggregate')">

## Reading/Writing Header-Information

All the header information can be collected in a one dimensional array by:

[header(14,5,10,11,13,15,16,17,18,19,20,21,22,23,24,25,26)]

The in/output would of each header information would be proced sequently. This in/output could be controlled by the command:

config:loop="if(header:count)"

It generates/reads a new xml-line for each field within the count-array.

Example:

<xhtml:div class="[header(14,5,10,11,13,15,16,17,18,19,20,21,22,23,24,25,26)]" 
config:loop="if(header:count)">

## IF-command for selecting information

Specific information from different cells in the same row can be selected by an if-command.

The if-command have the following structure:

[if instruction then ‘execution’ else if instruction then ‘execution’]

The ‘instruction’ can be: content(n) == ‘value.

“==” stands for if equal and “!=” stands for if not equal.

The “content(n)” stands for a content in a specific cell number and the “value” itself represents the specific value for the ‘content’. The ‘value’ will be represented between inverted commas.

The ‘execution’ represents the specific output into the XML schema or input into the excel spreadsheet.

Example:

<xsd:element name="[content(4)]" 
	type="[if content(13) == 'Basic' then 'cct:[content(9)]Type' else if 				content(13) == 'Aggregate'  then 9]" id="[content(2)]" 
	minOccurs="[content(12:regexp(s/\.\..*//g))]" 
	maxOccurs="[content(12:regexp(s/\.\..*//g))]" 
	config:row="if(content(12) != 'Aggregate')>

## Concatenation

It is possible to concatenate some another commands with some fixed values. Like:

'cct:[content(9)]Type'

The commands resides within further square brackets. The script concatenates this information together, if this script will generate a xml schema. It selects the information between the square brackets only, if the script generate an excel sheet.

Example:

<xsd:element name="[content(4)]" 
	type="[if content(13) == 'Basic' then 'cct:[content(9)]Type' else if 				content(13) == 'Aggregate'  then 9]" id="[content(2)]" 
	minOccurs="[content(12:regexp(s/\.\..*//g))]" 
	maxOccurs="[content(12:regexp(s/\.\..*//g))]" 
	config:row="if(content(13) != 'Aggregate')>

## Regular Expression

It is possible to use some regular expression for reading/writing some specific squences. Like:

[content(n:regexp(expression))]

The regular expression stands behind a colon after the number of the specific cell (n). The syntax of regular expressions are the same as in perl-scripts and shell-programming.

Example:

<xsd:element name="[content(4)]" 
	type="[if content(13) == 'Basic' then 'cct:[content(9)]Type' else if 				content(13) == 'Aggregate'  then 9]" id="[content(2)]" 
	minOccurs="[content(12:regexp(s/\.\..*//g))]" 
	maxOccurs="[content(12:regexp(s/\.\..*//g))]" 
	config:row="if(content(13) != 'Aggregate')>

Notices

OASIS takes no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights. Information on OASIS's procedures with respect to rights in OASIS specifications can be found at the OASIS website. Copies of claims of rights made available for publication and any assurances of licenses to be made available, or the result of an attempt made to obtain a general license or permission for the use of such proprietary rights by implementors or users of this specification, can be obtained from the OASIS Executive Director.

OASIS invites any interested party to bring to its attention any copyrights, patents or patent applications, or other proprietary rights which may cover technology that may be required to implement this specification. Please address the information to the OASIS Executive Director.

Copyright  © The Organization for the Advancement of Structured Information Standards [OASIS] 2001. All Rights Reserved.

This document and translations of it may be copied and furnished to others, and derivative works that comment on or otherwise explain it or assist in its implementation may be prepared, copied, published and distributed, in whole or in part, without restriction of any kind, provided that the above copyright notice and this paragraph are included on all such copies and derivative works. However, this document itself does not be modified in any way, such as by removing the copyright notice or references to OASIS, except as needed for the purpose of developing OASIS specifications, in which case the procedures for copyrights defined in the OASIS Intellectual Property Rights document must be followed, or as required to translate it into languages other than English.

The limited permissions granted above are perpetual and will not be revoked by OASIS or its successors or assigns.

This document and the information contained herein is provided on an “AS IS” basis and OASIS DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.