Web Services Context Specification (WS-Context)

Committee draft version 0.4

5 August 2004

Abstract

Web services exchange XML documents with structured payloads. The processing semantics of an execution endpoint may be influenced by additional information that is defined at layers below the application protocol. When multiple Web services are used in combination, the ability to structure execution related data called context becomes important. This information is typically communicated via SOAP Headers. WS-Context provides a definition, a structuring mechanism, and a software service definition for organizing and sharing context across multiple execution endpoints.

The ability to compose arbitrary units of work is a requirement in a variety of aspects of distributed applications such as workflow and business-to-business interactions. By composing work, we mean that it is possible for participants in an activity to be able to determine unambiguously whether or not they are participating in the same activity.

An activity is the execution of multiple Web services composed using some mechanism external to this specification, such as an orchestration or choreography. A common mechanism is needed to capture and manage contextual execution environment data shared, typically persistently, across execution instances.

In order to correlate the work of participants within the same activity, it is necessary to propagate context to each participant. The context contains information (such as a unique identifier) that allows a series of operations to share a common outcome.

Table of contents

1	Architecture	6

1.1 Invocation of Service Operations	6

1.2 Relationship to WSDL	7

1.3 Referencing and addressing conventions	7

2	Context	9

2.1 Context information and SOAP	11

3	Context Manager	13

4	Activities	15

5	Context Service	16

5.1 Status	16

5.2 Context Service messages	16

begin	18

complete	18

getStatus	19

setTimeout	19

getTimeout	19

5.2.1 State transitions	19

6	References	22

Note on terminology

The keywords "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT", "SHOULD", "SHOULD NOT", "RECOMMENDED", "MAY", and "OPTIONAL" in this document are to be interpreted as described in RFC2119 [2].

Namespace URIs of the general form "some-URI" represents some application-dependent or context-dependent URI as defined in RFC 2396 [3].

## Namespace

The XML namespace URI that MUST be used by implementations of this specification is:

http://www.webservicestransactions.org/schemas/wsctx/2003/03

### Prefix Namespace

| Prefix | Namespace |
| --- | --- |
| wsctx | http://www.webservicestransactions.org/schemas/wsctx/2003/03 |

## Referencing Specifications

One or more other specifications, such as (but not limited to) WS-CF may reference the WS-Context specification. The usage of the optional items in WS-Context is typically determined by the requirements of such as referencing specification.

# Architecture

An activity represents the execution of a series of related interactions with a set of Web Services; these operations are related via context. An activity is a conceptual grouping of services cooperating to perform some work; a context is the concrete manner in which this grouping occurs. The notion of an activity is used to scope application specific work. The definition of precisely what an activity is and what services it will require in order to perform that work, will depend upon the execution environment and application in which it is used.

Context is information about the execution environment of an activity that supplements information in application payloads. Management of the basic context type is facilitated by services defined in this specification. The specification also provides service interfaces for managing session-oriented protocols and representing the corresponding activities with contexts. The overall architecture of the context is hierarchical and decomposable, e.g., it is possible to use the context structure without reference to any activity model.

The first element of the WS-Context specification is the context structure. The context structure defines a normal model for organizing context information. It supports nesting structures (parent-child relationships) for related contexts, and mechanisms to pass context information by reference or by value. A single context type is not sufficient for all applications; it must be extensible in a manner specific to a referencing specification and Web services must be able to augment the context, as they require.

WS-Context defines a Context Service. The Context Service defines the scope of an activity and how information about it (the context) can be referenced and propagated in a distributed environment. The Context Service uses context to express basic information about the activity. The context is identified using a URI. The context contains information necessary for multiple Web services to be associated with the same activity. This information may be augmented when the context is created (by implementations of referencing specifications), or dynamically by application services as they send and receive contexts. Activities are represented by the Context Service, which maintains a repository of shared contexts. Whenever messages are exchanged within the scope of an activity, the Context Service can supply the associated context that may then be propagated with those messages.

## Invocation of Service Operations

How application services are invoked is outside the scope of this specification: they may use synchronous or asynchronous message passing.

Irrespective of how remote invocations occur, context information related to the sender’s activity needs to be referenced or propagated. This specification determines the format of the context, how it is referenced, and how a context may be created.

In order to support both synchronous and asynchronous interactions, the components are described in terms of the behavior and the interactions that occur between them. All interactions are described in terms of correlated messages, which a referencing specification may abstract at a higher level into request/response pairs.

Faults and errors that may occur when a service is invoked are communicated back to other Web services in the activity via SOAP messages that are part of the standard protocol. The fault mechanism of the underlying SOAP-based transport isn’t used. For example, if an operation fails because no activity is present when one is required, then it will be valid for the InvalidContextFault message to be received by the response service. To accommodate other errors or faults, all response service signatures have a generalFault operation.

Note: in the rest of this specification we will use the term “invokes operation X on service Y” when referring to invoking services. This term does not imply a specific implementation for performing such service invocations and is used merely as shorthand for “sends message X to service Y.” As long as implementations ensure that the on-the-wire message formats are compliant with those defined in this specification, how the end-points are implemented and how they expose the various operations (e.g., via WSDL [1]) is not mandated by this specification. However, a normative WSDL binding is provided by default in this specification.

Note, this specification does not assume that a reliable message delivery mechanism has to be used for message interactions. As such, it may be implementation dependant as to what action is taken if a message is not delivered or no response is received.

## Relationship to WSDL

Where WSDL is used in this specification it uses a synchronous invocation style for sending requests. In order to provide for loose-coupling of entities all responses are sent using synchronous call-backs. However, this is not prescriptive and other binding styles are possible.

For clarity WSDL is shown in an abbreviated form in the main body of the document: only portTypes are illustrated; a default binding to SOAP 1.1-over-HTTP is also assumed as per [1]. Complete WSDL is available at the end of the specification.

## Referencing and addressing conventions

There are multiple mechanisms for addressing messages and referencing web services currently proposed by the Web services community. This specification defers the rules for addressing SOAP messages to existing specifications; the addressing information is assumed to be placed in SOAP headers and respect the normative rules required by existing specifications.

However, the Context message set requires an interoperable mechanism for referencing web services. For example, context structures may reference the service that is used to manage the content of the context. To support this requirement, WS-CAF uses an open content model for service references. The open content model is supported by the service-ref element, shown in Figure 1.

<xs:element name="service-ref" type=”tns:ServiceRefType”/>

<xs:complexType name="ServiceRefType">

<xs:sequence>

<xs:any namespace="##other" processContents="lax" minOccurs="1" maxOccurs="1"/>

</xs:sequence>

<xs:attribute name="reference-scheme" type="xs:anyURI" use="required"/>

</xs:complexType>

Figure 1, service-ref Element

The reference-scheme is the namespace URI for the referenced addressing specification. For example, the value for WSRef defined in the WS-MessageDelivery specification [4] would be http://www.w3.org/2004/04/ws-messagedelivery.

The contents of the xs:any element contain a service reference as defined by the referenced specfication. For example, a WSRef to a Context Manager service would appear as below.

<wsdl11:service name="MyContextService" wsmd:portType="ctx:ContextManager"> <wsdl11:port name="myCtxPort" binding="ex:ctxServiceBinding"> <soapbind:address location="http://example.com/wsdl-example1/impl"/> </wsdl11:port> </wsdl11:service>

Figure 2 shows a representative WSRef.

<ctx:service-ref reference-scheme="ttp://www.w3.org/2004/04/ws-messagedelivery"> 
    <wsdl:service name="MyContextService" wsmd:portType="ctx:ContextManager"> 
        <wsdl:port name="myCtxPort" binding="ex:ctxServiceBinding"> 
            <soapbind:address location="http://example.com/wsdl-example1/impl"/> 
        </wsdl:port> 
    </wsdl:service> 
</ctx:service-ref>

Figure 2, example of a service-ref element

Messages sent to referenced services must use the addressing scheme defined by the specification indicated by the value of the reference-scheme element.

To preserve interoperability in deployments that contain multiple addressing schemes, there are no restrictions on a system, beyond those of the composite services themselves. However, it is recommended where possible that composite applications confine themselves to the use of single addressing and reference model.

# Context

Context is used to include protocol specific data for transmission in SOAP headers. The basic context structure is shown in Figure 3.

<xs:complexType name="ContextType">

<xs:sequence>

<xs:any namespace="##other" processContents="lax" minOccurs="0" maxOccurs="unbounded"/>

<xs:element name="context-identifier" type="xs:anyURI"/>

<xs:element name="context-service" type="xs:anyURI" minOccurs="0"/>

<xs:element name="type" type="xs:anyURI" minOccurs="0"/>

    <xs:element name=”context-manager” type=”tns:ServiceRefType”/>

<xs:complexType>

<xs:sequence>

<xs:element ref="service-ref" minOccurs="0" 
            maxOccurs="unbounded"/>

</xs:sequence>

<xs:attribute name="mustUnderstand" type="xs:boolean" use="optional" 
          default="false"/>

<xs:attribute name="mustPropagate" type="xs:boolean" use="optional" 
          default="false"/>

</xs:complexType>

</xs:element>

<xs:element name="child-contexts" minOccurs="0">

<xs:complexType>

<xs:sequence>

<xs:element name="child-context" type="tns:ContextType" 
            maxOccurs="unbounded"/>

</xs:sequence>

</xs:complexType>

</xs:element>

</xs:sequence>

<xs:attribute name="timeout" type="xs:int" use="optional"/>

</xs:complexType>

Figure 3, Context Service Context.

The context consists of the following items:

A mandatory URI called context-identifier. This identifier can be thought of as a “correlation” identifier or a value that is used to indicate that a Web service is part of the same activity. It must be globally unique.

An optional URI element, context-service, which identifies the issuing authority responsible for generating the context. This element may not be dereferenced and is only for unique identification. It must be globally unique.

An optional URI that indicates the type of the protocol supported by the context, i.e., it indicates how the information within a context may be interpreted. This element may not be dereferenced and is only for unique identification. It must be unique amongst the referencing specifications.

An optional service to get data associated with a context-identifier that resolves to a reference to a Context Manager web service.

An optional child-contexts element containing a list of child-context elements.

An optional timeout value, which indicates for how long the context information is valid; the after this period has elapsed, the context is considered to be invalid. A context is determined to be valid by its issuing authority. For example, the WS-Context specification defines an issuing authority called the Context Service. The timeout allows the issuing authority implementation to invalidate contexts automatically rather than have them remain valid forever. It is implementation dependant as to the interpretation of a context with no specified timeout value.

The context may contain information from an arbitrary number of augmenter services. The context structure is extended via the extensibility xsd:any element present in the schema for the ContextType.

Context propagation is possible using different protocols than those used by the application, as shown in Figure 4. The WS-Context specification does not assume a specific means by which contexts are associated with application messages, leaving this up to the referencing specification.

Figure 4, Services and context flow.

Contexts may be passed by reference or by value. Contexts that are passed by value are considered to be snapshot copies of the context at the point in time at which the context was created or augmented. Contexts that are passed by reference may always be de-referenced to retrieve the current “by value” copy of the context.

Contexts that are passed by reference must include the context-manager element. Dereferencing may be performed by a reference to a ContextManager Web service identified by a Web service reference contained in the context, as indicated by the context instance. Implementations or deployments may prefer to use a particular approach for reasons of efficiency (e.g., by-reference contexts that contain particularly large data blocks, by-reference copies of sensitive data with access control for dereferencing, or by-value copies of contexts with smaller blocks of protocol processing elements).

The choice of whether to transmit a full or abbreviated context is left to the sender of the context. It is however expected that when dealing with large context elements (those which subsume a large number of activities) that by-reference form will be used for efficiency. A sender who wishes to switch between full and abbreviated has the responsibility for ensuring that the dereferencing capability is available.

## Activities

As mentioned earlier, an activity is defined as a collection of Web service operation invocations performed within a valid context. An activity is created, runs, and then completes. An outcome is the result of a completed activity. The expected semantics of a web service within an activity are defined by specifications derived from WS-Context. These semantics are indicated in a context by a protocol identifier representing the protocol type of the activity. The activity itself is uniquely identified by a context-identifier element.

In a system, there may be a set of contexts C associated with an activity. There will typically be multiple contexts because context data structures may be copied by value from service to service and may be augmented to include data that is valid to the local execution environment. The contexts in C are not equivalent: each may reflect one service's view of the activity at a point in time. The initial context created for a specific activity is the base from which all other contexts may be derived.

A context is associated with one and only one activity; "compound" activity contexts do not exist. The set of operations represented by A may be used to define more than one activity; for example, the operations in A may include a context for a security protocol and a context for a transaction protocol, each representing a separate activity.

A Web service that performs an operation within an invalid context creates an invalid activity. It is up to the specifications using WS-Context to determine the implications of invalid activities (which may be insignificant or severe) and provide structuring mechanisms that avoid invalid activities if necessary.

Activities may be nested. If an activity is nested, then the global context may contain a hierarchy representing the activity structure. Each element in the context hierarchy may also possess a different context-identifier.

## Context information and SOAP

Where messages (either application messages, or WS-Context protocol messages themselves) require contextualization, the context is transported in a SOAP header block. While it is implicit that WS-Context actors understand contexts that arrive in SOAP header blocks, the context propagated with application messages must also be understood by their recipients. Hence in this case each SOAP header block carrying a context has the “mustUnderstand” attribute set to “true” and the recipient must understand the header block encoding according to its identifying URI. This is shown in Figure 5.

<?xml version="1.0" encoding="UTF-8"?>

<soap:Envelope xmlns:soap="http://www.w3.org/2002/06/soap-envelope">

<soap:Header =

mustUnderstand="1">

<context xmlns="http://www.webservicestransactions.org/schemas/wsctx/2003/03"  
      timeout="100"

xmlns:wsdl=”http://schemas.xmlsoap.org/wsdl/”

xmlns:soapbind=”http://schemas.xmlsoap.org/wsdl/soap/”>

<context-identifier>
        http://www.webservicestransactions.org/wsctx/abcdef:012345
      </context-identifier>

<context-service>
        http://www.webservicestransactions.org/wsctx/service
      </context-service>

<type>
        http://www.webservicestransactions.org/wsctx/context/type1

</type>

<child-contexts>

<child-context timeout="200">

<context-identifier>
            http://www.webservicestransactions.org/wsctx/5e4f2218b
          </context-identifier>

<context-service>
           http://www.webservicestransactions.org/wsctx/service

</context-service>

<type>http://www.webservicestransactions.org/wsctx/context/type1</type>

</child-context>

</child-contexts>

</context>

</soap:Header>

<soap:Body>

<!-- Application Payload -->

</soap:Body>

</soap:Envelope>

Figure 5, CTX Context Transported in a SOAP Header Block.

# Context Manager

If the context is passed by reference, then a receiver may require the information it contains. WS-Context defines an optional Web service interface, the Context Manager, which allows applications to retrieve and set data associated with a context. Figure 6 shows the message interactions for the context using the dereferencing call-back style mentioned earlier: solid lines represent the initial request invocations and dashed lines represent the response invocations.

Note, the Context Manager need not be the same endpoint as the Context Service.

Figure 6, Context interactions.

The ContextManager has the following operations, all of which contain the callback address for the ContextResponseHandler:

getContents: this message is used to request the entire contents of a specific context. It responds with either the contents message or an appropriate fault message.

setContents: the contents of the context are replaced with the context information provided. It responds with either the contentsSet message or an appropriate fault message. Note that concurrency control of a context passed by a reference is an implementation issue.

The ContextResponseHandler has the following operations, all of which must be contextualized with at least a minimal context header, i.e., the context identifier:

contents: this message returns the entire contents of a specific context.

contentsSet: this message is sent to indicate that contents of the context have been updated.

unknownContextFault: this message is sent to indicate that the specified context cannot be located.

generalFault: this message is sent to indicate that some other error has occurred during the enlistment.

The WSDL interfaces that elucidate these roles are shown in Figure 7.

<wsdl:portType name="ContextManagerPortType">

<wsdl:operation name="getContents">

<wsdl:input message="tns:GetContentsMessage"/>

</wsdl:operation>

<wsdl:operation name="setContents">

<wsdl:input message="tns:SetContentsMessage"/>

</wsdl:operation>

</wsdl:portType>

<wsdl:portType name="ContextResponseHandlerPortType">

<wsdl:operation name="contents">

<wsdl:input message="tns:ContentsMessage"/>

</wsdl:operation>

<wsdl:operation name="contentsSet">

<wsdl:input message="tns:ContentsSetMessage"/>

</wsdl:operation>

<wsdl:operation name="unknownContextFault">

<wsdl:input message="tns:UnknownContextFaultMessage"/>

</wsdl:operation>

<wsdl:operation name="generalFault">

<wsdl:input message="tns:GeneralFaultMessage"/>

</wsdl:operation>

</wsdl:portType>

Figure 7, WSDL Interfaces for ContextManager and ContextResponseHandler Roles.

# Context Service

The WS-Context specification defines a Context Service that supports the abstract notion of an activity and allows referencing specifications and services to scope work within these activities by sharing context. The basic infrastructure supports the lifecycle of contexts and ensures that each is uniquely identified. This section specifies how activities and contexts are modeled, managed, and represented by the Context Service.

## Status

During the existence of the activity its status will either be running, completing, or completed. An activity should report its current status when asked; there is no notion of automatically informing services when a specific state is entered:

<xs:simpleType name="StatusType">

<xs:restriction base="xs:string">

<xs:enumeration value="activity.status.ACTIVE"/>

<xs:enumeration value="activity.status.COMPLETING"/>

<xs:enumeration value="activity.status.COMPLETED"/>

<xs:enumeration value="activity.status.NO_ACTIVITY"/>

<xs:enumeration value="activity.status.UNKNOWN"/>

</xs:restriction>

</xs:simpleType>

The meaning of each of the above values is given below:

activity.status.ACTIVE: The activity is in the active state. An implementation returns this status after an Activity has been started and prior to its beginning completion.

activity.status.COMPLETING: The activity is in the process of completing. An implementation returns this status if it has started to complete, but has not yet finished the process. This value indicates that the activity may be performing activity specific work required to determine its final completion status, such as notifying participants of a failure. An activity must enter this state prior to completion.

activity.status.COMPLETED: The activity has completed.

activity.status.NO_ACTIVITY: There is no such activity.

activity.status.UNKNOWN: The Context Service cannot determine the current status of the activity. This is a transient condition, and a subsequent invocation should ultimately return a different status. An implementation may attempt to retry the appropriate invocation transparently if such a value is returned initially.

The diagram below indicates the transitions that an Activity can undergo.

Figure 8, Activity UML state diagram.

## Context Service messages

In order to be able to scope work within activities it is necessary for a component of the Context Service to provide an interface for activity demarcation. Since the Context Service maintains information on multiple activities, an activity context may be present on some operation invocations to determine the appropriate activity on which to operate. This context should be passed by reference, since it is only required for identification purposes.

Interactions with the Context Service occur between users (services) and the Context Service via the UserCTXService and CTXService interfaces respectively. The WSDL for these services is shown below and we shall describe the interactions in the following section.

<wsdl:portType name="CTXServicePortType">

<wsdl:operation name="begin">

<wsdl:input message="tns:BeginMessage"/>

</wsdl:operation>

<wsdl:operation name="complete">

<wsdl:input message="tns:CompleteMessage"/>

</wsdl:operation>

<wsdl:operation name="getStatus">

<wsdl:input message="tns:GetStatusMessage"/>

</wsdl:operation>

<wsdl:operation name="setTimeout">

<wsdl:input message="tns:SetTimeoutMessage"/>

</wsdl:operation>

<wsdl:operation name="getTimeout">

<wsdl:input message="tns:GetTimeoutMessage"/>

</wsdl:operation>

</wsdl:portType>

<wsdl:portType name="UserCTXServicePortType">

<wsdl:operation name="begun">

<wsdl:input message="tns:BegunMessage"/>

</wsdl:operation>

<wsdl:operation name="completed">

<wsdl:input message="tns:CompletedMessage"/>

</wsdl:operation>

<wsdl:operation name="status">

<wsdl:input message="tns:StatusMessage"/>

</wsdl:operation>

<wsdl:operation name="requestedContext">

<wsdl:input message="tns:RequestedContextMessage"/>

</wsdl:operation>

<wsdl:operation name="timeoutSet">

<wsdl:input message="tns:TimeoutSetMessage"/>

</wsdl:operation>

<wsdl:operation name="timeout">

<wsdl:input message="tns:TimeoutMessage"/>

</wsdl:operation>

<wsdl:operation name="invalidStateFault">

<wsdl:input message="tns:InvalidStateFaultMessage"/>

</wsdl:operation>

<wsdl:operation name="invalidContextFault">

<wsdl:input message="tns:InvalidActivityFaultMessage"/>

</wsdl:operation>

<wsdl:operation name="timeoutOutOfRange">

<wsdl:input message="tns:TimeoutOutOfRangeFaultMessage"/>

</wsdl:operation>

<wsdl:operation name="childActivityPendingFault">

<wsdl:input message="tns:ChildActivityPendingFaultMessage"/>

</wsdl:operation>

<wsdl:operation name="noPermissionFault">

<wsdl:input message="tns:NoPermissionFaultMessage"/>

</wsdl:operation>

</wsdl:portType>

Figure 9, CTXService WSDL.

In order to drive the Context Service, the following two roles (and associated services) are defined for the interactions:

CTXService: this has operations begin, complete, getStatus, setTimeout and getTimeout;

UserCTXService: this is the user/service callback endpoint address for the various CTXService operations. As such, it has operations begun, completed, status, timeoutSet, timeout, invalidStateFault, invalidActivityFault, timeoutOutOfRangeFault, childActivityPendingFault, noActivityFault, noPermissionFault, validContextExpectedFault.

The CTXService has the following operations, all of which are associated with the current context (if any). The UserCTXService endpoint address is exchanged during each operation in order to allow the Context Service to return the result of the invocation.

### begin

The begin operation creates a new context (based on the type parameter). A begin can be modeled as the first Web service in the Activity to register itself. An unique context identifier is created for the context such that any context information that is subsequently obtained will reference this identifier. If a context is present on the begin request then the newly created context will be nested within it. Otherwise, the context exists at the top level. If the activity is completing, or has completed, the invalidContextFault operation will be invoked on the received UserCTXService endpoint.

The timeout parameter is used to control the lifetime of a context. If the Activity has not completed by the time the timeout second elapse then it is subject to being completed automatically by the Context Service. The timeout can have the following possible values:

any positive value: the Activity must complete within this number of seconds.

-1: the Activity will never be completed automatically by the Context Service implementation, i.e., it will never be considered to have timed out.

0: the last value specified using the set_timeout method is used. If no prior call to the setTimeout operation has occurred for this thread, or the value returned is 0, then it is implementation dependant as to the timeout value associated with this Activity.

Any other value results in the Context Service calling the timeoutOutOfRangeFault operation on the UserCTXService endpoint.

Upon success, the new activity will be considered to be in the activity.status.ACTIVE state and the Context Service will invoke the begun operation of the UserCTXService.

If an invalid context is propagated on the begin request then the validContextExpectedFault operation is invoked on the UserCTXService.

The generalFault operation is invoked on the UserCTXService if an unexpected error or fault occurs.

The invalidProtocolTypeFault operation is invoked on the UserCTXService is the service cannot create a context of the required type.

### complete

A valid activity context is associated with this invocation. A Context Service implementation may impose restrictions on which Web services can terminate an activity, and in which case the noPermissionFault operation may be invoked on the UserCTXService.

A protocol-specific completion status value may accompany this invocation and may be used by the ContextService when terminating the activity. For example, one completion status for a transaction protocol might represent an abort signal. Some protocols may not make distinctions between success or failure in the termination of an activity and would not require any completion status.

Once complete, the Context Service invokes the completed method on the UserCTXService. If the Activity has begun completion, or has completed, then the invalidContextFault UserCTXService operation is called.

If an invalid context is propagated on the request then the validContextExpectedFault operation is invoked on the UserCTXService.

The generalFault operation is invoked on the UserCTXService if an unexpected error or fault occurs.

### getStatus

This operation is used to obtain the current Status of the activity referenced in the propagated context. The Context Service invokes the status operation on the associated UserCTXService to return the current status of the Activity. If there is no valid context associated with the context-identifier, the InvalidContextFault operation is invoked on the UserCTXService.

If an invalid context is propagated on the request then the validContextExpectedFault operation is invoked on the UserCTXService.

The generalFault operation is invoked on the UserCTXService if an unexpected error or fault occurs.

### setTimeout

No context is associated with this invocation. This operation modifies a state variable associated with the Context Service that affects the time-out period associated with the activities created by subsequent invocations of the begin operation when no timeout is specified (i.e., the begin timeout value is 0): this is a default timeout value associate with the service. If the parameter has a non-zero value n, then activities created by subsequent invocations of begin will be subject to being completed if they do not complete before n seconds after their creation. The timeout can have the following possible values:

any positive value: the Activity must complete within this number of seconds.

-1: the Activity will never be completed automatically by the Context Service implementation, i.e., it will never be considered to have timed out.

0: it is implementation dependant as to the meaning of passing 0 as the value.

A valid timeout value results in the Context Service calling the UserCTXService’s timeoutSet operation. Any other value results in the timeoutOutOfRangeFault operation being invoked on the associated UserCTXService.

The generalFault operation is invoked on the UserCTXService if an unexpected error or fault occurs.

### getTimeout

No context is associated with this invocation. Upon successful execution, this operation causes the Context Service to return the default timeout value associated with the service, i.e., the timeout that is associated with activities created by calls to begin when no timeout value is passed via begin. This need not be the value associated with the current Activity, however.

The generalFault operation is invoked on the UserCTXService if an unexpected error or fault occurs.

### State transitions

Figure 10 shows the state transitions for an activity and how they relate to the various message exchanges between the client/user of the Context Service and the Context Service. As mentioned above, in order to participate in these message interactions the client/user supplies a UserCTXService endpoint.

Figure 10, Activity state transitions and messages.

# References

[1] WSDL 1.1 Specification, see http://www.w3.org/TR/wsdl

[2] "Key words for use in RFCs to Indicate Requirement Levels," RFC 2119, S. Bradner, Harvard University, March 1997.

[3] "Uniform Resource Identifiers (URI): Generic Syntax," RFC 2396, T. Berners-Lee, R. Fielding, L. Masinter, MIT/LCS, U.C. Irvine, Xerox Corporation, August 1998.

# Comments

Bryan Murray: “What should be the behavior of the ContextRespondant if it sends a
getContents message and never receives a follow-up message?”

Bryan Murray: “Section 1.2, first para: The use of "synchronous" here is confusing.
Maybe "one-way" for the first use of synchronous and "asynchronous" for
the second use of synchronous would help. There is also a reference here
to other binding styles. Again an example would help a lot and some text
indicating that either all or part of the WSDL is normative and how an
implementer can provide other bindings and still be compliant with this
spec.”

I haven’t addressed this. The interaction is truly synchronous in the binding to HTTP, since no HTTP requests are fire-and-forget. But, I’m happy to change the text.

Bryan Murray: “Section 1.3: the 2 paragraphs above figure 2 seem to be redundant (1
XML, 1 text). I suggest removing both.”

I think he’s right, but since Greg added this text I’ll check with him.

Bryan Murray: “How does the ContextManager know where to send follow-up messages? There
is a sentence in the introduction to section 3 talking about a
dereferencing call-back style, but I did not find text describing this
style in detail. There is a mention of call-back in section 1.2 and
section 1.3 talks about a referencing structure, but there is no clear
description of how all these parts come together to instruct the
ContextManager where to send follow-up messages.”

Bryan has a few of these comments and I think we just need to add some text here. This stuff used to be in the AssertionType but has now been moved to the addressing spec. of choice. If that spec. doesn’t support ReplyTo then we’re in trouble.

Seems daft to state this explicitly, since unique is unique!

Seems daft to state this explicitly, since unique is unique!

Bryan Murray: “What should be the behavior of the ContextRespondant if it receives a
contentsSet message without ever having sent either a getContents or
setContents message?”

WS-Addressing has the notion of a Fault endpoint that could be used in this case. But I’m not sure how much detail we’d want to go into anyway, since potentially any message can always be received by any endpoint (in any specification!)

Bryan Murray: “Section 5.2, para above "begin": it says that an endpoint address is
exchanged during each operation. However, there is no description as to
how this is done. The WSDL does not contain any clues to this either.
Additional text is needed here. The same text should probably also be in
section 3.”

Now this was in the AssertionType in the “good old days”. Greg, can you provide some text now?