An OASIS White Paper

WS-RX TC Interop Scenarios

Scenarios for demonstrating WS-RM implementations

1/12/2006 Revision

By 
For OASIS

OASIS (Organization for the Advancement of Structured Information Standards) is a not-for-profit, international consortium that drives the development, convergence, and adoption of e-business standards. Members themselves set the OASIS technical agenda, using a lightweight, open process expressly designed to promote industry consensus and unite disparate efforts. The consortium produces open standards for Web services, security, e-business, and standardization efforts in the public sector and for application-specific markets. OASIS was founded in 1993. More information can be found on the OASIS website at http://www.oasis-open.org.

The purpose of the OASIS WS-RX TC is to define a protocol for reliable message exchanges between two Web services, through continued development of the Web Services Reliable Messaging specification.

Table of Contents

Introduction	4

Namespaces	4

Application Scenarios	5

One-Way Ping without RM	5

Req/Resp echoString without RM	5

Reliable Messaging Scenarios	7

Scenario 1.1 One-Way, Anonymous Client	7

Scenario 1.2 No App Messages	9

Scenario 1.3 Close Incomplete Sequence	11

Scenario 1.4 One-Way, Addressable Client	14

Scenario 2.1 Request-Reply, Addressable Client	17

Scenario 2.2 Request-Reply, Addressable Client, No Offer	22

Scenario 2.3 Request-Reply, Addressable Client, Offer declined	26

Scenario 2.4 Request-Reply, Anonymous Client	31

Secure Reliable Messaging Scenarios	36

Notes	37

# Introduction

This document contains a set of scenarios covering the common uses of the WS-RM protocol for the purposes of promoting the protocol itself and to assess the interoperability between various implementations. The scenarios described herein are not an exhaustive execution of the protocol, the rest of the protocol testing can be left for online interoperability testing and in-house QA by each vendor.

These scenarios also test the composition of WS-RM with WS-Addressing.  In each of these scenarios it is assumed that each participant will randomly disconnect themselves from the network in order to simulate network failures – although only the first RM scenario explicitly calls it out.

## Namespaces

Unless overridden by a namespace declaration inside an XML fragment, this document uses the following namespaces:

| Prefix | Namespace |
| --- | --- |
| s | http://www.w3.org/2003/05/soap-envelope or http://schemas.xmlsoap.org/soap/envelope |
| a | http://schemas.xmlsoap.org/ws/2004/08/addressing |
| r | http://docs.oasis-open.org/ws-rx/wsrm/200510 |

# Application Scenarios

## One-Way Ping without RM

The client sends a Ping application message to a service.

### Ping Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">urn:wsrm:Ping</a:Action>

<a:To s:mustUnderstand="1">

http://server-machine/Ping

</a:To>

</s:Header>

<s:Body>

<Ping xmlns="http://tempuri.org/">

<Text>Ping!</Text>

</Ping>

</s:Body>

</s:Envelope>

## Req/Resp echoString without RM

The client must be addressable and reachable by the service to enable this scenario. The echoString application takes two parameters: a string that will be echoed back to the client and a "sequence" string that will be used to identify, at the application level, which sequence this message is associated with.  The response message MUST contain all of the echo strings for this sequence concatenated together in the order received.

| Message # | Request(echo str, seq str) | Response |
| --- | --- | --- |
| 1 | Hello, Seq-1 | Hello |
| 2 | World, Seq-1 | HelloWorld |
| 3 | Bye, Seq-1 | HelloWorldBye |

### echoString Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">urn:wsrm:EchoString</a:Action>

<a:MessageID>

urn:uuid:db82b0df-3966-476b-b605-e26d9900d538

</a:MessageID>

<a:ReplyTo>

<a:Address>

http://client-machine/echoString

</a:Address>

</a:ReplyTo>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<echoString xmlns="http://tempuri.org/">

<Text>Hello</Text>

<Sequence>Seq-1</Sequence>

</echoString>

</s:Body>

</s:Envelope>

### echoStringResponse Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

urn:wsrm:EchoStringResponse

</a:Action>

<a:RelatesTo>

urn:uuid:db82b0df-3966-476b-b605-e26d9900d538

</a:RelatesTo>

<a:To s:mustUnderstand="1">

http://client-machine/echoString

</a:To>

</s:Header>

<s:Body>

<echoStringResponse xmlns="http://tempuri.org/">

<EchoStringReturn>Hello</EchoStringReturn>

</echoStringResponse>

</s:Body>

</s:Envelope>

# Reliable Messaging Scenarios

## Scenario 1.1 One-Way, Anonymous Client

This scenario exercises the basic form and pattern of reliable message exchange. It uses the synchronous, one-way message exchange pattern to send a Ping application message from a client to a service.

### Message Exchange

The client and service establish a reliable sequence with a CS/CSR handshake. The CreateSequenceResponse is returned on the HTTP response of the CreateSequence HTTP request.  The client may choose to include an optional “Offer” element even though it is not used in this scenario.  If it does, the server must still accept the request.

The client sends a series of one to three Ping messages, each of which carries a string, typically a unique one. Messages differ only by the value of the MessageID header, the presence or absence of the AckRequested indicator, and possibly the body contents.

The server sends back acknowledgements for each sequence message it receives. All acknowledgements are carried on HTTP responses. Each acknowledgement would typically acknowledge the range in the previous acknowledgement plus the message that was sent on the HTTP request – however, it is possible that that will not be the case in case the server decides not to accept the message.  If the server decides to accept the incoming message but does not choose to send back a SequenceAcknowledgement then the HTTP response for that message must be 202 Accepted.

A client may retransmit certain messages as it deems appropriate or as necessary.

Once the client receives an acknowledgement covering the full range of messages it has sent, it sends the TerminateSequence message to the service. The HTTP response for that message must be 202 Accepted.

This scenario calls for two additional steps:

1 – the scenario is started with one, or both, of the participants disconnected

2 – during the running of the scenario one, or both, of the participants will disconnect themselves

in order to simulate network failures.

The ReplyTo and the AcksTo EPRs must both be anonymous.

#### CreateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequence

</a:Action>

<a:ReplyTo>

<a:Address>

http://schemas.xmlsoap.org/ws/2004/08/addressing/role/anonymous

</a:Address>

</a:ReplyTo>

<a:MessageID>

urn:uuid:addabbbf-60cb-44d3-8c5b-9e0841629a36

</a:MessageID>

<a:To s:mustUnderstand="1">

http://server-machine/Ping

</a:To>

</s:Header>

<s:Body>

<r:CreateSequence>

<r:AcksTo>

<a:Address>

http://schemas.xmlsoap.org/ws/2004/08/addressing/role/anonymous

</a:Address>

</r:AcksTo>

</r:CreateSequence>

</s:Body>

</s:Envelope>

#### CreateSequenceResponse Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequenceResponse

</a:Action>

<a:RelatesTo>

urn:uuid:addabbbf-60cb-44d3-8c5b-9e0841629a36

</a:RelatesTo>

<a:To s:mustUnderstand="1">

http://schemas.xmlsoap.org/ws/2004/08/addressing/role/anonymous

</a:To>

</s:Header>

<s:Body>

<r:CreateSequenceResponse>

<r:Identifier>

urn:uuid:0afb8d36-bf26-4776-b8cf-8c91fddb5496

</r:Identifier>

</r:CreateSequenceResponse>

</s:Body>

</s:Envelope>

#### Ping Message Example

<s:Envelope>

<s:Header>

<r:Sequence s:mustUnderstand="1">

<r:Identifier>

urn:uuid:0afb8d36-bf26-4776-b8cf-8c91fddb5496

</r:Identifier>

<r:MessageNumber>1</r:MessageNumber>

</r:Sequence>

<a:Action s:mustUnderstand="1">urn:wsrm:Ping</a:Action>

<a:To s:mustUnderstand="1">

http://server-machine/Ping

</a:To>

</s:Header>

<s:Body>

<Ping xmlns="http://tempuri.org/">

<Text>Ping!</Text>

</Ping>

</s:Body>

</s:Envelope>

#### SequenceAcknowledgement Message Example

<s:Envelope>

<s:Header>

<r:SequenceAcknowledgement>

<r:Identifier>

urn:uuid:0afb8d36-bf26-4776-b8cf-8c91fddb5496

</r:Identifier>

<r:AcknowledgementRange Lower="1" Upper="1" />

</r:SequenceAcknowledgement>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/SequenceAcknowledgement

</a:Action>

<a:To s:mustUnderstand="1">

http://schemas.xmlsoap.org/ws/2004/08/addressing/role/anonymous

</a:To>

</s:Header>

<s:Body></s:Body>

</s:Envelope>

#### TerminateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/TerminateSequence

</a:Action>

<a:To s:mustUnderstand="1">

http://server-machine/Ping

</a:To>

</s:Header>

<s:Body>

<r:TerminateSequence>

<r:Identifier>

urn:uuid:0afb8d36-bf26-4776-b8cf-8c91fddb5496

</r:Identifier>

</r:TerminateSequence>

</s:Body>

</s:Envelope>

## Scenario 1.2 No App Messages

This scenario is a variant of 1.1 in which the sequence is terminated before any application messages are sent. The intention of this scenario is to test the new acknowledgement type wsrm:None.

### Message Exchange

The client and service establish a reliable sequence with a CS/CSR handshake. The CreateSequenceResponse is returned on the HTTP response of the CreateSequence HTTP request.

The client will send an AckRequested to the service without having sent any messages; the service should respond with a sequence acknowledgement that no messages have been received.

Once the client receives an acknowledgement covering the range of messages it has sent, it sends the TerminateSequence message to the service. The HTTP response for that message should be 202 Accepted.

The ReplyTo and the AcksTo EPRs must both be anonymous.

#### CreateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequence

</a:Action>

<a:ReplyTo>

<a:Address>

http://schemas.xmlsoap.org/ws/2004/08/addressing/role/anonymous

</a:Address>

</a:ReplyTo>

<a:MessageID>

urn:uuid:addabbbf-60cb-44d3-8c5b-9e0841629a36

</a:MessageID>

<a:To s:mustUnderstand="1">

http://server-machine/Ping

</a:To>

</s:Header>

<s:Body>

<r:CreateSequence>

<r:AcksTo>

<a:Address>

http://schemas.xmlsoap.org/ws/2004/08/addressing/role/anonymous

</a:Address>

</r:AcksTo>

</r:CreateSequence>

</s:Body>

</s:Envelope>

#### CreateSequenceResponse Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequenceResponse

</a:Action>

<a:RelatesTo>

urn:uuid:addabbbf-60cb-44d3-8c5b-9e0841629a36

</a:RelatesTo>

<a:To s:mustUnderstand="1">

http://schemas.xmlsoap.org/ws/2004/08/addressing/role/anonymous

</a:To>

</s:Header>

<s:Body>

<r:CreateSequenceResponse>

<r:Identifier>

urn:uuid:0afb8d36-bf26-4776-b8cf-8c91fddb5496

</r:Identifier>

</r:CreateSequenceResponse>

</s:Body>

</s:Envelope>

#### AckRequested Message Example

<s:Envelope>

<s:Header>

<r:AckRequested>

<r:Identifier>

urn:uuid:c5fe4fe1-c9c3-447e-af87-0406e049a86b

</r:Identifier>

</r:AckRequested>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/AckRequested

</a:Action>

<a:To s:mustUnderstand="1">

http://server-machine/Ping

</a:To>

</s:Header>

<s:Body/>

#### </s:Envelope>

#### SequenceAcknowledgement Message Example

<s:Envelope>

<s:Header>

<r:SequenceAcknowledgement>

<r:Identifier>

urn:uuid:0afb8d36-bf26-4776-b8cf-8c91fddb5496

</r:Identifier>

<r:None/>

</r:SequenceAcknowledgement>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/SequenceAcknowledgement

</a:Action>

<a:To s:mustUnderstand="1">

http://schemas.xmlsoap.org/ws/2004/08/addressing/role/anonymous

</a:To>

</s:Header>

<s:Body/>

</s:Envelope>

#### TerminateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/TerminateSequence

</a:Action>

<a:To s:mustUnderstand="1">

http://server-machine/Ping

</a:To>

</s:Header>

<s:Body>

<r:TerminateSequence>

<r:Identifier>

urn:uuid:0afb8d36-bf26-4776-b8cf-8c91fddb5496

</r:Identifier>

</r:TerminateSequence>

</s:Body>

</s:Envelope>

## Scenario 1.3 Close Incomplete Sequence

This scenario is a variant of 1.1 in which the sequence is closed before the full range of messages has been acknowledged. This tests the new Close mechanism.

### Message Exchange

The client and service establish a reliable sequence with a CS/CSR handshake. The CreateSequenceResponse is returned on the HTTP response of the CreateSequence HTTP request.

The client sends a series of two Ping messages, each of which carries a string, typically a unique one. Messages differ only by the value of the MessageID header, the presence or absence of the AckRequested indicator, and possibly the body contents. The message numbers for these two messages are 1 and 3 introducing a gap in the sequence.

The server sends back acknowledgements for each sequence message it receives. All acknowledgements are carried on HTTP responses. Each acknowledgement would typically acknowledge the range in the previous acknowledgement plus the message that was sent on the HTTP request – however, it is possible that that will not be in the case in case the server decides not to accept the message.

Once the client receives an acknowledgement for messages 1 and 3, it sends the CloseSequence message. Upon verifying the final acknowledgement range included on the CloseSequnceResponse message the client sends the TerminateSequence message to the service. The HTTP response for that message should be 202 Accepted.

The ReplyTo and the AcksTo EPRs must both be anonymous.

#### CreateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequence

</a:Action>

<a:ReplyTo>

<a:Address>

http://schemas.xmlsoap.org/ws/2004/08/addressing/role/anonymous

</a:Address>

</a:ReplyTo>

<a:MessageID>

urn:uuid:addabbbf-60cb-44d3-8c5b-9e0841629a36

</a:MessageID>

<a:To s:mustUnderstand="1">

http://server-machine/Ping

</a:To>

</s:Header>

<s:Body>

<r:CreateSequence>

<r:AcksTo>

<a:Address>

http://schemas.xmlsoap.org/ws/2004/08/addressing/role/anonymous

</a:Address>

</r:AcksTo>

</r:CreateSequence>

</s:Body>

</s:Envelope>

#### CreateSequenceResponse Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequenceResponse

</a:Action>

<a:RelatesTo>

urn:uuid:addabbbf-60cb-44d3-8c5b-9e0841629a36

</a:RelatesTo>

<a:To s:mustUnderstand="1">

http://schemas.xmlsoap.org/ws/2004/08/addressing/role/anonymous

</a:To>

</s:Header>

<s:Body>

<r:CreateSequenceResponse>

<r:Identifier>

urn:uuid:0afb8d36-bf26-4776-b8cf-8c91fddb5496

</r:Identifier>

</r:CreateSequenceResponse>

</s:Body>

</s:Envelope>

#### Ping Message Example

<s:Envelope>

<s:Header>

<r:Sequence s:mustUnderstand="1">

<r:Identifier>

urn:uuid:0afb8d36-bf26-4776-b8cf-8c91fddb5496

</r:Identifier>

<r:MessageNumber>1</r:MessageNumber>

</r:Sequence>

<a:Action s:mustUnderstand="1">urn:wsrm:Ping</a:Action>

<a:To s:mustUnderstand="1">

http://server-machine/Ping

</a:To>

</s:Header>

<s:Body>

<Ping xmlns="http://tempuri.org/">

<Text>Ping!</Text>

</Ping>

</s:Body>

</s:Envelope>

#### SequenceAcknowledgement Message Example

<s:Envelope>

<s:Header>

<r:SequenceAcknowledgement>

<r:Identifier>

urn:uuid:0afb8d36-bf26-4776-b8cf-8c91fddb5496

</r:Identifier>

<r:AcknowledgementRange Lower="1" Upper="1" />

</r:SequenceAcknowledgement>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/SequenceAcknowledgement

</a:Action>

<a:To s:mustUnderstand="1">

http://schemas.xmlsoap.org/ws/2004/08/addressing/role/anonymous

</a:To>

</s:Header>

<s:Body></s:Body>

</s:Envelope>

#### CloseSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CloseSequence

</a:Action>

<a:To s:mustUnderstand="1">

http://server-machine/Ping

</a:To>

</s:Header>

<s:Body>

<r:CloseSequence>

<r:Identifier>

urn:uuid:0afb8d36-bf26-4776-b8cf-8c91fddb5496

</r:Identifier>

</r:CloseSequence>

</s:Body>

</s:Envelope>

#### CloseSequenceResponse Message Example

<s:Envelope>

<s:Header>

<r:SequenceAcknowledgement>

<r:Identifier>

urn:uuid:0afb8d36-bf26-4776-b8cf-8c91fddb5496

</r:Identifier>

<r:AcknowledgementRange Lower="1" Upper="1" />

<r:AcknowledgementRange Lower="3" Upper="3" />

<r:Final/>

</r:SequenceAcknowledgement>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CloseSequenceResponse

</a:Action>

<a:To s:mustUnderstand="1">

http://schemas.xmlsoap.org/ws/2004/08/addressing/role/anonymous

</a:To>

</s:Header>

<s:Body>

<r:CloseSequenceResponse/>

</s:Body>

</s:Envelope>

#### TerminateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/TerminateSequence

</a:Action>

<a:To s:mustUnderstand="1">

http://server-machine/Ping

</a:To>

</s:Header>

<s:Body>

<r:TerminateSequence>

<r:Identifier>

urn:uuid:0afb8d36-bf26-4776-b8cf-8c91fddb5496

</r:Identifier>

</r:TerminateSequence>

</s:Body>

</s:Envelope>

## Scenario 1.4 One-Way, Addressable Client

This scenario exercises the second most basic form and pattern of reliable message exchange. It uses the asynchronous, one-way message exchange pattern to send a Ping application message from a client to a service.

### Message Exchange

The client and service establish a reliable sequence with a CS/CSR handshake. The CreateSequenceResponse is the first message to be sent on the “back channel.”

All HTTP responses in this scenario – both for the client and the service – are 202 Accepted.

The client sends a series of one to three Ping messages, each of which carries a string, typically a unique one. Messages differ only by the value of the MessageID header, the presence or absence of the AckRequested indicator, and possibly the body contents.

The server sends back acknowledgements for all received messages. The exact number of acknowledgement messages sent back and their location in the overall flow will vary among implementations. The acknowledgement ranges in these acknowledgements may vary, as well.

A client may retransmit certain messages as it deems appropriate or as necessary.

Once the client receives an acknowledgement covering the full range of messages it has sent, it sends a TerminateSequence message to the service.

The ReplyTo and the AcksTo EPRs must not be anonymous and must be reachable by the service. The service must send its messages on a separate HTTP channel.

#### CreateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequence

</a:Action>

<a:ReplyTo>

<a:Address>

http://client-machine/Ping

</a:Address>

</a:ReplyTo>

<a:MessageID>

urn:uuid:2a28544b-75d4-4227-ab15-b54cbfc95332

</a:MessageID>

<a:To s:mustUnderstand="1">

http://server-machine/Ping

</a:To>

</s:Header>

<s:Body>

<r:CreateSequence>

<r:AcksTo>

<a:Address>

http://client-machine/Acks

</a:Address>

</r:AcksTo>

</r:CreateSequence>

</s:Body>

</s:Envelope>

#### CreateSequenceResponse Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequenceResponse

</a:Action>

<a:RelatesTo>

urn:uuid:2a28544b-75d4-4227-ab15-b54cbfc95332

</a:RelatesTo>

<a:To s:mustUnderstand="1">

http://client-machine/Ping

</a:To>

</s:Header>

<s:Body>

<r:CreateSequenceResponse>

<r:Identifier>

urn:uuid:c5fe4fe1-c9c3-447e-af87-0406e049a86b

</r:Identifier>

</r:CreateSequenceResponse>

</s:Body>

</s:Envelope>

#### Ping Message Example

<s:Envelope>

<s:Header>

<r:AckRequested>

<r:Identifier>

urn:uuid:c5fe4fe1-c9c3-447e-af87-0406e049a86b

</r:Identifier>

</r:AckRequested>

<r:Sequence s:mustUnderstand="1">

<r:Identifier>

urn:uuid:c5fe4fe1-c9c3-447e-af87-0406e049a86b

</r:Identifier>

<r:MessageNumber>1</r:MessageNumber>

</r:Sequence>

<a:Action s:mustUnderstand="1">urn:wsrm:Ping</a:Action>

<a:From>

<a:Address>

http://client-machine/Ping

</a:Address>

</a:From>

<a:To s:mustUnderstand="1">

http://server-machine/Ping

</a:To>

</s:Header>

<s:Body>

<Ping xmlns="http://tempuri.org/">

<Text>Ping!!</Text>

</Ping>

</s:Body>

</s:Envelope>

#### Sequence Acknowledgement Message Example

<s:Envelope>

<s:Header>

<r:SequenceAcknowledgement>

<r:Identifier>

urn:uuid:c5fe4fe1-c9c3-447e-af87-0406e049a86b

</r:Identifier>

<r:AcknowledgementRange Lower="1" Upper="1"/>

</r:SequenceAcknowledgement>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/SequenceAcknowledgement

</a:Action>

<a:To s:mustUnderstand="1">

http://client-machine/Acks

</a:To>

</s:Header>

<s:Body></s:Body>

</s:Envelope>

#### TerminateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/TerminateSequence

</a:Action>

<a:From>

<a:Address>

http://client-machine/Ping

</a:Address>

</a:From>

<a:To s:mustUnderstand="1">

http://server-machine/Ping

</a:To>

</s:Header>

<s:Body>

<r:TerminateSequence>

<r:Identifier>

urn:uuid:c5fe4fe1-c9c3-447e-af87-0406e049a86b

</r:Identifier>

</r:TerminateSequence>

</s:Body>

</s:Envelope>

## Scenario 2.1 Request-Reply, Addressable Client

This scenario exercises a more complex WS-RM situation – one that requires a request-reply messaging pattern. The client must be addressable and reachable by the service to enable this scenario. The client sends echoString messages to the service and expects echoStringResponse messages in return.

### Message Exchange

The client and the service establish two WS-RM sequences with a dual CS/CSR handshake (i.e. wsrm:Offer and wsrm:Accept are present).

The client then transmits one to three requests on the client-to-server sequence. The HTTP response is 202 Accepted every time. The final request contains a “last message” indicator and includes the number of messages sent by the client.  Once the requests are processed there, the service replies with an equal number of responses. Note that the client will typically wait for the service to respond before initiating a new request but this is not mandatory.

When acknowledging messages, the client and the service may send stand-alone sequence acknowledgements or piggy-back the SequenceAcknowledgement header on a message that is conveniently being transmitted at the same time or close by.

Once the client receives an acknowledgement acknowledging the entire range of requests it will send a TerminateSequence message to the service and consider the client-to-service sequence complete.

When the service has sent the number of replies indicated in the request message containing the “last message” indicator  and received all of the acknowledgements for those replies it will send a TerminateSequence for the service-to-client sequence to any of the wsa:ReplyTo EPRs used on one of the echoString request messages (Note: This use of TerminateSequence with the wsa:ReplyTo EPR may need additional clarification in the WS-RM specification).

Note:  Pending resolution to issue i090, for the purposes of this interoperability test it is assumed that the RMS will only offer a sequence if it knows that it can process all the replies to the requests it sends on the outbound sequence.  Therefore the RMD can use the offered sequence for all replies to requests on the inbound sequence.

#### CreateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequence

</a:Action>

<a:ReplyTo>

<a:Address>

http://client-machine/RMreplies

</a:Address>

</a:ReplyTo>

<a:MessageID>

urn:uuid:9bddb76a-59cc-4e5b-a792-c6646998bf66

</a:MessageID>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<r:CreateSequence>

<r:AcksTo>

<a:Address>

http://client-machine/Acks

</a:Address>

</r:AcksTo>

<r:Offer>

<r:Identifier>

urn:uuid:5f7d5761-d6f7-446f-bea6-989a926ae712

</r:Identifier>

</r:Offer>

</r:CreateSequence>

</s:Body>

</s:Envelope>

#### CreateSequenceResponse Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequenceResponse

</a:Action>

<a:RelatesTo>

urn:uuid:9bddb76a-59cc-4e5b-a792-c6646998bf66

</a:RelatesTo>

<a:To s:mustUnderstand="1">

http://client-machine/RMreplies

</a:To>

</s:Header>

<s:Body>

<r:CreateSequenceResponse>

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

<r:Accept>

<r:AcksTo>

<a:Address>

http://server-machine/echoString

</a:Address>

</r:AcksTo>

</r:Accept>

</r:CreateSequenceResponse>

</s:Body>

</s:Envelope>

#### EchoString Message Example

<s:Envelope>

<s:Header>

<r:AckRequested>

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

</r:AckRequested>

<r:Sequence s:mustUnderstand="1">

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

<r:MessageNumber>1</r:MessageNumber>

</r:Sequence>

<a:Action s:mustUnderstand="1">urn:wsrm:EchoString</a:Action>

<a:MessageID>

urn:uuid:db82b0df-3966-476b-b605-e26d9900d538

</a:MessageID>

<a:ReplyTo>

<a:Address>

http://client-machine/replies

</a:Address>

</a:ReplyTo>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<echoString xmlns="http://tempuri.org/">

<Text>Hello</Text>

<Sequence>Seq-1</Sequence>

</echoString>

</s:Body>

</s:Envelope>

#### EchoString “last message” Message Example

<s:Envelope>

<s:Header>

<r:AckRequested>

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

</r:AckRequested>

<r:Sequence s:mustUnderstand="1">

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

<r:MessageNumber>1</r:MessageNumber>

</r:Sequence>

<a:Action s:mustUnderstand="1">urn:wsrm:EchoString</a:Action>

<a:MessageID>

urn:uuid:db82b0df-3966-476b-b605-e26d9900d538

</a:MessageID>

<a:ReplyTo>

<a:Address>

http://client-machine/replies

</a:Address>

</a:ReplyTo>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<echoString xmlns="http://tempuri.org/">

<Text>Hello</Text>

<Sequence>Seq-1</Sequence>

<LastMessage>3</LastMessage>

</echoString>

</s:Body>

</s:Envelope>

#### EchoStringResponse Message Example

<s:Envelope>

<s:Header>

<r:SequenceAcknowledgement>

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

<r:AcknowledgementRange Lower="1" Upper="1"/>

</r:SequenceAcknowledgement>

<r:AckRequested>

<r:Identifier>

urn:uuid:5f7d5761-d6f7-446f-bea6-989a926ae712

</r:Identifier>

</r:AckRequested>

<r:Sequence s:mustUnderstand="1">

<r:Identifier>

urn:uuid:5f7d5761-d6f7-446f-bea6-989a926ae712

</r:Identifier>

<r:MessageNumber>1</r:MessageNumber>

</r:Sequence>

<a:Action s:mustUnderstand="1">

urn:wsrm:EchoStringResponse

</a:Action>

<a:RelatesTo>

urn:uuid:db82b0df-3966-476b-b605-e26d9900d538

</a:RelatesTo>

<a:To s:mustUnderstand="1">

http://client-machine/replies

</a:To>

</s:Header>

<s:Body>

<echoStringResponse xmlns="http://tempuri.org/">

<EchoStringReturn>Hello</EchoStringReturn>

</echoStringResponse>

</s:Body>

</s:Envelope>

#### Client’s Acknowledgement Message Example

<s:Envelope xmlns:s="http://www.w3.org/2003/05/soap-envelope"

xmlns:r="http://docs.oasis-open.org/ws-rx/wsrm/200510"

xmlns:a="http://schemas.xmlsoap.org/ws/2004/08/addressing">

<s:Header>

<r:SequenceAcknowledgement>

<r:Identifier>

urn:uuid:5f7d5761-d6f7-446f-bea6-989a926ae712

</r:Identifier>

<r:AcknowledgementRange Lower="1" Upper="1"/>

</r:SequenceAcknowledgement>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/SequenceAcknowledgement

</a:Action>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body/>

</s:Envelope>

#### Client’s TerminateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/TerminateSequence

</a:Action>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<r:TerminateSequence>

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

</r:TerminateSequence>

</s:Body>

</s:Envelope>

#### Service’s TerminateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/TerminateSequence

</a:Action>

<a:To s:mustUnderstand="1">

http://client-machine/replies

</a:To>

</s:Header>

<s:Body>

<r:TerminateSequence>

<r:Identifier>

urn:uuid:5f7d5761-d6f7-446f-bea6-989a926ae712

</r:Identifier>

</r:TerminateSequence>

</s:Body>

</s:Envelope>

## Scenario 2.2 Request-Reply, Addressable Client, No Offer

This scenario is a variant of 2.1 in which the original sequence is created without the inclusion of the Offer element.

### Message Exchange

As in scenario 2.1 the client and service establish a reliable sequence for the echoString request messages.  Before the server can send the replies back to the client it must establish a new reliable sequence.  It does this with a simplex CS/CSR handshake back to the client.  Note, for our purposes the target EPR used must be the one the wsa:ReplyTo EPRs used in the first echoString request message.  The remaining part of this scenario is the same as scenario 2.1.

#### Client’s CreateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequence

</a:Action>

<a:ReplyTo>

<a:Address>

http://client-machine/RMreplies

</a:Address>

</a:ReplyTo>

<a:MessageID>

urn:uuid:9bddb76a-59cc-4e5b-a792-c6646998bf66

</a:MessageID>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<r:CreateSequence>

<r:AcksTo>

<a:Address>

http://client-machine/Acks

</a:Address>

</r:AcksTo>

</r:CreateSequence>

</s:Body>

</s:Envelope>

#### Service’s CreateSequenceResponse Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequenceResponse

</a:Action>

<a:RelatesTo>

urn:uuid:9bddb76a-59cc-4e5b-a792-c6646998bf66

</a:RelatesTo>

<a:To s:mustUnderstand="1">

http://client-machine/RMreplies

</a:To>

</s:Header>

<s:Body>

<r:CreateSequenceResponse>

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

</r:CreateSequenceResponse>

</s:Body>

</s:Envelope>

#### EchoString Message Example

<s:Envelope>

<s:Header>

<r:AckRequested>

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

</r:AckRequested>

<r:Sequence s:mustUnderstand="1">

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

<r:MessageNumber>1</r:MessageNumber>

</r:Sequence>

<a:Action s:mustUnderstand="1">urn:wsrm:EchoString</a:Action>

<a:MessageID>

urn:uuid:db82b0df-3966-476b-b605-e26d9900d538

</a:MessageID>

<a:ReplyTo>

<a:Address>

http://client-machine/replies

</a:Address>

</a:ReplyTo>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<echoString xmlns="http://tempuri.org/">

<Text>Hello</Text>

<Sequence>Seq-1</Sequence>

</echoString>

</s:Body>

</s:Envelope>

#### EchoString “last message” Message Example

<s:Envelope>

<s:Header>

<r:AckRequested>

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

</r:AckRequested>

<r:Sequence s:mustUnderstand="1">

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

<r:MessageNumber>1</r:MessageNumber>

</r:Sequence>

<a:Action s:mustUnderstand="1">urn:wsrm:EchoString</a:Action>

<a:MessageID>

urn:uuid:db82b0df-3966-476b-b605-e26d9900d538

</a:MessageID>

<a:ReplyTo>

<a:Address>

http://client-machine/replies

</a:Address>

</a:ReplyTo>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<echoString xmlns="http://tempuri.org/">

<Text>Hello</Text>

<Sequence>Seq-1</Sequence>

<LastMessage>3</LastMessage>

</echoString>

</s:Body>

</s:Envelope>

#### Service’s CreateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequence

</a:Action>

<a:ReplyTo>

<a:Address>

http://server-machine/echoString

</a:Address>

</a:ReplyTo>

<a:MessageID>

urn:uuid:77ddb76a-59cc-4e5b-a792-c6646998bf77

</a:MessageID>

<a:To s:mustUnderstand="1">

http://client-machine/replies

</a:To>

</s:Header>

<s:Body>

<r:CreateSequence>

<r:AcksTo>

<a:Address>

http://server-machine/echoString

</a:Address>

</r:AcksTo>

</r:CreateSequence>

</s:Body>

</s:Envelope>

#### Client’s CreateSequenceResponse Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequenceResponse

</a:Action>

<a:RelatesTo>

urn:uuid:77ddb76a-59cc-4e5b-a792-c6646998bf77

</a:RelatesTo>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<r:CreateSequenceResponse>

<r:Identifier>

urn:uuid:990ba104-815c-4d83-b2bb-47670a5f8099

</r:Identifier>

</r:CreateSequenceResponse>

</s:Body>

</s:Envelope>

#### EchoStringResponse Message Example

<s:Envelope>

<s:Header>

<r:SequenceAcknowledgement>

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

<r:AcknowledgementRange Lower="1" Upper="1"/>

</r:SequenceAcknowledgement>

<r:AckRequested>

<r:Identifier>

urn:uuid:990ba104-815c-4d83-b2bb-47670a5f8099

</r:Identifier>

</r:AckRequested>

<r:Sequence s:mustUnderstand="1">

<r:Identifier>

urn:uuid:990ba104-815c-4d83-b2bb-47670a5f8099

</r:Identifier>

<r:MessageNumber>1</r:MessageNumber>

</r:Sequence>

<a:Action s:mustUnderstand="1">

urn:wsrm:EchoStringResponse

</a:Action>

<a:RelatesTo>

urn:uuid:db82b0df-3966-476b-b605-e26d9900d538

</a:RelatesTo>

<a:To s:mustUnderstand="1">

http://client-machine/replies

</a:To>

</s:Header>

<s:Body>

<echoStringResponse xmlns="http://tempuri.org/">

<EchoStringReturn>Hello</EchoStringReturn>

</echoStringResponse>

</s:Body>

</s:Envelope>

#### Client’s Acknowledgement Message Example

<s:Envelope xmlns:s="http://www.w3.org/2003/05/soap-envelope"

xmlns:r="http://docs.oasis-open.org/ws-rx/wsrm/200510"

xmlns:a="http://schemas.xmlsoap.org/ws/2004/08/addressing">

<s:Header>

<r:SequenceAcknowledgement>

<r:Identifier>

urn:uuid:990ba104-815c-4d83-b2bb-47670a5f8099

</r:Identifier>

<r:AcknowledgementRange Lower="1" Upper="1"/>

</r:SequenceAcknowledgement>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/SequenceAcknowledgement

</a:Action>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body/>

</s:Envelope>

#### Client’s TerminateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/TerminateSequence

</a:Action>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<r:TerminateSequence>

<r:Identifier>

urn:uuid:5f7d5761-d6f7-446f-bea6-989a926ae712

</r:Identifier>

</r:TerminateSequence>

</s:Body>

</s:Envelope>

#### Service’s TerminateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/TerminateSequence

</a:Action>

<a:To s:mustUnderstand="1">

http://client-machine/replies

</a:To>

</s:Header>

<s:Body>

<r:TerminateSequence>

<r:Identifier>

urn:uuid:990ba104-815c-4d83-b2bb-47670a5f8099

</r:Identifier>

</r:TerminateSequence>

</s:Body>

</s:Envelope>

## Scenario 2.3 Request-Reply, Addressable Client, Offer declined

This scenario is a variant of 2.1 in which the original sequence is created without accepting the Sequence contained in the Offer element.

### Message Exchange

As in scenario 2.1 the client and service establish a reliable sequence for the echoString request messages.  Before the server can send the replies back to the client it must establish a new reliable sequence.  It does this with a simplex CS/CSR handshake back to the client.  Note, for our purposes the target EPR used must be the one the wsa:ReplyTo EPRs used in the first echoString request message.  The remaining part of this scenario is the same as scenario 2.1.

#### Client’s CreateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequence

</a:Action>

<a:ReplyTo>

<a:Address>

http://client-machine/RMreplies

</a:Address>

</a:ReplyTo>

<a:MessageID>

urn:uuid:9bddb76a-59cc-4e5b-a792-c6646998bf66

</a:MessageID>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<r:CreateSequence>

<r:AcksTo>

<a:Address>

http://client-machine/Acks

</a:Address>

</r:AcksTo>

<r:Offer>

<r:Identifier>

urn:uuid:5f7d5761-d6f7-446f-bea6-989a926ae712

</r:Identifier>

</r:Offer>

</r:CreateSequence>

</s:Body>

</s:Envelope>

#### Service’s CreateSequenceResponse Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequenceResponse

</a:Action>

<a:RelatesTo>

urn:uuid:9bddb76a-59cc-4e5b-a792-c6646998bf66

</a:RelatesTo>

<a:To s:mustUnderstand="1">

http://client-machine/RMreplies

</a:To>

</s:Header>

<s:Body>

<r:CreateSequenceResponse>

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

</r:CreateSequenceResponse>

</s:Body>

</s:Envelope>

#### EchoString Message Example

<s:Envelope>

<s:Header>

<r:AckRequested>

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

</r:AckRequested>

<r:Sequence s:mustUnderstand="1">

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

<r:MessageNumber>1</r:MessageNumber>

</r:Sequence>

<a:Action s:mustUnderstand="1">urn:wsrm:EchoString</a:Action>

<a:MessageID>

urn:uuid:db82b0df-3966-476b-b605-e26d9900d538

</a:MessageID>

<a:ReplyTo>

<a:Address>

http://client-machine/replies

</a:Address>

</a:ReplyTo>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<echoString xmlns="http://tempuri.org/">

<Text>Hello</Text>

<Sequence>Seq-1</Sequence>

</echoString>

</s:Body>

</s:Envelope>

#### Service’s CreateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequence

</a:Action>

<a:ReplyTo>

<a:Address>

http://server-machine/echoString

</a:Address>

</a:ReplyTo>

<a:MessageID>

urn:uuid:77ddb76a-59cc-4e5b-a792-c6646998bf77

</a:MessageID>

<a:To s:mustUnderstand="1">

http://client-machine/replies

</a:To>

</s:Header>

<s:Body>

<r:CreateSequence>

<r:AcksTo>

<a:Address>

http://server-machine/echoString

</a:Address>

</r:AcksTo>

</r:CreateSequence>

</s:Body>

</s:Envelope>

#### Client’s CreateSequenceResponse Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequenceResponse

</a:Action>

<a:RelatesTo>

urn:uuid:77ddb76a-59cc-4e5b-a792-c6646998bf77

</a:RelatesTo>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<r:CreateSequenceResponse>

<r:Identifier>

urn:uuid:990ba104-815c-4d83-b2bb-47670a5f8099

</r:Identifier>

</r:CreateSequenceResponse>

</s:Body>

</s:Envelope>

#### EchoStringResponse Message Example

<s:Envelope>

<s:Header>

<r:SequenceAcknowledgement>

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

<r:AcknowledgementRange Lower="1" Upper="1"/>

</r:SequenceAcknowledgement>

<r:AckRequested>

<r:Identifier>

urn:uuid:990ba104-815c-4d83-b2bb-47670a5f8099

</r:Identifier>

</r:AckRequested>

<r:Sequence s:mustUnderstand="1">

<r:Identifier>

urn:uuid:990ba104-815c-4d83-b2bb-47670a5f8099

</r:Identifier>

<r:MessageNumber>1</r:MessageNumber>

</r:Sequence>

<a:Action s:mustUnderstand="1">

urn:wsrm:EchoStringResponse

</a:Action>

<a:RelatesTo>

urn:uuid:db82b0df-3966-476b-b605-e26d9900d538

</a:RelatesTo>

<a:To s:mustUnderstand="1">

http://client-machine/replies

</a:To>

</s:Header>

<s:Body>

<echoStringResponse xmlns="http://tempuri.org/">

<EchoStringReturn>Hello</EchoStringReturn>

</echoStringResponse>

</s:Body>

</s:Envelope>

#### EchoString “last message” Message Example

<s:Envelope>

<s:Header>

<r:AckRequested>

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

</r:AckRequested>

<r:Sequence s:mustUnderstand="1">

<r:Identifier>

urn:uuid:3c0ba104-815c-4d83-b2bb-47670a5f8083

</r:Identifier>

<r:MessageNumber>1</r:MessageNumber>

</r:Sequence>

<a:Action s:mustUnderstand="1">urn:wsrm:EchoString</a:Action>

<a:MessageID>

urn:uuid:db82b0df-3966-476b-b605-e26d9900d538

</a:MessageID>

<a:ReplyTo>

<a:Address>

http://client-machine/replies

</a:Address>

</a:ReplyTo>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<echoString xmlns="http://tempuri.org/">

<Text>Hello</Text>

<Sequence>Seq-1</Sequence>

<LastMessage>3</LastMessage>

</echoString>

</s:Body>

</s:Envelope>

#### Client’s Acknowledgement Message Example

<s:Envelope xmlns:s="http://www.w3.org/2003/05/soap-envelope"

xmlns:r="http://docs.oasis-open.org/ws-rx/wsrm/200510"

xmlns:a="http://schemas.xmlsoap.org/ws/2004/08/addressing">

<s:Header>

<r:SequenceAcknowledgement>

<r:Identifier>

urn:uuid:990ba104-815c-4d83-b2bb-47670a5f8099

</r:Identifier>

<r:AcknowledgementRange Lower="1" Upper="1"/>

</r:SequenceAcknowledgement>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/SequenceAcknowledgement

</a:Action>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body/>

</s:Envelope>

#### Client’s TerminateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/TerminateSequence

</a:Action>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<r:TerminateSequence>

<r:Identifier>

urn:uuid:5f7d5761-d6f7-446f-bea6-989a926ae712

</r:Identifier>

</r:TerminateSequence>

</s:Body>

</s:Envelope>

#### Service’s TerminateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/TerminateSequence

</a:Action>

<a:To s:mustUnderstand="1">

http://client-machine/replies

</a:To>

</s:Header>

<s:Body>

<r:TerminateSequence>

<r:Identifier>

urn:uuid:990ba104-815c-4d83-b2bb-47670a5f8099

</r:Identifier>

</r:TerminateSequence>

</s:Body>

</s:Envelope>

## Scenario 2.4 Request-Reply, Anonymous Client

The application level aspects of this scenario are identical to those of the other Request-Reply scenarios – the client and the service use a request-reply messaging pattern to exchange messages.

In this scenario, however, the client is unreachable by the service. As a result, the service must use the HTTP response for all outgoing messages – whether they are application level or infrastructure level. The fact the client is anonymous makes this case especially interesting mainly because the service must rely on the client to make a call in order to be able to respond with a message of its own.

### Message Exchange

The client and the service establish two WS-RM sequences with a dual CS/CSR handshake (i.e. wsrm:Offer and wsrm:Accept are present). The CSR is carried on the HTTP response.

The client then transmits one to three requests on the client-to-server sequence. The HTTP response for each request carries:

- The response to that particular request.

- A “piggy-backed” SequenceAcknowledgement header acknowledging the current known state at the receiver.

Each request, except for the first one, also carries a piggy-backed acknowledgement acknowledging all the responses the client has received at the point the request was made.

Once the client received acknowledgements and responses for all its requests, it sends a TerminateSequence message to the service and considers the client-to-service sequence complete. The TerminateSequence message “piggy-backs” a SequenceAcknowledgement header acknowledging the entire range of responses the client received. Upon receiving the TerminateSequence, the service responds with a TerminateSequence of its own – for the service-to-client sequence – and considers that sequence complete.

If a reply never comes back and the HTTP request times out or aborts, the client must always retransmit that request. If the service already responded to an incoming request with a given message number, it must respond with a copy of the original reply. As a consequence, a request must be resent to allow for the retransmission of its reply even if the request has already been acknowledged (by another reply received on a different HTTP connection, for example).

Because the TerminateSequence message carries data critical to the graceful shutdown of the service-to-client sequence, the client must attempt to retransmit the message if it fails to receive a response. The client does, however, consider its sequence complete regardless of the reply it receives. On the other hand, a service will consider its sequence gracefully shutdown only once it has received all the acknowledgements and the TerminateSequence from the client. It just so happens that the full acknowledgement range and the TerminateSequence are part of the same message.

#### CreateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequence

</a:Action>

<a:MessageID>

urn:uuid:ecd75878-45a0-41db-a358-960969467056

</a:MessageID>

<a:ReplyTo>

<a:Address>

http://schemas.xmlsoap.org/ws/2004/08/addressing/role/anonymous

</a:Address>

</a:ReplyTo>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<r:CreateSequence>

<r:AcksTo>

<a:Address>

http://schemas.xmlsoap.org/ws/2004/08/addressing/role/anonymous

</a:Address>

</r:AcksTo>

<r:Offer>

<r:Identifier>

urn:uuid:a721a819-35ea-436b-8106-fdcd317016c7

</r:Identifier>

</r:Offer>

</r:CreateSequence>

</s:Body>

</s:Envelope>

#### CreateSequenceResponse Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/CreateSequenceResponse

</a:Action>

<a:RelatesTo>

urn:uuid:ecd75878-45a0-41db-a358-960969467056

</a:RelatesTo>

</s:Header>

<s:Body>

<r:CreateSequenceResponse>

<r:Identifier>

urn:uuid:2c8e5a86-abae-4dc6-960e-41c914228b03

</r:Identifier>

<r:Accept>

<r:AcksTo>

<a:Address>

http://server-machine/echoString

</a:Address>

</r:AcksTo>

</r:Accept>

</r:CreateSequenceResponse>

</s:Body>

</s:Envelope>

#### EchoString Message Example

<s:Envelope>

<s:Header>

<r:Sequence s:mustUnderstand="1">

<r:Identifier>

urn:uuid:2c8e5a86-abae-4dc6-960e-41c914228b03

</r:Identifier>

<r:MessageNumber>1</r:MessageNumber>

</r:Sequence>

<a:Action s:mustUnderstand="1">

urn:wsrm:EchoString

</a:Action>

<a:MessageID>

urn:uuid:baf71839-cb2c-4fd8-99f1-d59bfe8d3aa7

</a:MessageID>

<a:ReplyTo>

<a:Address>

http://schemas.xmlsoap.org/ws/2004/08/addressing/role/anonymous

</a:Address>

</a:ReplyTo>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<echoString xmlns="http://tempuri.org/">

<Text>Hello</Text>

<Sequence>urn:uuid:2c8e5a86-abae-4dc6-960e-41c914228b03</Sequence>

</echoString>

</s:Body>

</s:Envelope>

#### EchoStringResponse Message Example

<s:Envelope>

<s:Header>

<r:Sequence s:mustUnderstand="1">

<r:Identifier>

urn:uuid:a721a819-35ea-436b-8106-fdcd317016c7

</r:Identifier>

<r:MessageNumber>1</r:MessageNumber>

</r:Sequence>

<r:SequenceAcknowledgement>

<r:Identifier>

urn:uuid:2c8e5a86-abae-4dc6-960e-41c914228b03

</r:Identifier>

<r:AcknowledgementRange Lower="1" Upper="1" />

</r:SequenceAcknowledgement>

<a:Action s:mustUnderstand="1">

urn:wsrm:EchoStringResponse

</a:Action>

<a:RelatesTo>

urn:uuid:baf71839-cb2c-4fd8-99f1-d59bfe8d3aa7

</a:RelatesTo>

</s:Header>

<s:Body>

<echoStringResponse xmlns="http://tempuri.org/">

<EchoStringReturn>Hello</EchoStringReturn>

</echoStringResponse>

</s:Body>

</s:Envelope>

#### EchoString Message Example (2)

<s:Envelope>

<s:Header>

<r:SequenceAcknowledgement>

<r:Identifier>

urn:uuid:a721a819-35ea-436b-8106-fdcd317016c7

</r:Identifier>

<r:AcknowledgementRange Lower="1" Upper="1" />

</r:SequenceAcknowledgement>

<r:Sequence s:mustUnderstand="1">

<r:Identifier>

urn:uuid:2c8e5a86-abae-4dc6-960e-41c914228b03

</r:Identifier>

<r:MessageNumber>2</r:MessageNumber>

</r:Sequence>

<a:Action s:mustUnderstand="1">

urn:wsrm:EchoString

</a:Action>

<a:MessageID>

urn:uuid:515df164-45a9-49a9-ba72-8f05bb8b6182

</a:MessageID>

<a:ReplyTo>

<a:Address>

http://schemas.xmlsoap.org/ws/2004/08/addressing/role/anonymous

</a:Address>

</a:ReplyTo>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<echoString xmlns="http://tempuri.org/">

<Text>World</Text>

<Sequence>urn:uuid:2c8e5a86-abae-4dc6-960e-41c914228b03</Sequence>

</echoString>

</s:Body>

</s:Envelope>

#### Client’s TerminateSequence Message Example

<s:Envelope>

<s:Header>

<r:SequenceAcknowledgement>

<r:Identifier>

urn:uuid:a721a819-35ea-436b-8106-fdcd317016c7

</r:Identifier>

<r:AcknowledgementRange Lower="1" Upper="3" />

</r:SequenceAcknowledgement>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/TerminateSequence

</a:Action>

<a:To s:mustUnderstand="1">

http://server-machine/echoString

</a:To>

</s:Header>

<s:Body>

<r:TerminateSequence>

<r:Identifier>

urn:uuid:2c8e5a86-abae-4dc6-960e-41c914228b03

</r:Identifier>

</r:TerminateSequence>

</s:Body>

</s:Envelope>

#### Service’s TerminateSequence Message Example

<s:Envelope>

<s:Header>

<a:Action s:mustUnderstand="1">

http://docs.oasis-open.org/ws-rx/wsrm/200510/TerminateSequence

</a:Action>

</s:Header>

<s:Body>

<r:TerminateSequence>

<r:Identifier>

urn:uuid:a721a819-35ea-436b-8106-fdcd317016c7

</r:Identifier>

</r:TerminateSequence>

</s:Body>

</s:Envelope>

# Secure Reliable Messaging Scenarios

TBD

# Notes