Policy statement combination and reduction using XACML

Working draft 01, 21 March 2003

Document identifier: draft-xacml-wspl-cmbn-01.doc

Location: http://lists.oasis-open.org/archives/xacml/

Send comments to: xacml-comment@lists.oasis-open.org

Editors:

Tim Moses, Entrust (tim.moses@entrust.com)

Contributors:

Anne Anderson, Sun Microsystems

Simon Godik, Overxeer

Abstract:

This working draft describes a technique for combining XACML policy statements and deriving instructions for forming an access request that satisfies the policy.

Status:

This version of the specification is a working draft of the committee.  As such, it is expected to change prior to adoption as an OASIS standard.

If you are on the xacml@lists.oasis-open.org list for committee members, send comments there. If you are not on that list, subscribe to the xacml-comment@lists.oasis-open.org list and send comments there. To subscribe, send an email message to xacml-comment-request@lists.oasis-open.org with the word "subscribe" as the body of the message.

Copyright (C) OASIS Open 2003 All Rights Reserved.

Table of contents

1.	Glossary	3

2.	Introduction	3

3.	Model	3

4.	Combination	4

Step 1 – Combine Conditions	4

Step 2 – Combine Objectives	4

Step 3 – Combine Strategies	4

Step 4 – Combine Predicates	4

5.	Reduction	5

6.	Compilation	6

7.	References	6

Appendix A. Schema	7

Appendix B. Notices	8

# Glossary

Coincidence – A property of pairs of Predicates, Strategies or Objectives that enable them to be combined.

Condition – A conjunctive set of Objectives.

Objective – A disjunctive list of Strategies, in order of preference.

Strategy – A conjunctive set of Predicates.

# Introduction

This document describes a technique for combining XACML <Condition> elements to form a new <Condition> element, such that an access request that satisfies the new <Condition> element also satisfies all the original <Condition> elements.

This document also describes how to “compile” the resulting <Condition> element into a set of instructions for forming a conformant access request.

The requirements for these capabilities are explained in [WSPL Req].

# Model

The technique described here is applicable when the <Condition> element contains a set of one or more Objectives, all of which must be achieved, each Objective can be achieved by any one of one or more Strategies and each Strategy comprises one or more Predicates, all of which must evaluate to “True”.  That is, each <Condition> element is of the form shown in Example 1.

<and> !-- Condition

<or> !—Objective 1

<and> !—Strategy 1

<Predicate 1>

<Predicate 2>

</and>

<and> !—Strategy 2

<Predicate 3>

<predicate 4>

</and>

</or>

<or> !—Objective 2

<and> !—Strategy 3

<Predicate 5>

<Predicate 6>

</and>

<and> !—Strategy 4

<Predicate 7>

<Predicate 8>

</and>

</or>

</and>

Example 1

These restrictions are known to support (at least) the cryptographic-security application domain, which is one of the more complicated application domains.  They are expected to support other application domains as well.

There are three phases to the procedure: Combination, Reduction and Compilation.  These are described in the following sections.

# Combination

These are the steps for combining two policies.  More policies MAY be combined by repeating these steps.  Only <Condition> elements whose associated <Target> elements are identical, and whose parent <Rule> element Effect value is “Permit”, MAY be combined in this way.

## Step 1 – Combine Conditions

Concatenate the two <Condition> elements and delete the “</and><and>” that appears at the join.  The result is a set of Objectives, some pairs of which may coincide.

## Step 2 – Combine Objectives

In this step, coincident pairs of Objectives are identified and combined.  Objectives are said to coincide if one or more of their Strategies coincide (see below).  Coincident Objectives are combined by concatenating them, deleting the “</or><or>” at the join and deleting all non-coincident Strategies.

Note: non-coincident Strategies are not common to both policies.  Therefore, they are not candidate Strategies for interoperation.

## Step 3 – Combine Strategies

In this step, coincident pairs of Strategies within a single Objective are identified and combined.  Strategies are said to coincide if at least one of their Predicates coincide (see below).  Coincident Strategies are combined by concatenating them and deleting the “</and><and>” at the join.

Note: a Strategy may be paired with more than one other Strategy.  However, it is important to choose attribute definitions that do not result in inappropriate pairing of Strategies.

Note: the combining of Strategies may preserve the preferences of only one policy writer.

## Step 4 – Combine Predicates

In this step, coincident pairs of Predicates within a single Strategy are identified and combined, as shown in Table 1.  Predicates are said to coincide if they place constraints on identical attributes.

| One predicate | Other predicate | Success | Replacement predicate |
| --- | --- | --- | --- |
| equal(a,x) | equal(a,y) | x == y | equal(a,x) |
| equal(a,x) | greater-than(a,y) | x > y | equal(a,x) |
| equal(a,x) | greater-than-or-equal(a,y) | x ≥ y | equal(a,x) |
| equal(a,x) | less-than(a,y) | x < y | equal(a,x) |
| equal(a,x) | less-than-or-equal(a,y) | x ≤ y | equal(a,x) |
| greater-than(a,x) | greater-than(a,y) |  | greater-than(a,max(x,y)) |
| greater-than(a,x) | greater-than-or-equal(a,y) |  | greater-than-or-equal(a,max( ( x,y)) |
| greater-than-or-equal(a,x) | greater-than-or-equal(a,y) |  | greater-than-or-equal(a,max(x,y)) |
| less-than(a,x) | less-than(a,y) |  | less-than(a,min(x,y)) |
| less-than(a,x) | less-than-or-equal(a,y) |  | less-than-or-equal(a,min( ( x,y)) |
| less-than-or-equal(a,x) | less-than-or-equal(a,y) |  | less-than-or-equal(a,min(x,y)) |
| greater-than(a,x) | less-than(a,y) | x < y | N/A |
| greater-than(a,x) | less-than-or-equal(a,y) | x < y | N/A |
| greater-than-or-equal(a,x) | less-than(a,y) | x < y | N/A |
| greater-than-or-equal(a,x) | less-than-or-equal(a,y) | x < y | N/A |
| set-equals(a,x) | set-equals(a,y) | x == y | set-equals(a,x) |
| set-equals(a,x) | subset(a,y) | x ⊆ y | set-equals(a,x) |
| subset(a,x) | subset(a,y) | ∩ (x,y) ≠ 0 | subset (a,∩ (x,y)) |

Table 1 - Predicate combination

In the event that any condition shown in the “Success” column is not satisfied, the associated Predicates are incompatible and the <Condition> elements cannot be combined.

In the event that a Predicate contains an expression, then no combination can be performed.  Therefore, it is RECOMMENDED that Predicates contain only literal values.

( means the smallest value greater than.

( means the largest value less than.

∩ means set intersection.

# Reduction

The order of Strategies in each Objective reflects the preferences of the policy writer.  Therefore, the first Strategy of every Objective shall be retained.  All other Strategies shall be deleted.

Then the following substitutions SHALL be made.

| Predicate | Replacement predicate |
| --- | --- |
| greater-than(a,x) | equal(a, ( x) |
| greater-than-or-equal(a,x) | equal(a,x) |
| less-than(a,x) | equal(a, ( x) |
| less-than-or-equal(a,x) | equal(a,x) |
| subset(a,x) | set-equals(a,x) |

Table 2 - Predicate reduction

# Compilation

The resulting <Condition> element MAY be compiled to a set of instructions for creating a conformant request.  The procedure for compilation depends upon the target execution language.

Equality operators shall be converted to “assignment” operators in the target language.

# References

[WSPL Req]  Web-services policy language use-cases and requirements, working draft 01, 7 March 2003.  Located at: http://lists.oasis-open.org/archives/xacml/200303/msg00014.html

Schema

Notices

OASIS takes no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights. Information on OASIS's procedures with respect to rights in OASIS specifications can be found at the OASIS website. Copies of claims of rights made available for publication and any assurances of licenses to be made available, or the result of an attempt made to obtain a general license or permission for the use of such proprietary rights by implementors or users of this specification, can be obtained from the OASIS Executive Director.

OASIS has been notified of intellectual property rights claimed in regard to some or all of the contents of this specification. For more information consult the online list of claimed rights.

OASIS invites any interested party to bring to its attention any copyrights, patents or patent applications, or other proprietary rights which may cover technology that may be required to implement this specification. Please address the information to the OASIS Executive Director.

Copyright (C) OASIS Open 2003. All Rights Reserved.

This document and translations of it may be copied and furnished to others, and derivative works that comment on or otherwise explain it or assist in its implementation may be prepared, copied, published and distributed, in whole or in part, without restriction of any kind, provided that the above copyright notice and this paragraph are included on all such copies and derivative works. However, this document itself may not be modified in any way, such as by removing the copyright notice or references to OASIS, except as needed for the purpose of developing OASIS specifications, in which case the procedures for copyrights defined in the OASIS Intellectual Property Rights document must be followed, or as required to translate it into languages other than English.

The limited permissions granted above are perpetual and will not be revoked by OASIS or its successors or assigns.

This document and the information contained herein is provided on an “AS IS” basis and OASIS DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.